The Branch Box Design

10.03.2020

Alexey Bragin and Mickail Kholopov, BINP

The design of the Branch Box for the CBM and the HADES detectors is shown on the Fig. 1 and Fig. 2. The cryogenic scheme is shown on the Fig. 3 – the colors of the valves on this scheme and the design are the same. .

The temperature sensors are listed in the Tables 1 and 2.

Fig. 1. Design of the Branch Box, first view.

Fig. 2. Design of the Branch Box, second view.

Fig. 3. The Branch Box view.

Fig. 4. The assembled view of the Branch Box. There are 4 safety valves, while 3 on the scheme – do we need the safety valve for HADES cryogenic scheme reasons?

Fig. 5. The assembling part of the Branch Box. The top of the vacuum vessel will be welded after all pipes are assembles as seen here.

Table 1 – the list of the temperature sensors inside the Branch Box

| No | The placement of the temperature sensors | Designation | Serial number, data of calibration (example) |
| --- | --- | --- | --- |
| 1 | The 4.6 K helium from DB2 | BTV101 +1 | D6075405 , 30.10.2018 |
| 2 | The 50 K helium from DB2 | BTV301 +1 | P******9 |
| 3 | The 60 K return helium to DB2 from HADES | T3+1 | P*******0 |
| 4 | The 4.5 K return helium to DB2 from HADES | T4+1 | D******6 |
| 5 | The 4.5 K return helium to DB2 from CBM | T5+1 | D******2 |
| 6 | The 60 K return helium to DB2 from CBM | T6+1 | P******1 |

Total number 6 + 6 (spare for redundancy) = 12.

The D** sensors are special sensors for low temperatures (< 30 K), more expensive than P** sensors.

The P*** sensors are for >50 K temperatures.

Typically, BINP buys the D** sensors mostly uncelebrated. The calibration of these sensors is performed in BINP laboratory inside the cryostat with cryocooler.

Table 2 – the list of the pressure sensors inside the Branch Box

| No | The placement of the pressure sensors | Designation | Serial number, data of calibration (example) |
| --- | --- | --- | --- |
| 1 | The 4.6 K helium from DB2 | BPA101 |  |
| 2 | The 50 K helium from DB2 | BPA301 |  |
| 3 | The 60 K return helium to DB2 from HADES | P3 |  |
| 4 | The 4.5 K return helium to DB2 from HADES | P4 |  |
| 5 | The 4.5 K return helium to DB2 from CBM | P5 |  |
| 6 | The 60 K return helium to DB2 from CBM | P6 |  |