## Slide 1: Central Tracker
Cabling and Mechanics

## Slide 2: STT Layout
21-27 layers, from inner to outer radius:
8 Axial layers
4 Skewed double-layers (±2.89°)
5 Axial layers + 6 axial outer filling layers
2 2050 straws with 1200mm length
2 240 skewed straws with diff. length
4636 straws in total
All straws close-packed with <20µm gaps
Active volume ~ 85% (of cylindr. vol. 160/410mm)
X/X0 ~ 1.25% (2/3 tube wall + 1/3 gas)
One semi-barrel of STT

## Slide 3: Geometrical constraints
The Central Tracker (CT) has to fill a cylindrical volume surrounding the MicroVertex Detector and the target-beam cross pipe.
Geometrical constrains are:
int. Ø 150 mm, ext. Ø 418 mm,
length 1500mm + 150 mm upstream for electronics and services
This volume is split in two halves by the target-beam cross pipe.
150
150mm
4200mm
x
y
z
y
1500mm
150mm

## Slide 4: Present layout
Presently, two options are under developments. Both have to fit the same physical and mechanical requirements. We can therefore figure out a unique mechanical solution.

## Slide 5
Following the idea of a STT made of planar double-layers a Light Mechanical Frame has been designed
If the material of the Support Structure will be Aluminum:
Density 2.7g/cm3
Young’s modulus: 70 GPa
Radiation Length (Xo): 9 cm
Thermal expansion:24 ppm/°C
Total weight of the structure is 8.2 kg
Internal bars can be removed
STT detector assembly

## Slide 6: Support Structure prototype
FEM analysis results:
maximum deflection 0.03 mm

## Slide 7
Band prototypes
STT support frame
Fixing pin

## Slide 8
Some minor refinements have been studied to reinforce the edge bands of the straw modules and to test new fixing tools for the end-plugs
New fixing pin
Notes: Threaded = filettati
Nut = dado

## Slide 11
CENTRAL TRACKER MECHANICS
INFN-LNF - SPAS
-StrawTracker, Vertex Det., Cross Pipe are supported by a CENTRAL SUPPORT FRAME
CENTRAL SUPPORT FRAME PROTOTYPE: DONE !
STRAW SUPPORT FRAME PROTOTYPE: DONE !
AUXILIARY INSERTION STRUCTURE PROTOTYPE: DONE !
VERTEX PROTOTYPE: UNDER DEVELOPMENT;
CROSS-PIPE PROTOTYPE: PLANNED IN THE NEXT MONTHS.

## Slide 12
-CENTRAL SUPPORT FRAME IDEA.
-CENTRAL SUPPORT FRAME PROTOTYPE-
CENTRAL TRACKER MECHANICS
INFN-LNF - SPAS
THE PROTOTYPE OF THE CENTRAL SUPPORT FRAME HAS BEEN REALIZED IN THE INFN TURIN WORKSHOP.

## Slide 13
External support structure for assembly and insertion: Feb 2011
2000mm
1500mm

## Slide 14
-AN AUXILIARY INSERTION STRUCTURE IS NEEDED;
-CENTRAL SUPPOR FRAME PROTOTYPE;
-STRAW SUPPORT FRAME PROTOTYPE.
CENTRAL TRACKER MECHANICS
INFN-LNF - SPAS

## Slide 15
New Layout for Cable Routing after the March 2011 Meeting
Patch Panels
1500mm

## Slide 16: STT Cable Routing system

## Slide 17
Weight and Cabling for one half of STT
-Half STT houses ~2100 straws + preams + HV
• straw weight less than 6 Kg
• frame structure 9 Kg
• 5 kg preamp boards + short cabling, 2100ch × 10cm, + HV
• 5 kg gas manifolds
TOTAL WEIGHT ~ 25 Kg
-FEE boards (discriminators, TDC, …)
• cooling system ?
TOTAL WEIGHT ~ 20 kg?
-10m cables
• gas tubes: 2.7 kg 20 rilsan tubes (10in-10out) (5 mm , ~13.2 g/m, 1× gas line per 100 straws)
• signal cables:17 kg signal coax cables, 2100ch × 10m × 0.5mm 0.83 g/m
• HV cables: 80 kg for 60 HV channels (~1 mainframe), 3.5mm coax 130 g/m
• LV cables: 9.6 kg 64 LV double-cables 2.5mm x 10m 15g/m
TOTAL WEIGHT 100 kg cable weight (20kg/m)
Loads on STT Support Structure
Loads on Routing Support Structure

## Slide 18
5000 mm2
5000 mm2
Cable arrangement

## Slide 19: Electronics arrangement

## Slide 20
1500mm

## Slide 21: Backup

## Slide 25
-“ROUTING SUPPORT STRUCTURE” LOADS ANALYSIS (Loads for 1.5m cables)-
- Gas rilsan tubes: 4 dia.20mm (In-Out Main Lines): -----------------------------0,40Kg
Signal cables: signals coax cables - 2100chx3mx0.5mm: -----------------------2,55Kg
HV Cables: for 60 HV channels - (1 mainframe), 3.5mm coax: -----------------12,0Kg
LV cables: 64 LV double-cables - 2.5mmx5m: ----------------------------------1,50Kg
----------------------------------------------------------------------------------------------
TOTAL: --------------------17,00Kg
-“STT TRACKER” LOADS ANALYSIS (Half STT houses 2600 straws + preams + HV)-
Straw weight: ----------------------------------------------7,5Kg
Frame structure: ------------------------------------------9,0Kg
Preamp board + short cabling – 2600ch x 10cm + HV:---6,0Kg
Gas manifolds: ---------------------------------------------5,0Kg
FEE boards (discriminators, TDC,….): ---------------------?
Cooling system: ---------------------------------------------?
-ANALYSIS FOR AN HALF “SST TRACKER”-
-ANALYSIS FOR AN HALF “SST TRACKER”-
- Needed space: 5000mm^2
- See detailed “constrain reactions”