## Slide 1: Status of the Combined target project and Cryopump developments
Christian Mannweiler
Institut für Kernphysik
WWU
13th June 2023

## Slide 2: Two topics
The Combined target
The Cryopump

## Slide 3: Previously…
We are working on transforming a Cluster-jet target into a pellet target:
 | Cluster-jet target | Droplet/Pellet target
Temperature | 20-50 K | 15-20 K
Gas pressure | 5-18 bar | 0.5-1.5 bar
Nozzle design | Laval nozzle | Aperture
Further requirements |  | Piezo vibrator
Can easily be fulfilled by our pre-existing Cluster-jet target systems
Requires adaptation of our Cluster-jet target system

## Slide 4: Previously…
Simple process:
Only major change is performed at the nozzle system

## Slide 5: Hydrogen pellet generation was achieved
First stable operation (>3h) of the pellet target achieved!
Operational parameters:
  Nozzle diameter: 10µm
  Gas pressure: 0.8 bar
  Nozzle temperature: 16 K
  Piezo frequency: 485,5 kHz
  Pellet diameter: 12 µm (calculated)
However, this success has proven to not be reliably reproducible. There are still several challenges to be overcome

## Slide 6: The Combined target status
There are two major challenges:
  Nozzle clogging
  Transfer of sufficient cooling power to the nozzle

## Slide 7: Nozzle clogging
Issues created by nozzle clogging:
  Frequent disruption of operation, lengthy downtime
    Stable operation periods of months highly desirable for PANDA
  Unstable operating conditions (gas flow, vacuum chamber pressures etc.) greatly increases the difficulty of interpreting operational parameters

## Slide 8: Combatting nozzle clogging
Analysis of the impurities:
  Raman-microspectroscopy (with the kind support of AG Fallnich from the WWU)
10µm

## Slide 9: Nozzle clogging analysis
Raman spectrum is typical for metals but does not allow for more specific identification
Next step: Energy dispersive X-ray spectroscopy
  The nozzle is imaged using electron microscopy
  The characteristic X-ray spectrum is excited by the incident electrons
  Elemental make-up can be determined with high precision

## Slide 10: Nozzle clogging analysis
Raman spectrum is typical for metals but does not allow for more specific identification
Next step: Energy dispersive X-ray spectroscopy
  The nozzle is imaged using electron microscopy
  The characteristic X-ray spectrum is excited by the incident electrons
  Elemental make-up can be determined with high precision

## Slide 11: A first step forward
Before the target is operated it is “cryo flushed“ for several days
Promising increase in stability of the operating conditions
Allows for a better analysis of target parameters

## Slide 12: The Combined target status
There are two major challenges:
  Nozzle clogging
  Transfer of sufficient cooling power to the nozzle

## Slide 13: The cooling issue
Cold stage temperature
Piezo head temperature
As a response, heat shielding was installed around the nozzle

## Slide 14: Installation of heat shielding
Recent measurements have shown that this is not enough to cool down a completely free nozzle

## Slide 15: The cooling issue
The target has issues crossing the vapour curve
Even a slight improvement in the chamber pressure can help.

## Slide 16: The next steps
The experimental setup is currently being reworked
  Installation of additional pumping power (~factor 10 better vacuum)
  Test of the pumping station for the new beam dump
Further tests with cold flushing
Redesign of the piezo head

## Slide 17: Two topics
The Combined target
The Cryopump

## Slide 18: Location of the Cryopump
IP
Cryopump position
anti-proton beam
≈3m

## Slide 19: Status of the cryopump
Basic design is completed

## Slide 20: Status of the cryopump
Basic design is completed
Pump is designed to be modular
Technical drawings are currently in progress

## Slide 21: Thank you for your attention