## Slide 1
(High-Intensity heavy ion Accelerator Facility)
Guodong Shen
On behalf of HIAF Design Group
Institute of Modern Physics (IMP)
Chinese Academy of Sciences (CAS)
Feb. 14, 2024
Challenges and status of HIAF
5th Slow Extraction Workshop
in China

## Slide 2
Outline
Brief introduction to the HIAF
Challenges and key components
Present status and schedule
Summary
Notes: In my talk, I will give a brief introduction of HIAF project. The major challenges and development of key components will be reported. And then the status of series production and the schedule in the coming years. Finally a short summary will be presented.

## Slide 3
To explore the limit of nuclear existence
To study exotic nuclear structure
To understand the origin of the elements
To study the properties of High Energy
and Density Matter
……
SPIRAL2 at GANIL in Caen, France
FAIR at GSI in Darmstadt, Germany
FRIB at MSU in the U.S.
NICA at JINR, Dubna, Russia
EURISOL in Europe
High Intensity Heavy-ion
Accelerator Facility
HIAF in China
Available today
Fascinating and crucial questions
Next-generation facilities being constructed or proposed worldwide:
Brief introduction to the HIAF

## Slide 4
High Intensity Heavy-ion Accelerator Facility (HIAF)
Brief introduction to the HIAF
iLinac: Superconducting linac
Length:100 m
Energy: 17 MeV/u(U35+), 48MeV/u(H2+)
HFRS: Fragment Separator
Length: 192 m
Rigidity: 25 Tm
Pre + Main separator
resolution power: 1100
SECR: Super-conducting ECR Ion Source
Energy: 14keV/u
RF frequency: 45GHz
The 4th generation SC ECR Ion Source
0.05pmA 238U35+
SRing: Spectrometer ring
Circumference: 277.3m
Rigidity: 13-15 Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
BRing: Booster ring
Circumference: 569.1 m
Rigidity: 34 Tm
High intensity (238U35+,1e11 ppp)
Two planes painting injection
Fast ramping rate（3Hz）
High Energy Multi-disciplinary Terminal
External Target Terminal
Low Energy Multi-disciplinary Terminal
High Energy Density Terminal

## Slide 5
HIAF main parameters
To provide very high intensity heavy ion beam
Brief introduction to the HIAF
 | SECR | iLinac | BRing | HFRS | SRing
Length / circumference (m) | --- | 114 | 569.1 | 192 | 277.3
Final energy of U (MeV/u) | 0.014 (U35+) | 17 (U35+) | 835 (U35+) | 800 (U92+) | 800 (U92+)
Max. magnetic rigidity (Tm) | --- | --- | 34 | 25 | 15
Max. beam intensity of U | 50 pμA (U35+) | 28 pμA (U35+) | (1~2)1011ppp (U35+) | ------- | (2~5) 1011ppp (U92+)
Operation mode | DC | CW or pulse | fast ramping (12T/s, 3Hz) | Momentum-resolution 1100 | DC, deceleration
Emittance or Acceptance (H/V, ·mm·mrad, dp/p) |  | 5 / 5 | 200/100, 0.5% | 30mrad(H)/15 mrad(V), 2% | 40/40, 1.5% (normal mode)
High intensity beam preparation remains a top priority of dynamics research.

## Slide 6
Issue 1: How to accumulate high intensity heavy ions in BRing?
Challenges:
High Injection Gain (>56 to achieve 1e11 for U35+)
Low beam loss (<5% due to dynamic vacuum)
Solution:
Two-plane painting injection exploits H&V phase space to improve injection gain.
Emittance increases following correlated painting arise lots of aperture loss.
An elaborate injection parameters optimization and artful ES collimator is essential to fulfill the design requirement.
100 turn
Gain = 60
Uncontrolled loss = 2.1%
Challenges and key components
Ions | Plane | Gain | Intensity W/O SC
238U35+ | H | 26 | 4.61010
 | V | 13 | 2.31010
 | H+V | 80~100 | (1.4~1.8)1011
Hollow phase space
→ emittance increasement
ES collimator

## Slide 7
Issue 2: How to deal with serious beam loss?
Challenges:
Space Charge effect, dynamic vacuum effect and collective instability dominate intensity limitation.
A dedicated simulation platform CISP-GPU is developed for coupling high intensity dynamics research.
Stabilization efforts are performed to achieve the intensity goal.
Challenges and key components
tune scan with SC and real magnet
loss distribution of dynamic vacuum
stabilization of collective instability
Fast ramping (12T/s) is essential to suppress beam loss. High performance requirement to power supply, RF system and vacuum chamber.

## Slide 8
Key component 1: Full energy storage fast cycling power supply
Challenges:
A high ramping rate (38000A/s)
A broad dynamic range of I, high precision(±1e-4)
Shock to the power grid(±180MW in total)
Breakthrough:
Innovative topology based on full-energy store and excitation voltage switched.
Capacitor for full-energy store, excitation voltage switched for high precision.
The first of series verified the key technology and design successfully.
Challenges and key components
Low voltage source
High voltage source
Topology of PS
First of series
First of series test results

## Slide 9
Key component 2: Nanocrystalline soft magnetic alloy loaded cavity
Challenges and key components
Challenges:
Wide band (p-U, 0.3~2.1MHz)
High Voltage (12T/s, 285kV)
Fast response (bunch compression, 10μs)
Fabrication of MA core module and core cooling at intense power dissipation are not established.
Breakthrough:
Over ten years exploration from small(φ90), medium (φ460), to large (φ780) MA core.
International leading level key parameters.
The performance and reliability demonstrate well in the protype.
60kV, 3Hz test
FOS MA system
Test result of key parameters
Magnetic alloy loaded cavity

## Slide 10
Key component 3: Lined thin-walled vacuum chamber
Challenges and key components
Challenge:
Ribs supported thin wall chamber: Special material P506 steel or thick ribs(~12mm stainless steel for BRing)
Ceramic chamber: Vitreous bonding, cannot bake
Breakthough:
A novel ceramic ring lined thin wall vacuum chamber are designed for HIAF.
Excellent compressive property of ceramic.
The reliability and vacuum performance increase remarkably by 3 iterations.
Ceramic
0.3mm stainless steel
Thickness: 5mm
Thickness: 4mm
Thickness: 4mm
1st Gen
99% Ceramics
2nd Gen
ZrO2, Au coating
3rd Gen
TC4, NEG coating
Side view

## Slide 11
Present status and schedule
Quadrupole magnets
Dipole magnets
Power supplies
Dipole vacuum chambers
MA loaded cavities
BPMs
More than 50% of the hardware series fabrication are completed. The series installation and joint commissioning will start in Feb. 2024.

## Slide 12
Present status and schedule
The civil construction and supporting facilities is in the closeout phase. They will accomplish in Apr. 2024.

## Slide 13
Present status and schedule
HIAF construction time schedule
The first ion beam provided by FECR is at the middle of 2024;
The low energy ion beam of iLinac is expected at the middle of 2025;
The high energy ion beam from BRing is in September of 2025
The Day One Experiment in SRing will be in April of 2026
2019 | 2020 | 2021 | 2021 | 2022 |  | 2023 |  |  | 2024 |  | 2025 |  |  | 2026 | 
Civil construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Electric power, cooling water, compressed air, network, cryogenic, supporting system, etc. | Electric power, cooling water, compressed air, network, cryogenic, supporting system, etc. |  |  |  |  |  |  |  |  |  |  |  | 
ECR design & fabrication |  |  |  |  | SECR installation and commissioning |  |  |  |  |  |  |  |  |  | 
 | Linac design & fabrication |  |  |  |  |  | iLinac installation and commissioning |  |  |  | Day one exp | Day one exp |  |  | 
Prototypes of PS, RF cavity, chamber, magnets, etc. |  |  |  | fabrication |  |  |  |  | BRing installation & commissioning |  |  |  | Day one exp |  | 
 |  |  |  |  |  |  |  |  | HFRS & SRing installation & commissioning |  |  |  |  |  | Day one exp
 |  |  |  |  |  |  |  | Terminals installation |  |  |  |  |  |  | 

## Slide 14
High-Intensity Heavy Ion Accelerator Facility-HIAF
HIAF welcome all of you !!!
Huizhou, 2025
World-class scientific user facility for international scientists and researchers