## Slide 1: SIS100 extraction layout: Influence of nonlinear beam dynamics
D. Ondreka, B. Galnander, S. Sorge, GSI
5th SX Workshop, MedAustron, 13.02.2024

## Slide 2: Contents
Lattice design criteria
Constraints on SX
Effect of nonlinearities on SX
Impact of field errors
SX schemes for SIS100
Challenges for operation
Summary and Outlook

## Slide 3: SIS100: Overview
Basic parameters
  Circumference 1083m (= 5 x SIS18)
  Max. magnetic rigidity 100Tm
  Max. ramp rate 4T/s
  Mostly super-ferric magnets
Ion optical layout
  Super-periodicity 6, 14 cells per period
  DF focusing structure (charge separator lattice)
  Optimized for operation with intermediate charge state ions
Working modes
  Batch injection from SIS18
  Slow extraction to fixed targets
  Fast extraction of compressed single bunches to fixed targets or storage rings
SIS100 optical parameters (SE) | 
Qh / Qv | 17.31 / 17.4
Q’h / Q’v | -20.3 / -20.6
αp | 0.005
γt | 14.2

## Slide 4: SIS100: Charge Separator Lattice
Increased intensities due to low charge states
  No stripping losses, lower space charge
  FAIR design ion U28+ (instead of U73+)
  Large transverse emittances in relation to rigidity
Stable vacuum becomes critical issue
  High electron loss cross section with residual gas
  Lost particles create avalanche due to desorption
  Tighter constraint than space charge
SIS100 optimized for low charge states
  DF doublet confining losses to well defined spots
  Strong focusing to maximize catching efficiency
    Tunes ~18, nat. chromaticities ~ -20
    Challenging for SX due to large emittances
  Cryo-catchers limit acceptance for SX
FAIR | SIS18 | SIS100
Ion | U73+ | U28+
Max. Energy | 1 GeV/u | 2.7 GeV/u
Max. Intensity | 1010/s | 1011/s
Catching efficiency for different tunes
Collimation of U29+
Vacuum instability by desorption
e-loss cross sections
A. Shevelko
Cryo-catcher prototype

## Slide 5: SIS100: Slow Extraction Layout
Third order resonant extraction
  Resonance tune Qr = 52/3
  Excited by six sextupoles with harmonic distribution
  42 additional chromaticity sextupoles
  Large natural hor. chromaticity Q’x = -18
Extraction channel
  2 electrostatic wire septa (ES)
  Vertical extraction through Lambertson septum (LS)
  Single orbit bump at ES/LS
  3 magnetic septa (MS)
  Lambertson steerer (LX) for hor. correction
Slow extraction schemes
  Baseline: Transverse RF KO extraction
  Alternative: Tune ramp or similar
  Reasons for alternative scheme
    Uncertainties about micro-spill structure
    Fall-back options for KO exciter failures
LX
Extraction channel (V)
SR
SV
SH
SH
SH
SH
SV
SV
SIS100 slow extraction optic: envelopes
MS
LX
Extraction channel (H)
SIS100 extraction orbit
ES1+2
LS
MS+LX
LS cross section

## Slide 6: Constraints: Extraction Channel
Geometric constraints
  ES kicks deliver 16mm separation at LS
  Leaves design margin of ±4mm (for δ=0) at LS
  Position response from ES1 to LS 15mm/mrad
  Constrains SX separatrices
    Permissible angular spread at ES1 ±0.25mrad
    Spiral pitch at ES limited to |step/pitch| > 11.5 m/rad
Consequences for SX schemes
  Small angular spread despite large emittances
  Curvature of separatrices must be limited
  Limits simplest tune-sweep SX scheme to emittances below 5 mm*mrad
Hor. emittances for SX in SIS100
x
x’
ES
Tune-sweep SX
LS
ES1
ES2
left margin
right margin
Beam transport from ES to LS (δ=0)
normalized phase space
LS margins at ES1

## Slide 7: Constraints: Spiral Step
Thermal load on ES wires
  SIS100: 100μm W-Re25% wires at 1N tension
  High dE/dx of heavy ions like U28+
  Temperatures critical for small spiral step
  Spiral step must be at least 8 to 10mm
Particle amplitudes over last three turns
  Strongly constrained by cryo-catchers
  Cryo-catcher distribution matched to amplitudes
  Spiral step must not exceed 12 to 14mm
Amplitudes over the last three turns
Last three turns in sector 4
Matched acceptance at cryo-catchers
Thermal load on ES wires for U28+ design intensities
400 MeV/u
5mm step
1011 ions/s
Ø 100 mm
W-Re25%
W-Re3.3%
Courtesy N. Pyka, GSI

## Slide 8: Nonlinearities in SX
Systematic effects relevant for SX design
  Amplitude-dependent tune shift (ADTS)
  Momentum-dependence beyond chromaticity
  Parasitic resonances
Random effects left for error studies
Simplest lattice for 3rd order resonant SX
  Sextupoles for resonance excitation only
  No resonance but extraction resonance excited
Additional nonlinearities in real SX lattices
  Sextupoles for chromaticity correction
  Quadrupole fringe fields (pseudo-octupole)
  Higher multipoles from field errors of main magnets
Type of NL | Source | Effect
Quadrupole fringe fields | Quadrupoles | ADTS in first order of the pseudo-octupole strengths
Even multipoles | Allowed errors of quadrupoles | ADTS in first order of the multipole strengths
Odd multipoles | Resonance sextupoles | ADTS in second order of the multipole strengths Momentum-dependent ADTS by feed-down from dispersion
 | Chromaticity sextupoles | 
 | Allowed errors of dipoles | 
Sextupoles | Resonance sextupoles | Excitation of unwanted resonances

## Slide 9: Field Errors of Main Magnets
General remarks on main magnets
  Super-ferric magnets with small aperture
  Field quality expected to be inferior to NC magnets
Dipoles
  All dipoles measured at GSI serial test facility
  Multipole data available up to order 7
  Average data based on 110 dipoles
  B3 and B5 significant for SX
  Allowed components included into SX design as systematic multipoles (B3, B5, B7)
  Other components included in error studies
Quadrupoles
  Field measured by manufacturer
  Presently ~20 magnets measured
  Multipole data available up to order 10
  B6 unexpectedly large
  Allowed components included into SX design as systematic multipoles (B6, B10)
  Other components included in error studies
n | ¦knL¦ * mn-1
3 | 0.03 … 0.09
5 | 300 … 400
7 | 7∙106 … 2∙107
n | ¦knL¦ * mn-1
6 | 7∙103 … 104
10 | 1012 … 2∙1012

## Slide 10: Systematic Field Errors: Geometric Effects
Main dipoles
  Significant effect of higher orders in combination with other nonlinearities, e.g. chromaticity correction
  Caused by creation of ADTS in second order of odd multipole strengths (6-pole, 10-pole, …)
Main quadrupoles
  Both B6 and B10 cause ADTS in first order of multipole strength
  Effect independent of presence of other nonlinearities, e.g. chromaticity correction
ADTS in second order of sextupole strength
Dipole errors without and with chromaticity correction
Quadrupole errors without and with chromaticity correction

## Slide 11: Systematic Field Errors: Chromatic Effects
Main dipoles
  Create even multipoles (4-pole, 8-pole, …) by feed-down from dispersion
  B3 (6-pole) reduces hor. chromaticity (tune-shift independent of amplitude)
  Higher orders cause δ-dependent ADTS
Main quadrupoles
  No significant effects beyond chromaticity itself
δ-dependent ADTS from B5 (10-pole) error
δ-dependence for same particle-tune without and with dipole B5
δ-dependence for same particle-tune without and with dipole B5

## Slide 12: KO SX with Systematic Field Errors
Separatrices with systematic errors (εx = 8μm)
KO extraction with small chromaticity
  Chromaticity correction minimizes δ-dependence
    Separatrix size, angular spread at septum
  Small separatrix size for high rigidities desired
    Reduces power requirements on KO exciter
Mitigation of geometric ADTS
  Compensated by octupole correctors
    2nd-order ADTS from strong chromaticity sextupoles
    1st-order ADTS from quad B6 and B10
  Settings may depend strongly on separatrix size
Mitigation of chromatic ADTS
  Dipole B5 like k3l ≈ 2 on octupoles for δ = 10-3!
  Compensation impossible with SIS100 correctors
    Requires 10-pole magnets in dispersive location
    May be considered as future upgrade
  Increases angular spread for small tune distances
No guarantee that acceptable settings can be found for any separatrix size
Separatrices with systematic errors (εx = 28μm)
 | full | base
εx/μm | 28 | 28
ΔQx | 0.019 | 0.021
k3lres/m-2 | 0.56 | 0.44
k4l/m-3 | -2.0 | 8.0
B6/units | 8 | 0.0
 | full | base
εx/μm | 9 | 8
ΔQx | 0.007 | 0.007
k3lres/m-2 | 0.29 | 0.30
k4l/m-3 | 3.5 | 6.0
B6/units | 6 | 0.0
Step/mm | 7 … 12
Ratio/(m/rad) | 13 … 16
Step/mm | 9 … 10
Ratio/(m/rad) | 14 … 24

## Slide 13: A simple commissioning scheme?
KO SX in SIS100 requires precise control of many nonlinear effects
  Hard to observe or verify in the machine
  Settings may be sensitive to parameter mismatches
Idea: start with simple scheme
  Tune-sweep SX with natural chromacity
    Avoid strong chromaticity sextupoles
  Small emittance to keep angular spread low
Questionable in presence of field errors
  Strong influence for small tune distances
  Curvature caused by quadrupoles’ B6 and B10 increases spiral pitch
  Momentum-dependent curvature caused by dipoles’ B5 increases angular spread
  Perhaps for tiny emittance and momentum spread?
Tune-sweep SX with baseline lattice
Tune-sweep SX with systematic errors
Step/mm | 8 … 11
Ratio/(m/rad) | 20
Step/mm | 2 … 13
Ratio/(m/rad) | 5 … 13

## Slide 14: COSE as Alternative Scheme
Constant Optics Slow Extraction (COSE)
  Momentum-driven scheme developed at CERN
  Extraction induced by rigidity ramp Bρ(t)
  Requires sufficiently large chromaticity
  Separatrix for single particle characterized by
    fixed machine tune Qx
    time dependent δ(t) = 1 - Bρ(t)/(qp)
COSE for SIS100 looks promising
  Sufficiently small angular spread reachable
  Tentative settings with different chromaticity
    Small chromaticity: amplitude selection
    Large chromaticity: momentum selection
  Further studies needed to confirm applicability
COSE separatrices for small emittance
COSE separatrices for large emittance
Step/mm | 7 … 10
Ratio/(m/rad) | 16 ... 21
Step/mm | 7 … 9
Ratio/(m/rad) | 16 … 18
εx/μm | 28
ΔQx | 0.002
Q’x | -12
k3lres/m-2 | 0.40
k4l/m-3 | -12
B6/units | 8
εx/μm | 11
ΔQx | 0.004
Q’x | -3.5
k3lres/m-2 | 0.26
k4l/m-3 | 1.5
B6/units | 6

## Slide 15: Other NL Effects
Parasitic resonance constraining WP
  Vertical tune had to be moved to Qy=17.4
    Original Qy=17.8 not suitable for high intensities
  Coupling resonance excited by sextupoles
    Driving term for Qx+2Qy now about equal to 3Qx
    No compensation with existing magnets
  Luckily available space in Qy appears sufficient
Effect of random field errors
  First error studies on KO SX performed
    Orbit corrected for distortions by alignment errors
    Error model for dipoles and quadrupoles based on spread of magnetic measurements
  Design appears to be robust against errors
Low-loss injection regions
Courtesy A. Oeftiger, GSI
(1, 2, 52)
(1, 2, 53)
(3, 0, 52)
(1, -2, -18)
(1, -2, -18)
old WP
WP
Normal sextupole lines
Losses on coupling res. vs. Qy
Losses through random errors
S. Sorge, B. Galnander et al., TUPM099, IPAC23

## Slide 16: Challenges for Operation
Higher-order effects play important role for SX from SIS100
  Increased complexity due to required compensation of nonlinearities
Challenge: simplified model for defining optimal settings
  Large parameter space for control of SX parameters
    Tunes (2) and chromaticities (2)
    Distribution of resonance (6) and chromaticity (7) sextupole strengths
    Choice of octupole (2) strengths
  Solution not uniquely defined by SX parameters
    Spiral step e.g. depends on resonance strength, tune distance and ADTS
  Present results mostly obtained by ‘educated tuning’ in tracking simulations
  Can we find a computationally faster yet sufficiently predictive model?
Challenge: control of parameters in real machine
  Far fewer observables than in simulations
  Ambiguity in source of deviations for critical parameters (step/pitch)
  How to commission SX with the least number of degrees of freedom?
  How to introduce complexity in small steps?

## Slide 17: Summary and Outlook
SIS100 has tight constraints for SX due to optimization for low charge-state ions
Nonlinearities including systematic magnet errors affect the dynamics significantly due to ADTS
Robust settings for KO SX in the presence of field errors have been found
COSE SX has been identified as a promising alternative scheme
Explore COSE option further including error and sensitivity studies
Try to find simplified model to reduce dependence on tracking
Devise a reasonable commissioning scheme
Study upgrade options for installing higher-order multipole correctors

## Slide 18: Thanks for your attention!
Thanks to all who have contributed and continue to contribute to the development of slow extraction for FAIR.
October 2023

## Slide 19: Choice of SX scheme
Control of separatrix parameters required
  Size and orientation (crossing angle)
  Spiral step and pitch
Fixing chromaticity, parameters depend on
  Machine tune Qx,0
  Momentum deviation δ
Comparison of SX schemes
  Tune-sweep SX
    2D dependence on Qx,0(t) and δ
    Parameters must be matched for each Qx,0 and δ
  Transverse knock-out SX
    Fixed Qx,0, matching for δ only
    Ideally small difference in separatrix sizes
  Momentum-driven SX
    Fixed Qx,0, matching for δ only
    Separatrix sizes must vary down to zero
Tune-sweep SX
For SIS100, KO and momentum-driven SX are the only reasonable choices due to strong δ-dependence of separatrix parameters
Knock-out SX
hor. excitation
Momentum-driven SX
δ-change