## Slide 1
Matthew Alvarez and Kathrine Laureto
5th Slow Extraction Workshop at MedAustron in Wiener Neustadt
13 February 2024
Electrostatic Septa Development at FNAL
Fermi National Accelerator Laboratory

## Slide 2: Introduction
Mu2e experiment will study rare neutrinoless decays of muon to an electron
Septum: foil ribbons
Top Functional Requirements
  High extraction efficiency:
    Greater than 98.5%
  Radiation stability:
    2+ years of operation
Beam Parameters | Nominal Value
Particles Type | Protons
Kinetic Energy | 8.0 GeV
Spill Duration | 43 ms
Total Number of Protons in a Spill | 1e12
Beam Power | 8 kW
Septa Kick | 2 mrad
Septa Active Length | 3 m
ESS1
ESS2
Quad magnet
Wilson Hall

## Slide 3: Mechanical Overview
Frame Assembly
Cathode
High Voltage Feedthrough (HVF)
Cathode Standoffs (CS)
Vacuum Vessel
  Instrumentation Cross
  3x 300L/s Ion Pumps
Beam Direction
HVF
CS
Vacuum Vessel
20kV SHV Feedthrough
Instrumentation Cross
Frame
ESS2 (643 foils)
ESS1 (544 foils + 1 diffuser)
Cathode
HVF
HVF
CS x3
CS x2

## Slide 4: Mechanical Overview: Frame Assembly
Frame
  Interchangeable for ESS1 and ESS2
  Material: Aluminum 7075
  Length: 171.5cm
Springs
  17-7PH CH900 Stainless Steel springs
  Both tensions (1kg) and retracts the foil ribbon
  Higher foil retraction speed ~80m/s (290kph or 180mph)
Clearing Electrodes
  ±8kV provided by 20kV SHV
Frame
Springs
Springs
Clearing electrodes
Baffles

## Slide 5: Mechanical Overview: Frame Assembly
Foil Ribbons (W3Re)
  Tungsten-Rhenium foil
  25µm thick x 1mm wide
  Higher mechanical tension than wires
  Narrower beam cross section than wire
    100µm (MI-52 Septum) vs. 25µm (Mu2e Septum)
Diffuser Foil
  ESS 1 Diffuser length: 33.9cm
  50µm thick W3Re diffuser foil
  Looking into Titanium foil, 70µm
ESS1
Diffuser foil

## Slide 6: Mechanical Overview: Cathode
Material: 304SS
Mechanical Polish: Ra=0.05µm (2µin) with a mirror finish
ESS1 Cathode
  Length: 133.6cm
ESS2 Cathode
  Length: 166.4cm
Adjustable gap between cathode and foils
Pockets machined to minimize weight
  Reduces cantilever stresses on ceramic standoffs
Plan to use electropolishing on the cathodes
ESS2
ESS2
ESS1

## Slide 7: Mechanical Overview: High Voltage Feedthrough (HVF)
Materials
  PEEK (yellow)
  Al203 (white) ceramic
  304SS (grey and green)
  Kovar (blue)
3M FC-40 liquid dielectric
47Ω resistor
Plunger assembly
  Maintains electrical continuity for different cathode-anode gaps
In
Out
47 Ω Resistor
Plunger Assembly
A
A
Section A-A
B
B
Section B-B

## Slide 8: Mechanical Overview: Cathode Standoff (CS)
Supports the cathode
Materials
  Al2O3 (white) ceramic
  304SS (grey and green)
  Kovar (blue)
Port Aligners
  Cathode-Anode gaps of 5-20mm
Wavy Washers
Port Aligner
Cathode
Cathode
Cathode
Old Re-entrant Skirt Design
New Re-entrant Skirt Design

## Slide 9: Mechanical Overview: Vacuum Vessel and Fully Assembled Septum
ESS1 Production Septum
CS
HVF
CS
Instrumentation Cross

## Slide 10: Assembly
Install cathode
Install frame
Install HVF
Step 1
Step 2
Step 2
Step 3

## Slide 11: Assembly
4. Set gap between frame and cathode
5. Reference septa to external fiducials (not pictured)
Step 4
Step 4
Step 4

## Slide 12: Transportation
Transportation of septum from assembly facility to Muon delivery ring (2.7km or 1.7miles)
Septum uses rubber cribbing to dampen any shock from transport
Truck speed limited under 5 mph (8km/h)
Transport Cart
Rubber Cribbing

## Slide 13: Transportation
ENDAQ sensors used
  Data range up to 20g
  Sample rate 1000Hz
  Pressure, temperature, and humidity measurement taken at 1Hz
Sensor placement (3 total)
  2 accelerometers placed on the vacuum vessel
  1 sensor placed on the truck
Measured entire process from rolling on the floor to lifting it with cranes
Largest acceleration measured during transport: 1.7g (max 2g)
Septum

## Slide 14: Challenges and Puzzles
Shortage of vendors
  Loss of expertise
  Cathode, frame, foil ribbon, and polishing vendors
Dust and particulate mitigation in the septa
Finding a replacement for FC-40
HVF
CS
HVF

## Slide 15: Current Status
Built and tested the full-scale prototype of ESS2
  Installed the prototype in the Muon delivery ring
Updated the production septa design from lessons learned
Assembled the first production septum ESS1
  Conditioning/troubleshooting
Began assembly of the production septum ESS2
Looking forward for running them in beam in 2024

## Slide 16: Thank you!

## Slide 17: Optional Slides of Interest

## Slide 18: High Level Overview
Mechanical and Electrical Requirements
Number of Septum units: 2
  ESS1
    Cathode length is 133.6cm
    544 foils + 1 diffuser foil
  ESS2
    Cathode length is 166.4cm
    673 foils
Foil
  Spacing: 2.54mm
Total active length of septa: 3m
Total Kick: 2mR
  Electric Field strength: 100kV (nominal)

## Slide 19: ESS 1 Frame 1 Measurement Data

## Slide 20: Foil Production
Fabricated onsite
  On-the job training required for technician
Foil vendor: H. Cross Company
  Material certificates required
  Foil measurement tolerances required
Material: W3Re
Foil Geometry
  Foil width is .040” (1000um) ±.003” (76.2um)
  Foil thickness .001” (25um) ±.0001” (2.5um)

## Slide 21: Foil Production
Foil Assembly
  Produce 5 foil assemblies at one time
  25 tons required to crimp the joint
    2.5 tons per crimped joint
  Press
    SPECAC 25 ton press
Foils will be tested to certify and ensure the load is sufficient and the tool is not wearing.
Press
Crimping Fixture
N2 Gas (ionizing)
W3Re Spool
Foil Storage Fixture
Springs and Tubes
304SS Ferrule
W3Re Foil
17-7PH SS Spring
304SS Ferrule
W3Re Foil
17-7PH SS Spring

## Slide 22: Assembly: Cleaning Septum Parts Procedure
Goal: Ensure all parts are cleaned to achieve the best vacuum (E-9 torr)
Processes for cleaning parts (depends on the part)
  Dawn dish soap
  DI water rinse
  Ultrasonic tank
  Drying with N2
  Alcohol bath
  Alcohol wipe
Procedure Outlines
  Cleaning of hardware
  Cleaning of specific septum parts (frame, ceramics, cathode)
Materials to be cleaned
  304SS, 316SS, 18-8SS, 17-7PH SS, W3Re, Al 6061, Al 7075 (frame), Kovar, Al 203, silver plated bolts, PEEK, Nylon, ABS, etc.

## Slide 23: Assembly: Installing Foils onto the Frame
Two people are required, one on either side of the table
Hazard analysis required for access into the cleanroom

## Slide 24: Assembly: QC Frame (Prototype)
Frame will be measured to see if it is acceptable
If not acceptable, we will need to machine it again with the geometry we require
  Send back to vendor
  Hand lap and measure to achieve desired profile
Align the foil plane relative to the beam
Forward and backward
0.060
0.050
0.040
0.030
0.020
0.010
0.000
-0.010
-0.020
Diffuser area
Shadow area
80μm
+x
+x

## Slide 25: Assembly: Installing Cathode
3 people required
  Two people to support the cathode on each end
  One person installs cathode standoffs
Ion pump port plugs are installed prior to be placed on the die cart
Port Plug

## Slide 26: Assembly: Installing the Frame
Trolleys are attached to the back of the frame
  Both are removed gradually until the frame support brackets are installed
Frame vessel installation fixture
  Rolls the frame within vessel
Frame push fixture
  Supports the frame to allow the frame support brackets to be installed
Trolley
Frame vessel installation fixture
Frame Push Fixture

## Slide 27: Assembly: Installing the Frame
Frame support bracket
Frame vessel installation fixture
Frame push fixture
Frame support bracket
Frame support bracket is installed while fixtures support frame within the vacuum vessel
After brackets are installed, the supports are removed
Cathode and frame are aligned

## Slide 28: Assembly: Placing Septum on Transport Cart
Septum is placed on slings and placed on the transport cart
Ion pumps are installed
Vacuum flanges are installed

## Slide 29: Transportation Data: Vessel Sensor P13
1
2
3
4
5
6

## Slide 30: Transportation Data: Truck F50 (Truck only)
4
5