## Slide 1
ML Techniques in Spill Regulation for Mu2e
Aakaash Narayanan
Slow Extraction Workshop, Wiener Neustadt, Austria
14 February 2024

## Slide 2: Resonant Extraction for Mu2e
Main types of spill non-uniformities:
  Slow variations in the spill rate
  Fast random ripples (noise)
  Higher order harmonics from power supply
Spill ripples negatively impact the data:
  Detector pile-up
  Reconstruction inefficiency
  Dead time
We need to mitigate:
  Slow varying noise that could span across many spill.
  Fast variations that could arise within one spill.
Goal:
Spill Duty Factor = > 0.6
Maximum Intensity in DR | < 1 X 1012 | protons
Revolution time in DR | 1.694 | s
Orbit length of DR | 505.294 | m
Horizontal tune in DR | 9.650 to 9.666 | 
Protons per extracted pulse | < 4 X 107 | protons
Spill Duty Factor | >60% | 
Single spill duration | 43 | ms
Beam Power | 8 | kW
Maximum Intensity in DR | < 1 X 1012 | protons
Revolution time in DR | 1.694 | 
Orbit length of DR | 505.294 | m
Horizontal tune in DR | 9.650 to 9.666 | 
Protons per extracted pulse | < 4 X 107 | protons
Spill Duty Factor | >60% | 
Single spill duration | 43 | ms
Beam Power | 8 | kW
Beam Parameters for Resonant Extraction
Extraction scheme is to excite 3rd integer resonance using fixed strength harmonic sextupoles and move the beam tune closer to 29/3 using dedicated fast tune-ramping quadrupoles.

## Slide 3: Spill Regulation System
The SRS would also be dealing with the n*60 Hz harmonic noise content arising from the power supplies. The controller will determine the harmonic content of the ripple and apply feedforward corrections.
SPILL REGULATION SYSTEM
Slow Regulation
Fast Regulation
Harmonic Content Tracker
The slow regulation controller will be tracking the slow changes in the spill profile producing corrections to the tune quadrupole current ramp to achieve the uniform spill rate.
The fast regulation system would be supplemented on top of the slow regulation in order to correct for instantaneous ripples in the spill intensity.
The SRS would also be dealing with the n*60 Hz harmonic noise content arising from the power supplies. The controller will determine the harmonic content of the ripple and apply feedforward corrections.

## Slide 4: Spill Regulation System
The SRS would also be dealing with the n*60 Hz harmonic noise content arising from the power supplies. The controller will determine the harmonic content of the ripple and apply feedforward corrections.
SPILL REGULATION SYSTEM
Slow Regulation
Fast Regulation
Harmonic Content Tracker
The slow regulation controller will be tracking the slow changes in the spill profile producing corrections to the tune quadrupole current ramp to achieve the uniform spill rate.
The fast regulation system would be supplemented on top of the slow regulation in order to correct for instantaneous ripples in the spill intensity.
The SRS would also be dealing with the n*60 Hz harmonic noise content arising from the power supplies. The controller will determine the harmonic content of the ripple and apply feedforward corrections.

## Slide 5: Fast Regulation Loop
The fast regulation loop deals with instantaneous noises that affect the spill quality within one spill.
The instantaneous fluctuations within one spill due to random noises can be large. In the SRS, this is handled by the fast PID loop controller.
We assume here that this noise (ripples) have a random nature or otherwise are a semi-random component of regular harmonic noise that the harmonic controller is not able to suppress.
The correction signal to counter the noise will superimpose on top of the ideal tune ramp provided by the slow regulation.
The three main parameters to control the spill quality in the fast regulation loop are the three gain values of the PID controller:

## Slide 6: Using Machine Learning
We explore using machine learning (ML) algorithms to tune the PID gain values to achieve an improved spill quality.
The spill quality is quantified by ‘Spill Duty Factor’ (SDF), defined by:
where is the variance in the extraction rate computed for one full spill, assuming the average intensity is normalized to 1.
We use a simplified semi-analytical model to simulate the dynamics of resonant extraction in order to generate training data for the machine learning algorithm.

## Slide 7: Physics Simulator Model
TRANSIT DELAY
NOISE GENERATION
PID RESPONSE
MACHINE LATENCY
BEAM EXTRACTION
SPILL MONITOR
CORRECTED QUADRUPOLE CURRENT
1
2
6
5
7
3
4
Notes: E.g., Like RFKO, latency in longitudinal dynamics, etc.,

## Slide 8: Physics Simulator Blocks
NOISE GENERATION
PID RESPONSE
1
2
The noise for one full spill is generated in terms of extraction rate. We assume a log-normal distribution for the noise spectrum.
Since the source of noise could emanate from any of the elements in the ring, the noise is pre-generated before the spill and is added directly as fluctuations in the spill.
Ideal spill is normalized to an expectation value of 1.
With the full extraction rate known, the PID calculates the error at every time step and computes the control signal.
At every time step, the difference between the ideal spill and the actual spill is computed, and the PID calculates the control signal to be given to counter the noise in the spill rate.

## Slide 9: Physics Simulator Blocks
TRANSIT DELAY
FIELD SHIELDING EFFECT (LATENCY)
3
4
The SS beam pipe would screen high frequency components of the quadrupole field.
The PID response in the simulator is thus passed through a low-pass filter to simulate the steel beam pipe screening any magnetic field variations greater than 1 kHz.
Once the particle is unstable, it does not get immediately extracted once it gets unstable. It takes some finite amount of turns to get to the septum location.
Transit time studies were done to determine the number of turns particles take to get extracted. This delay is modelled into the physics simulator.

## Slide 10: Physics Simulator Blocks
BEAM EXTRACTION
SPILL MONITOR
CORRECTED QUADRUPOLE CURRENT
6
5
7
According to our analytical model, the ideal tune current ramp is taken to be a logarithmic function in time. The delayed and low-pass filtered PID response is superimposed with the idealized logarithmic quadrupole current curve.
With the corrected quad current ramp, the total extracted beam intensity is computed for the full spill duration. This would be the fast regulated spill.
The spill monitor block computes the spill rate for one full spill at a time step of 10 kHz (which is the total gain bandwidth of the SRS). We assume the spill monitor to be fast enough to not affect the loop.

## Slide 11: PID Tuning Scheme Using ML Simulator
The ML simulator uses the physics simulator iteratively to compute loss functions and optimize the gain values.
In the very first iteration, the neural network assigns random gain values and calls the physics simulator. The physics simulator then outputs the PID loop regulated spill rate, from which the spill duty factor is calculated.
Once the SDF is calculated, a loss function is defined to train the ML model:
The machine learning tool used in the optimization of the PID gains is PyTorch (version 1.8.1).
PHYSICS SIMULATOR
ML
MODEL
EVERY FULL SPILL…

## Slide 12: Differentiable Machine Learning Simulator
The loss value, along with the previous three gain values, are fed into the neural network.
The neural network then calculates the gradient of the loss function with respect to the PID gain i.e., and backpropogates to update the weights in the direction of minimization of the loss function, outputting new gain values.
Backpropagation is done through with Adaptive Momentum (Adam) optimizer:
where:
  denotes the network parameters, i.e., weights and biases of the network,
  denotes gradient w.r.t the network parameters, is the loss function,
  are constants
  is the learning rate
Figure: A. Narayanan, M. Thieme, et. al, “Optimizing Mu2e Spill Regulation Algorithms”, IPAC 2021

## Slide 13: Backpropagation Scheme
With the updated gain values, the physics simulator is run again for a full spill, but this time with a completely new random noise profile.
After the 2nd full spill, the SDF and the loss function are again computed and fed into the neural network to compute the loss gradients.
The neural network again updates the weights and gives a new set of , and the physics simulator is called again.
This is done iteratively until the loss function becomes minimal (i.e., the PID loop’s performance becomes maximal).
We refer to this approach as a Hybrid ML Simulator because only those functions which must be differentiable (i.e., computable) are made so. This allows functions such as noise generation and tune ramps to be pre-computed and excluded from the more computationally expensive gradient calculation and backpropagation steps.
Notes: In the end, state that the gains are determined and next is to..

## Slide 14: Differentiable Simulator - Results
The sensitivity of control varies across the spill duration.
To characterize this sensitivity, our system divides the full spill into subdomains.
The ML simulator optimizes within each of the subdomain with every spill.
Notes: Lot of text… cut down. Maybe shorten the bullets.

## Slide 15: ML Optimization at work…
A. Narayanan, M. Thieme, et. al, “Optimizing Mu2e Spill Regulation Algorithms”, IPAC 2021

## Slide 16: PID Gain Evolution
A. Narayanan, M. Thieme, et. al, “Optimizing Mu2e Spill Regulation Algorithms”, IPAC 2021

## Slide 17: Spill Regulation ML Model
We next explore the possibility of a Machine Learning agent entirely replacing the PID controller, instead of simply tuning the gains of the PID controller.
Since the spill is temporally sensitive, a Recurrent Neural Network was chosen to train the model to emulate the PID controller.
To over come that, LSTM and GRU are a type of neural network that have ‘internal loops’ that enables connecting temporally sensitive past information to perform present tasks.
Image source: https://colah.github.io/posts/2015-08-Understanding-LSTMs/
RNNs typically suffer from ‘short-term’ memory (the ‘vanishing gradient problem’).

## Slide 18: GRU ML Model Replacing PID
Spill data of previous time steps
Time window size =
S= [stn-tw, stn-tw+1, …, stn]
no. of spill data before
PHYSICS SIMULATOR
I(tn)
S
I
GRU Neural Net
with 2 hidden layers
S = [stn-tw+1, stn-tw+2, …, stn+1]
no. of spill data before
ML agent
Quad current
Spill data for

## Slide 19: GRU Model Matching PID Performance
Raw SDF
Relative performance to PID
SDF =
Blue line =
A. Narayanan, J. Jang, M. Thieme, et al., “ML Techniques in Slow Spill Regulation System for Mu2e”, NAPAC 2022.

## Slide 20: GRU Model Performance
A. Narayanan, J. Jang, M. Thieme, et al., “ML Techniques in Slow Spill Regulation System for Mu2e”, NAPAC 2022.

## Slide 21: Performance vs Bandwidth
Notes: We developed a tool and using that we can see how BW is important.

## Slide 22: Reinforcement Learning
The action function is defined as the set of actions taken by our agent in its environment.
The state function is defined as the set of environment parameters that affect the course of our agent.
The reward function is defined as a value we assign to a specific action taken in a specific state
As the agent progresses in time, we accumulate a set of (
Reinforcement Learning (RL) is a type of ML technique that enables an agent to interact with the environment by trial and error using feedback from its own actions and experiences.

## Slide 23: Reinforcement Learning – fun example
Action space:
  Accelerate at constant rate
  Decelerate at constant rate
  Turn right at fixed angle
  Turn left at fixed angle
State space:
  The raw 96x96 pixels of every frame
Rewards:
  -0.1 for every passing frame
  1000/Ntiles for every track tile visited
  Episode finished when all tiles are visited

## Slide 24: Reinforcement Learning – fun example

## Slide 25: Reinforcement Learning in Resonant Extraction
The action variable is defined as the set of actions taken by our agent in its environment.
The state variable is defined as the set of environment parameters that affect the course of our agent.
The reward value is defined as a value we assign to a specific action taken in a specific state
In the case of slow spill, the action space is continuous as the control signal’s magnitude could be any real number. To deal with continuous action space, we use policy-based actor-critic methods whereby two neural networks are trained.
RESONANT
EXTRACTION

## Slide 26: Reinforcement Learning in Resonant Extraction
The action variable is defined as the set of actions taken by our agent in its environment.
The state variable is defined as the set of environment parameters that affect the course of our agent.
The reward value is defined as a value we assign to a specific action taken in a specific state
Quadrupole current
In the case of slow spill, the action space is continuous as the control signal’s magnitude could be any real number. To deal with continuous action space, we use policy-based actor-critic methods whereby two neural networks are trained.
RESONANT
EXTRACTION

## Slide 27: Reinforcement Learning in Resonant Extraction
The action variable is defined as the set of actions taken by our agent in its environment.
The state variable is defined as the set of environment parameters that affect the course of our agent.
The reward value is defined as a value we assign to a specific action taken in a specific state
Quadrupole current
In the case of slow spill, the action space is continuous as the control signal’s magnitude could be any real number. To deal with continuous action space, we use policy-based actor-critic methods whereby two neural networks are trained.
RESONANT
EXTRACTION
etc.,

## Slide 28: Reinforcement Learning in Resonant Extraction
The action variable is defined as the set of actions taken by our agent in its environment.
The state variable is defined as the set of environment parameters that affect the course of our agent.
The reward value is defined as a value we assign to a specific action taken in a specific state
Quadrupole current
In the case of slow spill, the action space is continuous as the control signal’s magnitude could be any real number. To deal with continuous action space, we use policy-based actor-critic methods whereby two neural networks are trained.
RESONANT
EXTRACTION
etc.,
Scaled with regulation
performance

## Slide 29
[ 21.345]
Actor value :
a real number
ACTOR NETWORK
STATES
RESONANT
EXTRACTION
The actor network takes in the state space variables as the input and outputs the action (i.e., the control signal) to be superimposed to the tune ramp quad current.
This action is played for the next time step and the new spill rate is obtained.
Reinforcement Learning - Actor Critic

## Slide 30: Reinforcement Learning - Actor Critic
[ 0.5638]
Critic value :
a real number
CRITIC NETWORK
REWARDS
The critic network takes in the reward values for the episode and gives out a value ‘criticizing’ the how good the action taken was.
This is fed back into the actor network so it takes a better action the next time.
RESONANT
EXTRACTION
This way, the both the networks together directly learns the policy.

## Slide 31: Reinforcement Learning - Actor Critic
ACTOR MODEL
CRITIC
MODEL
RESONANT
EXTRACTION
OBSERVE STATE
OBTAIN REWARD
LOSS
TAKE ACTION
RL AGENT
Actor learns to act better.
Critic learns to criticize better.

## Slide 32: Reinforcement Learning - Initial Results

## Slide 33: Reinforcement Learning - Initial Results

## Slide 34: Reinforcement Learning - Neuralized PID Approach
A neutralized PID policy function to optimize the SDF of the spill.
Uses the same physics simulator but with an inductive bias of PID based policy to formulate the state vector.
The PPO algorithm, an RL technique plays a central role in optimizing policy functions to enhance decision-making in sequential tasks and we specifically chose PPO to refine our reward function.
Reward function:
where

## Slide 35: Reinforcement Learning - Neuralized PID Approach

## Slide 36: Reinforcement Learning - Neuralized PID Approach

## Slide 37: Reinforcement Learning - Neuralized PID Approach

## Slide 38: THANK YOU

## Slide 39: GRU ML Model Replacing PID
Spill data of previous time steps
Time window size =
S= [stn-tw, stn-tw+1, …, stn]
no. of spill data before
PHYSICS SIMULATOR
I(tn)
S
I
GRU Neural Net
with 2 hidden layers
Stn+1 = [stn-tw+1, stn-tw+2, …, stn+1]
no. of spill data before
ML agent
Quad current
Spill data for