## Slide 2: Replacement of electrostatic septa with crystal technology
Y. Dutheil, P. Arrutia, L.S. Esposito, M. Fraser, B. Goddard, F. Velotti CERN, Geneva, Switzerland

## Slide 3: Outline
SPS slow extraction layout
Crystal technology
Extraction concepts with crystals
Plans at CERN before 2026
Conclusion

## Slide 4: SPS slow extraction
Slow extraction of 400 GeV/c proton beam towards North Area
  Presently extracting in the order of 1019 protons per year
Radiation levels
  Consequences for personnel intervention, equipment lifetime, …
Future prospects
  Loss reduction with beam dynamics and shadowing of the electrostatic septa
  Activation reduction with different material
  Intervention time mitigation
Electrostatic septa in the SPS tunnel LSS2

## Slide 5: Layout of SPS extraction
Nominal slow extraction conditions
Electrostatic septum
  Combined deflection of 440 µrad
Magnetic septum
  Thickness of ~5 mm
  Present gap opened ~20 mm
Electrostatic septa
Magnetic septa protection absorber
G. Ladarola & F. Velotti, gitlab.cern.ch/sps-projects/sx_xsuite_sps
G, Ladarola et. al., github.com/xsuite
Phase space at the entrance to the first electrostatic septum

## Slide 6: Required crystal extraction performance
Aims
  Aiming for similar gap at magnetic septum
  For an extraction efficiency >99.5%
Associated crystal parameters
  Short length to minimize nuclear interaction
  Angle of 400 µrad to 800 µrad
  Large channeling efficiency

## Slide 7: Crystal technologies
Several crystal types have been manufactured and tested [2,3]
  Wide range of size (2 to 70 mm) and angle (30 µrad to 13 mrad)
  Thick crystal up to 20 mm are possible but not the whole surface is exploitable [2]
Critical angle for straight silicon crystal at 400 GeV is 10urad and Rc=1m
  For a bent crystal
  For 10m radius, crystal provides 100 µrad/mm but 200 µrad/mm is feasible mechanically
  Volume reflection ~14 µrad
Efficiency measured at 400Gev [2]
  Channeling up to 68% and 54% respectively for angular spread within 5 µrad (1/2 θc) and 10 µrad (1θc)
  Volume reflection up to 90%
Present discussion on the feasibility of crystal slow extraction overlooks crystal manufacturing methods and limitations on the resulting crystals
[1] M. D'andrea, application of crystal collimation to LHC, PhD 2021, link
[2] R. Rossi, Measurements of coherent interactions of 400 GeV protons in silicon bent crystals, link
[3] S. Cesare, Analysis of long crystal channelling efficiency from hadron beam test data, Workshop FixedTarget ICJLAB, 2023, link

## Slide 8: Crystal characteristics : mapping
Model
  Xsuite EverestCrystal with SiliconCrystal material
  Probed with a perfect pencil beam of protons at 400 GeV/c
Case of a Silicon crystal 4 mm long and R=10 -> 400 µrad
G, Ladarola et. al., github.com/xsuite
Scattering
Volume reflection
Volume capture
Channeling
Dechannelling
1
1
2
3
4
5
2
3
5
4
Incoming
Angle
0 µrad
Incoming
Angle
-150 µrad

## Slide 9: Crystal characteristics : effect of length
Model
  Xsuite EverestCrystal with SiliconCrystal material
  Probed with a perfect pencil beam
  Fixed deflection at 400 µrad and variation of the crystal length
Channeling
  Maximum channeling efficiency ~80%
  Dechannelled particles populate the space between circulating and extracted beam
  Scattering
Non channeling fraction
  In average not deflected by the crystal
  Scattering angle is reasonable with sigma between 5 and 20 µrad
Optimisation
  The sum of channelled and non-channelled can be maximized to around 95%
  Non-channelled beam behaviour after the scattering needs to be evaluated
G, Ladarola et. al., github.com/xsuite

## Slide 10: Crystal characteristics : effect of energy
Model
  Xsuite EverestCrystal with SiliconCrystal material
  Probed with a perfect pencil beam
  Fixed crystal length of 2 mm
  crystal angle scaling with to account for the larger beam divergence and extraction angles at lower energy
Channeling
  Below ~100 GeV/c the influence of scattering becomes significant
  Drop in efficiency above 1 TeV remains to be confirmed
  Channelling seem to favor higher energies
Example of 25mm crystal with 20 GeV/c protons
  Very short bending radius crystal may benefit to low energy applications
G, Ladarola et. al., github.com/xsuite

## Slide 11: Extraction concept : Non-resonant channelling
Concept by P. Arrutia [1]
  Optics far from resonance (e.g. LHC optics)
  Crystal is located in a region with large dispersion (e.g. arc)
  Beam slowly pushed towards crystal via momentum change
Status and follow-up points
  Simulation being set up to quantify whether
    efficiency of crystal is high enough to kick most particles out
    Scattering from crystal is small enough to keep particles within channelling region
  Perhaps one could operate with an array of crystals in multi-volume reflection
  Can we actually install a crystal in the arc?
  How do we bump the beam towards the crystal?
  Do we have enough aperture at injection to avoid hitting the crystal?
[1] P. Arrutia, Prospects of replacing the SPS ZS by bent crystals, SLAWG#72, 2023

## Slide 12: Extraction concept : Resonant Channelling
Present slow extraction in the SPS is resonant and momentum driven
Simplest scheme replaces the electrostatic septa by a crystal
  Single crystal 4 mm long and R=10 provides 400 µrad channelling angle
Possible crystal locations around QFA.21610
  Tilted separatrix prevents the use of single crystal
  Spiral step is maintained as for nominal slow extraction to kept the separation between extraction and circulating beam
Present slow extraction with electrostatic septa
Quadrupole entrance
Quadrupole exit

## Slide 13: Extraction concept : Resonant channelling
Crystal placed in the middle of a quadrupole to minimize the tilt of the separatrix
3 crystals with overlapping channelling acceptance
  Allows increased coverage of the channelled angle
  Increasing angle sequence also channels dechannelled particles from previous crystals
Scheme remains limited by single pass efficiency
  Possible to increase the number of crystals at the price of increased scattering
.
.
.

## Slide 14: Extraction concept : Resonant channelling
Extraction with 3 arrays of crystal to increase efficiency and depopulate the beam density at the septum
Trajectories clear the present thin septum aperture
Limitations
  Model with crystal inside a quadrupole
  Crystal arrays without space not errors
More comprehensive simulations and more realistic layout remain to be done

## Slide 15: Extraction concept prospects
Several concepts being explored
Non-resonant & channelling
  Momentum driven
  TFB excitation or direct bump on crystal controlled via feedback
Resonant & channelling
  Nominal extraction with one or multiple crystals
  D. Veres (PhD supervisor M. Giovanozzi), multipass channelling with recirculation
Volume reflection
  Seem limited by the deflection angle in-par with the scattering angle
  May be limited to cleaning the gap and assist a channelling scheme

## Slide 16: Plans at CERN for 2023 and 2024
Presently 2 crystals at the SPS
  In long straight section 2 (North area extraction) crystal used for crystal shadowing
  In long straight section 4 crystal tested for non-local shadowing
  See F. Velotti’s talk
Possible benchmark of models using a channelling concept with presently installed crystals
Needs for a facility in the SPS to test crystals and extraction concepts
Machine experiment plan for 2024 and strategy towards the Long Shutdown starting in 2026

## Slide 17: Conclusion
SPS extraction
  Presently uses electrostatic septa
  Already very efficient but 400 GeV/c proton induces significant activation
  Present and future experiment request higher intensities
Crystal technology
  In-house R&D of crystal at CERN is progressing (See L. Esposito’ talk)
  Channelling provides large deflection but has fundamental efficiency limits
  Behaviour at lower energy may not allow direct usage of channelling for extraction
Present beam dynamics modelling using Xsuite and its crystal implementation
Several extraction concept being explorer for the CERN SPS
  Presently the first ideas are being modelled
  Comprehensive and realistic models are required to ensure the feasibility of each scheme
  Experiment plan possibly making use of the 2 existing crystal in the SPS needs to be developed for the next 2 years