## Slide 1: SHERPA “Slow High-efficiency Extraction from Ring Positron Accelerator”
Dr. Marco Garattini (SHERPA P.I.)
National Laboratory of Frascati (LNF) - National Institute of Nuclear Physics (INFN)
(D. Annucci, O. R. Blanco-Garcia, P. Gianotti, S. Guiducci, A. Liedl,
E. Long, M. Mancini, T. Napolitano, M. Raggi, P. Valente)
“Slow Extraction Workshop 2024”, 13th February 2023
Young Researcher Grant
(2020-2022)

## Slide 2
R&D study to extract a high-quality e+ (or e-) beam from one of the DAΦNE rings
The idea is to use coherent processes in a bent crystal to steer the positron beam
VS
Current BTF spill parameters:
Energy spread: Δp/p < 0.5 x 10-2
  Emittance: ε < 10-5 rad⋅m
  Length: Δt ~ 300 ns
Target spill parameters:
Energy spread: Δp/p < 10-3
Emittance: ε < 10-6 rad⋅m
Length: Δt ~ ms
Channeling
e+ (< 500 MeV)
DAΦNE
BTF
Bent crystal
The SHERPA project
With the SHERPA beam, PADME (“Positron Annihilation into Dark Matter Experiment”) could increase the statistics by a factor ~104 and its sensitivity by a factor ~102,
largely extending the discovery potential. Now it is limited by VETO pile-up and BKG
Immediate application:
This technology can be used for all kinds of lepton particles, positive and negative !!!

## Slide 3: Coherent processes in bent crystals
Θout
ΔΘ
Θin
AM
AM
VR
VC
DC
CH
Θc
3
DC
Dechanneling
4
VR
Volume reflection
5
VC
Volume capture
2
CH
Channeling
crystal
[1-2]
Test beam on the CERN-SPS extraction line H8
(in the framework of the UA9 experiment)

## Slide 4: Extraction from DAΦNE
The beam halo population is steadily sustained switching off RF, or tuning them properly (e+ & e- loose energy by Synchrotron Radiation)
A bent crystal, properly oriented, intercepts the diffusive halo and kicks it by coherent deflection through the inter-planar potential
It might provide a continuous multi-turn extraction with high-efficiency and a
better spill quality in a simpler and cheaper way than resonant extraction
Better control of the extraction time and more collimated extracted beam
Minor ring modifications are necessary !!!
Crystals could also support the resonant approach  crystal-resonant hybrid extraction
Unstable region in the phase space acting on sextupoles
driving the tune towards
the resonant value
(e.g. 3rd order)
gradually eject particles driving them out of the stable region towards the separatrix. Septum is needed.
THE SHERPA INNOVATION:
energy loss by synchrotron radiation + bent crystal =
not-resonant multi-turn ultra-slow extraction by a bent crystal [5,6,7]
The most common approach to extract slowly from a circular accelerator is
Resonant multi-turn slow extraction technique [27]

## Slide 5: Sub-GeV lepton crystal beam steering
In the depth of the crystal (z) the fraction of channeled particles decreases exponentially
LD is the dechanneling length, proportional to the particle energy
Particle and bent crystal dependent
In Silicon LD is ~400 μm for ~500 MeV e+ (~25 mm for 7 TeV p+)
Very thin crystals (~15 μm) to reduce the dechanneling and increase the channeling efficiency
Challenging, but feasible
Moreover, a thin crystal will not affect so much the circulating beam
The crystal robustness is guaranteed by several test performed with multi-GeV hadrons [10,26],
but must be considered and evaluated
Encouraging results already obtained with sub-Gev particles using thin crystals
[11,12,13,14,15,16]
High-energy
Hadrons
crystal
Sub-GeV
Leptons
crystal

## Slide 6: DAΦNE crystal slow-extraction layouts
New extraction line
The e+ ring to be modified
The new BTF extraction line
Other existing elements
DAΦNE
Main rings
DAΦNE
Dumping ring
Slow-extraction points
Crystal characterization
apparatus (BTF-2)
New
PADME
options
Actual
PADME
Crystal

## Slide 7: SHERPA extraction simulations
DAΦNE Dumping Ring solution
DAΦNE Main Ring solution
Not local extraction
Injection of pulses ~ the ring length. RF off
Particles slowly lose energy (e.g. by Sync. Rad.) until pass through the crystal that gives a kick to circulating particles
The particles extracted in another point of the ring by the septum
Same hardware of the actual accumulator (except for the crystal)
Some changes in the optics parameters
e+ cross the crystal and are extracted by the same septum used to fill the main ring
Actual configuration, except for the crystal and the extraction septum)
Some changes in the optics parameters
e+ cross the crystal and is extracted around the I.P. (2 different solutions)
MAD-X simulation studies (O. Blanco, S. Guiducci), without changing the layout of the rings (but only the currents), show that with a crystal deflection of 1 mrad it is possible to obtain
pulses of 0.2 ms (Damping Ring) and up to 0.4 ms (Main Ring)
[29] M. Garattini et al., PRAB 25 (2022) 033501

## Slide 8
The Dumping Ring (DR) solution
The best solution:
Extraction septum already present
No hardware modification, except for the Crystal device
Only optics parameter changes
Lower accomplishment and maintenance costs
Extraction steps:
Injection of 100 ns bunches (filling the DR circumference), 10 mm off-axis
The crystal has a transversal displacement of 30 mm from the beam pipe center, to intercept only particles that lose 1 % of the nominal energy (~ 510 MeV)
The crystal will impart to e+ a ~ 1 mrad deflection 
It means ~20 mm horizontal displacement at the septum position, enough to be extracted
Switching off RF, e+ lose spontaneously (for S.R.) 1% of their energy in ~ 1000 turns:
- e+ have 1% of energy spread, so half of them will be extracted in few turns after injection
- The remaining e+ will be slowly extracted in ~ 2000 turns
(1)
(2)
High
Close to 1/4
Displacement at Septum
1 mrad
DR

## Slide 9: Time distribution of the spill
Rate of e+ kicked by the crystal with −20 mm of displacement (or more) at the extraction point
100 turns = 0.1 μs
103 e+ simulated
First try, without any optimization and no hardware modification
Spill length ~ 0.2 ms  ~ 103 times longer than the longer BTF bunch !!!
Tuning the RF, it should be possible to adjust the spill length and time distribution, especially for the first 100 turns
Quite flat time distribution

## Slide 10: The SHERPA Silicon Crystal
“Silicon postal stamp” only 15 μm thick!
Crystal bending holder by LNF (design INFN-Fe/LNL)
2 from CINEL Company
3 improved by LNF workshop
Ultra-thin Crystal by INFN-Fe
5 High quality samples
2 Low quality samples
Quasi-mosasic bending along (111) planes
Beam direction

## Slide 11: Serial production of crystal systems
Only beam measurements can provide crystal/bending quality
In 2023, we managed to glue and bend two INFN-Fe silicon crystals using the first prototypes of bending holder produced at LNF-INFN in 2021
Simplifying gluing, mounting and bending procedure, also an “home-made” bending holder (10 times cheaper!) is able to obtain the same results
INFN-Fe crystal bent by LNF-INFN holder
INFN-Fe crystal bent by CINEL holder
In the next future we will glue and bend other 2 crystal samples
At the first try and without breaking any samples!!! = )

## Slide 12
Crystal characterization at LNF-BTF
BTF apparatus scheme for crystal characterization
~ 3 m
BTF 450 Mev e+ & e-
Tests are perfomed in vacuum
2D Detector (TimePix3)
Crystal chamber
Ultra-thin (27 μm) Mylar windows

## Slide 13
The Crystal chamber
Brass collimator:
Length: 20 cm
Gap: 0.5 x 0.5 mm2
3 axis goniometer
BTF 450 Mev e+ & e-
Ultra-thin (15 μm) Crystal
Crystal characterization at LNF-BTF

## Slide 14: BTF crystal characterization
e+ CH
e- CH
Preliminary!
In December 2023 we manage to characterize the first SHERPA crystal
- We observed ~ 1 mrad deflection of 450 MeV e+ & e- by channeling in bent crystal
- The crystal works very well, analysis is ongoing to estimate efficiency
TimePix3 image
First observation for e+ at E < GeV !!!
TimePix3 image
INFN-Fe
Crystal
+
LNF-INFN
holder

## Slide 15
1) Asymmetric e+ (high energy) e- (low energy) colliders for dark matter studies [22]
2) High quality photon production using e+ channeled in crystal lattices [23]
3) μ production and manipulation in the future μ+/μ- colliders. e+ beams on low density target e- can produce μ with very low emittance and energy spread, reducing cooling procedures [24,25]
4) e+ extraction, collimation, etc…, will be crucial for the new generation of leptons colliders like FCC-ee.
5) Crystals are innovative, effective and cheap, and can also be applied in medical and industrial accelerators, with a strong social-economic impact in the near future
Scientific and technological impact
6) The same is valid for every kind of leptons, negative included
7) The same is valid for higher energies leptons
e+ & e- beam manipulation will be useful not only for PADME…

## Slide 16: Conclusions
SHERPA aims to study and implement a system to slowly extract a high-quality e+ (or e-) beam from one of the DAΦNE accelerator rings using a bent crystal
The proposal is based on ultra slow not-resonant extraction, but crystals could also support the resonant approach
SHERPA’s studies demonstrated the crystal non-resonant slow extraction feasibility both on the Dumping and Main DAΦNE rings
The PADME experiment might be the first user of the SHERPA beam, obtaining enormous advantages in terms of duty-cycle and sensitivity
Three crystal system prototypes are ready, and two are under construction. One of them was characterized in 2023
SHERPA is scientifically interesting per se: indeed no crystal-assisted extraction of positrons has been used so far. Moreover, high-quality positron beams are very rare.
SHERPA can provide an important scientific and technological impact on lepton physics

## Slide 17: References
[1] M. Biryukov, Y. A. Chesnokov, and V. I. Kotov, “Crystal channeling and its application at high-energy accelerators”. Springer Science & Business Media, 2013
[2] W. Scandale et al, PRL 98, 154801 (2007)
[3] F. Ferroni for the RD22 Collaboration, Nuclear Instruments and Methods in Physics Research A 351 (1994) 183-187
[4] The RD22 Collaboration, Phys. Lett. B 357 (1995) 671-677
[5] A. G. Afonin et al., Phys. Rev. Lett. 87.9 (2001): 094802
[6] Fraser, M. A., et al. “Experimental results of crystal-assisted slow extraction at the SPS.”(arXiv preprint arXiv:1707.05151) (2017)
[7] F. Addesa et al., “The SE-CpFM Detector for the Crystal-Assisted Extraction at CERN-SPS”, IBIC’17, MI, USA, 20-24 August
[8] F. M. Velotti et al., Phys. Rev. Accel. Beams, 22.9: 093502 (2019)
[9] F.M. Velotti et al., IPAC2019, Melbourne, Australia (doi:10.18429/JACoW-IPAC2019-THXXPLM2) (2019)
[10] W. Scandale, M. Garattini et al., European Physical Journal C, EPJC-19-09-144.R1 (2019)
[11] S. Bellucci et al., Nucl. Instrum. Meth. Phys. Res. B 252 (2006) 3–6
[12] S. Bellucci et al., JETP Lett. 2013, Vol. 98, No. 11, pp. 649–651
[13] Guidi V. et al., Phys. Rev. Lett. 108.1 (2012): 014801
[14] W. scandale et al., Physics Letters B 734 (2014) 1–6
[15] A. Mazzolari et al., Phys. Rev. Lett. 112 (2014) 135503
[16] Y. Takabayashi et al., Phys. Lett. B 751 (2015) 453
[18] M. Campbell et al., Nucl. Instrum. Meth. A 633 (2011) S1-S10
[19] A. Natochii et al., JINST 14 P03018 (2019)
[21] M. Raggi, EPJ Web Conf. 142 (2017) 01026
[22] B. Wojtsekhowski et al., arXiv:1705.00051 [physics.acc-ph]
[23] U.I. Uggerhøj, Nucl. Instrum. Meth. B355 (2015) 35
[24] G. S. Sushko et al., J. Phys.: Conf. Ser. 438 (2013) 012018
[25] M. Antonelli et al., Nucl. Instrum. Meth. in Phys. Res. A 807 (2016) 101–107
[26] W. Scandale, M. Garattini et al., JINST_061P_0621 (2021)
[27] S. Guiducci et al., IPAC2018, Vancouver, BC Canada
[28] E. Bagli et al., Eur. Phys. J. C (2014) 74:2996 [29] M. Garattini et al., Phys. Rev. Accel. Beams 25 (2022) 033501
[30] D. Annucci, “Sub-GeV positron channeling in bent crystals” (MasterThesis 2022)

## Slide 18
Thank you for your attention !
And thank you very much to the whole SHERPA team, LNF and CSN5!!!
LNF: P. Gianotti, S. Guiducci, O. R. Blanco-Garcia, A. Liedl, M. Mancini, T. Napolitano
INFN-Roma1: P. Valente, M. Raggi, D. Annucci, E. Long
And also to:
INFN-Fe: V. Guidi, A. Mazzolari, L. Bandiera, M. Romagnoni, M. Soldani, M. Tamisari, A. Sytov
INFN-LNL: S. Carturan, D. De Salvador, F. Sgarbossa
“ The higher you climb,
the further you see.
He who sees further,
dreams longer”
Walter Bonatti (Italian Climber)

## Slide 19: SPARE

## Slide 20: Existing e+ beams
There is no slow extraction of primary positron anywhere in the world !!!
Electron-positron colliders
Super KEKB and BEPC-II
  No extracted beam
DAΦNE
  Primary (< 500 MeV) and secondary (< 700 MeV) positrons.
  From LINAC, not extracted
VEPP
  Not an extracted beam, but by-pass in the VEPP-3 ring (510 MeV)
Secondary positrons
DESY-II
  0.5 to 6 GeV/c positrons
CERN SPS North Area
  H4 “dedicated” beam-line, but production also possible in H2 and may be H6-H8
  Up to 200 GeV with variable purity

## Slide 21: Proposed high-energy positron beams
Electron-positron colliders
DAΦNE
- Proposal for resonant and not-resonant extraction of primary positrons at 510 MeV
- Proposal for LINAC modifications for bunch extension < 300 MeV
CESR
- Proposal for 𝑛 + 1/3 resonant extraction of primary positrons at 6 GeV not approved
LINAC-based
CEBAF at Jefferson Lab
- Proposal for 11 GeV primary positron source (JPOS), not yet approved, ≈5 years of
construction
- Possibility of secondary positron beams, ???
FACET-II at SLAC
- Proposal for 10 GeV primary positrons (produced from extracted electrons, damped
and re-accelerated)
- Approved but staged to Phase-2, > 2022

## Slide 22: Crystal extraction history
  (1990-95) - RD22 at the CERN-SPS as a test bed of beam extraction at LHC: crystal high-efficiency extraction of multi-GeV p+ [3-4]
  (1993-98) - E853 at the FNAL-Tevatron as a test bed for the SSC: crystal high efficiency extraction of 900 GeV p+
  (2001) - The CERN-INTAS programmes on crystal technology: crystal high efficiency extraction of 70 GeV p+ by a short crystal (in IHEP U-70) [5]
  (2016) - UA9 at CERN-SPS: crystal assisted not-resonant & not-local slow extraction of 270 GeV p+ in the TT20 north area extraction line [6,7]
  (2018) - UA9 at CERN-SPS: crystal “virtual” not-resonant local beam extraction of 270 GeV p+ in channeling mode
  (2018) - UA9 at CERN-SPS: crystal shadowing of the ES-septum and assisted resonant slow extraction of 400 GeV p+ [8,9]

## Slide 23
Primary Beam
Crystal
+
Goniometer
DAΦNE e+ beam
Extracted beam
Energy loss by Synchrotron Radiation (RF off)
Beam halo
Multi-turn not resonant slow extraction
Not-local extraction
A e+ not deflected by the crystal not necessary will be lost, but can be extracted in a next turn

## Slide 24: The Main Ring (MR) solution
e+ x-displacement at the crystal position as a function of number of turns
At the crystal: 8 mm at turn 6
e+ x-displacement at the septum position as a function of number of turns
At the septum: ~ 20 mm at turn 6
The beam can be deflect by the crystal and extracted in the same turn
Same approach of the DR case

## Slide 25: Crystal piezo bending holder
~ 15 μm Crystal
Crystal bending by
linear piezo-motor
Torsion correction
by piezo-finger actuator
The crystal bending and its torsion can be controlled and corrected remotely and in real time !!!
Innovation:
Crystal bending holder by LNF (design INFN-Fe/LNL)
2 prototypes
Ready
+
2 prototypes
to be mounted

## Slide 26: Crystal gluing and mounting system upgrade
Simpler and accurate gluing of the silicon crystal on the bending holder
Old gluing system and procedure
(INFN-Fe and LNL- INFN)
Special double sided tape
+
Inside vacuum oven
2022
INFN-Fe
crystals
VS
New gluing system and procedure (LNF-INFN)
Gluing crystal
support
Simple two-components
glue
2023
LNF-SPCM
holder
CINEL
holder

## Slide 27: Crystal/holder support and box
This 3D-printed support is very useful during the gluing procedure and also to fix the crystal for a safe transport and manipulation
At LNF-SPCM we also realized a dedicated support
+
box for the crystal/holder system

## Slide 28: Sub-GeV crystal beam steering: e+ & p+
Ultra-thin crystal mirroring
2012 – Mirroring and Volume-reflection of 2 MeV p+ [13] (nanometric crystal!!!)
- ultrathin silicon crystal (100 nm, half wavelength of the planar channeling oscillation)
- Deflection: ~ 5 mrad (CH), ~1 mrad (VR)
- Efficiency: 58% (CH), 42% (VR)
UA9 in 2014 – Mirroring of 400 GeV p+ [14]
- 26,5 µm thick silicon crystal
- Deflection: ~ 10 µrad (CH)
- Efficiency: 80% (CH)
Sub-GeV e+ crystal beam steering in two different configuration
at the BTF (Beam Test Facility, INFN-LNF):
2006 – Channeling of 480 MeV e+ [11]
- 1 mm thick silicon crystal
~10 mrad with ~10% of efficiency
2013 – Multi volume reflection of 100 MeV e+ [12]
5 bent silicon crystals in a raw
5 x ~100 µm thick silicon crystal
5 mrad with ~30 % of efficiency
The idea is to use the solid expertise developed to
scale crystal extraction from multi-GeV hadron beam to < 1 GeV positron beam

## Slide 29: Sub-GeV crystal beam steering: e-
2014 – (MAMI) Channeling of 855 MeV e- [15]
30 μm Silicon crystal (111),
Deflection: 910 μrad
Efficiency: 20%
2014 – (MAMI) Volume reflection of 855 MeV e- [15]
30 μm Silicon crystal (111),
Deflection:191 μrad
Efficiency: 77%
2016 – (SAGA-LS) mirroring of 255 MeV e- [16]
ultrathin silicon crystal (0.74 µm, half wavelength of the planar channeling oscillation), deflection
Deflection: 450 µrad
Efficiency: 29%
Also e- crystal beam steering has been performed in different conditions, giving useful references for leptons coherent effects in bent crystals and for thin crystal technology
Negative particle deflection is always less efficient then for positive ones

## Slide 30: SHERPA 2.0: what else to extract from DAΦNE
By-pass of the dumping ring
The e+ & e- rings has to be separated at the interaction points
Adjust the DAΦNE ring optics to fit with the crystal system
Mount the crystal system (gonio, crystal & monitoring)
An extraction line
New extraction line
The e+ ring to be modified
The new BTF extraction line
Other existing elements
DAΦNE
Dumping ring
Not included in the project presented here…

## Slide 31: The crystal/goniometer assembly
Measurement table
Beam
Crystal
Axis1- Linear
Axis2- Rotational
Axis4- Linear
Axis3- Tilt

## Slide 32: Crystal simulations
To simulate coherent processes in crystals exist several crystal simulation routine, both full analytical and Monte Carlo
They are mainly focused and optimized to high energy hadrons particles, benchmarked with a large amount of data available in literature
At the moment in SHERPA we are developing two Monte Carlo routines, adapting them to sub Gev leptons (e- and e+): GEANT4 [28] and FLUKA, ideal to simulate crystal behavior integrated in an accelerator machine
The GEANT4 routine shows nice performance for sub-GeV e-, and now we are developing the sub-GeV e+ version (CHeff for e+ is higher w.r.t. e-)
The FLUKA one is developing in collaboration with the FLUKA team at CERN
SHERPA data with sub-GeV e- and e+ will be extremely useful also for simulation benchmark in the next future

## Slide 33: Crystal simulations (e-)
MAMI measurements [15]
GEANT4 Monte Carlo
simulations [28]
We managed to well reproduce the angular scan of a “SHERPA like” crystal tested at the MAMI facility with 855 MeV e- [PRL 112, 135503 (2014)]
The difference in channeling efficiency (~ 10%) is probably due to the “rechanneling process”, not yet implemented in 2021…
The CHeff for negative particles is always lower w.r.t. positive particles
CHeff = 20%

## Slide 34: Crystal simulations (e+)
Analytical simulations
GEANT4 Monte Carlo
simulations [28]
We did also a comparison between GEANT4 Monte Carlo simulations and Analytical one of a “SHERPA like” bent crystal for 855 MeV e+
Preliminary
The difference from Analytical and Monte Carlo simulations is probably due to lack of the data benchmark
Measurements and data analysis are in progress to improve simulations…
Analytical: CHeff ≅ 80%
GEANT4: CHeff ≅ 88%

## Slide 35: CERN SPS crystal extraction (UA9)
2016 - slow not-local extraction of 270 GeV p+ in channeling mode [6,7(M.G.)] beam into the TT20 extraction line towards the North Experimental Area of the SPS was demonstrated using the extraction septa and a bent crystal
UA9 CpFM
(“Cherenkov for proton Flux Measurements”)
detector for SPS and LHC has seen the extracted beam
Extraction in 2 turns
2018 - “Virtual” not-resonant local beam extraction of 270 GeV p+ in channeling mode
Joint activity with TE/ABT and EN/STI
Circulating beam
270 GeV p+
NDCH(xi)/dx
NCH
Extracted beam
0.2 mm thick virtual septum
Edge of the circulating beam core
loss ratio R ≈ NDCH / NCH= ~6 ‰
Halo density in channeling mode along the horizontal axis
(self-normalized to the total No of impinging particles)
Timepix

## Slide 36: Shadowing of the ES-septum with a bent crystal
Xn
Channeled particles
not impacting the septum
Septum
Phase space during resonant extraction
Xn’
Schematic crystal shape for shadowing
A loss reduction at the ZS of 40%
was recorded on
1-second 400 GeV spill
Protons are deflected 5m upstream of the ES, to avoid loss with the anode wires
Joint activity with TE/ABT and EN/STI
Angular position actuator
180 𝜇rad bent crystal

## Slide 37: SPS slow extraction with crystal shadowing
This technique is developed to reduce the number of particles on the SPS
extraction septum (ZS wires) and consequently the extraction losses
A crystal is used upstream to shadow the ZS wires deflecting the particles that would hit him
In 2018, a feasibility test has been performed and a reduction of 40 % of losses with protons and 30 % with lead ions was observed

## Slide 38: SHERPA APPLICATIONS
Resuming the main goals
Spill features pursued:
- Energy spread: Δp/p < 10-3
- Emittance: ε < 10-6 rad⋅m
- Length: ms < Δt < s
The most immediate application of such beam is PADME [21], already running at the BTF, but currently strongly limited by the duty cycle
With the e+ beam from the LINAC, the maximum rate on the target is <102 e+/ns, keeping the event pile-up and the background at an acceptable level
Using the SHERPA extraction, PADME could increase the statistics by a factor 104 and its sensitivity by a factor 102, obtaining a cutting-edge discovery potential
Even an unrealistic very bad extraction efficiency of 5%, with the worst-case scenario of a beam pulse length of 100 μs, SHERPA still improves by a factor 50–100 the PADME sensitivity with respect to the plain LINAC beam
A beam with such characteristics is interesting for any kind of fixed target experiment
Current spill features from LINAC:
- Energy spread: Δp/p ~ 10-3
- Emittance: ε < 10-5 rad⋅m
- Length: Δt ~ 200 ns
VS

## Slide 39: Quasi c.w. positron beam applications
PADME dark photon sensitivity
(invisible decays)
6 months of data-taking at DANE
using resonant estraction, 0.4 ms spills
(optimistic)
PADME dark photon sensitivity
(invisible decays)
1 month of data-taking at DANE
using ultra-slow extraction,
(10-4 extraction efficiency)
(P. Valente, Ferrara workshop on crystal applications, 13 Apr. 2019: https://agenda.infn.it/event/15101/)
PADME is searching for invisble decays of a dark photon A’ eventually produced in the annihilation: e+ e- → A’ γ (e+ beam on fixed target e-)
ε2 = coupling parameter
ε2 = coupling parameter
3 days
30 days
PADME@BTF