## Slide 1: Slow Extraction of Mixed He-2+ and C-6+ Beams for Online Range Verification
5th Slow Extraction Workshop 2024
Wiener Neustadt / MedAustron – 12.-14.02.2024
Elisabeth Renner, Matthias Kausel
elisabeth.renner@tuwien.ac.at
Nadia Gambino, Florian Kühteubl, Valentin Kirchweger, Fabien Plassard, Dale Prokopovich, Claus Schmitzer, Markus Wolf

## Slide 2: Outline
Motivation for mixed 4He2+ and 12C6+ beams
Feasibility study for delivering mixed beams at MedAustron
Considerations for slow extraction of the mixed beam
Outlook & conclusion

## Slide 3: Mixed Beams for Online Range Verification
4He2+ and 12C6+ exhibit very similar charge-to-mass ratio.
  Simultaneous acceleration & delivery to irradiation room could be possible.
  Extraction at (almost) same energy per nucleon
Helium has around 3 times the range of carbon at the same energy per nucleon.
  Possibility for online range verification, ion CT, …
  If extracting an intensity ratio of He:C=1:10, 4He2+ accounts for only of the dose delivered to the patient [1].
  Note: Helium Bragg peak needs to traverse patient, only possible for larger tumor depths.
  Described & proposed in refs. [1-3].
  First experimental results at GSI in 2023 – See David Ondreka’s talk!
Schematic mixed beam irradiation, Mazzucconi et. al [1]
[1] D. Mazzucconi et.al (2018), https://doi.org/10.1002/mp.13219
[2] L Volz et al (2020), Phys. Med. Biol. 65 055002
[3] Graeff et al (2018), https://doi.org/10.1016/j.ejmp.2018.06.099

## Slide 4: Feasibility Study: Mixed Beams @ MedAustron?
Background: MedAustron delivers 12C6+ and p+ for clinical treatment, 4He2+ is currently being commissioned for non-clinical research.
Objective: Assess the feasibility of delivering a mixed beam for nonclinical research (IR1).
C. Accelerate and extract mixed beam
A. Assess options for
producing the mixed beam in novel sources,
+ transport through LINAC.
D. Mixed beam detection:
“Mixed beam dose delivery system”
Detectors for online range verification & imaging in IR1
B. Assess options for mixing the beam during injection.
PhD student started in 2023
Collaboration between MedAustron, TU Wien & HEPHY
Infrastructure at MedAustron:
Separate ion sources producing 4He2+ (q/m≈0.5) and 12C4+ (q/m≈1/3)
Transport with different q/m through the LINAC, stripping after the LINAC
(Nearly) same q/m≈0.5 in the synchrotron

## Slide 5: Scenarios for Mixed Beam Generation
Generation in a single ion source is currently not possible at MedAustron.
  Would require novel source and depending on the source LINAC upgrades (LINAC can only accelerate ).
Investigate sequential injection into the synchrotron as (temporary) alternative production scheme:
  “Double multi-turn injection”
    1st injector cycle: Inject 4He2+ into synchrotron + maintain beam at flat bottom (~1s)
    2nd injector cycle: Inject 12C6+ on top of 4He2+ :
      Adapt injection bump to sustain small He core
    Capture, acceleration + extraction of ion mix
  Status:
  Managed to operate injector in proposed way & inject He and C sequentially*.
  So far, no show-stoppers from the control system identified.
  Next steps: optimize injection bump, harmonize injection energy, capture, acceleration, …
* Note: So far, tests focused on demonstrating technological feasibility. He-2+ was still lost when injecting C-6+, injection has not yet been optimized.
Matthias Kausel, Valentin Kirchweger

## Slide 6: Slow Extraction of Mixed He-2+ & C-6+ Beams

## Slide 7: Objective & Simulation Set-Up
Objective: Proof-of-principle simulations of the slow extraction of the mixed He2+/C6+ beam to identify challenges & propose mitigation:
Results serve as input for mixed beam generation and detection studies.
Preliminary aim: deliver constant and/or known intra-spill particle fluence ratio of the two species:
Simulation performed using Xsuite [4]:
Enables 6D-tracking of ions with non-nominal , also for bunched beams.
Results in this presentation obtained using custom version with fixed bugs concerning non-nominal q/m, as described in issue 446 [5].
[4] https://github.com/xsuite/xsuite [5] https://github.com/xsuite/xsuite/issues/446
Preliminary target is ~ He:C = 1:10 
Is ion distinction possible in a dose delivery system?
  Yes: Possibility to adapt and/or scanning during the spill ?
  No: Can we guarantee a constant species ratio?
Many thanks to all Xsuite developers :)

## Slide 8: Transverse Distribution Prior to Extraction
The considered options for generating the mixed-beam result in different initial horizontal emittances.
Thus, for the current proof-of-principle simulations, we consider a range of horizontal emittance ratios!
I) Mixed beam generation in ion source
He-2+
C-6+
He-2+
C-6+
Assume:
II) Sequential injection + mixing at flat-bottom
Note: All simulations performed with 10k He-2+ and 10k C-6+ particles  Results will be subsequentially normalized to assumed initial intensity ratio of 1:10
Assume:

## Slide 9: Longitudinal Distribution Prior to Extraction I
4He2+ has higher rigidity than 12C6+ (reference particle) due to the smaller q/m.
… behaves in a magnetic field like a particle with (see e.g. [7])
    nominal charge-to-mass ratio, i.e. ,
    and an effective relative momentum per mass offset
A particle with
  and a relative momentum per mass offset
[7] P. Hermes (2016), PhD Thesis, CERN-THESIS-2016-230, https://cds.cern.ch/record/2241364/

## Slide 10: Longitudinal Distribution Prior to Extraction II
Synchronous 4He2+ and 12C6+ with same revolution frequency
Rigidity + path length difference yields relative velocity offset (see e.g. [6])
here:
[6] P. Bryant (1993), The Principles of Circular Accelerators and Storage Rings, Chapter 7.7.6
He-2+
C-6+
and hence relative momentum per mass offset
which depend on the difference between extr. and transition energy
Crucial for small medical machines, e.g. @ MedAustron
Due to the rigidity offset, 4He2+ is accelerated to a slightly higher momentum/mass than 12C6+.

## Slide 11: Tune Distribution Prior to Extraction I
[7] P. Hermes (2016), PhD Thesis, CERN-THESIS-2016-230, https://cds.cern.ch/record/2241364/
Momentum per mass distribution
He-2+
C-6+
Tune distribution
here: ,

## Slide 12: Tune Distribution Prior to Extraction II
Consequently, the tune separation between 4He2+ and 12C6+ depends on the extraction energy ().
He-2+
C-6+
here: ,
here: ,

## Slide 13: Proposed Extraction Strategy
A
A
Q
Q
Baseline: Extraction based on amplitude selection (RFKO)
Multiple knobs for controlling intra-spill ion fluence ratio depending on emittance ratios, extraction energy, …
    E.g., (tune separation), sextupole strength (ratio of stable areas), RFKO excitation signals / combinations, … .
Next slides: first, illustrative examples ...
For now, coasting beams preliminarily based on machine settings within the parameter range described in [8]  to be adapted
Today: RFKO excitation (no variation of , …)
[8] F. Kuehteubl, IPAC23, doi:10.18429/JACoW-IPAC2023-TUPM091
See talk by F. Kühteubl in the afternoon!
He-2+
C-6+
Summary/Requirements: Aim to simultaneously extract (with similar particle fluence) two ion species, which can feature
energy-dependent tune separation (
and potentially different horizontal phase space distributions.

## Slide 14: Test Case 1: He & C with Similar Horizontal Emittances
A
B
C
Emittance ratio:
Extraction energy: 400 MeV/u
Intensity ratio in the synchrotron: He:C=1:10
Excitation: single, constant BPSK signal with
Note: Example to show dependency, non-optimized excitation for C-extraction
A. Initial helium peak during sextupole ramp
Turn 150k
B. Extract with depending on applied signal.
C. Flexibility to abort extraction once majority of C is extracted.
Here arb. threshold = 90% of C extracted.
He-2+
C-6+
 Flexibility to close chopper
Work in progress

## Slide 15: Test Case 1: Sensitivity to PSK Side Lobes
E = 400 MeV/u
E = 150 MeV/u
Re. B) First tests to assess impact of applied RFKO signal on (t) by changing BW of BPSK signal
Demonstrates sensitivity of
to frequencies of nulls and maxima of the side lobes.
Next: combine more targeted multiple (amplitude modulated) signals, adapt Q’ etc. to stabilize ,, …
Work in progress

## Slide 16: Test Case 2: “Pre-Heating” of Helium Core
Emittance ratio:
Extraction energy: 400 MeV/u
Intensity ratio in the synchrotron: He:C=1:10
Excitation: single, constant BPSK signal with
Ramp sextupole + start extraction
He-2+ heating
For selectively increase 4He2+ emittance prior to extraction:
Apply RFKO excitation only (mainly) in frequency range of 4He2+.
Here: first example using frequency modulation
Demonstrates beneficial effect, to be optimized!
A
B
A
B
Work in progress

## Slide 17: Conclusion & Next Steps
Take aways:
Study the feasibility of delivering a mixed beam for nonclinical research (TU Wien, MedAustron, HEPHY).
Proof-of-principle simulations using Xsuite for slow extraction of ion mix currently being performed.
Due to the beam rigidity offsets between He-2+ and C-6+, RFKO selected as baseline extraction mechanism.
Evaluating robustness of extraction to differences in momentum/mass between He-2+ and C-6+ (depending on extr. & transition energy) & impact of different horizontal emittance ratios.
Desired input: what is the acceptable range for the intra-spill ion fluence ratio?
Only the beginning of the journey - next steps:
Study different scenarios to further develop extraction set-up, …
  RFKO signal composition,
  machine settings (chromaticity, tune, momentum spread),
  momentum acceptance of extraction line,
  ripples, bunched beams, …
Thank you for your attention!