## Slide 1: Beam dynamics in accelerators: nonlinear dynamics and experiments Wolfram Fischer, BNL 1st XBEAM-XRING Workshop – Beam Dynamics meets Magnets 2-4 December 2013, Darmstadt
Notes: 40 min (including questions) = 32 slides

## Slide 2: Acknowledgments
N. Abreu/Milas, R. Bartolini, J. Bengtsson, O. Boine-Frankenheim, A. Burns, M. Bai, M. Blaskiewicz, O. Brüning, Y. Cai, A. Chao, R. Calaga, J. Camas, P. Cameron, G. Crockford, E. Carlier, L. Ducimetière, M. Ellison, A. Faugier, G. Ferioli, E. Forrest/P. Nishikawa, G. Franchetti, M Furman, D. Gall, J. Gareyte, P. Görgen, J.J. Gras, M. Giovannozzi, X. Gu, W. Herr, B. Holzer, I. Hofmann, G. Hofstätter, H. Jakob, R. Jung, J. Koopman, J.-P. Koutchouk, H.-J. Kim, M. Laffin, J. Laskar, T. Linnecar, Y. Luo, N. Malitsky, W.W. MacKay, E. Metral, E. McIntosh, I. Milstead, C. Montag, S. Nagaitsev, K. Ohmi, S. Peggs, F. Pilat, V. Ptitsyn, G. Robert-Demolaize, T. Roser, T. Satogata, W. Scandale, F. Schmidt, P. Schmüser, M. Seidel, T. Sen, G. Stancari, S. Tepikian, V. Shiltsev, M. Syphers, F. Ruggiero, R. Talman, R. Tomàs, D. Trbojevic, A. Valishev, M. Vogt, L. Vos, S.M. White, F. Willeke, V. Ziemann, F. Zimmermann, …

## Slide 3
Content
Stability of single particle motion – the dynamic aperture
Sources and descriptions of nonlinear magnetic fields
Experimental methods and simulation tools to assess stability of motion

## Slide 4
Particle motion in storage rings
- dipoles (bending) define design orbit - total bend angle = 2p
N
S
- quadrupoles (focusing) define s-dependent beam envelope (for given e) - focusing force proportional to transverse amplitude - number of transvers oscillations per turn = tune nx,y
N
N
S
S
Already possibilities for instabilities
n = integer and dipole error
n = half integer and quadrupole error
Magnet pictures from W. MacKay and T. Satogata, USPAS 2013.
s

## Slide 5
Sources of nonlinear fields
Sextupoles – correct for change in focusing strength for particles with energy deviations dp/p
Octupoles – introduce tune spread and Landau damp instabilities
Field errors of magnets, in particular
  superconducting magnets without pole tips
  when/where beam is large (injection, final focus quadrupoles)
amplitude
force
quadrupole
sextupole
octupole
higher order multipole magnets create very fast rising field at high amplitudes (strong nonlinearity)
Tevatron quadrupole
N
N
N
S
S
S

## Slide 6
Particle motion with nonlinear forces
Oscillation frequencies (tune n) is amplitude dependent
Infinite number of resonances: k, l, p integers (not all are equally dangerous)
L. Evans, LHC w/ BB, CERN courier (2008).
x
x’
Nonlinear forces give rise to chaotic motion. Sextupole already can generate all nonlinear phenomena.

## Slide 7: Hamiltonian description of motion
particle coordinates
1/Kx,z – bending radii
(Ax,Az,As) – vector potential
equations of motion
solved piece-wise in a simulation
G. Ripken and F. Schmidt, DESY 95-063 and CERN SL/95-12 (AP).
Hamiltonian near a resonance
detuning
resonance driving term
action-angle variables
actions (Ix,Iy) are constants for linear motion
tunes

## Slide 8
Nonlinear phenomena in storage rings
Phenomena observed in experiment and simulations:
Amplitude detuning
Resonance driving terms
Phase space deformations
Smear (amplitude variations)
Tune response matrix (sampling nonlinear fields with closed orbit distortions, G. Franchetti, PRST-AB 11, 094001 (2008))
Resonance island in phase space
Echoes (only possible with detuning)
Tune and amplitude diffusion
Halo formation
Beam size growth
Particle loss
Dynamic aperture

## Slide 9
Chaotic particle motion
Motion in nonlinear systems (accelerators) is chaotic at large amplitudes chaotic = deterministic but not predictable chaoticity tested by following distance d of 2 initially closed particles
Regular motion: d ~ t
10-5
Chaotic motion: d ~ exp(t)
Chaotic particle motion gives to a dynamic aperture
1

## Slide 10
The dynamic aperture
DA range
DA depends on time scale of interest
Frank Schmidt, Ph.D. Thesis (March 1988)

## Slide 11
Tune modulation phase diagram
Dynamic aperture also affected by time-dependent machine parameters,
e.g. tune modulation from 50/60 Hz power supply harmonics
T. Satogata et al., PRL 68, pp. 1838 (1992)
Resonance island with tune modulation

## Slide 12
Field description – circular multipoles
B0 magnetic field at reference radius r0 with r0 ≈ 2/3 or beam pipe radius
b1 dipole, b2 quadrupole, …, a1 vertical dipole, a2 skew quadrupole, … bn,an usually given in units of 10-4 of B0
Now standard notation, previously US also used b0 for dipole dipole etc. and different sign for an
y
x
r
q
r0
Multipoles can be measured with rotating coils or hall probes.

## Slide 13
P. Schnizer et al., IEEE Transactions on Applied Superconductivity, Vol. 18, No. 2, pp. 1605-1608 (2008). P. Schnizer et al., EPAC’08, pp. 1703-1705 (2008).
Used if elliptical beam pipe must be filled with beam, e.g. SIS100.
New coordinates:
h0 reference ellipse
B1 elliptical dipole, B2 elliptical quadrupole, …, A1 elliptical vertical dipole, A2 elliptical skew quadrupole, …
Field description – elliptical multipoles, see Talk P. Schnizer

## Slide 14
AGS warm snake
AGS cold snake
RHIC cold snake
Helical magnets used e.g. for wigglers/undulators, spin manipulations, muon cooling.
New coordinates:
l helical wave length, k helical wave number
B1 helical dipole, B2 helical quadrupole, …, A1 helical vertical dipole, A2 helical skew quadrupole, …
Field description – helical multipoles

## Slide 15: Fringe fields – important for short magnets (small rings)
Descriptions on previous slides for infinitely long magnets – a good approximation for large machines
For short magnets (small rings) fringe fields can dominate beam dynamics
Fringe fields often models with computer
Some analytical models available
R. Baartman, PRST-AB 15 074002 (2012).
Analytical potential for quadrupoles, long and short
Smooth change in strength function resulting lower field aberrations

## Slide 16
Nonlinear fields from beam-beam interaction
Amplitude dependence of beam-beam kick fundamentally different from magnets strength not monotonically increasing in BB cannot be described by multipoles for r ≈ s
beam-beam kick
magnet kicks
electric field
magnetic field
(the other beam is not like a magnet – at least 50% of the force is from the electric field)
Tevatron
RHIC

## Slide 17: Primary beam observation tools
Beam Position Monitors (BPMs) – Turn-by-Turn
  Buttons (higher frequency resolution)
  Striplines (higher sensitivity)
Beam Profile Monitors
  Wire scanners
  Ionization Profile Monitors
  Synchrotron Light Monitors (mostly e+/e−)
Beam Loss Monitors (BLMs)
  Ionization chambers
  PIN diodes
Kickers to fill the aperture
AC dipoles for sustained oscilation
Collimators to define the aperture
…
LHC
B.R. Poole, et al. PAC’97
R. Connolly et al. BIW10

## Slide 18: Experimental techniques
Make small beam (pencil beam) – approximation for single particle
Kick beam to amplitude of interest OR use AC dipole (dipole oscillating near tune but outside distribution, M. Bai – AGS)
Observe beam in BPMs
Observe time dependent profile

## Slide 19: Simulation tools – particle tracking
Particle tracking
Simulate single particle motion
Model for all accelerator components (magnets, drifts, cavities, …)
Integrator (often kick approximation) – symplectic for hadron beams
Programs: SixTrack, MAD, SimTrack, Lifetrack, …
Simulations steps
Good model of linear machine (orbit, coupling, chromaticity, beta-beat, misalignments)
Include known effects such as tune ripple, …
Analysis of short-term behavior (phase space, chaoticity, …)
Reproduce detuning
Long-term tracking
Parameter scans (e.g. multipole error range and distribution)

## Slide 20
Nonlinear phenomena in storage rings
Phenomena observed in experiment and simulations:
Amplitude detuning
Resonance driving terms
Phase space deformations
Smear (amplitude variations)
Tune response matrix (sampling nonlinear fields with closed orbit distortions, G. Franchetti, PRST-AB 11, 094001 (2008))
Resonance island in phase space
Echoes (only possible with detuning)
Tune and amplitude diffusion
Halo formation
Beam size growth
Particle loss
Dynamic aperture
[Reference: Accelerator Handbook, Nonlinear experiments]

## Slide 21
Experimental Poincaré surface of section – IUCF
D.D. Caussyn et al., PRA 46, pp. 7942 (1992)
45 MeV cooled p beam, kicked to different amplitudes
Used to beam position monitors (BPMs) to reconstruct beam position and angle at one location in the ring
Phase space plot shows 3rd order resonance
Can be compared to a simulation

## Slide 22
Amplitude dependent tune measurement – VEPP-4M
V. Kiselev et al., PA 57, pp. 65 (1997)
1.8 GeV e− beam, kicked to different amplitudes
FFT of 4096 turns
Linear dependence for sextupoles and octupoles (nonlinear for higher order multipoles, and beam-beam)
Can be compared to a simulation
Horizontal betatron tune as function of horizontal action (emittance)

## Slide 23
Measurement of resonance driving terms – RHIC
R. Tomàs et al., PRST-AB 8, 024001 (2005)
10 GeV/n Au beam
Sustained transv. oscillation with an AC dipole (sustained oscillation)
Observation of oscillation around the ring with BPMs
Resonance driving terms derived
Compared to a simulation

## Slide 24
Experimental frequency map – ALS
D. Robin et al., PRL 85, pp. 558 (2000); FMA: H.S. Dumas, J. Laskar, PRL 70, 2975 (1993).
1-2 GeV e− beam, kicked to different amplitudes
Frequency Map Analysis (FMA) of 1024 turns identified resonances
Compared to Frequency Map Analysis (FMA) of model

## Slide 25
Amplitude diffusion measurement – HERAp
M. Seidel, PhD Thesis, DESY 94-103 (1994)
920 GeV p beam, collimator retracted
Empty transv. space fills again with beam
Observed with loss monitor at collimator
Can be compared to a simulation (difficult – needs many particles, has large errors)

## Slide 26
Amplitude diffusion measurements in halo
G. Stancari, Beam-Beam 2013 (2013).
[F. Zimmermann, PA 49, pp. 67-104 (1995) calculated DJ over ~40 orders of magnitude]

## Slide 27
Echoes
measurement in RHIC, Au79+ injection
hor
ver
Echoes well known in plasma physics, proposed for accelerators by G. Stupakov (1992), observed in longitudinal plane in Fermilab AA (1996) and SPS (1996).
echo response sensitive to amplitude diffusion
Can be compared to a simulation – too insensitive for IBS [S. Sorge et al, ICAP 2006]
dipole kick
filamentation
quadrupole kick
echo

## Slide 28
Dynamic aperture measurement
Dynamic aperture = largest amplitude where most particles will survive over a time-period of interest
In simulation:
Place particles over amplitude range, track over time period of interest  survival plot
In experiment:
Place particle over amplitude range (kick), observe transverse profile as function of time
Frank Schmidt (1988).

## Slide 29
Dynamic aperture measurement
1. Kick beam over aperture to have many particles over border of stability (due to detuning beam will filament in phase space)
2. Measure transverse profile as function of time (wire scanner, IPM)
Note: Filling aperture with many small kicks is possible, but gives poor signal at DA.
Time-dependent dynamic aperture

## Slide 30
Dynamic aperture measurement and simulation – SPS
W. Fischer, M. Giovannozzi, F. Schmidt, PRE 55, pp. 3507 (1995)
120 GeV p beam, kicked to 5 rms beam sizes
Time-dependent transverse profile measured with wire scanner
Compared to a simulation: agreement within 10%, over 5 min

## Slide 31: Integrable Optics Test Accelerator (IOTA) at Fermilab
S. Danilov and S. Nagaitsev, PRST-AB 13, 084002 (2010); S. Nagaitev, AAC (2013).
e/p storage ring 50-150 MeV
Goal of IOTA is to provide
practical nonlinear focusing with zero resonance strength with either
Special magnets
Electron lenses
Successful implementation could accommodate very large tune spread
Example of stable trajectory in nonlinear lattice
(x,px)
(y,py)
(x,y)
(x,y,px)

## Slide 32
Summary
SIS-100 transverse apertures at injection (0.2 GeV/u)
dynamic
aperture
magnet
aperture
lattice
aperture
beam
G. Franchetti (2008)
Nonlinear magnets are needed to correct for chromatic aberrations (sextupoles), and to suppress instabilities (octupoles)
Nonlinear magnetic fields also arise from magnet errors (especially in superconducting magnets without pole tips)
These fields give rise to a dynamic aperture (limit for stable amplitudes – DA depends on time scale of interest)
Nonlinear dynamics experiments have shown that well-prepared simulations can predict DA within 10-20% over time scales of minutes, simulations also useful for time scales of hours
Today there is enough computing power to calculate DA directly (even with parameter scans); faster precursors that must be correlated with the DA are only needed for preparation (e.g. phase-space distortions, detuning, smear, tune-diffusion, test for chaoticity)

## Slide 33
AGS warm snake pictures
Example of helical magnet