## Slide 1
SIS18 Injection:
Parameter studies on MTI with space charge and longitudinal aspects
Sabrina Appel, GSI, Beam physics

## Slide 2: Outline
- Introduction to the injection process into the SIS18 (specific aspects)
- Longitudinal aspects
- Multi-turn injection model and parameter studies
- UNILAC emittance, horizontal tune and effect of space charge
- Summary and Outlook
Notes: Work the statement stronger out!
Codes and model should explain!

## Slide 3: Overview injection into SIS18
- We assume that the longitudinal and transverse planes are decoupled
- Final full momentum spread after injection should be within the rf bucket area
- The micro-bunches debunch, filament and form a
coasting beam within a few turns
- Horizontal multi-turn injection
- During injection the RF in the SIS18 is turned off
- Transverse beam size (4 rms physical emittance) should be within the machine acceptance
Trev=5 μs
(equivalent parabolic distribution)
(equivalent K-V distribution)

## Slide 4: Longitudinal beam quality Debunching of the micro-bunches
- The space charge energy of the micro-bunches is transformed into incoherent thermal momentum spread
- Debunching in the SIS18:
- Longitudinal perveance
- The geometry factor describes the influence of the transversal beam distribution on the longitudinal motion
- See for more information:
S. Appel, O. Boine-Frankenheim, Phys. Rev. ST Accel. Beams 15, 054201 (2012)

## Slide 5: Longitudinal beam quality Debunching of the micro-bunches
- Measured momentum spread in SIS18 after injection (dc beam)
I [mA] (Uran equivalent)
Minimum momentum spread given by SC
- Since the SC effect depends on the initial micro-bunches length, the micro-bunches are stretched in the TK (further optimization might be possible)
- Space charge and the initial momentum spread from UNILAC are the main sources of the momentum spread in SIS18!

## Slide 6: Horizontal multi-turn injection into SIS18
- Beams are stacked until machine acceptance is reached
Measured MTI performance in SIS18 (low intensities)
Trev=5 μs
≈20 turns
Anode
Cathode
300 kV
SIS electrostatic injection septum
- Loss should be as low as possible (activation, damage, vacuum)
Notes: Altitude

## Slide 7: Multi-turn injection Model and quality parameters
- Loss
- Loss maxima
- To achieve high intensity the beams should be packed as compact as possible
- Loss of particles at the septum due to the betatron
oscillation, if the orbit is not reduced fast enough
End of injection
(optimal)
- Intensity
- MTI model implemented in the tracking codes PATRIC (GSI) and pyORBIT (Oak Ride Lab.)
- Both codes include a 2D space charge solver
ns: Effectively stacked turns (multiplication factor)
n: Injected turns
- Quality:
t
Notes: certain

## Slide 8: MTI: Emittance and tune dependency Simulation results
- MTI efficiency depends very strongly on the initial emittance and fractional tune!
- Animation of MTI
(Horizontal phase space)
- Arm formation given by fractional tune
- Orbit bump reduction - Horizontal tune
- Position of beam center
- Acceptance limitation due to septum
- No optimization for loss
Notes: Take place

## Slide 9: MTI simulation studies Comparison between experiment and simulations (low intensity)
- No space charge effects
- In the simulation the same parameters were used for the bump reduction and the measured emittance as in the experiment
- The loss maxima are located at the same fractional tunes
- Measurement results provided by Y. El-Hayek, GSI
- Measurements and simulations are in good agreement for the first time for the SIS18 injection
- In this measurements the loss for Qx=4.17 is larger as generally (optimization possible)
Notes: One fifth; A quarter, one third

## Slide 10: MTI simulation studies Space charge effects for FAIR design intensities
- Space charge affects the betratron motion of the individual particles
- With space charge the maxima of the efficiency are shifted
- Therefore also the injection efficiency
The increase of intensity and emittance compensate each other and the shift is nearly the space charge shift of the micro-bunches
- In the most cases:
- Space charge tune shift
Changes during injection
- Mirco-bunch
- For Qx= 4.18 a beam loss minimum for low and high intensity beams exists (FAIR currents)
Notes: Work the statement stronger out!

## Slide 11: Optimization of intensity and loss (quality)
- Goal (After we found the optimum tune):
Find best compromise between compact packing and loss by varying the speed of bump reduction
- Simulation parameters: Ah = 150 mm mrad, Qx= 4.17
- Current and brilliance for the linac with 2x1011 U28+ particles stored in SIS18
mm mrad
3
5
7
10
I
mA
B (norm.)
mA / (mm mrad)
10
15
16
20
3.3 (21)
3.0 (19)
2.3 (15)
2.0 (13)
t
μs
140
80
75
60
Reduction parameter (normalized to beam radius)
slow reduction
fast reduction
Notes: Loss machining

## Slide 12: Collimation
- Scraped-off beam edges of Gaussian distribution
Effect of collimation in the TK (before injection)
Loss
Intensity
- Note: Quality parameters includes the scraped-off particles
- Non collimation (blue line):
- Collimated (red line):
- Intensity is reduced by ~ 20% and emittance by ~ 30%
Loss in SIS18
Number of turns
0.0
0.5
1.0
1.5
2.0
5
4
3
2
1
0
0
10
20
30
40
50
60
70
Intensity
- Loss in the SIS18 could be reduced
- Similar intensity could be injected

## Slide 13: Summary and Outlook
- Dependence of the MTI efficiency on initial beam distribution should be studied more accurately
- Space charge is one important source of the ‘initial’ momentum spread in SIS18!
- Stretching of the micro-bunches in the TK could help (limited by the available bunchers)
- For high intensity beams the momentum spread could be larger than the rf bucket area
- MTI quality (intensity + loss) depends very strongly on the initial emittance and hor. tune!
- Space charge leads to a tune shift of the beam loss maxima
Longitudinal:
Transverse:
Outlook:
- For Qx= 4.18 a beam loss minimum for low and high intensity beams exists (FAIR currents)
- Current and brilliance required in order to achieve the FAIR parameters are be shown
- Possible influence of skew quads on the MTI efficiency
- The MTI model and micro-bunch parameters (long. + trans.) from UNILAC with space charge must be verified accurately with measurements