## Slide 1
1)– CENTRAL TRACKER INTEGRATED ITEMS:
> Central Tracker, “Assembly & Insertion Auxiliary Structure”.
> “CSF”- Central Tracker Support Frame (In collaboration with MVDTorino group);
> “Straw-Tubes Tracker”, Support Frame;
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
- ST_TRACKER, MAIN MECHANICAL ISSUES -
-THE AIM OF THIS TALK IS TO SUMMARIZE ALL THE WORK THAT HAS BEEN DONE FOR EACH
MECHANICAL ITEMS.
- IN ADDITION I ATTEMPT TO DESCRIBE THE STILL OPEN PROBLEMS, THE CRITICAL
SITUATIONS AND SPCIFY THE INVOLDED GROUPS.
2)- “Straw-Tubes Tracker Services”, Support Frame;
3)- “Straw-Tubes Modules / Electronic ….. / Gas Manifold System” Integration.

## Slide 2
CENTRAL TRACKER INTEGRATED ITEMS: “Assembly & Insertion Auxiliary Structure” ………
…THINGS DONE ………………
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
-The general design , the main dimensions and the operating steps
has been fixed;
A full scale prototype has been realized in INFN
Frascati workshop.
ASSEMBLY AUXILIARY STRUCTURE.”.
INSERTION AUXILIARY STRUCTURE.”.
- Involved groups Frascati, Torino.

## Slide 3
-A) The general design and the main dimensions are fixed;
-B) Preliminary mechanical solutions to support the “Cross Pipe” has been developed;
-C) The preliminary structural calculations has been made ;
-D) A full scale prototype has been realized in collaboration with Torino Group.
CENTRAL TRACKER INTEGRATED ITEMS: “CSF – Central Tracker Support Frame” ………
…THINGS DONE ………………
-TARGET : ACCEPTABLE MAX DISPLACEMENT (Due the Titanium Cross Pipe thickness): 0.05mm
> Hypothesized material: 8xM55J+ Rohacell+8xM55J
>Translational values – Magnitude Max 0.0197mm
> Von Mises: Max 3.75MPa
JUELICH – OCTOBER 2013 - D.Orecchini / B. Giraudo / P.Gianotti
A
B
C
D
- Involved groups: Frascati,Torino.

## Slide 4
- CROSS PIPE
- ST_TRACKER
- CENTRAL SUPPORT FRAME
DISTANCE BETWEEN THE OUTER
FACES OF THE RAILS
874
- RAIL UP
- RAIL DOWN
- A) The general design and the main dimensions are fixed;
- B) The preliminary structural calculations have been made ;
- C) Mechanical solutions to support and move the frame has been developed;
- D) A full scale prototype has been realized.
- A set of measurements has been made (details in the next slides)
CENTRAL TRACKER INTEGRATED ITEMS: “Straw Tubes Tracker Support Frame” ………
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
…THINGS DONE ………………
A
B
C
D
- Involved groups: Frascati.

## Slide 5
….THINGS TO DO ………
-The solutions to support the “Cross Pipe” have had a preliminary approval by the “Cross Pipe” people.
A common development of the final solution is still to be worked-out
-However, all the final design, is still evolving.
- Involved groups: Torino and Frascati.
- Involved groups: Torino, Frascati and Juelich (Cross-Pipe people).
JUELICH – OCTOBER 2013 - D.Orecchini / B. Giraudo / P.Gianotti
CENTRAL TRACKER INTEGRATED ITEMS: “CSF – Central Tracker Support Frame” ………

## Slide 6
- STT Support Frame: Protective Skins Proposal.
INNER SKIN
HALF TRACKER WITH ASSEMBLED PROTECTIVE SKINS.”.
HALF TRACKER WITH EXPLODED PROTECTIVE SKINS.”.
INNER SKIN
OUTER SKIN
OUTER SKIN
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
- OUTER SKINS: Three integrated pieces
- KEVLAR PROTECTIVE SKINS –
-KEVLAR MAIN CHARACTERISTICS:
-Excellent light weight
-Good Radiation Length =28cm ( CF 25cm – Aluminum 9 cm)
-Good resistance to hits.
-Good thermal insulation
-Low electrical conductivity.
- BAD ASPECTS:
-Preliminary economic evaluation:
Skins plus molds: 16000€
- PROTECTIVE SKINS –
-MATERIAL PROPOSED: Kevlar
-THICKNESS HYPOTIZED: 1mm
- INNER SKIN: One piece
- Involved group: Frascati.

## Slide 7
- STT SERVICES SUPPORT FRAME
- ST_TRACKER
STT (Straw Tubes Tracker ) “Services Support Frame”:
-The general design and the main dimensions are fixed and the
solution to support and move the frame is the same
of the ST_Tracker;
-The preliminary structural calculations has been made with
positive results;
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
- CLASCHES BETWEEN BW-EMC AND
SST_SERVICES FRAME HAVE BEEN RESOLVED.
Hypothesized material: Aluminum Alloy
>Translational values – Magnitude Max 0.4mm
> Von Mises: Max 29,5MPa (Max 95MPa)
…THINGS DONE ………………
- Involved group: Frascati.

## Slide 8
TO CHECK THE ASSEMBLING PROCEDURES FOR THE “CROSS PIPE”;
….. inside the “Central Tracker Components” …………..
- TO CHECK THE ASSEMBLING PROCEDURES FOR WHAT CONCERN THE “VERTEX” ASSEMBLY;
CENTRAL TRACKER INTEGRATED ITEMS: ………
….THINGS TO DO ………
- Involved groups: Torino, Frascati and Juelich (Cross-pipe people ).
JUELICH – OCTOBER 2013 - D.Orecchini / B. Giraudo / P.Gianotti
- TO DEFINE THE ASSEMBLING PROCEDURES FOR WHAT CONCERN THE “ VERTEX CABLING & GAS SYSTEM”,

## Slide 9
-TO CHECK THE PROBLEMS RELATED WITH THE “CABLING & GAS SYSTEM” ON THE SUPPORT STRUCTURE .
- TO CHECK THE ASSEMBLING PROCEDURES OF THE “CENTRAL SUPPORT FRAME” ON THE “ASSEMBLING STRUCTURE”.
TO CHECK THE INSERTING PROCEDURES OF THE COMPLETE “CENTRAL TRACKER.”.
CENTRAL TRACKER INTEGRATED ITEMS ……………
….THINGS TO DO ………
JUELICH – OCTOBER 2013 - D.Orecchini / B. Giraudo / P.Gianotti
- Involved groups:Torino Frascati and Juelich
(Cross-Pipe and Straws Tracker groups).
….. And for what concerns the “Central Tracker” general assembly …………..

## Slide 10
STT (Straw Tubes Tracker ) “Services Support Frame”:
-A detailed solution for the integration between the straws modules, the
electronics cards, the cables, the gas manifolds, etc. is still under development.
- Involved groups: Frascati , Juelich and Krakow people.
-The new proposed route of the “gas pipes” (outside the STT outer encumbrance)
has been accepted by the DIRC group.
- Involved groups: Frascati and GSI-DIRC .
-The geometry in the backward side will be surely modified
due the integration with the evolution of the“DIRC Read-Out”
geometry.
- Involved groups: Frascati and GSI-DIRC.
-A final solution for an integrated system of the patch-panels (STT-Vertex-BW-EMC)
placed outside the magnet is still to be developed.
- Involved groups: Frascati ,Torino and BW-EMC people.
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
….THINGS TO DO ………

## Slide 11
- STRAW TRACKER ELECTRONICS INTEGRATION.
SUPPORT END-PLATE
HV DISTRIBUTION
READ-OUT ELECTRONICS MODULES
CABLE SUPPORT STRUCTURE
STRAW MODULES
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
….THINGS TO DO ………
…THINGS DONE ………………
- The general design and the main components location;
-The preliminary mechanical solutions to support and manage
the different components.
- All the detailed solutions are still to develop waiting the definition of the
electronic components.
- Involved groups: Frascati, Juelich and Krakow.

## Slide 12
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
KEL 20 PAIRS CONNECTOR
(Staggered one respect to the other)
STAGGERED FLAT CABLES
- STRAW TRACKER ELECTRONICS INTEGRATION.
….THINGS TO DO ………
…THINGS DONE ………………
…… PRELIMINARY INTEGRATION IDEA OF READ-OUT MODULES …….
- THE GOAL IS TO DEFINE ALL THE COMPONENTS AND TO REALIZE A
SIGNIFICANT PROTOTYPE.
DUE THE VERY HIGH DENSITY OF THE COMPONENTS, IT’S FUNDAMENTAL
TO CHECK ALL THE ASPECTS :
  COMPONENTS ASSEMBLING
  FLAT MANAGEMENT AND ROUTING
  MANAGEMENT OF THE SERVICE SUPPORT FRAME
- Involved groups: Frascati, Juelich and Krakow.

## Slide 13
- STRAW TRACKER GAS SYSYTEM INTEGRATION.
GAS PIPES GUIDE
STRAW MODULES
SUPPORT END-PLATE
GAS MANIFOLD SYSTEM
- THE GOAL IS TO DEFINE THE CONCEPTS AND THE
COMPONENTS THAT ALLOW THE REALIZATION OF
A SIGNIFICANT PROTOTYPE.
… IN A DEDICATED TALK VINCENZO LUCHERINI WILL SHOW YOU MORE IN DETAILS
THE GAS SYSTEM IDEA DEVELOPED IN FRASCATI………………
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
…THINGS DONE ………………
- PRELIMINARY INTEGRATION IDEA OF THE SYSYTEM.
….THINGS TO DO ………
- Involved groups: Frascati, Juelich and Krakow.

## Slide 14
EMC_BW
Limit
TUBE LENGTH: 1400mm
- STRAW-TUBES TRACKER : General layout.
380
1020
30
30
20
20
1500
1460
10
20
GEM Forward
Limit
560
1150
430
1070
110
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
40
Free Space
Free Space
40
IP

## Slide 15
- STRAW TUBES TRACKER SUPPORT FRAME: Geometrical survey test………
A series of geometrical tests has been performed with the help of the “LNF Alignments Service” with a “laser tracker”.
The aim of these tests, was to verify fluctuations of values ​​of concentricity between the “positioning and support holes” of the straws modules, realized on the two end-plate of the support frame.
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
A second series of geometrical tests has been performed to characterize the behavior of the “Support Frame” under the simulated load transmitted by the “Straw Modules”, the electronics and the gas system components.

## Slide 16
Y
Z
x
FORWARD PLATE
BACKWARD PLATE
1)- It has been defined a medium plane detected on the “Backward Plate”.
2)- Respect to this plane, It has been defined an orthogonal axis (z).
- STT Support Frame: Laser Tracker Survey_1
AUXILIARY ASSEMBLY FRAME
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
- In a first configuration, the “Support Frame” has been mounted in his
“working position”, attached on the “Central Support Frame” prototype.
- In this way we can check all the stresses that the frame should have
suffered due to its handling and the adaptation to the
geometry of the support frame

## Slide 17
- It has been given a reference numbering to the “Straw modules Support Holes.
- B1 – B2 – B……….. for the “Backward Plate”.
- F1 – F2 – F………….for the “Forward Plate”.
BACKWARD PLATE
Y
x
- STT Support Frame: Tracker Laser Survey_1
AUXILIARY ASSEMBLY FRAME
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti

## Slide 18
“X” DEVIATIONS
MIN: -0,23mm
MAX: -0,49mm
Average: -0,38
“Y” DEVIATIONS
MIN: -0,54mm
MAX: -0,76mm
Average: -0,65
“Z” DEVIATIONS
MIN: 0,04mm
MAX: -0,20mm
Average: -0,07
- STT Support Frame: Tracker Laser Survey_1 Results

## Slide 19
Y
Z
x
FORWARD PLATE
BACKWARD PLATE
- STT Support Frame: Laser Tracker Survey_2
GRANITE TABLE
1)- It has been defined a medium plane detected on the “Backward Plate”.
2)- Respect to this plane, It has been defined an orthogonal axis (z).
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
-In a second configuration, the “Support Frame” has been placed on a granite table, avoiding to give it any possible distortions.
This configuration is necessary to obtain a comparison with the
results of the survey of the previous configuration.
A first goal is to understand the intrinsic degree of precision of the
frame.
A second aspect is try to quantify the deformations caused by the
“Central Support Frame”.

## Slide 20
- It has been given a reference numbering to the “Straw modules Support Holes.
- B1 – B2 – B……….. for the “Backward Plate”.
- F1 – F2 – F………….for the “Forward Plate”.
BACKWARD PLATE
Y
x
- STT Support Frame: Tracker Laser Survey_2
1
78
GRANITE TABLE
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti

## Slide 21
- STT Support Frame: Tracker Laser Survey_2 Results
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
“X” DEVIATIONS
MIN: -0,24mm
MAX: -0,37mm
Average: -0,29
“Y” DEVIATIONS
MIN: -0,31mm
MAX: -0,58mm
Average: -0,45
“Z” DEVIATIONS
MIN: 0,07mm
MAX: -0,12mm
Average: -0,05

## Slide 22
LOADS
MICROMETERS
A
B
-It has been made a survey of the behavior of the two plates (Backward e Forward), under load.
1)- Have been placed two micrometers “A” e “B” under the plates.
2)- Have been loaded the two plates with six different conditions of load.
BACKWARD PLATE: EXPECTED LOAD 7.5 Kg
FORWARD PLATE: EXPECTED LOAD 5.5 Kg
- STT Support Frame: Behavior of the Support Frame Under Load.
JUELICH – OCTOBER 2013 - D.Orecchini / P.Gianotti
In this test the aim was to characterize the behavior of the support frame under the simulated loads of the supported components .
It has been simulated a series of increasing loads, measuring the displacements by means of two micrometers positioned under the profile of the frames.
STT Support Frame - Preliminary Loads Analysis

## Slide 23
- BACK-UP SLIDES -

## Slide 24
-TO TEST AND DEVELOP THE EQUIPMENT AND PROCEDURES.
….. And about inserting in the apparatus …………..
CENTRAL TRACKER INTEGRATED ITEMS: ………
….THINGS TO DO ………
- Involved groups:“Torino” ,”Frascati” (and “Juelich” people???).
JUELICH – OCTOBER 2013 - D.Orecchini / B. Giraudo / P.Gianotti

## Slide 25
STT (Straw Tubes Tracker ) “Support Frame”, things to do:
-A final solution for the inner and outer skins is under development.
- Involved groups:“Frascati” people.
-A series of survey of the “coaxiality” between the geometry of the two “End-plates” has been made.
An improvement of the “connection system” between the end-plates is under development.
- Involved groups:“Frascati” people.
-The final solution for the interface between the “Support and Shifting Rails”,
and “Up & Down” support beam, is still be to be developed;
- Involved groups:“Frascati” and “GSI” people.
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti

## Slide 26
- Forward Z-coordinate necessary for the Central Tracker rails: 1150
- CT SUPPORT BEAM LENGHT-
550mm
1142mm
1692mm
- TOTAL LENGHT OF THE «STRAW TRACKER»

## Slide 27
30mm
13,5mm
6,6mm
FLAT CABLE CONNECTOR
ELECTRONIC CARD CONNECTOR
25,5mm
10mm
7mm
E_Card
- Approx. weight of connector: 3g / Each
- FLAT CABLE CONNECTORS -

## Slide 28
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti

## Slide 29
296 Flates
(2960 Ch.)
13mm
0,65mm
Flat cable cross section (8,5)10mm^2/each
(In twisted region of the cable)
- Total: 10x296 = 2980mm^2
Weight: 0.017 kg/m
-The encumbrance of the connectors
has not been considered!
- PATHWAYS OF FLAT CABLES BUNCHES -
9
13
13
17
19
24
14
13
17
17
22
23
9
13
13
17
19
24
54
41
95
106
95
53
54
41
53
Theoretical needed cross section for the
lateral pathway: 2980 mm^2
Notes: in reality we would have had considered 3478 = 2318 tubes + 1160 control lines

## Slide 30
296 Flates
(2960 Ch.)
13mm
0,65mm
Flat cable cross section (8,5)10mm^2/each
(In twisted region of the cable)
- Total: 10x296 = 2980mm^2
Weight: 0.017 kg/m
-The encumbrance of the connectors
has not been considered!
- LOADS OF FLAT CABLES BUNCHES -
9x0,33=2,97m
13x0,24=3,12m
13x0,14=1,82m
17x0,16=2,72m
19x0,045=0,855m
24x0,06=1,44m
14x0,23=3,22m
13x0,23=2,99m
17x0,14=2,38m
17x0,14=2,38m
22x0,045=0,99m
23x0,045=1,035m
9x0,23=2,07m
13x0,24=3,12m
13x0,14=1,82m
17x0,16=2,72m
19x0,045=0,8,55m
24x0,06=1,44m
54
41
95 Flats
12mx0,017=0,204Kg
106 Flats
13mx0,017=0,22Kg
95 Flats
12mx0,017=0,204Kg
53
54
41
53
Theoretical needed cross section for the
lateral pathway: 2980 mm^2
296 FLATS - 0,70Kg
Notes: in reality we would have had considered 3478 = 2318 tubes + 1160 control lines

## Slide 31
Weight: 0,0162Kg/m
L = 50mm
-Thinner cables exist, but we have only 40...
Out diam.: 3.2 mm
- HV CABLES -

## Slide 32
Weight: 0,0162Kg/m
Outer diam: 6 mm
- GAS PIPES -

## Slide 33
13 HV Cables
13 HV Cables
13 HV Cables
-The encumbrance of the
connectors has not been
considered!
20 HV Cables
20 HV Cables
12 Gas Pipes
12 Gas Pipes
4 Gas Pipes
(From the Forward Side)
8 Gas Pipes
(From the Forward Side)
4Gas Pipes
(From the Forward Side)
- Cross Section 8,1mm^2/each
- Total: 8,1x20 = 162mm^2 (Each Pathway)
- Weight: 0,0162 Kg/m
- Cross Section 28,26mm^2/each
- Total: 28,26x12 = 340mm^2 (Each Pathway)
- Weight: 0.016 kg/m
13
13
7
6
8 Gas Pipes
(From the Forward Side)
- PATHWAYS OF HV CABLES AND GAS PIPES -
GAS PIPE DATA
HV CABLE DATA
Theoretical needed cross section for each
top & bottom pathway: 162+340= 502mm^2

## Slide 34
13 HV Cables
13 HV Cables
13 HV Cables
-The encumbrance of the
connectors has not been
considered!
20 HV Cables
20 HV Cables
12 Gas Pipes
12 Gas Pipes
4 Gas Pipes
(From the Forward Side)
8 Gas Pipes
(From the Forward Side)
4Gas Pipes
(From the Forward Side)
- Cross Section 8,1mm^2/each
- Total: 8,1x20 = 162mm^2 (Each Pathway)
- Weight: 0,0162 Kg/m
- Cross Section 28,26mm^2/each
- Total: 28,26x12 = 340mm^2 (Each Pathway)
- Weight: 0.016 kg/m
13
13
7
6
8 Gas Pipes
(From the Forward Side)
- LOADS OF HV CABLES AND GAS PIPES -
GAS PIPE DATA
HV CABLE DATA
Theoretical needed cross section for each
top & bottom pathway: 162+340= 502mm^2

## Slide 38
30mm
13,5mm
6,6mm
FLAT CABLE CONNECTOR
ELECTRONIC CARD CONNECTOR
25,5mm
10mm
7mm
E_Card
- Approx. weight of connector: 3g / Each
- FLAT CABLE CONNECTORS -

## Slide 40
Cabling options and improvements could be tested on the available prototype once we realize also a
prototype of the cabling support system.
The prototype of the “Straw Tracker Support Structure”, will be shipped to Juelich in the next weeks.
CENTRAL TRACKER INTEGRATED ITEMS: “Straw Tubes Tracker Support Frame” ………

## Slide 41
AN “EXTRA PART” HAS BEEN REALIZED TO ALLOW THE TEST OF THE “INSERTION OPERATIONS”.
INFN-(TURIN / LNF)
GSI – November / December 2010 (B. Dulach - B.Giraudo - D. Orecchini)
-“AUXILIARY ASSEMBLING STRUCTURE” PROTOTYPE-
THE PROTOTYPE OF THE “AUXILIARY ASSEMBLING STRUCTURE”, HAS BEEN COMPLETED IN INFN FRASCATI WORKSHOP.

## Slide 42
1°SKATE
2°SKATE
ALUMINIUM SKATE
- RECOMMENDED FLATNESS AND
PARALLELISM TOLERANCES.
- INDUCED SAG (Progressive insertion of metallic plates).
- RAILS
- SUPPORT BEAM
STT (Straw Tubes Tracker ) “Support Frame”, things done_2:
A TEST WITH PROGRESSIVELY BIGGER SAG VALUES OF THE RAIL
SYSTEM, HAS BEEN DONE.
-“Assembly & Insertion Auxiliary Structure” prototype.
-THE RESULTS ARE:
THE SYSTEM WORKS ANYWAY FOR VALUE OF THE SAG UP TO 0.8mm
BUT THE MAX VALUE OF SAG ACCEPTABLE FOR A SMOOTH MOVEMENT, IS 0.5mm
GSI – DECEMBER 2012 - D.Orecchini / P.Gianotti
-There are indications (Jost preliminary calculations) that the present
max sag of the up support beam with the CT load is ∼ 1mm.