## Slide 1: Status and Perspectives of the ELI–NP Research Facility
“European Nuclear Physics Conference – EuNPC”
August 31 – September 4, 2015, Groningen, The Netherlands
GOVERNMENT OF ROMANIA
Structural Instruments
2007-2013
EUROPEAN UNION
Călin A. Ur
for the ELI–NP Team

## Slide 2: Extreme Light Infrastructure in a Nutshell
Extreme Light Infrastructure
Pan–European Research Center
Target: implement the world’s largest laser research infrastructure
Infrastructure: distributed over three complementary pillars (CZ, HU, RO) – user facilities
Strategy: first ESFRI project to be fully implemented in newer EU member states
Funding: novel model combining ERDF funds for the implementation and contributions to an ERIC for the operation
ELI–DC

## Slide 3: Extreme Light Infrastructure – Beamlines
Short–pulse secondary sources of radiation and particles
multidisciplinary applications in molecular, biomedical and material sciences
physics of dense plasmas, warm dense matter, laboratory astrophysics
high-power, high-repetition-rate lasers for high-field physics experiments with focused intensities of about 10²³ W/cm2, investigating exotic plasma physics, and non-linear QED effects
Dolni Brezhany, near Prague, Czech Republic

## Slide 4: Extreme Light Infrastructure – ALPS
Ultra short laser pulses with high repetition rates
light source with frequencies between THz and X–ray
study of extremely fast dynamics by taking snap–shots in the attosecond scale of the electron dynamics in atoms, molecules, plasmas and solids
research with ultrahigh intensity lasers.
Szeged, Hungary

## Slide 5: Extreme Light Infrastructure – Nuclear Physics
Nuclear Physics research with extreme electromagnetic fields
Host for two major systems
Based on the National Physics 2 x 10 PW High–Power Lasers System
Platform in Magurele (Bucharest)
High Brilliance Gamma Beam System
Thales Optronique
EuroGammaS

## Slide 6: Extreme Light Infrastructure – Nuclear Physics
Nuclear Physics experiments
Nuclear Photonics
      Nuclear Resonance Fluorescence
      Photo–fission & Exotic Nuclei
      Photo–disintegration and Nuclear Astrophysics
complementary to other ESFRI Large Scale Physics Facilities
(FAIR, SPIRAL2)
    Nuclear Physics diagnostics
      Laser–Target interaction characteristics
    Laser Ion driven nuclear physics
              Laser–Target interaction characteristics
Applications based on high intensity laser and very brilliant γ beams complementary to the other ELI pillars

## Slide 7
ELI–NP – Experimental Building Layout
HPLS
Laboratories
Experiments
GBS
Platform supported on dampers
Anti–vibration platform
±1 mm @ < 10 Hz

## Slide 8
ELI–NP Implementation Timeline
2010 2011 2012 2013 2014 2015 2016 2017 2018
Laser System – installation
Gamma Beam – installation
ELI–NP White Book
Feasibility Study
Cost estimate 293M€
Preparation of the Application
E.C. Eval. & Funding Approval
Procurement Gamma Beam
Procurement Laser System
Experimental Areas TDR
Recruitment
Building

## Slide 9
ELI–NP Building the Experiments
White Book ⟹ Day–1 Experiments
Towards TDR of experiments with intense laser beams at ELI-NP
June 27-28, 2013 – Bucharest-Magurele (Romania)
Towards TDR of experiments with brilliant gamma-ray beams at ELI-NP
July 25-26, 2013 – Bucharest-Magurele (Romania)
building the main working groups
conveners and local liaisons
ELI-NP TDRs at Midway – High Power Laser March 16-17, 2014 – Bucharest-Magurele (Romania)
ELI-NP TDRs at Midway – SystemGamma Beam System
March 16-17, 2014 – Bucharest-Magurele (Romania)
added new working groups
applied physics
ELI-NP Science Program and Instruments: Technical Design Reports
February 18-20, 2015 – Bucharest-Magurele (Romania)
final TDRs
definition of the experimental setups
June 2015 – Scientific evaluation of the TDRs by ISAB

## Slide 10
The High–Power Lasers System 2 x 10 PW
Based on OPCPA
Provided by THALES Optronique & Thales Romania
July 12th, 2013
Lasers
Experiments
Compressors & Diagnostics

## Slide 11
ELI–NP HPLS schematic layout
2 x 0.1 PW 10Hz
2 HPLS up to 10 PW – 6 outputs
2 x 1 PW 1Hz
2 x 10 PW 0.1Hz

## Slide 12
ELI–NP HPLS Parameters
~ 250 J
~ 25 fs
Intensity ~1024 W/cm2

## Slide 13
HPLS Experimental Areas
10 PW
10 PW
0.1 PW
1 PW

## Slide 14
Laser Driven Nuclear Physics
Convener: M. Roth (TUD) ELI-NP Liaison: F. Negoita (IFIN-HH)
1. Nuclear fusion reactions from laser-accelerated fissile ion beams P. Thirolf (LMU)
Goal: Production of nuclei around rich N~126 waiting point et al.
2. Nuclear (de-)excitations induced by lasers F. Hannachi (CENBG/IN2P3) et al.
Goal: Observation of NEET/NEEC processes in plasma. Changes in nuclear T1/2
3. Nuclear reactions in laser plasma S. Tudisco (LNS/INFN) et al.
Goal: Understanding screening effect in plasma conditions
4. Neutron production and other applications
4.1 Hot plasma confinement for
high flux neutron generation
S. Moustaizis (TU.Crete) et al.
4.2 Neutron production in light ion reactions
S. Kar (QUB), J.Fuchs (LULI) et al.
4.3 Muon-source and muon catalysed fusion
S.R.Mirfayzi, S.Kar (QUB)
Topic Stellar photoreaction
e + g + A in E7
Production and
photoexcitation of isomers
GBS
MeV g
LPA
~MeV e-
H.Utsunomiya (Konan U.) et al.
I. Combined laser/gamma

## Slide 15
Laser Driven Nuclear Physics
Nuclear (de–)excitations in plasma
NEET observed in cold targets.
Never observed
in plasma.
NEEC was never observed
Significant changes in lifetimes are predicted in plasma conditions:
F. Hannachi (CENBG/IN2P3) et al.

## Slide 16
Laser Driven Nuclear Physics
Peta-Watts
1018 Atoms/cm3
D.C. Carrol et al., New J. of Phys. 12 (2010) 045020
6×1020 W/cm2
The method requires
measuring high energy neutrons
Study of screening factor – The method and cases
S. Tudisco (LNS/INFN) et al.

## Slide 17
Laser Particle Acceleration – RPA
Target Normal Sheath
Acceleration (TNSA)
Radiation Presure
Acceleration (RPA)
P.McKenna, CETAL Workshop, Bucharest, Nov. 19, 2013
Direct action of the ponderomotive force of the laser on the surface electrons
Ultrathin targets (< 100–200 nm)
Highly efficient energy conversion (> 60%)
Ions and electrons accelerated as a neutral bunch avoid Coulomb explosion
Solid state beam density :
1022 – 1023 e/cm3
Short pulse high–power lasers ➞ strong charge separation by laser–matter interaction
➞ intense electric fields ➞ ion acceleration
Conversion of laser radiation into kinetic energy of relativistic electrons in mm thick targets
Electrons move and recirculate through the solid target and appear at the surfaces where give rise to intense longitudinal electric fields

## Slide 18
Materials in Extreme Environments
* Testing of new materials for accelerator components
- materials at fast energy deposition & mixed radiation fields
- laser induced shock waves
- laser modification of materials
* Evaluation of high energy ionizing radiation effects in materials
* Biological science research
  - radiation effects on bio-molecules & cells
* Testing and developments of detectors
* Irradiated optical components testing, Materials for fusion energy systems
Irradiation of components for space radiation studies
Convener: Marilena Tomut (GSI) ELI-NP Liaison T. Asavei

## Slide 19
AIM: System with outstanding key features
high peak brilliance (>1021 ph/s・mm2・mrad2・0.1%bwd), high spectral density (> 0.5・104 ph/s・eV), tunable energy (0.2 – 19.5 MeV), quasi–monochromatic (relative bandwidth < 0.5%), high degree of linear polarization (> 95%)
GBS
ELI–NP Gamma Beam System
GBS

## Slide 20
ELI–NP Gamma Beam System Concept
dN/dE
THE SOLUTION: Inverse Compton Scattering of laser pulses on relativistic electron pulses
  high intensity / small emittance e– beam from a warm LINAC
  very brillant high rep./rate int. laser
  small collision volume
Ee–
qL = 8o
EL = 2.3 eV
Eg < 19.5 MeV
laser
g–ray beam
e–
1995 2000 2005 2010 2015 2020
year
LNBL
PLEIADES
HIGS
T-REX
MEGA-ray
ELI–NP
Brilliance
ph/(mm2・mrad2・s・0.1%bw)
1013
1015
1017
1019
1021
< 0.5%
Good bandwidth
➞ Collimated g beam

## Slide 21
March 19, 2014
Academic Institutions
INFN (Italy), Sapienza University (Italy), CNRS (France)
Industrial Partners
ACP Systems (France), ALSYOM(France),
COMEB (Italy), ScandiNova Systems (Sweden)
Provider – EuroGammaS Association
19/03/2014
Academic Institutions
STFC (UK), ALBA Cell (Spain)
Industrial Partners
Amplitude Systems (France), Amplitude Technologies (France), Cosylab (Slovenia),
Danfysik (Denmark), Instrumentation Technologies (Slovenia), M&W Group (Italy),
Research Instruments (Germany), Toshiba (Japan)
… and sub – contractors
ELI–NP Gamma Beam System

## Slide 22
Gamma Beam System Layout
e– RF LINAC
Low Energy
300 MeV
Interaction Laser
High Energy
Interaction Laser
Low Energy
Photo–gun
Laser
e– RF LINAC
High Energy
720 MeV
Photo–gun
e– source
Provider – EuroGammaS Association

## Slide 23
Gamma Beam System Layout
e– RF LINAC
Low Energy
300 MeV
Interaction Laser
High Energy
Interaction Laser
Low Energy
Photo–gun
Laser
e– RF LINAC
High Energy
720 MeV
Photo–gun
e– source
Low Energy
Gamma Beam
< 3.5 MeV

## Slide 24
Gamma Beam System Layout
e– RF LINAC
Low Energy
300 MeV
Interaction Laser
High Energy
Interaction Laser
Low Energy
Photo–gun
Laser
e– RF LINAC
High Energy
720 MeV
Photo–gun
e– source
High Energy
Gamma Beam
< 19.5 MeV

## Slide 25
Energy (MeV) | 0.2 – 19.5
Spectral Density (ph/s∙eV) | > 0.5∙104
Bandwidth rms (%) | ≤ 0.5
# photons per pulse within FWHM bdw. | ≤ 2.6∙105
# photons/s within FWHM bdw. | ≤ 8.3∙108
Source rms size (mm) | 10 – 30
Source rms divergence (mrad) | 25 – 200
Peak brilliance (Nph/sec∙mm2∙mrad2∙0.1%) | 1020 – 1023
Radiation pulse length rms (ps) | 0.7 – 1.5
Linear polarization (%) | > 95
Macro repetition rate (Hz) | 100
# pulses per macropulse | 32
Pulse–to–pulse separation (nsec) | 16
Two stage system:
Low–energy stage: Eg < 3.5 MeV
  March 2017
High–energy stage: Eg < 19.5 MeV
September 2018
ELI–NP Gamma Beam Features
Ee–
qL = 8o
EL = 2.3 eV
Eg < 19.5 MeV
laser
g–ray beam
e–

## Slide 26
Energy (MeV) | 0.2 – 19.5
Spectral Density (ph/s∙eV) | > 0.5∙104
Bandwidth rms (%) | ≤ 0.5
# photons per pulse within FWHM bdw. | ≤ 2.6∙105
# photons/s within FWHM bdw. | ≤ 8.3∙108
Source rms size (mm) | 10 – 30
Source rms divergence (mrad) | 25 – 200
Peak brilliance (Nph/sec∙mm2∙mrad2∙0.1%) | 1020 – 1023
Radiation pulse length rms (ps) | 0.7 – 1.5
Linear polarization (%) | > 95
Macro repetition rate (Hz) | 100
# pulses per macropulse | 32
Pulse–to–pulse separation (nsec) | 16
Two stage system:
Low–energy stage: Eg < 3.5 MeV
  March 2017
High–energy stage: Eg < 19.5 MeV
September 2018
ELI–NP Gamma Beam Features

## Slide 27
Energy (MeV) | 0.2 – 19.5
Spectral Density (ph/s∙eV) | > 0.5∙104
Bandwidth rms (%) | ≤ 0.5
# photons per pulse within FWHM bdw. | ≤ 2.6∙105
# photons/s within FWHM bdw. | ≤ 8.3∙108
Source rms size (mm) | 10 – 30
Source rms divergence (mrad) | 25 – 200
Peak brilliance (Nph/sec∙mm2∙mrad2∙0.1%) | 1020 – 1023
Radiation pulse length rms (ps) | 0.7 – 1.5
Linear polarization (%) | > 95
Macro repetition rate (Hz) | 100
# pulses per macropulse | 32
Pulse–to–pulse separation (nsec) | 16
Two stage system:
Low–energy stage: Eg < 3.5 MeV
  March 2017
High–energy stage: Eg < 19.5 MeV
September 2018
ELI–NP Gamma Beam Features
One pulse
~ 1 ps
~ 105 photons

## Slide 28
Gamma Beam Experiments
separation energy Sn or Sp
AX
A`Y


n or p


‘
Photodisintegration, Photofission, Photoactivation
Nuclear Resonance Fluorescence - NRF

## Slide 29
Gamma Beam Experiments
Fundamental Research
  Nuclear Resonance Fluorescence (A.Zilges U.Cologne, C.A.Ur)
  Nuclear Astrophysics (g,p) (g,a) (M.Gai U.Conn, O.Tesileanu)
  Photonuclear Reactions (g,n) (H.Utsunomiya U.Konan, F.Camera U.Milano and
  INFN, D.Filipescu)
  Photofission&Studies of Exotic Nuclei (A.Krasznahorkay ATOMKI Debrecen,
  F.Ibrahim IPN Orsay, D.L.Balabanski)
Applications
  Gamma Imaging (H.Ohgaki U.Kyoto, V.Iancu)
  Material Science with Positrons (C.Hugenschmidt TU Munich, N.Djourelov)
  Medical Radioisotopes (D.Niculae IFIN-HH Bucharest, M.Bobeica)
R&D Gamma Beam Diagnostics Detectors
  Gamma Beam Delivery and Diagnostics (H.Weller U.Duke, C.A.Ur)
  Broad International Collaboration
  Germany, USA, Japan, Italy, Hungary, France,
  Poland, Vietnam, Switzerland, UK, Russia, ……….

## Slide 30
Nuclear Resonance Fluorescence
Electromagnetic dipole response of nuclei
Photoresponse of weakly abundant p–nuclei and actinides
Rotational 2+ states of the nuclear scissor modes
Pygmy Dipole Resonances
G0 and G/G0 measurements
Access to nuclear observables
Excitation Energy Er
Spin and parity J, p
Decay Energies Eg
Partial Widths Γi/Γ0
Multipole Mixing d
Decay Strengths B(pl)
Level Width Γ (eV)
Separation threshold
g

## Slide 31
Discovery Frontiers for NRF at ELI–NP
Availability frontier
access to rare isotopes
photoresponse of weakly abundant p–nuclei
and actinides
Sensitivity frontier
weak channels
rotational 2+ states of the nuclear
scissor modes
Precision frontier
high statistics
G0 and G/G0 measurements

## Slide 32
Nuclear Resonance Fluorescence
8 x TIGRESS – type Clover detector (segmented) with back–catcher (eph ~ 6%)
4 x 3”x3” LaBr3(Ce) detectors
ELIADE = ELI–NP Array of DEtectors
Instrumentation:
CAD : C.Petcu and E.Udup

## Slide 33
Nuclear Astrophysics
Molecular states and symmetries in light nuclei
Photodisintegration – astrophysics interest
  the 16O(γ,α)12C reaction
  the 24Mg(γ,α)20Ne reaction
  the 22Ne(γ,α)18O reaction
  the 19F(γ,α)18O reaction
  the 21Ne(γ,α)17O reaction
Instrumentation:
Large–area Si DSSD array
eTPC (35x20x20 cm3)

## Slide 34
Gamma Above n Threshold
Studies of GDR and PDR decay
Studies of spin–flip M1 resonances
Absolute (g,n) cross section measurements, e.g. p–process related measurements:
  the 138La(g,n) 137La reaction
  the 181Ta(g,n)180Ta reaction
  the 180Tam(g,n)179Ta reaction
Instrumentation:
3He neutron counter array
LaBr3(Ce) / CeBr3 array – high–energy gamma rays
Li–glass and NE213 liquid scintillator array – neutrons

## Slide 35
Photofission
Studies in the 2nd and 3rd minimum of the fission barrier: measurement of transmission resonances, angular and mass distributions of the fragments
Rare fission modes: ternary fission
Structure of neutron–rich nuclei: the rare–earth neutron–rich deformed region
Instrumentation:
System of multi–target Frisch–gridded twin ionization chambers and DSSD detectors
Array of 12 x THGEM detectors

## Slide 36
Photofission and Exotic Nuclei
ALTO, ARIEL, etc.
Photofission cross section for 238U
Caldwell et al., Phys. Rev. C 21 (1980) 1215

## Slide 37
Photofission and Exotic Nuclei
ALTO, ARIEL, etc.
ELI-NP
Inverse Compton Scattering
Photofission cross section for 238U
Caldwell et al., Phys. Rev. C 21 (1980) 1215
~1011 photons/s

## Slide 38
IGISOL Setup
β-decay studies at the IGISOL beam line :
Test of the SM around the doubly-magic 132Sn;
Studies of the onset and fading away of deformation in the A = 100 Sr–Zr region;
Studies of collective excitations in the A = 150 deformed region;
Studies of octupole excitations in Sm-Nd nuclei.
Emphasis on refractory elements that can be separated with the IGISOL technique;

## Slide 39
Gamma Beam Industrial Applications
Active interrogation – Nuclear resonance fluorescence
Nuclear waste management
Cargo screening/Material identification
Origin of objects
Metal count in food and in plants
Density screening in ill tissues
High resolution imaging – Radiography and Tomography
Test quality of industrial objects (engines faults, steel quality)
Test strength of sinterization/welding
Phase distribution
Diffusion
NRF + CT: Elemental/isotopic maps
Non–destructive Inspection
2θ

## Slide 40
Summary
a new nuclear physics research facility is being constructed at Bucharest
  systems with features beyond state–of–the–art : HPLS and GBS
➞ many new research opportunities and challenges
  nuclear physics
    Laser Driven Nuclear Physics, combined laser–gamma
    NRF, photofission, photodissociation
  applications
    materials in extreme environments
    non–destructive inspection of materials
    positrons for material sciences

## Slide 42
Main Components of the Gamma Beam System
Warm electron RF Linac (innovative techniques)
multi–bunch photogun (32 e– microbunches of 250 pC @100 Hz RF)
  2 x S–band (22 MV/m) and 12 x C–band (33 MV/m) acc. structures
  low emittance 0.2 – 0.6 mm⋅mrad
  two acceleration stages (300 MeV and 720 MeV)
High average power, high quality J–class 100 Hz ps Collision Laser
  state–of–the–art cryo–cooled Yb:YAG (200 mJ, 2.3 eV, 3.5 ps)
  two lasers (one for low–Eg and both for high–Eg)
Laser circulation with mm and mrad and sub–ps alignment/synchronization
  complex opto/mechanical system
  two interaction points: Eg < 3.5 MeV & Eg < 19.5 MeV
Gamma beam collimation system
  complex array of dual slits
  relative bandwidths < 5 x 10–3
Gamma beam diagnostic system
  beam optimization and characterization: energy, intensity, profile

## Slide 43
Photogun Laser
Time structure of the electron beam
producing 32 replica (before the last amplifier)
Photocathode Laser
based on Ti:Sa amplifier
cryo–cooled
@ 100 Hz
Photocathode = Copper
500 pC = max. charge
→ 250 mJ / pulse
Output: UV (266 nm)
> 3 mJ , 32 pulses
TDR – arXiv:1407.3669 [physics.acc-ph]
MULTIBUNCHING

## Slide 44
Main Components of the Gamma Beam System
Main requirements are:
Low transmission of gamma photons (high density and atomic number)
Continuously adjustable aperture (to adjust the energy bandwidth in the entire energy range)
Avoid contamination of the primary beam with production of secondary radiation
Collimation aperture varies from 20 mm to less than 1 mm, depending on the beam energy
Tungsten slits – 20 mm thick
14 independent slits with 25.7o relative angle

## Slide 45
Main Components of the Gamma Beam System
Electrons rep. rate –macropulses 100 Hz
32 micropulses @ 16 ns
K.Dupraz et al., Phys.Rev. STAB 17 (2014) 033501
‘Dragon–shaped’ Laser Recirculation
Laser rep. rate – 100 Hz → laser recirculation
e– beam
≈ 7o
≈ 0o
Laser beam
insertion
Laser beam
spots map a
circle on the
parabolic mirrors

## Slide 46
Nuclear Resonance Fluorescence
ELI–NP
/ 1000
HIgS @ Duke U.
Courtesy of N.Pietralla
138Ba (pol g,g‘)
GEANT4 by G.Suliman
Background radiation in the detectors
@ ELI –NP
Compton scattering of the beam
511 keV from positrons annihilation
Segmented Clover detectors + digital DAQ
Reduce the 511 keV background
Distinguish events from different pulses of gamma beam
⬇︎

## Slide 47
The ELIADE Array – Background Reduction
Background radiation in the detectors
Compton scattering of the beam
511 keV from positrons annihilation
Segmented Clover detectors + digital DAQ
Reduce the 511 keV background
Distinguish events from different pulses of gamma beam
Eliminate pile-up events
C.Petcu and E.Udup

## Slide 48
Cryogenic Stopping Cell
γ beam
technical design
at GSI, Darmstadt
50% efficiency,
5 ms extraction time
at a rate of ~ 107 ions/s
He gas @ 70 K
pressure 300 mb and 10 mb
> 100 V/sm DC field
RF carpet

## Slide 49
Photofission

## Slide 50
Gamma Beam Industrial Applications
Object
ELI-NP
γ beam
Two experimental methods will be carried out:
  Scattering NRF – Standard Method in Nuclear Physics Study
  Self-absorption/Transmission NRF (proposed by Bertozzi in 2005)
    Main interest in SNM control management
Witness foil (sample)
Object
ELI-NP
γ beam
High intensity gamma beam and small bandwidth
Tunable energy
High efficiency detector array – ELIADE
Active interrogation – Nuclear resonance fluorescence

## Slide 51
Gamma Beam Industrial Applications
Two tomography tables with biaxial movement and rotation
Various collimators with collimation holes between 0.2 mm and 5 mm.
High volume detector for pencil-beam
2D detector for cone-beam: CCD based gamma-ray camera or 2D flat panel
Implementation: 2015 -2017
Operation: 2018
Industrial Radiography and Tomography

## Slide 52
Positrons for Material Sciences
The ELI-NP e+ factory
Production method
(, e+e–) reaction;
circular polarized –beam
I= 2.4×1010 s-1
E< 3.5 MeV
W converter
Estimated e+ beam parameters
moderated e+ intensity 1.9×106 s-1
degree of e+ spin polarization 31%
Spectrometers
PALS – Positron Annihilation Lifetime
Spectroscopy
CDBS – Coincidence Doppler Broadening
Spectroscopy
TOF–PAES – Positron annihilation initiated
Auger Electron Spectroscopy
GiPALS – Gamma induced PALS