## Slide 1
The European Spallation Source:
Plans for Commissioning and Initial Operations
WAO 2014
Marc Munoz, on behalf of the whole ESS team
www.europeanspallationsource.se
October, 2014

## Slide 2: European Spallation Source
Main headlines
The world’s leading source for slow neutrons
A user facility providing outstanding scientific performance:
High intensity: 30 to 100 times more brightness than ILL,
High reliability
High safety
Environmentally friendly
Good economy
Technical scope
5 MW long pulse spallation source 2.86 ms, 14 Hz, protons
Target: Rotating wheel, He gas cooling
22 instruments, bispectral moderators
1.843 B€ to build, 140 M€/y
450 - 500 employees
Receiving 2000-3000 users per year

## Slide 3: The ESS project
International collaboration
Partner Countries:
52.5% Construction
85% Operations
~70%/30% In-Kind/Cash
Sweden and Denmark:
47.5% Construction
15% Operations
100% Cash

## Slide 4: Main milestones of the project
2014
Construction work starts on the site
2009
Decision: ESS will be built in Lund
2025
ESS construction complete
2003
First European design effort of ESS completed
2012
ESS Design Update phase complete
2019
First neutrons on instruments
2023
ESS starts
user program
Notes: Mention licenses

## Slide 5: The ESS projects(s)

## Slide 6: Collaboration During Pre-Construction
Sebastien Bousson
Pierre Bosland
Santo Gammino
Søren Pape Møller
Roger Ruber
Ibon Bustinduy
CERN
The National Center for Nuclear Research, Swierk
Anders J Johansson
Roger Barlow
Partners for the Accelerator. Similar arrangement for the Target and Neutron Instruments
Notes: PDM, managing of information, etc

## Slide 7: Green Light!
Swedish Minister 4 July 2014: Ready to Build ESS
Groundbreaking:
2 September 2014

## Slide 8: Start of the Construction

## Slide 9: ESS production of neutrons for science
Linear proton accelerator (600 m)
Neutron science systems
Target station
Notes: Superconducting linac
Solid-state rotating tungsten target
The latest instrument suite

## Slide 10: ESS Linac Parameters
Particle species p
Energy 2.0 GeV
Current 62.5 mA
Average power 5 MW
Peak power 125 MW
Pulse length 2.86 ms
Rep rate 14 Hz
Max cavity surface field 45 MV/m
Operating time 5200 h/year
Reliability (all facility) 95%
603 m
Tuning dump

## Slide 11: RF systems
Main features:
One RF power source (klystron, IOT, ...) per resonator
Two klystrons per modulator for ellipticals
Pulsed-cathode klystrons for RFQ, DTL
Gridded tubes (tetrodes or IOTs) for spokes
Klystrons for medium-beta ellipticals, and as backup for high-beta
Developments with industry for high-power IOTs
 | Frequency (MHz) | No. of couplers | Max power (kW)
RFQ | 352.21 | 1 | 900
DTL | 352.21 | 5 | 2150
Spokes | 352.21 | 26 | 350
Medium betas | 704.42 | 32 | 900
High betas | 704.42 | 88 | 1100
SNS klystron gallery
Layout of ESS linac tunnel and klystron gallery

## Slide 12: Target
Proton beam
Proton beam window
Tungsten wheel
Moderator
Neutron guides
Shutters
Iron blocks
Tungsten slabs in 33 sectors
Cooled with helium gas, 3 kg/s, 0.3 MPa, 20/200 °C
Rotational speed 25.5 rpm
Wheel diameter 2.5 m
Shaft length > 5 m
Lifetime ~ 5 years (@ 5 MW)

## Slide 13: Moderator-Reflector Plug
Cooldown of the MeV neutrons to meV neutrons
Cold moderators
  Super-critical H2 at 20 K and 1.5 MPa
  Aluminium alloy vessel
  Expected lifetime ~ 1 year @ 5 MW
Water moderator assemblies
Light water-cooled Be reflector
“Flat” moderator concept proposed last summer to significantly increase neutron brightness (factor ≳3)
Moderators
Inner Be reflector
Outer SS reflector
TDR moderator concept

## Slide 14: Reference Suite of 22 Instruments
Initial plans. 1st set of instruments still under discussion

## Slide 15: Activities in construction, Initial and Steady-State Operation phases
The construction phase: Includes design, project management, administration, manufacturing, acceptance tests, installation and cold commissioning (without beam) of systems in the accelerator, target and instruments. It also includes hot commissioning (with beam) of parts of the accelerator. The construction phase will partly overlap with the initial operations phase.
The initial operations phase: Includes the hot commissioning, operation, maintenance and repair of all systems and activities for the ramp-up of beam power. It includes the cold (and hot) commissioning of instruments and systems needed for significant beam powers and steady state operations. It includes the main part of the construction of instruments funded by resources that are additional to the construction funding. It includes the start and operation of a user program.
The steady state operations phase: Include operation, maintenance and repair of all systems. It includes upgrades, cold and hot commissioning of existing instruments and potentially construction of new instruments. It includes a full user programme.

## Slide 16: High level plan for Initial Operations
Construction Project completes in 2025
Neutron spallation source construction complete at the end of 2022
16 instruments and user support construction completed at end of 2025
Initial Operations Phase (2019 – 2022, 4 years until spallation source complete)
  Begins with 1st neutrons
  1 year for activities necessary to produce first neutrons in 2019
  3 years to improve accelerator performance and commission initial instruments
Initial User Program Operations (2023 – 2025, 3 years)
  Support necessary for reliable instrument operations for non expert public users and the basis for cost sharing post construction
  Cold commissioning of (16 first) instruments funded within the construction project
Steady State Operations (2026 onwards)
Notes: Working group different projects
Developing procedures for operation

## Slide 17: Time Schedule: Linac point of view
2014: finish of the redesign
July 2014: Approval of the project
Sept 2014: Groundbreaking
2014-2016: Building construction
2016-2019: Installation, except High Beta modules
Jan-Oct 2019: Commissioning warm Linac, Spokes and Medium Beta to target.
End 2019: 1st protons on Target, Neutron production. Start of Hot Commissioning.
2021 Installation High Beta modules 1-11
2022 Installation High Beta modules 12-21
2026 5 MW operation
Notes:   Energy
  Climate
  Health
  Agriculture
  Digital society

## Slide 18: Linac Commissioning
3 main stages:
Test outside ESS:
  IS+LEBT+RFQ at Saclay. Final agreement currently under discussion.
Systems testing:
  Verification of the various systems without beam: Cryogenics, RF, MPS, etc
Beam commissioning:
  Verification of the system with proton beam.
  Optimization of the parameters of the Linac: energy, power, losses minimization
  Delivery of protons to Target for Target commissioning and neutron production
  Using Faraday cups and Tuning Dump before going to the Target
  Reduced power beam (low current, short pulse, low repetition rate)

## Slide 19: Beam Commissioning
Divided in 4 steps (dates are indicatives only, coordination with installation should be done early next year):
Normal conducting: Commissioning Jul 2018-5 February 2019 (not continuous)
  Using Faraday cups along the Linac
Spoke and medium beta: Commissioning April 2019-Nov 2019
  Commissioning to Tuning Dump: April -May 2019
  Commissioning to Target: May 2019-Jul 2019
  Buffer-Late Finish: Sept 2019-Nov 2019
High beta cryomodules 1-11: Commissioning 13 July 2021 to 6 September 2021
High beta cryomodules 12-21: Commissioning 26 August 2022 to 22 September 2022 (installation after the commissioning of modules 1-11, and initial operation started)

## Slide 20: Planning
Initial plan of the procedures to follow during beam commissioning finished
Created list of Objectives for each section of the Linac
Created list of Procedures to reach the objectives for each section.
From the procedures list, we are in the process to extract requirements, including::
  Beam Instrumentation required for Beam Commissioning
  Beam mode to be used
  Software needed
  Training needed
  Other resources and personnel needs

## Slide 21: Example: MEBT - Objectives
Based in our L3 requirements
MEBT:
Transmission > 99.3%
Output beam current, 6.5 mA  63 mA
Output beam energy controllable within ±10 keV of design
Flat top length, 5 us  3 ms
Pulse length (nominal) < 2.860020 ms
Twiss parameters matched throughout flat-top
Transverse 99% output emittance less than that in integrated lattice design
Longitudinal 99% output emittance less than that in integrated lattice design

## Slide 22: Example: MEBT - Procedures

## Slide 23: Next steps in the planning
Integration of the beam commissioning with the installation planning
Definition of the commissioning team
Finishing of requirements for commissioning
Training and licenses
Interface with Target and Neutron Instruments commissioning
How we document the process? For the moment jira+wiki
Crosscheck with the commissioning of similar machines (mainly SNS and Linac4)

## Slide 24: Operators
~21 operators needed for operations
Ongoing discussions about:
  Where they belong inside the ESS organization?
  When to hire them?
  Are some of them to be ready for beam commissioning?

## Slide 25: Instruments: planning and commissioning
1st
Neutrons
2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
 |  |  |  |  |  | 3 | 6 | 6 | 5 | 4 | 3 | 2 | 2 | 2 | 1
 |  |  |  |  |  |  |  | 3 | 6 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 9 | 11 | 15 | 17 | 19 | 22
Construction Budget
Expected Instruments in hot commissioning
Plans for
Instruments (1-22)
Initial Operations Budget
Steady-Sate Budget
Expected Instruments in Initial Science Programme
Start of Instrument Construction
Expected Instruments in Science Programme
Scheduled Neutron Production
On
Off
Regular Call for User Proposals
…..
Engineering Design
Construction of Instruments
# 1-16
# 17-22
Engineering Design
Construction of Instruments

## Slide 26: Technical plan for Initial Operations
Criteria for start of Initial Operations: Cold commissioning completed for all systems needed for producing and delivering a measurable number of moderated spallation neutrons to an instrument and for detecting them in the instrument. Technical Strategy
Initially keep radioactivity and doses low to allow hands on maintenance.
Ramp up power quickly to find limitations and increase reliability before user operations start.
Ramping of the power using peak current, energy and repetition rate.
Start with modest operation schedule: 180 days/y for neutron production. Ramp up to 200 days/year when facility has matured

## Slide 27: Priorities during Initial Operations
Agreement between the different project of ESS (Accelerator, Target and Instruments) about the priorities during the Initial Operations.
Still under negotiations.
The first priority is always safety of the components. We should minimize losses in the Linac.

## Slide 28: Accelerator commissioning and ramp up
Phase 1: Front end, NC linac, spoke CMs, and medium-ß CM
Phase 2: Installation and commissioning of high-ß CM
Phase 3: Consolidation and ramp-up
Pulse length 2.86 ms to enable instrument commissioning
Phase 1
Phase 2
Phase 3
Installation cryo 1-11
Installation cryo 12-21

## Slide 29: Alternative ramping
The possibility to use a different repetition rate during initial operation is under study.
The consequences on some experiments and in the target is being evaluated.
Reduces the range of currents.
Chart: Energy, Power
| 43651.0 | 43739.0 | 43831.0 | 43891.0 | 44013.0 | 44075.0 | 44197.0 | 44256.0 | 44317.0 | 44470.0 | 44531.0 | 44576.0 | 44621.0 | 44682.0 | 44743.0 | 44835.0 | 44927.0 | 45108.0 | 45292.0 | 45536.0 | 45658.0 | 45748.0 | 45901.0
Energy [GeV] | 0.4 | 0.42259 | 0.44622 | 0.46162 | 0.49295 | 0.50886 | 0.54019 | 0.55534 | 0.571 | 0.561 | 1.3 | 1.3 | 0.8 | 0.91172 | 0.99414 | 1.0766 | 1.1883 | 1.3 | 1.3 | 1.3 | 2 | 2 | 2 | 1.7 | 1.7259 | 1.7768 | 1.8286 | 1.8973 | 1.9316 | 1.9569 | 2
Power [MW] | 0.035464 | 0.037467 | 0.15825 | 0.28649 | 0.61186 | 1.2632 | 1.341 | 1.3786 | 1.4175 | 1.4039 | 0.32532 | 0.65065 | 0.070928 | 0.16167 | 0.35256 | 1.3363 | 2.9499 | 3.2272 | 2.9279 | 3.2532 | 0.5005 | 1.001 | 1.5015 | 0.30388 | 0.61701 | 2.2233 | 2.1965 | 3.7984 | 4.8339 | 4.8972 | 5.005
Current [mA] | 31 | 31 | 62 | 31 | 62 | 62 | 62 | 62 | 62 | 62.5 | 6.25 | 12.5 | 31 | 62 | 62 | 62 | 62 | 62 | 56.25 | 62.5 | 6.25 | 12.5 | 18.75 | 62.5 | 62.5 | 62.5 | 30 | 50 | 62.5 | 62.5 | 62.5
RepRate [Hz] | 1 | 1 | 2 | 7 | 7 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 1 | 1 | 2 | 7 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 1 | 2 | 7 | 14 | 14 | 14 | 14 | 14

## Slide 30: Neutron source modes of operation
Installation of High Beta Cryomodules

## Slide 31: Tentative Operations schedule 2020
Tentative – used as a tool for coherence in plans

## Slide 32: Tentative Operations schedule 2025
Tentative – used as a tool for coherence in plans
Two long shutdowns for maintenance. Other small maintenances possible during OS or studies day.

## Slide 33: Conclusion
ESS looks for a proper balance between early scientific success and safe/reliable ramp-up program.
This requires: adequate commissioning of the neutron source itself and instruments (big difference with reactor based installations), good coordination between all groups involved
Plans are developed along the following lines:
  Accelerator program with a gradual ramping of current and energy to minimize losses and doses, and priority in availability
  Instruments: ambitious construction program (in-kind contributions!!) but reasonable commissioning time, early access for selected demonstration experiments
  Full user program in 2023
  Full power circa 2026
ESS will adapt its strategy to reality
Come and visit us
in 5 years from now!

## Slide 34: Extra slides

## Slide 35: Evolution of neutron sources
Berkeley 37-inch cyclotron
350 mCi Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ISIS
Pulsed Sources
ZING-P
ZING-P/
KENS
WNR
IPNS
ILL
X-10
CP-2
Steady State Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Effective thermal neutron flux n/cm2-s
(Updated from Neutron Scattering, K. Skold and D. L. Price, eds., Academic Press, 1986)
FRM-II
SINQ
SNS
ESS
J-PARC
0 1 2 3
Time (ms)

## Slide 36: Initial Operations - main activities for instruments
Initial Operations - Instruments
Follows the “cold” commissioning without beam.
Begins with hot commissioning (with neutrons) and scientific commissioning of first instruments. Requires a few month with beam
Optimisation and corrections, calibration experiments
First calls for “Best effort” experiments in 2022
Ensures reliability before start of regular User Programme
User Programme will include six instruments in 2023, with 2-3 additional instruments available per year

## Slide 37: Plans for initial operations
Plans for initial operations under revision based on the feedback from advisory committees, governing committees, reviews, and internal planning
  Initial Operations should be triggered by activities related to the production of neutrons and not accelerator commissioning (STC);
  The ramp up of the instrument program should be realistic (STC and Ops review);
  Start with modest operation schedule: 180 days/y for neutron production. Ramp up to 200 days/year when facility has matured (Ops Review);
  The transition from construction into operations should recognize the need for continuity in staffing and support (Ops Review); and,
  Operations support should include the capital budgets needed to complete and maintain the 22 public instruments (Ops Review and Internal Plans).

## Slide 38: Licensing - Time Schedule
Detail Plan approved
Radiation Protection Act
Environ- mental
Code
Planning & Building Act
Building
Application
(ESS)
Application
EIA
Environmental
Impact
Assessment
Application
PSAR
Preliminary
Safety
Analysis
Report
Building Permit
EC
SSM
Permit & conditions to construct
Construction
& Operation
Permit
SSM
Swedish Radiation Safety Authority
EC
Environmental
Court
Lund Municipality
2012-01-01 2013-01-01 2014-01-01 2014-06-01
Court Hearing
SSM Permit to construct expected before summer 2014. Ground break can start after building permit with execution warranty, expected 12/6 14.00.

## Slide 39
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
ESS Program
Conventional
Facilities
Accelerator
Target
Neutron
Scattering
Systems
Integrated
Control Systems
Building
Commissioning
Concluding
Design
Design
Construction
Commissioning
Design & Prototyping
Procurement
Installation
Commissioning
Design
Procurement
Installation
Commissioning
Installing
Construction
Ground Break
First installations (of Machine Systems)
First Neutrons
Machine 2.0 GeV
Accelerator, Target, Aux, Office, Lab & Instr Bldngs*
570 MeV
Instrument Selection - Decision
Design
Commissioning
Construction
Design
Development
Commissioning
CS Network Operational
3 Instruments ready for Comm.
Initial Operation
Installed for 2.0 GeV
16 Instr
End Of Construction
Start Of Construction
Concept Devlopment
Licensing
Preliminary Design Acccelerator Bldngs
Detailed Design Accelerator Bldngs
Earth Works
G01 Linac Tunnel
G02 Klystron Bldng
Cryo Kompressor Bldng
Medium Beta Fabrication
Spoke Series Procurement
High Beta Fabrication
Installation Phase 1
Installation Phase 2
Innstr 16 – Cold Comm.
Innstr 16 – Constr & Inst.
Top-Level ESS Project Schedule
1st Call for User Proposals
Main Schedule for Licenses and Permits
- 12 June 2014 – Environmental court permit
- 15 July 2014 – SSM license to construct
- 2015 – SSM license to install
- 2016 – SSM license for test operations - 2019 – SSM license for beam on target
- 2020 – – SSM license for increasing steps in beam power
- 2023 – – SSM license for full operations

## Slide 40: Ramping up to full ops

## Slide 41: Scheduling modes

## Slide 42
At present 916 activities 2019-2023. Detailing and structuring ongoing.
Initial Operations planning

## Slide 43
Initial Operations planning