## Slide 1: Operation of GSI and FAIR
David Ondreka
WAO 2014, Mainz, 31.10.2014

## Slide 2: Overview
GSI
  Facility
  Operation
FAIR
  Project
  Facility
  Operation
Outlook

## Slide 3: GSI Helmholtzzentrum für Schwerionenforschung GmbH
Facility for research with heavy ions
Scientific program:
Atomic and Plasma Physics
Nuclear and Hadron Physics
Material Sciences
Your route to GSI...

## Slide 4: GSI Accelerator Complex
Experimental Areas (~20)
Ion Sources
SIS18
ESR
UNILAC
Max. Energies | 
p | 4.5 GeV/u
Ne10+ | 2.0 GeV/u
U73+ | 1.0 GeV/u
U28+ | 0.2 GeV/u
Max. Intensities | 
p | 1011
Ne10+ | 5·1010
U73+ | 3·109
U28+ | 3·1010
ESR
Energy 800 – 3 MeV/u
Electron cooling
Stochastic cooling
Deceleration
Single particle detection
UNILAC
Low energy beams
3.6 – 11.4 MeV/u
Pulse length 0.1 – 5 ms
Rep. rate 50 Hz
SIS18
High energy beams
Slow extraction (≤10s)
Fast extraction (1 turn)
Bunch compression
Rep. rate 0.1 – 1 Hz
Ion Sources | 
ECRIS | Gases
MUCIS | 
CHORDIS | 
PIG | Gases Metals
MEVVA | Metals
VARIS | 

## Slide 5: GSI Scientific Highlights
SIS18
ESR
UNILAC
Ion Radiotherapy
Cave M
SHE
Super Heavy Elements
112Cp
110Ds
111Rg
107Bh
109Mt
108Hs
FRS
Exotic Nuclei

## Slide 6: GSI Operation
GSI operating conditions
  Operation 24/7
  1 shift leader + 2 operators
  Support by physicists for set-up
  On-call duty for technical problems
Parallel operation
  UNILAC, SIS18, ESR independent
  3 different ion species
  5 parallel experiments
Experiments demand high flexibility
  General beam time coordination
    Switching of ion species (weekly)
    Adjustment of schedule (monthly)
  Daily coordination in noon meeting
    Variation of beam parameters (E, N, T)
    Change of beam sharing
  Success of GSI as research institute is highly linked to this flexible operation!
Parallel Operation in the GSI facility
Unilac
SIS18
ESR
SIS18
ESR
UNILAC
Typical GSI beam time plan
GSI main control room

## Slide 7: Facility for Antiproton and Ion Research
Scientific Motivation:
Continuation and extension of GSI’s heavy ion research program
Breaking limits of GSI
    Primary beam intensities: 100x
    Secondary beam intensities: 10000x
    Primary beam energies: 10x
    Production of Antiprotons
    High brilliance through cooling
Scientific questions
    Properties of ‘cosmic matter’
    Matter in the early universe
    Origin of hadron masses
    Origin of the chemical elements
    Matter under extreme conditions
Atomic/Plasma/Applied Physics
Nuclear Structure
Strong Interactions
Nuclear Matter and Hadrons
  More information: www.fair-center.eu

## Slide 8: FAIR Project Milestones
FAIR Conceptual Design Report | 11 / 2001
BMBF approval of FAIR | 02 / 2003
Baseline Technical Report | 03 / 2006
Official start of FAIR project | 7.11.2007
Technical Design Report | 12 / 2008
Signing of FAIR convention | 4.10.2010
Foundation of FAIR GmbH | 4.10.2010
Granting of project funds | 6.11.2011
Start site clearance | 12 / 2011
Start Procurement Accelerator | 01 / 2012
Radiation protection permit | 12.06.2012
Construction permit | 29.10.2012
Start pile construction work | 03 / 2013
End pile construction work | 05 / 2014
2001
2014
Start SIS18 upgrade | 11 / 2014
Start construction work | 2016
SIS18 re-commissioning | 2017
FAIR buildings completed | 2019
FAIR accelerators installed | 2019
FAIR facility operational | 2020
2020

## Slide 9: FAIR Facility
SIS100
HESR
CR
SIS300
RESR
NESR
FLAIR
SIS18
p-Linac
from Unilac
pbar
RIB
CBM
APPA
PANDA
SFRS
SIS100 beam parameters |  | 
 | Emax | Nmax
p | 29 GeV/u | 2.5·1013
U73+ | 10 GeV/u | 1.0·1010
U28+ | 2.7 GeV/u | 5.0·1011
SIS100
Primary beams
Slow extraction (1 – 100s)
Fast extraction (1 turn)
Bunch compression
Rep. rate 0.01 – 2 Hz

## Slide 10: FAIR Site: Construction Work
Construction site cleared
Access road constructed
1400 concrete piles implanted
  Stabilization of ground
  Minimization of settlement
google.maps
quadcopter
FAIR Webcam

## Slide 11: FAIR Procurement Status
Procurement of FAIR components
  Several large series started
    SIS100 dipoles and RF cavities
    HEBT dipoles and quadrupoles
  Many pre-series components under testing
  Many components to be ordered next year
  Bulk will arrive from 2016 on
  Consistent with project schedule
Upgrade program for GSI accelerators
  SIS18 and UNILAC upgrade programs for FAIR injector mode
  Upgrades started, to be completed in 2017
GSI campus infrastructure
  Testing areas for site acceptance tests
  Cryogenic magnet testing facilities
    Prototype test facility for SIS100 dipoles
    Serial test facility for SIS100 dipoles and string tests
SIS18 H=2 Cavity
Serial test facility
p-Linac Klystron
Super-FRS Dipole
SIS100 Dipole
p-Linac CH Cavity

## Slide 12: FAIR Operation
Goal: Maximal scientific use
  Maximization of beam on target through parallel execution of experiments in FAIR
  Requires sophisticated coordination of the various accelerators and transfer lines
Boundary conditions
  Similar flexibility requirements as for GSI
    Longer beam times for main experiments (statistics, polarity changes)
    Still shorter beam times for tests
    GSI operation will continue
  Operation of GSI/FAIR by 5 operators
    4 beam operators, 1 cryo operator
    Basis for operating cost estimates
    Only two additional operators for FAIR
    Requires very good support from the operating environment
Details specified in operating concept
  Presently being worked out
“The operation of FAIR will be uniquely versatile in that up to five research programmes with five different particle beams can be carried out at the same time. This will be achieved by coordinating beam operation in both the synchrotrons and adjacent storage and accelerator rings. In this way, each experiment can make maximum use of the highest available beam intensity.”

## Slide 13: FAIR Operation: pbar Chain
Beam production
  p-Linac: 1013 p, 70 MeV/u
  SIS18: 6·1012 p, 4 GeV/u, 2.7 Hz
  SIS100
    4 Injections from SIS18: 2·1013 p
    Acceleration to 29 GeV/u
  pbar-Target
    Production of pbar
    Conversion efficiency ~10-5
  CR
    Stochastic cooling of pbar ~10s
  HESR
    Accumulation (~1010 pbar, ~15 min)
    Acceleration to 14 GeV/u
    Physics experiments ~15 min
Natural gaps to be filled
  10 s cooling time in CR
  15 min physics time in HESR

## Slide 14: FAIR Operation: RIB Chain (fixed target)
Beam production
  Unilac: 2.5·1011 U28+, 11.4 MeV/u
  SIS18: 1.5·1011 U28+, 200 MeV/u, 2.7 Hz
  SIS100
    4 Injections from SIS18: 5·1012 U28+
    Acceleration to 1.5 GeV/u
    Slow extraction
  SFRS
    Target: Production of secondaries
    Separator: Selection of goal RIB
    Caves: Physics experiments
Leaves gaps for SIS18
  Duration depending on extraction time
  May be used for beam in GSI TH or ESR

## Slide 15: FAIR Operation: pbar/RIB and RIB
pbar production will run over long times due to small conversion efficiency
In MSV, 15 min accumulation followed by 15 min physics
Possible szenario
  HESR accumulation: Run RIB during CR cooling time
  HESR physics: Run RIB stand-alone
Gaps in SIS18 may also be filled
  Short gaps: beam for ESR/CRYRING
  Long gaps: slow extraction to GSI TH
Control system requirements
  Patterns integral concept of the FAIR CS
  Automatic switching between two patterns based on beam request by HESR
  FAIR CS must allow simultaneous tuning
    Control room architecture
    Control system design

## Slide 16: FAIR Operation: Beam Set-up Procedures
Set-up of the pbar/RIB pattern
  Initialize complete pattern (no beam)
  Switch to set-up pattern for main proton beam
  Tune proton beam successively on set-up dumps up to highest intensity
  Tune beamlines to target
  Add RIB chain, tune similarly
  In parallel, set-up CR and HESR
Challenges
  Possible influence of RIB on pbar (hysteresis)
  Destructive BI for tuning RIB extraction
  Parallel exp. may change frequently: How to avoid disruption of pbar chain?
Requirements on CS for patterns:
  Creation of patterns from beam time plan
  Creation of set-up patterns from real pattern
  Execution of set-up procedures

## Slide 17: FAIR Control System: Developments
Control system for FAIR
  Completely new design
  Collaboration with CERN
    FESA framework for front-ends
    LSA framework for settings management
    Timing system (White Rabbit)
    User Interfaces
Prototype systems at SIS18
  BI: BPMs, Screens
    Routine use for orbit correction and steering
  Settings: machine model, applications
    Commissioning H=2 cavity
    Resonance compensation
Operational at CRYRING (2015)
  Prototype of FAIR control system
  FESA front-ends for
    Magnet PCs, RF, HV, RFQ
    BPMs, Trafos, Screens, Cups, Grids
  Operating applications
  Test bench for FAIR operation concepts
CUPID (Scintillating screens)
TOPOS (SIS18 BPM system)
jMirko (Online optics)
ParamModi (Settings)
SIS18 Hierarchy (Machine model)
YASP (Orbit control)

## Slide 18: Operation of FAIR: New Main Control Room
New main control room required
  More space needed for additional machines and infrastructure (e.g. cryo)
  Central console for survey, monitoring, and administrative purposes
  Console arrangement to support parallel tuning of independent beams
  Acoustic separation of areas
  Daylight conditions
  Modern, ergonomic equipment
Additional requirements
  Integration of meeting room
  Representative architecture
GSI main control room
FAIR main control room (DRAFT)
  Details will be worked out by project group “FAIR main control room” based on operating concept
Test console

## Slide 19: Outlook
2015
2016
2019
2018
2017
2020
GSI
FAIR civil construction
FAIR accelerator installation
FAIR accelerator comm.
FAIR physics operation
FAIR
Upgrade measures
Shielding reinforcement
Align- ment
Re- comm.
Physics operation in GSI
Injector comm.
FAIR physics operation
Roadmap for operation of GSI and FAIR
CRYRING commissioning
CRYRING stand-alone operation
These are exciting times, so stay tuned!

## Slide 20: Acknowledgments
Thanks to the colleagues providing material:
P. Kowina, C. Omet, B. Schlei, P. Schütt, P. Schwab, P. Spiller C. Sturm, D. Varentsov, B. Walasek-Höhne, W. Vinzenz
Thanks to all colleagues of FAIR@GSI sharing the big work load of converting the FAIR idea into reality!
Thank you for your attention!