## Slide 1
Our investigation is performed through the interview to a personnel who made a mistake based on SHELL model.
Investigation of human error
Improvement of the training program
for newcomers by human factor analysis
Hiromi. Inokuchi1, Shigekazu.Fukuda1, Katsumi.Okumura1, Izuimi. Kobayashi2
1National Institute of Radiological Sciences (NIRS), 4-9-1 Anagawa, Inage, Chiba 263-8555, Japan (Here after called NIRS)
2Accelerator Engineering Corporation, 3-8-5 Konakadai, Inage, Chiba 263-0043, Japan(Here after called AEC)
Introduction
We, NIRS, have experienced a number of troubles that interrupt a beam supply
or therapy treatment by human errors in a year.
The occurrence rate was 0.3 per 100 operating hours every year.
We investigated the cause of human errors and reviewed the training program
for newcomers.
As a result of this review and improvement, we successfully
have reduced errors by 20% in 6 months of this year
Compared to those of last years.
Figure 1 shows the trend of occurrence rate of human errors.
FIG-1. Rate of human error (3 month moving average)
Figure2 is the Swiss Cheese model which represents the structure of failure or accident by human errors. The holes in the slices represent weaknesses in individual parts of the system.
It is very important to reveal all factors for investigation.
L
L
H
E
m
s
Software
Hardware
Environment
Live ware（other person）
Live ware（themselves）
E
s
H
L
L
m
Management
The SHELL Model is defined as “the relationship of human factors and the aviation environment”
Chart: 
Year of 2013 | 0.4245 | 0.4899 | 0.38521 | 0.45872 | 0.30303 | 0.29586 | 0.16704 | 0.15936 | 0.33473 | 0.58972 | 0.46056 | 0.4548
Year of 2014 | 0.36232 | 0.30469 | 0.14881 | 0 | 0.1444 | 0.17544 | 0.22259
Fig-2. Swiss cheese model
Software
☐ Is it easy to understand the manual ?
☐ is there the problem in a procedure ?
Hardware
☐ Is it easy to misunderstand ?
☐ Is there protection to prevent miss ?
Environment
☐ Is time of deadline approaching ?
☐ Is there the problem to access them ?
Live ware (other person)
☐ Is the information conveyed definitely?
☐ Is order clear ?
Live ware (self)
☐ Are you trained ?
☐ Do you understand the procedure ?
The analysis of error factor below 5 years experience
Analysis
We analyzed all human errors including near-miss error that occurred last year .
The near miss error was reported by person who made near-miss.
We analyzed those errors by various approach, such as work phase, failure conditions, error factors and experiences.
The failure condition analysis
FIG-5. The analysis by failure condition for therapy support
FIG-6. The analysis by failure condition for accelerator
Chart: 
| data file selection errors | machne operation error | preset switch or other error | course change operation error | beam calibration error
 | 3 | 5 | 10 | 2 | 1
Presetting data or switch position etc.(occupy 42%)
There was no typical trend in this analysis.
Example of questioner !
The work phase analysis
Fig-3. The analysis by work phase for therapy support
FIG-4. The analysis by work phase for Accelerator
A preparation occupied about 50% in both tasks, therapy support and accelerator operation,.
FIG-7 . The analysis by Error factor
The Error factor analysis
FIG-8. Human error relating experience
Chart: 
| less than 5 years | 6 to 10 years | 11 to 15 years | 16 to 20 years
 | 61 | 6 | 25 | 20
More than 50% persons were less than 5 years experience.
Conclusion
More than 50% of the errors were caused by the fact that persons having less than five-year experiences lack some prerequisite knowledge. Refer to FIG-9.
Focused on person who has within 5 years experience
Chart: 
| less than 5 years | 6 to 10 years | 11 to 15 years | 16 to 20 years
 | 61 | 6 | 25 | 20
FIG-9. The error factors of personnel within 5 years experience
As a result of this analysis,
☐ We have reviewed and improved the training program for newcomers.
☐ Also modified the classroom training to be performed by two instructors.
While one instructor is lecturing, the other instructor is taking care of the person who has a poor understanding of the lecture at the same time.
NIRS HIMAC overview
Reason same as preparation, FIG-3& -4,.
Month
Rate per 100 operation hours
Chart: 
| Inspection phase | Quality assurance | Preparation of a therapy | irradation | After process of therapy | experiment | Other
 | 4 | 6 | 17 | 1 | 3 | 2 | 0
Preparation(occupy 50%)
There are lot of work steps, therefore occurrence of error potential is higher than other works.
Chart: 
| Preparation for machine operation | machine operation | beam calibration
 | 11 | 6 | 4
Preparation(occupy 50%)
There are lot of work steps, therefore occurrence of error potential is higher than other works.
Chart: 
| Communication | knowledge | pressure | slip | supposition | other
 | 14 | 32 | 14 | 28 | 23 | 1
There was no typical trend.
Chart: 
| Communication | knowledge | pressure | slip | supposition | other
 | 4 | 31 | 12 | 10 | 4 | 0
Chart: 
| communication | knowledge | pressure | slip | supposition | other
 | 0 | 11 | 4 | 4 | 9 | 0
Lack of knowledge was occupied about 50%
Year of 2013
Year of 2014
Reduce to about 40%
The experience analysis
Chart: 
| data file handling error | data file selection error | measurement equipment selection error | data input error | beam or course change order error | caliculation error | damage | equipment setting error | installation error | measurement process error | measurement error | switch operation error | other
 | 15 | 6 | 9 | 4 | 5 | 2 | 5 | 2 | 2 | 5 | 3 | 26 | 7