## Slide 1: New Implementation FairLinks
and a Fast Event Builder
| Tobias Stockmanns

## Slide 2: Current Implementation Event Based
MC Track
EntryNr
1
MVD Point
Pixel Digi
Pixel Cluster
Pixel Hit
2
…
FairLink (FileID / EntryNr / BranchID / Index / Weight)
DataObject (FairLink / Data)

## Slide 3: Current Implementation
Each DataObject contains a set of links to the objects used to create the DataObject
Set of links stored in each DataObject
MC match between reconstructed hit and MC: follow the links (Hit->Cluster->Digi->Point)
Works well for event based data
For time based data it works but it is extremely slow!

## Slide 4: Current Implementation Time Based
MC Track
EntryNr
1
MVD Point
Pixel Digi
Pixel Cluster
Pixel Hit
32
…
20
…
…

## Slide 5: Future Implementation
DataObjects not anymore in same entry
Follow FairLinks needs permanent switch between entries  very time consuming
Solution: store in each DataObject all FairLinks to previous data (not only to stage directly before)
Drawback: Memory and disk storage consumption rises

## Slide 6: Future Implementation
Data
FairLinks
Data
TRef
FairLinks
Current
Future
Separate Branch
Can be disabled
+
FairLinks Manager
Selector:
  Which links to store
  Which to ignore
FairLinks stored in object
Always on

## Slide 7: Results
37 : MVDHitsPixel
0 : [(-1/0/1/4/2) (-1/0/36/0/1) (0/0/3/0/2) (0/20/25/0/1) (0/20/25/17/1) ]
1 : [(-1/0/1/3/4) (-1/0/36/1/1) (0/0/3/7/4) (0/20/25/1/1) (0/20/25/3/1) ]
2 : [(-1/0/1/0/1) (-1/0/36/6/1) (0/0/3/14/1) (0/20/25/12/1) ]
3 : [(-1/0/1/4/3) (-1/0/36/2/1) (0/0/3/2/3) (0/20/25/2/1) (0/20/25/19/1) (0/20/25/22/1) ]
4 : [(-1/0/1/3/2) (-1/0/36/4/1) (0/0/3/6/2) (0/20/25/9/1) (0/20/25/20/1) ]
(-1/0/1/4/2)
FileID
EventID
BranchID
Index in
TClonesArray
MCTrack
Cluster
MCPoint
Digi
…

## Slide 8: Summary
New concept for storage of FairLinks to better cope with TimeBased simulation
  All FairLinks directly available in each DataObject
  Storage of FairLinks separated from Data
  Connection via persistant TRef
  FairLinks can be disabled
  FairLinksManager to select what to store and what not
Where to get it?
  Is part of FairRoot in the latest releases of the trunk in Git repository

## Slide 9: TimeGapEventBuilder
Looks for time gaps in data stream of one sub detector
Selects hits between gaps and groups them into “pseudo event”
Takes time width of “pseudo event” to select data of other sub detectors depending on their time resolution to build complete event
MVD
STT
Event 1
Event 2
Event 3

## Slide 10: Simulation Results
400 DPM events
50 ns average time between events complete time based simulation
MVD Pixel as event builder, MVD Strip and STT as addition detectors

## Slide 11: Time Width of Event Data

## Slide 12: Event Quality
0) Number of merged events
1) All hits in one pseudo event from one real event
2) More the one real event in pseudo event
5) Data of one event in more than one pseudo event

## Slide 13: Number of Events in PseudoEvent
Events per PseudoEvent
Events per PseudoEvent
Events per PseudoEvent

## Slide 14: Event Display

## Slide 15: Summary and Outlook
TimeGapEventBuilder very simple event builder for first stage of processing
Already quite good for MVD (> 50% clean events for MVD)
Possible to use different sub-detectors as start event builders
Possible to vary window size to improve purity or completeness of events
Can be used for all type of detectors