## Slide 1: Oleksiy Dolinskyy 23rd October , 2014
The Collector Ring project at FAIR

## Slide 2: FAIR layout of accelerators
Collector Ring

## Slide 3: Outline
Why do we need the Collector Ring.
The features of this ring.
Present layout.
The main components.
Experimental devices.
Present status and plans.

## Slide 4: Beams from separators
29 GeV protons from SIS100
target station
3 GeV antiprotons
From the SupeFRS
CR
740 MeV/u RIBs
Secondary ions are needed for experiments
antiprotons (pbar)
radioactive ion beams (RIB)

## Slide 5
Target station for antiproton production
First quadrupole
of separator
target
horn
29 GeV Protons from SIS100
antiprotons
Ti window
inside: Ni rod (r = 15 mm, L = 10 cm) within graphite cylinder (r = 1 cm)
20 mrad < q < 80 mrad can be collected
I = 400 kA
Distance target center - lens: 220 mm
more simple and reliable, less expensive

## Slide 6: Production yield of antiprotons
yield =
pbars in the ellipse
primary protons
11 cm Ni target (d = 3 mm) in a graphite container, 0.62 mm (rms) beam spot.
E(p), E(pbar) | 29 GeV, 3 GeV
acceptance | 240 mm mrad, 6%
protons / pulse | 1013
pulse length | single bunch (50 ns)
cycle time | 10 s
240 mm mrad
Less then 7 % of produced particles on the target can be trapped by the pbar separator and the CR
Phase space after horn lens

## Slide 7
Simulations predict a yield of 2 × 10-5 pbar/p.
( For 1013 protons one gets 2x108 pbars (only target/horn))
Considering 50% of losses due to nonlinear beam dynamic of pbar-separator and the CR one expects 108 pbars in a single bunch.
Pbar beams have huge momentum spread (6%)and emittance (240 mm mrad)
For PANDA experiments in the HESR 1011 pbars are required.
3 order of magnitude of pbars must be somewhere accumulated.
Before accumulation the beam must be cooled.
For beam cooling the CR will be used.
For accumulation the RESR was planned.
In this context the storage ring complex was planned:
Production yield of antiprotons

## Slide 8: Storage Rings of the FAIR
Separators
Production and delivering of pbar and RIBs to the CR
CR – Collector Ring
fast pre-cooling of the hot ion beams
RESR – Recycled Experimental Storage Ring
accumulation of antiproton beams
fast deceleration of rare isotopes
NESR – New Experimental Storage Ring
experiments with stored ion beams
deceleration of antiproton beams
BR=13 Tm
NESR
CR
RESR
Pbar-separator
Super-FRS

## Slide 9: accumulation of pbars
In MSV 0-3 of FAIR project the RESR and NESR will not be build
The cooled beams from the CR will be transferred directly to the HESR, where the accumulation takes place.
Because of the small momentum acceptance of HESR only 1010 pbars will be accumulated.

## Slide 10
Main task of Collector Ring
- Fast pre-cooling of the hot ion beams coming from separators
- The ring has been designed specially to have efficient cooling of the very hot ions

## Slide 11
Tasks of the CR
1. Cooling of secondary beams of radioactive ion beam (RIB)
e=200 mm mrad
Dp/p=3 %
 1.5 sec
e   0.5 mm mrad
Dp/p  0.05 %
CR
extraction RI beams to the HESR
2. Cooling of antiproton beams (Pbar)
e =240 mm mrad
Dp/p=6 %
e   5 mm mrad
Dp/p  0.1 %
extraction Pbar to the HESR
 10 sec
CR
3. Mass spectrometer of radioactive ions RI (TOF)
e  =100 mm mrad
Dp/p=1 %
CR
 few turns
Injection RI beams from the Super-FRS
Injection from antiproton separator
Injection RI beams from the Super-FRS
Δf

## Slide 12
Present layout of the CR and main components
RF – cavities
Stochastic cooling
Pick-Up
Stochastic cooling
Kickers
Injection Kicker
magnets

## Slide 13: The basic features of the CR
The large momentum (up to 6%) and transverse (up to 240 mm*mrad) acceptances require large aperture magnets (up to 400 mm).
Operation at the static maximum filed level corresponding to the bending power of B=13 Tm.
It is dedicated ring, which design is optimized to perform fast cooling.
4. Using the same hardware the cooling system is build for cooling of both antiproton and heavy ion beams.
5. Mass measurement in isochronous mode operation.
6. Variability of the optics at ring. Three basic optics are applied.

## Slide 14
The Vertical corrector coil is embedded in the sextupole. The technical design is under development. 3 mrad kick strength is required.
The BPM is embedded in the wide aperture quadruople magnet
CR magnets in arcs

## Slide 15: CR for cooling
CR is designed to have optimal cooling for all ions using the same hardware
The cooling is performed by two steps:
1. Fast bunch rotation to reduce only the
momentum spread by factor of 3.
2. Stochastic cooling to reduce both the
momentum spread and transverse beam
emittance.

## Slide 16: First step of cooling- RF bunch rotation
Using bunch rotation RF cavity the momentum spread is reduced
from 6% to the less than 2%. Time of such cooling is about 3 ms
Δp/p=6%
Δp/p=2%
Δp/p=6%
Δp/p=2%

## Slide 17
RF Cavity for bunch rotation
Total voltage (5 cavities) | 200 kV
Peak voltage per cavity | 40 kV
Peak dissipation per valve | 393 kW
Peak dissipation per valve into ring cores | 648 kW
Peak power per valve | 1040 kW

## Slide 18: Second step of cooling- Stochastic cooling
After bunch rotation Stochastic cooling is applied to reduce
both the beam emittance and momentum spread
Momentum spread is reduced from 2% to 0.1%
Cooling time for antiproton beam is about 10 s

## Slide 19: Stochastic cooling
Pickup – to detect the beam parameters
(Energy deviation with respect to the reference energy; transverse deviation with respect to the reference orbit )
Kicker – to correct: the energy; particle angle.
Electronics – to proceed the signal, (amplify and transfer to the kicker)
There are specific requirements to the ring
to have efficient cooling:

## Slide 20: Stochastic cooling
Phase advance must be 900 or plus
a multiple of 1800.
On can say:
The quantum number of a phase between Pickup and Kicker is required.
This is one of the main requirements to
storage ring to cool ion in the transverse
phase space.
n=0,1,2…

## Slide 21: Stochastic cooling in the CR
Bad mixing
Good mixing
The CR is designed to have required η parameter both for antiproton and RIB beams. Optic and positions of PU and KI are optimized to have required phase advances between all pairs of PU-KI.
Filter cooling PU (1-2 GHz)
Palmer cooling PU
CR upgrade: 2-4 GHz cooling system
η=0.01 (pbars)
η=0.18 (RIBs)
η=0.0 (Isochron)

## Slide 22
Rib mode (gamma-tr=2.7), gamma=1.8
Pbar mode (gamma-tr=3.8) gamma=4.2
Isochronous mode (gamma-tr=1.8, gamma=1.8
Dx (m)
0 10 20 25
path length s (m)
0
111
dispersion function over a half of the ring
CR: Requirements to the rings optics
pick-up
kicker
One needs 13 independent power supplies for quadrupole magnets to have
a flexibility in optic variation
The ring lattice should be adjustable to different slip factors (gamma-tr).

## Slide 23: Stochastic cooling
Δp/p
Cooling time
εx,y
Evolution of the Rms values of the Emittances and Momentum spread during SC cooling in the CR for the antiproton beam
Rms Emittance

## Slide 24: Stochastic cooling: Prototype Pickup tank at GSI

## Slide 25
CR Stochastic cooling:
Prototype Pick-up tank at GSI
Electrode
double-module
cryoshield at 80 K
flexible BeCu
sheet at 30 K
technical challenge cryoshield:
made of oxygen-free copper,
gilded galvanically
to reach very low thermal emmissivity
(expected < 2% from measurements
performed on speciments in our lab)
Motor
drive
unit
4 half-shells, each 1 m long
Cu-cryoshield succesfully mounted
in the prototype pick-up tank
Fall 2013: gilding of the cryoshield by contractor

## Slide 26: Other CR main components:
Dipole magnets
Quadrupole magnets
Sextupole magnets
Experimental devices

## Slide 27: Dipole magnet and its vacuum chamber
  The final specifications for the laminated dipole magnets has been agreed with BINP experts and officially approved. The contract between FAIR and BINP for the dipole production can be established.
  The preliminary specifications for dipole vacuum chamber have been prepared.

## Slide 28: CR planned quadrupole
CR quadrupole | wide | narrow
effective length | 1 m | 0.5 m
Pole radius | 156 mm | 95 mm
Required horizontal aperture | 400 mm | 180 mm
Required vertical aperture | 180 mm | 180 mm
Maximum gradient | 4.9 T/m | 9 T/m
ESR quadrupole | Long | Short
effective length | 1.27 m | 0.83 m
Pole radius | 150 mm | 150 mm
horizontal aperture | 300 mm | 300 mm
vertical aperture | 300 mm | 300 mm
Maximum gradient | 6.2 T/m | 6 T/m

## Slide 29
24 sextupole magnets (6 families) are needed for :
* Chromaticity correction
* Control of the dispersion function
* Avoiding synchrobetatron coupling
8 octupole correctors (2 families )
for minimizing of the fringe field effect of quadrupoles in the isochronous mode operation
24 sextupole magnets
(6 families)
ΔQh,v≈ 0.02 in Pbar mode
ΔQh,v ≈ 0.02 in RIB mode
after correction
without correction
Sextupole magnets for
nonlinear correction

## Slide 30
Experimental devices

## Slide 31
Isochronous Mode of the CR
1. γt = γ = 1.84 (E = 782.5 MeV/u)
2. γt = γ = 1.67 (E = 624.1 MeV/u)
3. γt = γ = 1.43 (E = 400.5 MeV/u)
Isomeric beams, Lifetimes and Masses
Isochronous mode ( γtr = γ ) is required for fast mass measurements.

## Slide 32: Isochronous mode
Optic parameters in the isochronous mode

## Slide 33
Isochronous condition at CR
≈0
≈0
Ideal isochronicity can be guarantied only
for one m/q ion applying correction scheme
(sextupole, octupole, decapole correctors).
Frequency calibration by velocity measurement with
two TOF detectors.

## Slide 34
H. Geissel and Yu. Litvinov, J. Phys. G31 (2005) S1779--83
Good isochronous conditions are fulfilled only
in a small range.
One has to reduce momentum acceptance!
or use 2 TOF detectors for velocity measurement!
TOF detectors

## Slide 35
Isochronous conditions at CR
≈0
≈0
Field errors of the magnets
Stability of magnet power converter (mainly dipole)
Closed orbit distortion
Large transverse acceptance (100 mm*mrad)

## Slide 36
Schottky detectors
Using Schottky detectors one can measure a frequency of short lived single ions within 10 ms.
The dedicated design of the Schottky detectors for CR is ongoing within the ILIMA collaboration.
The beam intensity can be measured simultaneously with a frequency detection.
To correct non-isochronous conditions the velocity or magnet rigidity of each particle can be measured . For this a special transversal detector is being developed by ILIMA.
To have a good resolution of measurements several detectors will be installed in the CR.

## Slide 37: Experimental devices
15 Schottky resonators in the ring

## Slide 38: Experimental devices
There is interest in the determination of beta delayed particle emission (like beta-delayed neutrons or two neutron emission)
To measure the life-time of short lived nuclides coming from Super-FRS the two particle detectors will be installed in the ring
The design of the detectors is ongoing within ILIMA collaboration.
To have high resolving power the detectors should be placed at high dispersive place of the CR (in the middle of arcs)

## Slide 39: Experimental devices
2 Pocket detectors
CR02EKD1
CR04EKD1

## Slide 40
Civil construction
For civil construction planning major assumptions have been made.
Detailed requests for the supply room conditions were specified and delivered to the building planers
3D CATIA model of the ring and building is continued and completed
Major collisions have been identified and removed.
Coordination of external companies is ongoing permanently

## Slide 41
CR cable routes (first approach)
Müller & Bleher Firma makes design of the cable routes

## Slide 42
The CR is a special ring that is designed for fast cooling both RIB and antiprotons.
Stochastic cooling is an essential task of the CR
The optical layout of the ring is chosen such to meet the requirements for most efficient stochastic cooling
The flexibility in setting the transition energy γtr to an optimal value is extremely important.
Furthermore: the injection/extraction elements, RF cavities, SC elements must be placed also at appropriate locations
One should remember that one needs to install enough diagnostic instruments, experimental devices to meet their specific requirement.
To realize the CR project the international collaboration is established....
Overview

## Slide 43
CR Project at BINP
  Last year FAIR, GSI and BINP had discussion to transfer the technical supervision of the CR to BINP (Novosibirsk, Russia).
  It is agreed that the major part of the Collector Ring will be constructed at BINP
  MoU signed on a visit in
  Novosibirsk

## Slide 44
Present status of the CR project
  IKRB meeting (01.04.20014) assigns a major part of the CR components (63 %) to the BINP
  FAIR and GSI have signed updated collaboration contract, where the major part of responsibility for CR (which is foreseen for BINP) is returned back to FAIR.
  FAIR Council decision was positive on 9 July 2014.
  Collaboration Contract for technical coordination of Construction of CR between FAIR and BINP was signed in August 2014.

## Slide 45: In-kind for main components
RF cavities (GSI in-kind)
Stochastic cooling system (GSI in-kind)
All Magnets (BINP, Russia in-kind)
Power supply (BINP, Russia in-kind)
Kicker magnets (BINP, Russia in-kind)
Vacuum system (BINP, Russia in-kind)
Diagnostic devices (BINP/ITEP/GSI in-kind)
Experimental set-up (GSI in-kind)
Civil construction and cable planning (FAIR Site&Building)