## Slide 1
Status of the CBM – MVD…
M. Deveaux, GU Frankfurt
for the CBM-MVD collaboration.
…and what it has to do with this picture.

## Slide 2: HIC for FAIR in climatic science
Corall reefs form annual rings.
Distance and density [g/cm³] depends on climax..
Idea:
Take proves from reefs
Reconstruct climax data
Challenge:
Rings hard to see by eye.
Density information needed.
=> Needs calibrated X-ray

## Slide 3: Standard X-ray
Visual
Standard X-ray
Rings easy to see, but
Uses standard X-ray tube => Contineous spectrum.
Uses standard X-ray film => Non-linear and non-trivial response.
Use monochromatic source (e.g. Am-241 => 59.9 keV)
Use single particle counting (e.g. scintillator detector)
Raster scan probe with high resolution
Together with Prof. E. Gischler (Geology GU Frankfurt), supported by DFG
B.E. Chalker, D.J. Barnes,
„Gamme sensitometriy for the measurement of skeletal density“,
Coral Reefs (1990) 9:11-23

## Slide 4: A dedicated X-ray
241Am
Probe
PMT
Scintillator
FAIR – Electronics
Collimator
PADIWA Board
known from
CBM – RICH
PANDA – DIRC

## Slide 5: First results
Linearity
Spatial resolution
„Pixel“: 500x500 µm²

## Slide 6: First results
Visual
Standard X-ray
Density Scan (this work)
Looks promising. More to come, stay tuned.
Note: HIC for FAIR is doing climate science 

## Slide 7: Back to CBM
We are here

## Slide 8: Open charm reconstruction: Concept
Primary Beam: 25 AGeV Au Ions (up to 109/s)
Primary
vertex
Secondary
vertex
Short lived particle
D0 (ct = ~ 120 µm)
Detector 1
Detector2
Target
(Gold)
z
Reconstruction concept for open charm
Central Au + Au collision (25 AGeV)
A good time resolution to distinguish
the individual collisions (few 10 µs)
Very good radiation tolerance
(>1013 neq/cm²)
Reconstructing open charm requires:
Excellent secondary vertex
resolution (~ 50 µm)
=> Excellent spatial resolution (~5 µm)
=> Very low material budget (few 0.1 % X0)
=> Detectors in vacuum

## Slide 9: Performances of MAPS (2003)
 | Required | Hybrid pixels
Single point res. [µm] | ~ 5 | ~ 30
Material budget [ X0 ] | ~ 0.3% | 1%
Time resolution [µs] | few 10 | 0.025
Rad. hardness [n/cm²] | > 1013 | >> 1014
CCD
~ 5
~0.1%*
~100
<< 1010
MIMOSA-5 (2001)
3.5
~0.1%*
~25000
~ 1012
*Sensor only
MAPS provide an unique compromise between:
sensitivity
high rate capability
R&D is needed on radiation tolerance and read-out speed.

## Slide 10: CBM activities: Grilling glue with X-rays
Before grilling.
+
=
After grilling.

## Slide 11: Why grilling glue?
The CBM-MVD
3
2
1
0
MVD
CAD model
Station
Ladder
MAPS
Monolithic Active Pixel Sensor

## Slide 12: Progresses in Sensor R&D
From D. Doering,
PhD – defense, 31.03.2015
Sensor R&D is being continued… almost there. But how to glue them?

## Slide 13: Study on gluing sensors
Glue requirements | Epoxy based | Silicone based
Radiation tolerance | Yes | Limited
Easy to rework | No* | Yes
Low material budget | Yes | No
Strength | Yes | Medium
Low outgassing | Yes | No
Soft at -20 C | No* | Yes
High thermal conductivity | No* | No
Not very convincing.
What to do?
Develop your own glue.
Development at the Rutherford Appleton Laboratory (RAL)
Synergy with the ATLAS expreiment
RAL-247 features:
Glass temperature (Tg) @ -45 C
viscosity of below 100 mPa.s.
curing time 48h @ +50 C and more than a week at 20 C.
Tolerance to radiation ?
Novel glue seems to match CBM-MVD requirements

## Slide 14: PRESTO: PREcurser of the Second sTatiOn
PRESTO:
15 Sensors (MIMOSA26AHR)
  50µm thick
  33 MPixel of 18.4x18.4µm²
150µm thin CVD – diamond support
Novel ultra-thin cables
New DAQ system
Needed / Study:
Sensor commisioning
10 FPCs
Support
Adhesive
R/O electronics
Cooltec®
Heat-sinks

## Slide 15: New cables – Material budget
Chart: 
| 2 x Si | 2 x Glue | CVD diamond | 2 x FPC
Datenreihen1 | 30.6224 | 4.1471 | 35.6198 | 29.6106
Hypothetical Al-based FPC material budget (max) ≈ 0.31-0.35% x/X0
PRESTO material budget:
Maximum ≈ 0,35-0.40% x/X0
Average ≈ 0.25-0.30% x/X0
1st tests: it works !!!
Quality: under investigation
x/X0 [%]
Benchmark for station >0 = 0.5% x/X0

## Slide 16: PRESTO - Integration

## Slide 17: PRESTO - Integration

## Slide 18: PRESTO - Integration

## Slide 19: PRESTO – Precision of Integration
Chart: 
| 0-4 | 5-9 | 10-14 | 15-19 | 20-24 | 25-29 | >29
12 8 4 1 1 2 1 | 12 | 8 | 4 | 1 | 1 | 2 | 1
Measured edge-to-edge distance [µm]
# entries
Keyence microscope
Effective resolution ~1 µm
Misaligned sensors
Alignment precision much better then goal ( ~100 μm)

## Slide 20: PRESTO – Vacuum compatible gluing
Task: Find procedure for vacuum compatible gluing (no bubbles)
Solution (dummy chip on glas):
Keep glue 1 hour in desiccator (remove bubbles)
Use defined amount of glue
5 µl
4 µl
3 µl
Bubble (too few glue)
Perfect results with 5µl/sensor
Procedure for vacuum-compatible gluing of 50 μm thin sensors was established.

## Slide 21: The CBM MVD digitizer
3
2
1
0
MVD
CAD model
Digitizer - Represent:
Response of sensors.
Precise geometry of MVD.
Limitations of internal bandwith.
Misallignment.
Eventually raw data.
Use on green cube one day:
Should be data parallel.
Should be suited for parallel processing.
Adapt to progress in sensor R&D
Flexible implementation needed.
Should be easy to exchange/extend models.

## Slide 22: Where are we parallel?
MVDPlugin
CbmMvdSensor
DataSheet
CbmMvdGeoInformation
TGeo-
Manager
Tasks (Methods like digitizer)
CbmMvdSensor
Buffers (Local data handling)
3
2
1
0
MVD
CAD model
Data parallel:
All data required for computing is kept by CbmMvdSensor
Tasks of Sensor => 1 Sensor – 1 Threat (shared memory needed).
No conflicting RAM-access during processing.
Flexible:
MVD-Detector = Array of CbmMvdSensor.
Plugins may be exchanged - even during run time.
Using multiple sensor models in parallel is straight forward.

## Slide 23: Where is the progress?
Beam
Beam
Old Geometry
New Geometry
Front- and back-side of
station are separated.
Sensor overlap
is represented.

## Slide 24: What did we learn (so far)?
Row (30 bit)
+ Window (30 bit)
0
1
2
3
4
3x454x300 pixels,
pitch 22x33 μm
30 μs integration time
Limitations per FSBB
6 windows per 32 columns
9 windows per 256 columns 18 windows per sline (454 columns)
640 data packets per frame
CDS
A
ADC
SUZE
DATA OUT
Pixel
Column
Pixels
Pixels
Pixels
SUZE-02
Sensor
3 cm
1 cm
0.3 cm
SUZE-02
SUZE-02
FSBB
FSBB
UrQMD
GEANT3
MVD Digitizer
SUZE-2

## Slide 25: What did we learn so far?
Generated data words per frame which produce the bandwidth limit.
Current bandwidth (FSBB) is suited for:
10 MHz p-A (first station at 5 cm)
100kHz A-A (first station at 10 cm)
Neq [1/Ai Ion/cm2

## Slide 26: Background rejection with the MVD
Goal:
Probe fireball with light vector mesons (ρ, ω and ϕ) decaying to e+/e- - pairs.
Challenge:
Need to reduce background.
0 ->  e+ e-
medium -> e+ e-
No MVD
Charge,
Momentum,
ID
RICH
STS
Track fragment
Track segment
Global track
…
Charge, Momentum
Idea:
Use MVD to find second decay partner.
Eliminate identified background pairs.
Chart: 
Gain with MVD [%] | 26.0671 | 40 | 40 | 43.2836 | 46.1538
0-0.15
0.15-0.6
0.6-1.2
ω e+ e-
 e+ e-
GeV/c2
Tracking of low momentum tracks, helps to suppress background (mainly from conversion) as being e.g. well established by HADES collaboration.

## Slide 27: Summary and Conclusion
Wide range of activities towards the CBM-MVD
Precursor of station 2 in 2015
Flexibility to adopt to physics case
The CBM sensors is almost defined, tuning w.r.t. R/O stage, synergy with other experiments, mainly STAR (running!) and ALICE upgrade
TDR expected in 2015
Sometimes, research works
in mysterious ways.