## Slide 1: FRRC - PANDA Meeting, Moscow / ITEP, May 26, 2015 G.Alexeev (for muon group) Muon System Status Report
* Approval of Muon TDR by FAIR Council (22 Sept. 2014) -> open way to
writing the JINR-FAIR contract (available budget ?!)
* Description of Muon System in PANDAroot:
- Barrel, End Cap, Muon Filter –> JINR, Dubna
- Forward Range System –> INFN, Torino
* Test beam activity at CERN:
- Full assembly of Range System Prototype ( wire & strip R/O, analog & digital FEE)
- Design of T9/PS/CERN beam line diagnostics upgrade (time-of-flight, Čerenkov)
- Stand alone PANDA/COMPASS DAQ at CERN
* Preparation for mass production:
- contacts with main producers (MDTs components, FEE ASIC chips, … )
* Plans for 2015:
- Preparation of the JINR-FAIR contract
- Muon System in PANDAroot – install/debug software (autumn 2015)
- Range System Prototype – put in operation (cosmic, beam test depends on PID upgrade)
- Modifications to T9 beam line diagnostic equipment ( TOF - autumn 2015, Čerenkov - ?)
- R&D @ test stand in JINR (high rate effects, new FEE ASIC chips etc.)

## Slide 2: Geant4 Computer Model for the Muon System
* Geometrical description
  Geant4 geometrical description of the most complex Barrel part of Muon System is practically ready; the End Cap, Muon Filter and Forward Range System are in progress
  Description of the Range System Prototype (to be placed on PS T9 beam line) is ready
  * Simulation of signals from the MDTs (digitization)
  Algorithm based on our experience with Range System Prototype (CERN) is being implemented

## Slide 3: Geant4 view of Barrel (a) and its cut at target zone (b)
Steel absober (in white)
Zero bi-layer (in blue)
MDTs inner layers (in blue)
(a)
(b)

## Slide 4: Geant4 view of End Cap and Muon Filter (a) and its vertical cut (b)
MDTs layer (in red)
End Cap
Muon Filter
(a)
(b)
steel ribs
(in white)

## Slide 5
‘chess board’ zero bi-layer
‘standard’ bi-layer
digitization
RSP model and data collected at T9/PS/CERN run 2012 are being used to tune digitization algorithm

## Slide 6: BEAM: e,µ,π,p (3 GeV/c, trigger: S1 (Ø 11,5 cm) & S2 (Ø 3,5 cm)), Range System Prototype data of T9/PS/CERN run 2012
µ
h
µ
h
wire hits (in green)
strip hits (in blue)

## Slide 7: ‘Chess board’ zero bi-layer (fragment)
MDT
tube
wire direction
U-strip, -45 deg.
V-strip, + 45 deg.
Strips are formed from 2 cm x 2cm squares by soldering
Brackets to fix MDTs to strip board

## Slide 8: Test of ‘chess board’ zero bi-layer preamplifier A-32
A-32 board
One of two MDTs layers

## Slide 9: Putting second MDT layer on ‘chess board’ zero bi-layer

## Slide 10: Test of ‘chess board’ zero bi-layer fully screened with aluminum foil (~ 0,1 mm thick)
A-32 preamplifier box

## Slide 11: Test pulse from strips as seen after A-32 and ADB-32 amplification (induced by positive pulse on MDT wire)
ADB-32 card
No oscillation and small noise

## Slide 12: Moving of RSP by crane for putting in vertical position and further assembly with detecting planes and tests with cosmic at CERN
External surface for zero bi-layer fixation

## Slide 13: Fixation of ‘chess board’ zero bi-layer to RSP external surface
A-32 preamp shielding box
ADB-32 card

## Slide 14: RSP equipped with all detectors and big portion of ‘on chamber’ FEE in vertical position (for cosmic tests)
A2DB-32 cards for wire R/O,
2160 channels
Strip R/O side, ADB-32 cards are removed during MDT planes insertion,
2026 channels

## Slide 15: RSP in vertical (cossmic test) position ‘bottom side’ (for RSP position on beam) is pictured
Barrel structure
EC & MF structure
FRS in total

## Slide 16: Fragment of RSP ‘bottom side’ Barrel structure (Fe/30mm + gap/30mm)
Fe
30mm
Gap
30mm
Flexible
material
MDTs & strip board
in aluminum foil

## Slide 17: Assumed upgrades to T9 beam line for π/μ separation < 1-2 GeV/c: S1,S2 time-of-flight scintillator counters based at ~ 16-24 m to each other, pressurized (up to 60 atm) Cherenkov counter C3, magnetic analysis of incoming muon momenta with ~ +/- 1% accuracy
‘old’ position
New S1 position

## Slide 18: T9/PS/CERN beam line after reconstruction of 2013-14
Vacuum beam pipe interruption in T9/PS/CERN for S1 insertion
T10/PS/CERN beam zone

## Slide 19: Čerenkov counter (up to 60 atm), schematic view
photo-sensor, PMT
mirror
high pressure vessel

## Slide 20: Čerenkov counter (up to 60 atm), main dimensions

## Slide 21: T9 Test Beam Diagnostic Equipment (photo-detectors)
PMT XP1020UR (Čerenkov counter)
time resolution σt = 70 ps
3σ TOF µ/π separation for P≤0.9 Gev/c
MCP-PMT XP85112 (TOF counters)
time resolution σt = 36 ps
3σ TOF µ/π separation for P≤1.3 Gev/c

## Slide 22: Test stand for digital R/O cards MWDB at CERN 21 cards (4032 ch) were tested/debugged/repaired
MWDB card (192 ch)

## Slide 23
`
SBC
MUX
(master)
GeSiCA
GeSiCA
3 crates (VME 6U)
MWDB (RJ-45)
port
1÷8
port
1÷8
port
1÷8
8
8
8
RW
(RJ-45)
2
1
1
1
port
1÷8
Ethernet
PC
TRIGGER
(NIM)
DAQ crate (VME 6U)
T0=1ch.
BOS
(NIM)
Stand-alone DAQ Block-diagram
GeSiCA
TCS
EOS
(NIM)
fiber
Spill Buffer
Slink (optical fiber)
Mem 1GBx2
ODIN
rear card
1Gb Switch
(version 5, developed and completed in cooperation with COMPASS DAQ experts)
VP-917/012-16

## Slide 24: Stand-alone DAQ units status
1). VME crate x 3 (received & tested)
VME64 crate; 8U; 21 slots; fan; +5V 115A/230A;
+/-12V 46A
2). 6U VME Single Board Computer VP 917/012-16 x 2 units (received & tested)
2-core 2.5 GHz i7-3555LE; 16GB DRAM; 2PMC/XMC slots;
Ethernet port; 2.5 “HDD SATA-III 500GB;
Splitter cable for VGA/Keyboard/Mouse/COM-Port/USB
3). 6U VME Single Board I/O Register V977 x 2 units (received & tested)
16 channels; NIM or TTL Input/Output signals
4). 6U VME GeSiCA x5 units + MUX x 2 units (Control and Acquisition unit)
readout-driver (received, to be tested with DAQ): 8 front-end serial interfaces (Rj-45); 512 MB internal FIFO memory; S-Link output interface
5). TCS module x 2 units (offer is being paid, to be tested with DAQ units)

## Slide 25: Simplified Schematic of Xilinx FPGA Prototype R/O Module (192ch) (to be tested with Range System Prototype at CERN; if results will be positive, the Artix 7 chip may be regarded as basis for the final PANDA/DAQ)
Artix 7
XC7A200T-2FBG676I
MAX9173
X 48
JTAG
N25Q256A
Config. Mem.
(6)
LVTTL
DAC
AD8842
Analog Electronics, ADB-32
HCPL-2400
DS92LV222
TRIGGER
DS90C032
CLK
SETUP
CY7B923
DATA
COMPASS DAQ
(192ch)
LVDS
Thresh
Conservative part, to be kept to final PANDA DAQ
Part to be replaced with respect to final PANDA DAQ

## Slide 26: Contacts with industry
* MDTs components:
- ALU profile -> Agrisovgaz (www.agrisovgaz.ru), reliable partner,
Kaluga Region, Russia
- End plugs (active & passive) -> Mars, reliable partner, Erevan,
Armenia
- Plastic envelope (Noryl) -> in search for partner, two companies
study the technology to extrude Noryl
plastic (Mars, Erevan and EPPI limited,
Moscow
* Front End Electronics:
- ASIC chips -> Integral, reliable partner, Minsk, Belorussia
- Assembly of cards -> Marathon, reliable partner, Moscow,
Russia
* Mechanical structures: pending clarity with magnet

## Slide 27: Final variant of detector plane shielding developed at Dubna test stand – was implemented in Range System Prototype at CERN
Preamplifier shielding box
ADB-32 cards
HV/S-8 cover (GND bus)
Shielding free edges
All results of shielding tests were applied to this final detector plane version
Preamplifier shielding box consists of several Al plates which provide:
shielding of A-32 cards (from detector and each other),
shielding of input strip-to-preamp-wires
preamplifier GND connections
Fully equipped detector plane was tested for a month – no performance changes were observed

## Slide 28: MDT counting characteristics after irradiation by 1.5 and 3.1 Coulomb / cm2 NO AGEING !
Collected charge is increased by factor 3 compared to ‘threshold value’ in 1 C/cm presented for ECE referees last year

## Slide 29
High rate performance (wires & strips) studied at Dubna test stand

## Slide 30: Backup slides

## Slide 31
MDTs layer
Zero bi-layer

## Slide 32: RSP in vertical position (for cosmic test)
A2DB-32 cards for wire R/O

## Slide 33
DAQ Status Summary
1). The final version of the stand-alone DAQ is ready
2). Hardware for DAQ was mostly received, last unit is expected in summer 2015
3). The development of the DAQ software/firmware is currently in progress
at CERN, ready/tested code is expected in autumn 2015

## Slide 34: Table of conditions for written events; T9/PS/CERN run 2012
P[Gev/c] | Trigger | Composition | N of events | file # , Comments
Spectrum | S3*S4 | cosmic | 635 | f39, S3 & S4 on RSP top
Spectrum | S3*S4 | cosmic | 8375 | f41,S3 on top & S4 on bottom
0.5 | S1*S2 | - (e,μ,π) | 6575 | f85, strips on
0.5 | S1*S2 | + (e,μ,π,p) | 27374 | f83, strips on
1 | S1*S2 | + (e,μ,π,p) | 3087 | f65
1 | S1*S2*vetoC1 | + (μ,π,p) | 90 000 | f68
2 | S1*S2 | + (e,μ,π,p) | 3161 | f80, strips on
2 | S1*S2+Pb | + (μ,π,p) | 1087 | f81, 2.5 cm Pb brick in beam, strips on
3 | S1*S2 | + (e,μ,π,p) | 11766 | f77
3 | S1*S2*C2 | + (e,μ) | 3283 | f78
3 | S1*S2*C2+Pb | + (μ) | 299 | f79, 2.5 cm Pb brick in beam, strips on
5 | S1*S2 | + (e,μ,π,p) | 9702 | f56
5 | S1*S2*C1*C2 | + (e) | 2181 | f57
5 | S1*S2*C1*C2 | + (e,μ) | 1217 | f58
5 | S1*S2*C1*C2 | + (e,μ) | 200 000 | f59
5 | S1*S2 | + (e,μ,π,p) | 6407 | f69, strips on
5 | S1*S2*C2 | + (e,μ) | 3201 | f70, strips on
5 | S1*S2*C2 | + (e,μ) | 13266 | f71, strips on
7 | S1*S2 | + (e,μ,π,p) | 11940 | f75, strips on
7 | S1*S2*C2 | + (e,μ) | 3492 | f76, strips on
10 | S1*S2 | + (e,μ,π,p) | 9899 | f72, strips on
10 | S1*S2*C2 | + (e,μ) | 1213 | f73, strips on
10 | S3*S4 | + (e,μ,π,p) | 7405 | f74, beam + halo, strips on