## Slide 1
Update of MVD services and requests
DCDC circuits
Optoelectronic (GBTx + VTRX) boards
Cooling plant
Services on platform in front of the magnet
Daniela Calvo
MVD group

## Slide 2
MVD services - DCDC circuits

## Slide 3
MVD service - DCDC circuits
24 blocks arranged in 3 sectors
(2112 DCDC circuits)
4 PCBs (left and right difference)
housing 22 DCDC circuits each

## Slide 4
MVD services – first prototype
88 DCDC circuits (22 DCDC circuits each row)
Weight (without cables): ~ 1.3 Kg
Dimension (without cables):
455 mm (with cooling connectors) x 85 mm x 63 mm

## Slide 5
MVD services - Request
ONLY HALF of the needed CROSS SECTION is AVAILABLE for cables
IT IS NECESSARY MORE SPACE around the beam pipe for the MVD
Available cross section: 56000 mm2
(between beam pipe and inner BEMC diameter)
Cooling pipes and supports: 9000 mm2
(dashed ring – challenge solution!)
DCDC circuits leave only ~ half of cross section for cables (needed cross section: 22300 mm2) and they will fill the empty parts between the circuits anyway.
(not reccommended!)

## Slide 6
MVD services – Optoelectronic boards

## Slide 7
Optoelectronics board, old version
76 mm
60 mm
12 bars with 16 GBT boards each
(192 circuits)
Interspace between PCBs: 20 mm

## Slide 8
Optoelectronic board, new version – GBTx + VTRX
GBTx and VTRX on opposite sides, then 4.8 Gbit/s signals routed using vias
Two power supply connectors to fit the routing of the power supply cables, in fact two mounting configuration of the boards are foreseen.
Additional chip to distribute the SC out signal to the two connectors towards the FEE.
The cooling of the GBTx in this configuration should be easier (to be verified!).
The board dimension is larger than the estimated values ( 3 years ago) anyway.
86 mm
25.4 mm
15.5 mm

## Slide 9
Interference between optical fiber connectors and signal cables !!
Opto. board, new version – board routing
16,5 mm
Signal cable
Thermal bridge (copper)
20 mm

## Slide 10
Opto. board, new version – board number
Each connector includes : 5 e-links + SC signal
22 additional boards
  to maintain the symmetry left– right during the routing of the semi disks and semi cylinders of the barrel part
  to be able to send the SC signal to each pixel or strip module without connection between different modules
86 mm
25.4 mm
It is necessary to increase the GBT board number from 192 to 214.
It means 2 additional optoelectronic boards each bar, one each side

## Slide 11
Requests
Interdistance:
15 mm longer
Additional 80 mm to arrange the 192 longer optoelectronics boards
Additional 86 mm to arrange an additional board along the rod
Additional 120 mm to avoid interference between optical fibers and signal cables
Possible solution ?: to shift upstream the beam pipe flange
A DCDC block (or partial block) has to be cut out, anyway!
IT IS NECESSARY MORE SPACE around the beam pipe for the MVD

## Slide 12
MVD services – Cooling plant

## Slide 13
Cooling plant ouside the pit
PLC
INLET RACKS (PIXEL, STRIP, SERVICES)

## Slide 14
Cooling plant inside the pit
RETURN RACKS (PIXEL, STRIP, SERVICES)
INLET PUMP + WATER CLEANING UTIT
TANK+ VACUUM PUMP

## Slide 15
Cooling plant - line paths inside PANDA Hall
RETURN LINES
INLET LINES

## Slide 16
MVD services in front of the magnet

## Slide 17
Racks - request
MVD
MVD
Use the racks starting from the top (222 U – 50% left and 50% right).
The reduction to 188 U is still under investigation.

## Slide 18
Patch panels for cables - request
Patch panels
for MVD cables
Patch panels for MVD cables positioned close the BEMC support (left and right) with duct to route cables from racks.
A specific system could move and rotate the duct for positioning the patch panels at the external side of the racks, during the installation of detectors.
The system could be positioned on the top of the racks

## Slide 19
Routing of the cooling pipes and patch panel - request
The duct for the cooling pipes to the patch panels needs to be positioned under the platform floor
It should be a solution to foresee also the patch panel (for the cooling part) under the platform during the detectors installation. A system could move and rotate the patch panel to the final position, near the BEMC support. But it is necessary to go trough the platform floor.
platform
platform
Vertical section
Patch panel
Duct - cooling pipes