## Slide 1: FAIR magnets fiducialisation WP 7.5
Dominique Missiaen

## Slide 2: Agenda
Introduction to Fiducialisation
Status

## Slide 3: Fiducialisation
In order to align a magnet in a tunnel, some external references called «fiducials»
  Have to be measured w.r.t a reference axis
    Magnetic axis for the 33 cold multiplets
    Magnetic axis/yoke for the 24 warm dipoles
  The magnetic axis and roll angle is measured by the Magnet group and transfered on some «references»

## Slide 4: Fiducialisation set up

## Slide 5: Fiducialisation Layout
Courtesy Antoine Kosmicki

## Slide 6
Courtesy Antoine Kosmicki

## Slide 7: Fiducialisation
 | Number offiducials | Requested number (GSI) | CERN | Requested accuracy (mm at 1s) | CERN Accuracy (mm at 1 s) | Roll angle (mrad)
Long Multiplets | 12 | 4 (not on the same side) | As much as possible | 0.2 | 0.08 | 
Small multiplets | 8 | 4 (not on the same side) | As much as possible | 0.2 | 0.08 | 
dipoles |  |  | As much as possible | 0.5 | 0.08 | 0.5

## Slide 8: Requirements
  4 positions per bench on a stable floor
  At least 6 network points per bench on a stable floor
  The supporting has to be realised exactly the same way for the fiducialisation as for the tunnel !!
    Supporting system is done by GSI ?

## Slide 9: Co-ordinates system
Mean plane
Beam trajectory
Optics Entry point
Optics Exit point
Y
X
Z
Fid1 (x1,y1,z1)
  Y axis is the magnetic axis
  XY plane given by the roll angle

## Slide 10: Questions
  Do you prefer the origin to be the magnetic center ?
  longitudinal reference is measured on the cryostat ?
Mean plane
Beam trajectory
Optics Entry point
Optics Exit point
Y
X
Z
Fid1 (x1,y1,z1)

## Slide 11: Status of the Wp
  Acquisition of an instrument
    AT402
    Reception At CERN 2 days ago
      Together with a BProbe

## Slide 12: Fiducials
  CCR1.5
  Diameter ?
  Offset ?
  Magnetic or not ?

## Slide 13: Status of the WP
  Infrastructure
      Most of Network points available from LHC cryo-magnets fiducialisation
  Software
    Automatisation of the measurement/data processing could be done using «Measurement Plan» from Spatial Analyzer

## Slide 14
Thank you for your attention
Questions ?