## Slide 1: UPDAte on C-RORC FOR PANDA
Common Read-Out Receiver Card

## Slide 2: Introduction
Less optical cables
Higher bandwidth to storage
Possible processing on GPU
Used by ALICE DAQ & HLT

## Slide 3: C-RORC Board
Performance
  Xilinx Virtex-6 FPGA
  12 optical links
  Gen2 x8 PCI Express
  2 DDR3 SO-DIMMs
  Total Bandwidth up to 4000MB/s

## Slide 4: Possible Read-Out Chain
CN
CN
CN
CN
CN
CN
CN
CN
CN
CN
CN
CN
CRORC
3x Quad SFP
PC
PCIe
ComputeNodes borrowed
From Belle II
FEE
DC
Maybe instead of CN?

## Slide 5: Development Status
Drivers installed and self test passed
  Core and drivers provided by H. Engel
Implemented to existing core:
  Pattern generator
  Output send via PCIe to HDD
    Reached up to 400 MB/s on one channel limited by SSD write speed

## Slide 6: Outlook
Implementation of usability of SFP lanes
  Adapting clocks, Line Rate,
Possible protocol between CNs and CRORC:
  Aurora
  Same like Data Concentrators (push forward)
Connection test
Beam test in Mainz 10.-14. December