## Slide 1: X-RAY SPECTROSCOPY EXPERIMENTS AT EBIS FACILLITY IN KIELCE
Ł. Jabłońskia, D. Banaśa, J. Braziewicza, J. Czuba, P. Jagodzińskib, A. Kubala-Kukuśa, U. Majewskaa, D. Sobotaa, I. Stabrawaa, J. Szlachetkoa and M. Pajeka
aInstitute of Physics, Jan Kochanowski University, Kielce, Poland
bDepartment of Mathematics and Physics, Kielce University of Technology, Kielce, Poland

## Slide 2: Kielce EBIS facility (Dreebit)
Dresden EBIT ion source
beam guiding components (Einzel lens, deflectors)
beam diagnostics (Faraday cups)
Charge state separation (double focusing analyzing magnet)
multipurpose target chamber
UHV system (10-10 mbar)
DC and pulsed beams (10ns to 100 s per pulse)
Typical ions energy 1 - 20 keV x q
Experimental chamber (+XPS system)
dipole magnet
HV supplies & controls
EBIT source

## Slide 3: charge states distribution
Measurement of Xeq+ and Arq+ beams charge states for different confinement times in the EBIS-A ion source.
Xeq+ (q = 10 - 44) and Ar + (q = up to 18) ion beams
DC mode:
Xe44+: ~ 4104 ions/s
AC mode:
Xe44+ : ~ 7105 ions/s

## Slide 4: X-ray spectroscopy
Experimentsts in the EBIT:
Experiments in the chamber:
Measurements of X-rays emitted in various atomic processes (electron excitation/ deexcitation, radiative recombination, X-ray fluorescence) in the EBIT plasma
Measurements of X-rays emitted in interaction of highly charged ions with surfaces (formation of „hollow atoms”)

## Slide 5: X-ray spectrometers
X-ray INCAWave (Oxford Instruments)
X-ray XFlash (Bruker GmbH)
X-ray/ EUV energy range: 70 eV–15 keV
6-crystals diffraction spectrometer
Resolution = 1-20 eV
UHV compatibile via differential pumping
Silicon Drift Detector (30 mm2 active area)
Energy resolution - 127 eV (Mn K)
Be window - 12.5 μm

## Slide 6: INCA Wave X-ray spectrometer
Declared resolution confirmed!
The INCAWave X-ray spectrometer will be used in the "out-of-focus" geometry, which needs additional investigations to determine its energy resolution and acceptance of lateral extensions of x-ray source.

## Slide 7: XFlash SDD X-ray detector
The detector energy resolution –
down to ~60 eV
Thin beryllium window (12.5 μm) gives the opportunity to measure X-rays in low energy region (above 600 eV)

## Slide 8: EBIT ion source: X-ray spectrum of Xeq+ ions
X-rays emitted in EBIT carry information about various atomic processes such as:
Radiative recombination
X-ray fluorescence
Direct excitation/deexcitation to L-shell
Deexcitation to M-shell
Notes: The low-resolution x-ray measurements deliver information important for understanding the dynamics and equilibration of the atomic processes occurring in the EBIT plasmas.
In turn, the high resolution studies of EUV/x-ray from the EBITs yield precise characteristics of a structure of few-electron ions and thus are important for testing the atomic structure calculations, in particular, using the relativistic multiconfiguration Dirac-Fock (MCDF) approach including QED corrections.

## Slide 9: EBIT ion source: X-ray spectrum of Xeq+
Radiative recombination to L-shell wasn’t observed (no holes in the L-shell)

## Slide 10: EBIT ion source: X-ray spectrum of Xeq+
Transitions to L-shell was observed (indication of direct electron impact excitation process)

## Slide 11: EBIT ion source: X-ray spectrum of Xeq+
Transitions to M-shell was observed (deexcitation to the holes in M-shell or direct electron impact excitation/deexcitation)

## Slide 12: X-rays emitted in interaction of HCI with surface
X-rays emitted in interaction of Xeq+ ions with beryllium foil
Kinetic energy of ions: ~3 keV×q
Ion charge states: Xe26+, Xe27+, Xe35+, Xe40+
X-ray measured by SDD XFlash detector

## Slide 13: X-rays emitted in interaction of HCI with surface
Measurements of xenon M-X-rays emitted from the interaction of Xeq+ ions with Be foil.

## Slide 14: Interaction of HCI with surface
Auger Cascade
Resonat capture
Solid
Ion
X-rays
J. Burgdörfer, F. Meyer 1993 Phys. Scripta T46 225

## Slide 15: Xe35+ electron configuration
4p
4f
4d
4s
3d
3p
3s
N
M
Hypersatellite
Satellite
B. Rudek et al. 2012 Nature Photonics 6 858

## Slide 16: X-ray spectrum of Xe35+
Transitions from high Rydberg states up to n=20 (consistent with COB model)
Relative intensity of hypersatellites:
Ih~1/(m-1)α
m=2÷10 α=0÷1.1
experimental broadering and broadering caused by satellite structure

## Slide 17: Satellite structure of M-X-rays
Relative intensity of satellites:
Is~1/(n-1)
n=1÷14

## Slide 18: Relative population of electrons in high n-states
I~Nk
Increase of relative population of electrons in high n-states („hollow atoms”)

## Slide 19: Summary
X-rays emitted from EBIT ion source carry information about atomic processes which occur in the cold, magnetized plasma
Analysis of M-X-ray spectra from interaction of higly charged ions with surface indicate formation of „hollow atoms”
Satellite and hypersatellite structure should be taken into acount to corectly interpret the spectra in both experiments
More complex MCDF calculation of electron binding energies are needed

## Slide 20
Thank you for your attention!

## Slide 21: XPS system: multiprobe surface analysis
PHOIBOS 100 electron/ion energy analyser with 1D-DLD
X-ray source (Al/Ag) with quartz monochromator (160 meV)
X-ray source (Mg/Cr)
Ultraviolet source (HeI, HeII)
Scanning e-beam (4 μm)
Scanning ion-beam (100 μm)
Flood e-gun
Cleaning/sputtering ion source
Electron beam evaporator
5-axis VT (100-1000 K) sample manipulator
XPS/UPS, SEM/SAM, AES, ISS, GEXRF (planned)

## Slide 22: Internal dielectronic excitation?