## Slide 1: Introduction to Accelerator Physics
D. Ondreka, GSI
Operator Training 2016

## Slide 2: Outline
Introduction
Particles and units
Relativity
Charged particles in fields
Magnets
Charged particle dynamics
Emittance and acceptance

## Slide 3: Experimenters wishes
What are these fancy symbols here about: p, Au, N, Ni ?
What do these funny numbers mean: 3.6MeV/u, 300-1000MeV/u, 1e8/spill ?
What do our accelerators have to do with all this?

## Slide 4: Elements and Isotopes
Elements
  atomic building blocks of matter
  characterized by atomic number Z
    number of protons in nucleus and electrons in neutral atom
    one-to-one correspondence to chemical symbol X
Isotopes
  variants of the same element with different number N of neutrons
  identified by mass number A = Z + N
  same electron configuration, hence same chemical properties
  only few isotopes stable
Notation
AX
 | Z | A | N | Abundance
40Ca | 20 | 40 | 20 | 96.9%
48Ca | 20 | 48 | 28 | 0.2%
neutron-rich nucleus, often used for SHE experiments

## Slide 5: Elements
Ordering of elements according to atomic number Z and electron configuration
(Source: http://www.pctheory.uni-ulm.de/didactics/quantenchemie/html/PSE-F.html)

## Slide 6: Isotopes
Ordering of elements according to proton number Z and neutron number N
Source: http://moriond.in2p3.fr/radio/moriond-huyse.ppt

## Slide 7: Ions
Acceleration requires charged particles (we’ll come to that...)
Ions
  created by removing electrons from atoms (or molecules)
  characterized by their charge state Q
  notation for ions of atoms (i.e. isotopes)
  notation for molecules similar
    examples: H2+, H3+, CH3+
  creation of ions from neutral particles in ion sources
  increasing of charge state by stripping in gas or foils
AXQ
 | Z | Q | #electrons
48Ca | 20 | 0 | 20
48Ca10+ | 20 | 10 | 10

## Slide 8: Ion Masses
Acceleration of ions depends on mass of ion
  Need to know the masses of ions
SI units impractical:
  mp ≈ mn ≈ 1.7·10-27 kg
Atomic mass units (AMU)
  definition of atomic mass unit:
  for general isotopes we define a mass number M:
  small difference between A and M:
    mass excess ME:
    missing electrons for ions:
    significant for high precision exp. (e.g. mass measurements in storage rings)
 | SI units | AMU | ME
u | 1.661·10-27 kg | 1u | 0
mp | 1.672·10-27 kg | 1.007u | 0.007
mn | 1.675·10-27 kg | 1.009u | 0.009
m(12C) | 1.993·10-26 kg | 12u | 0
m(48Ca) | 7.965·10-26 kg | 47.953u | -0.047
me | 9.109·10-31 kg | 5.5·10-4u | n.d.
m(12C) = 12u = A·u
m(AX) = M·u ≈ A·u
m(AXQ) = (M - Q·Ae)·u
ME/M < 0,1% (except e.g. p, d)
M = A + ME
Z·Ae /M < 0,05%
but this is the origin of nuclear power...

## Slide 9: Ion Energies
Experimentalists require ions with a certain kinetic energy
  usually specified as kinetic energy per atomic mass unit
  example: 238U73+, E=1GeV/u, Nions=109 particles
  what’s this mysterious ‘GeV’?
    elementary charge:
    when pushed by a voltage of 1V, a particle with charge e gains energy 1eV
    in SI units:
    prefixes for saving digits: 1000eV=1keV, 1000keV=1MeV, 1000MeV=1GeV
  what’s the kinetic energy of the beam in the example?
    A = 238, ME = 0.05u, Q = 73  M = 238.01, m = M·u
    Eion = M·u·E = 238.01GeV
    Ebeam = Nions· Eion = 109·238.01GeV = 238.01·1018eV ≈ 40J
      kinetic energy of a walking man: E = 1/2·m·v2 = 1/2·80kg·1(m/s)2 = 40J
      if deposited in 1ml of water: heating by 10 degrees, dose 40000Gy
e = 1.602·10-19C
      charge of proton and electron (up to sign)
1eV = 1.602·10-19J

## Slide 10: Relativity: Mass and Energy
Mass and energy are equivalent
What’s the energy of a mass unit?
  speed of light (constant of nature):
  energy of 1u:
    u·c2 ≈ 1.661·10-27kg·(2.998·108m/s)2 ≈ 1.4925·10-8J
    1eV ≈ 1.602·10-19J
    u·c2 ≈ 931.6·106eV
    precise value:
Expression of masses as energies in convenient units
  consider 238U73+: m·c2 = M·u·c2 = 238.01·u·c2 = 221.7GeV
  also written as: m = 221.7GeV/c2
E = mc2
c = 299792458 m/s
u·c2 = 931.494 MeV

## Slide 11: Relativity: Energy
Energy equivalent to mass is referred to as rest energy
  will use symbol E0 from now on:
  use special symbol Eu for amu:
Kinetic energy of ion always proportional to mass
  write kinetic energy as:
  E is referred to as kinetic energy per nucleon (or per atomic mass unit)
Total energy is the sum of rest and kinetic energy
  again proportional to mass:
Comparison of total energy to rest energy
  defines the relativistic gamma:
  examples:
    injection into SIS18: E = 11.4MeV/u  γ = 1 + 11.4/931.5 = 1.01
    extraction from SIS18: E = 1GeV/u  γ = 1 + 1000/931.5 = 2.07
E0 = mc2 = M·uc2
Eion = M·E
Eu = uc2
γ = Etot/Eu = 1 + E/Eu
M·Etot = M·(E + Eu)

## Slide 12: Relativity: Velocity
Velocity expressed in units of the speed of light
  defines relativistic beta:
Gamma and beta are related
  Lorentz factor:
  can be inverted:
Velocity bound by speed of light
  Look again at γ = 1 + E/Eu
    E=0  γ = 1  β = 0
    E ->∞  γ ->∞  β -> 1
    range of beta:
  Ions never reach the speed of light
    but they can come quite close: (e.g. p@LHC: E=7TeV, γ≈7500, 1-β≈10-8)
v = β·c
γ = 1/√(1 - β2)
β = √(1 - 1/γ2)
0 ≤ β < 1

## Slide 13: Relativity: Momentum
Momentum is an important kinematical quantity
  conserved if no forces act on the particle
  deflection in a magnet is proportional to momentum (we’ll come to that...)
Related to the other relativistic parameters
  proportional to mass:
  non-linear relation to velocity:
  non-linear relation to energy:
  example: E = 1GeV  pc = 1692GeV or p = 1692GeV/c
pion = M·p
pc = γ·β·Eu = β/√(1 - β2)·Eu
pc = √(E·(E + 2·Eu))
here we’ve omitted the /u for convenience...

## Slide 14: Relativity: Non-Relativistic Limit
Newton’s physics recovered for small energies
  Newton’s relations for momentum:
  check of velocity relation:
    let β -> 0  pc = β/√(1 - β2)·Eu -> β·Eu = c·u·βc = c·u·v
  check of energy relation:
    let E -> 0  pc = √(E·(E + 2·Eu)) ->√(2·Eu·E) = c√(2·u·E)
How far does Newton’s arm reach?
  depends on required precision
    consider relation between momentum and velocity
    define deviation from Newton’s relation by:
    below this β, deviation from linearity smaller than ε
p = √(2·u·E)
p = u·v
ε | γ | β | E
0.1 | 1.11111 | 0.436 | 103MeV/u
0.01 | 1.01010 | 0.141 | 9.4MeV/u
0.001 | 1.00100 | 0.045 | 932keV/u
0.0001 | 1.00010 | 0.014 | 93.2keV/u
0.00001 | 1.00001 | 0.004 | 9.32keV/u
β/(βγ) = 1 - ε with 0 < ε < 1
last line still corresponds to 1300km/s = 1.3m/μs!

## Slide 15: How Relativistic are GSI and FAIR?
UNILAC (β < 0.15) and CRYRING (β < 0.25) close to non-relativistic
SIS18 and SIS100 practically always relativistic
SIS100 for protons at extraction pretty relativistic (γ ≈ 30)
For comparison: LHC @ 7 TeV  γ ≈ 7500 (now this is ultra-relativistic...)
CRYRING

## Slide 16: Lorentz Force and Magnetic Rigidity
Lorentz force on charged particles in electromagnetic fields
  general equation involving 3D vector quantities (F, E, v, B, p)
  electric field E will accelerate particle if aligned with v
  force by magnetic field B always perpendicular to v -> no acceleration
  change of momentum per nucleon proportional to Q/M
Particle in homogenous magnetic field B
  energy remains constant
  trajectory is circle with radius ρ satisfying:
  fundamental relation for accelerator physics
  quantity Bρ denoted magnetic rigidity
  the larger Bρ, the harder it is to deflect the particle by a magnetic field
  for fixed p rigidity determined by mass-to-charge ratio M/Q
F = Q·e ( E + v x B) = M·dp/dt
B·ρ = M/Q·p

## Slide 17: Manetic Rigidity: Examples
Ions |  | SIS18 Inj. | SIS18 Ext. | SIS100 Ext.
 |  | E=11.4MeV/u | E=1GeV/u | E=1.5GeV/u
Ion | M/Q | Bρ [Tm] | Bρ [Tm] | Bρ [Tm]
40Ar18+ | 2.22 | 1.08 | 12.5 | 16.6
40Ar10+ | 4.00 | 1.95 | n.a. | 30.0
86Kr33+ | 2.61 | 1.27 | 14.7 | 19.5
86Kr16+ | 5.38 | 2.62 | n.a. | 40.3
238U73+ | 3.26 | 1.59 | 18.4 | 24.4
238U28+ | 8.50 | 4.14 | n.a. | 63.7
Protons | SIS18 Inj. (UNILAC) | SIS18 Inj. (p-Linac) | SIS18 Ext. | SIS100 Ext.
 | E=11.4MeV/u | E=70.0MeV/u | E=4GeV/u | E=29GeV/u
M/Q | Bρ [Tm] | Bρ [Tm] | Bρ [Tm] | Bρ [Tm]
1.007 | 0.49 | 1.26 | 16.3 | 100

## Slide 18: Deflection in Dipoles
Dipole with a uniform field deflects a charged particle by an angle θ
θ depends on arc length L and magnetic field B
L depends on θ and radius ρ
Particle with magnetic rigidity Bρ
Quantity B·L is referred to as integral magnetic field
Deflection angle given by
Macroscopic angles to bend transfer lines or create circular accelerators  bending magnets
Microscopic angles to correct beam trajectory or closed orbit  steering magnets
θ
L
ρ
L = θ·ρ
B·L = θ·Bρ
θ = B·L/Bρ

## Slide 19: Dipoles as Separators
Consider particles with fixed p but different M and Q in a dipole field B
  assume B·L same for all M, Q
  deflection angle given by
Charge separation
  assume same M, but different Q
  let only one angle θ pass and vary B, then Q proportional to 1/B
Mass separation
  assume same Q, but different M
  let only one angle θ pass and vary B, then M proportional to B
θ = Q/M · B·L/p
Some separator magnets are rather large...
...and one can build separators with more dipoles.

## Slide 20: Example: Spectrometer
Charge separation behind gas stripper
Mass (isotope) separation

## Slide 21: Dipole Magnets
Homogeneous field desired
At GSI and FAIR electromagnets with and iron core are used
B field created in gap g between two parallel iron poles N and S
B field excited by current in coil with N windings
B field can be calculated
Choice of coils
  Normal conducting (water cooled)
    e.g. SIS18, ESR, FRS
  Super-conducting (liquid He cooled)
    e.g. SIS100, Super-FRS
H core dipole
C core dipole
Window frame dipole
B = μ0·N·I/g
μ0 = 4π·10-7Tm/A (constant of nature)
e.g. ESR, CRYRING
e.g. SIS18, SIS100
N
S
N
S
g
B
N
S

## Slide 22: Bending Magnets @ GSI and FAIR
Machine | Type | N | θ [deg] | ρ [m] | L [m] | Bmax [T] | BLmax [Tm] | Bρmax [Tm]
SIS18 | H | 24 | 15 | 10.4 | 2.7 | 1.8 | 4.9 | 18.7
ESR | C | 6 | 60 | 6.25 | 6.5 | 1.6 | 10.5 | 10.0
CRYRING | C | 12 | 30 | 1.20 | 0.63 | 1.2 | 0.75 | 1.44
SIS100 | H | 108 | 3.33 | 52.6 | 3.1 | 1.9 | 5.8 | 100.0
CR | H | 24 | 15 | 8.13 | 2.1 | 1.6 | 3.4 | 13.0
HESR | H | 44 | 8.18 | 29.4 | 4.2 | 1.7 | 7.1 | 50.0
And a large variety of bending magnets in the transfer lines and at the experiments...

## Slide 23: Particle Motion in Dipole Magnets
Can we build circular accelerators from dipoles only?
Start two particles in same field
  same momentum, same position
  different angle
Use particle A’s trajectory as reference and measure deviation of B’s trajectory along the circle
  particle B oscillates around particle A
  such oscillations characterize transverse motion in accelerators
  referred to as betatron oscillations
  more about that later... (see talk on ‘Transverse Dynamics’)
2π
0
deviation
Particle B
Particle A

## Slide 24: Stable or Unstable Motion
In the previous example, horizontal trajectories close on themselves
  could be repeated infinitely
  motion considered to be stable
  focusing effect of the dipole field
What about the vertical motion?
  particle A at zero position and angle
  particle B with same position but small angle at start
  the dipole field has no influence on the vertical motion of both particles
  position of particle B grows without bounds over many turns
  motion considered to be unstable
Need focusing in the vertical direction
Horizontal relative motion
2π
0
horizontal dev.
4π
Vertical relative motion
2π
0
vertical dev.
4π

## Slide 25: Quadrupole Magnets
Quadrupole magnet has 4 poles symmetric about the center
By symmetry the B field on the longitudinal axis is zero
  particle passes straight through the center with no deflection
  quadrupole magnet is straight
B field depends linearly on position
  horizontal direction:
  vertical direction:
  B’ referred to as field gradient
Integral quadrupole strength
  focusing power for particles with Bρ
  analogous to angle of a dipole
Hyperbolic contour
x · y = constant
Magnetic field
By = B’·x
Bx = -B’·y
k·L = B’·L/Bρ

## Slide 26: Effect of Quadrupole Magnets
Forces on particles determined by arrangement of poles
  arrangement
    focusing in horizontal plane
    defocusing in vertical plane
    denoted focusing quadrupole (QF)
  arrangement
    defocusing in horizontal plane
    focusing in vertical plane
    denoted defocusing quadrupole (QD)
Forces linear in transverse position
  particles receive deflection proportional to their position
  similar to lenses in optics except that lenses (de)focus in both planes
N | S
S | N
Force on particles
S | N
N | S
Focusing quadrupole (QF)
x
s
QF
y
s
QF

## Slide 27: Focusing with Quadrupole Magnets
Neither QF nor QD can focus in both x and y simultaneously, but...
Combinations of QF and QD with overall focusing in x and y possible
Idea:
  put QD in place where horizontal offsets are small
  put QF in place where vertical offsets are small
  then effect of QD on x respectively QF on y should be small
Different arrangements possible
  FODO: smallest field gradients
  Doublet: long free section
  Triplet: symmetric beams
x
QD
QF
QD
y
QD
QF
QD
FODO
Doublet
Triplet

## Slide 28: Transverse Phase Space
Consider again focusing by QF in the horizontal plane
  parallel input trajectories  particles characterized by position x
  at focal point, all particles have x = 0  particles characterized by angle x’
In general, position x and angle x’ needed to fully describe particle
  aggregated into vector
  can be depicted in 2D coordinate system called phase space
  convergent trajectories have negative x’ for positive x and vice versa
  opposite sign for divergent trajectories
Vertical plane completely analoguos
x
s
x
x’
focal point
QF

## Slide 29: Quadrupole Effect Quantitatively
Consider thin quadrupole at s = 0
Input vector (just in front of quad)
Output vector (just behind quad)
  same position x1 (thin quad)
  angle of trajectory: -x1/f (x1<< f)
Vector downstream of quad at s
  angle fixed in drift space
  position change linear in s
x
s
f

## Slide 30: Matrix Formalism
Matrices and vectors
  mathematical structures with a very powerful calculus (linear algebra)
  easily implemented in computer programs
  very convenient for representing particle transport through accelerators with linear forces
  takes some time getting used to it...
Multiplication rules for matrices and vectors
Matrix · Vector = Vector
Matrix · Matrix = Matrix
Multiplication not commutative...
..but associative

## Slide 31: Quadrupoles and Drifts as Matrices
Effect of thin quadrupole with focal length f described by matrix
  first row: position x is unchanged and does not depend on angle x’
  second row: quad changes angle x’ by amount proportional to position x
Effect of drift space of length L
  first row: position x changes by amount proportional to angle x’
  second row: angle unchanged
Can be visualized in phase space
x
x’
x
x’

## Slide 32: FODO Focusing
Alternating focusing and defocusing quadrupoles separated by drift spaces
FODO cell can be repeated many times (periodic FODO channel)
Dipole magnets installed between quadrupoles for curved accelerators
  approximately like drift spaces
Efficient focusing structure regarding necessary fields for given aperture
Periodic solution exists
  output beam same as input beam
  ellipses in phase space
  other beam shapes may lead to troubles (mismatch)
QF
QD
QF
L
L
FODO cell
Matrix formalism allows to split quads easily...
Just for the curious and brave...
Matrix of FODO cell

## Slide 33: FODO Tracking: Trajectories
Trajectories in horizontal plane
QF
QD
QF
L
L
Trajectories in vertical plane
Particle tracks obtained by tracking random sample of particles
General properties of FODO structure visible, but where are the limits?
Tracks obtained by tracking 20 particles

## Slide 34: FODO Tracking: Envelopes
Shape of beam emerges when tracking lots of particles
Envelope can actually be calculated from L and f ( talk on transverse optics)
QF
QD
QF
L
L
Envelopes in horizontal plane
Envelopes in vertical plane
Tracks obtained by tracking 2000 particles

## Slide 35: FODO Focusing: Mechanical Analogue
Ball rolling without friction in a gutter can’t escape due to force of gravity
Particles diverging from nominal orbit focused back by quadrupoles

## Slide 36: FODO Tracking: Cross section
Cross sections reflect the change of beam size through FODO cell
In real accelerator observable using scintillating screens
  not possible for beam in a circular accelerator
  typically not inside of quadrupoles, of course...
QF
QD
QF
L
L
Beam cross sections in x-y

## Slide 37: FODO Tracking: Phase Space
QF
QD
QF
L
L
Horizontal phase space
Vertical phase space
Important property of beam, but not directly observable in a real accelerator
  how would you measure the angle of a trajectory simultaneously with position?

## Slide 38: FODO Tracking: Beam Profiles
Projections of phase space onto position can be observed
  beam profiles measured by SEM-grids, MWPCs, BIFs, IPMs
  very important information for set-up of accelerators and beamlines
QF
QD
QF
L
L
Vertical beam profiles
Horizontal beam profiles

## Slide 39: FODO Tracking: Mismatch
QF
QD
QF
L
L
Horizontal phase space
Vertical phase space
Important property of beam, but not directly observable in a real accelerator
  how would you measure the angle of a trajectory simultaneously with position?

## Slide 40: Emittance
Oscillation amplitude of single particles normally conserved
  remember the frictionless gutter: ball will oscillate forever
  measure of transverse energy
Transverse energy referred to as single particle emittance
  transverse energy created by random motion in the source
  conserved (at best) until final target
  measure of disorder of particles in the beam
  impossible to create truly parallel beam (would be completely ordered)

## Slide 41: Beam Size and Emittance
Periodic solution of FODO cell characterized by ellipses
  aspect ratio defined by quadrupoles
  for upright ellipses, aspect ratio described by beta functions βx/y
  area of ellipse written as
  emittance εx/y measure for beam size
Emittance is constant in FODO cell
  small width implies large angle spread
  limits the beam spot size at a target
  impossible to create parallel beam
Skew ellipses  talk on Transverse Optics

## Slide 42: Emittance Change
Sources of emittance growth
  scattering in stripping foil or targets
  ellipse mismatch
  non-linear fields
Ways to shrink emittance
  acceleration shrinks emittance according to ε ~ 1/p ~ 1/Bρ (adiabatic damping)
  electron cooling (SIS, ESR) and stochastic cooling (ESR) available to create very small emittances
Unnecessary emittance growth can limit performance
  beam losses due to beam size growth
  larger beam spot size at targets

## Slide 43: Emittance and Acceptance
Emittance: area of phase space ellipse containing a fraction of particles (e.g. 95%)
  may grow due to mismatch, non-linear fields, beam interaction with pipe, etc.
  does not take into account deviations of beam center from ideal orbit
Acceptance: maximum area of the ellipse possible without ever losing particles (by hitting beam pipe)
  acceptance in general smaller than physical aperture of beam pipe
  need some margin for deviations of beam center and emittance growth

## Slide 44: Non-Linear Magnets: Sextupoles
Magnet with six poles
Field depends quadratic on position
  forces on particles non-linear
  in general no analytic solutions
  can even lead to chaotic motion
Frequently used in accelerators
  correction of momentum dependent effects on betatron oscillations (e.g. SIS18, ESR, FRS)
  essential for slow extraction (SIS18)
  compensation of unavoidable field errors in main magnets (dipoles)
N
S
N
N
S
S
By ~ x2 for y=0
Particle motion during slow extraction (SIS18)

## Slide 45: Non-Linear Magnets: Octupoles
Octupoles for SHIP beamline
  deformation of ellipse by non-linear field of octupoles
  uniform distribution in cross section
  higher beam intensity at equal maximum particle density on target

## Slide 46: Summary
Definition of elements and isotopes
Special relativity and electro-dynamics
  masses, energies and mass-energy relation
  Relativistic particle motion and non-relativistic limit
  Lorentz force and magnetic rigidity
Motion of charged particles in magnetic fields
  dipoles as bending magnets and separators
  quadrupoles as focusing magnets
  non-linear magnets for more sophisticated purposes
Particle tracking and transverse phase space
  vectors for description of particles and matrix formalism
  FODO focusing structure
  emittance and acceptance

## Slide 47: Thank you for your attention!
These slides contain material I found in talks of the following colleagues: W. Bayer and M. Maier (GSI), R. Steerenberg (CERN), K. Peach (Oxford University)
I’m very grateful for the possibility of profiting from their excellent material.