The Focussing Light Guide Disc DIRC design
Klaus Föhl
Workshop on Fast Cherenkov Detectors
Gießen – Rauischholzhausen
12 May 2009

---
Existing DIRC
DIRC is already something known, see BaBar
2-dimensional
imaging type
Ba

---
Experiments longing for “new” DIRC
WASA experiment at COSY
measure beta for PID
measure beta for energy determination
forward phase space to cover: theta=5-23deg for PANDA, theta=3-17deg for WASA

---
Focussing Light Guide Disc DIRC

---
Light Guide – Shape Optimisation
focal plane oriented normal to magnetic field direction

---
Focussing Light Guides - Comparison
sigma*sqrt(12)
similar improvement for thinner quartz+LiF plate

---
Cherenkov Radiation Dispersion
different directions
for different colours
n_group
n_phase
Dispersion correction principle:
material with similar n
but different dn/dlambda
LiF
dispersive prism
component
600nm
400nm
300nm
N.B. choice of corrector materials rather limited

---
Qualitative LG Assessment

---
thanks to Marko Zühlsdorf and Oliver Merle
Quantitative LG Assessment
Intensity I(z)
first demonstrator setup
to verify proper optics
of workshop machined
Focussing Light Guides

---
   Photon Statistics (WASA example)

---
Photon Hit Pattern (PANDA example)

---
Particles & Background
Photon pattern analysis performed
for several particles in the disc
and for background photons present.
Signal+background pattern below
analysed without using photon timing
information (yet...).

---
PANDA Endcap FLG-disc-DIRC
optical disc r=1100m
128 optical elements
4096 pixels

---
Compromises
radiator thickness choice is influenced by external conditions
light guide size is limited as well
thicker or shorter LiF (less elongated aspect ratio) makes one loose some photons
not enough space
for full zig-zag, some
photons hitting rear edge

---
Expansion Volume - Effect

---
What if? no Lithium Fluoride
only one material, same mechanical properties
same expansion coefficient
no glueing of quartz and LiF
full ledge length usable for reflection

---
DIRC detector / prototype for WASA
acrylic glass radiator
no UV wavelengths
less detector pixels

---
Sigma Errors
pixel
imaging
straggling
tracking
chromatic
PANDADIRC
3-6mrad
1-4.5mrad
1.4mrad (2GeV/c)
0.4mrad
5mrad
WASADIRC
20mrad
3-10mrad
1.2mrad at 2GeV/c
3.4mrad (or better)
2mrad

---
Eta’: pp  ppη’ (p=3.35GeV/c)
entire range is punch-through energies
most energies below threshold for vertical radiator disc

---
CEARA-Detektor
Cherenkov-Emissions-Analysierender Ringscheiben-Apparat

---
WASA DIRC into 130mm wide layer
status of discussions December 2008:
fit a DIRC disc into a slice 130mm thick

---
Systematic Effect in Analysis

---
FLG thicknesses 80mm and 40mm
PANDA DIRC simulation

---
Performance with limited angular range
WASA DIRC simulation

---
Disc DIRCs for PANDA and WASA
WASA experiment at COSY

---
Summary
Focussing Light Guide disc DIRC design presented
looked at some optical aspects
DIRC performance assessed in simulations
forward angular range in
  - PANDA: PID detector
  - WASA: energy resolution improvement
layout can be fine-tuned to experimental needs

---
Dispersion Correction

---
only one material, same mechanical properties
  - same expansion coefficient
no glueing of quartz and LiF
full ledge length usable for reflection

---
Eta’: pp  ppη’ (p=3.35GeV/c)
entire range is punch-through energies
most energies below threshold for vertical radiator disc