## Slide 1: Direct Detection of the Elusive 229Thorium Isomer: Milestone towards a Nuclear Clock
P.G. Thirolf, LMU München
1
Clock basics
229mTh properties and prospects
Experimental approach & setup
Isomer decay study results
Verification studies
Summary & Perspectives

## Slide 2: Functional Principle of Clocks
2
periodic event
(oscillation)
counting device
examples:
- rotation of earth, moon phases
- pendulum, spring
- quartz crystal
- atomic transitions
- nuclear transitions ?
examples:
- sun dial
- mechanical clocks
- ‘digital’ clocks
- microwave, laser
rising frequency

## Slide 3: Clock Accuracies
3
accuracy: 1s /day
world record (NIST): 1s / year
Mechanical clocks
Quartz clocks
Atomic clocks
nuclear clocks ??
accuracy: 1s / month
world record: 10-12
accuracy: 10-14
world record: 10-18
229mTh

## Slide 4: Clock properties
4
Energy transfer
f excitation frequency
Quality factor Q:
best clock:
- highest oscillation frequency (f large)
- as precise as possible (Df small)
microwave atomic clocks: Q ~ 1010
‘optical’ atomic clocks: Q ~ 1014
nuclear clock: Q > 1015 ??
continuous operation:
- feedback on resonance
- optimum energy transfer at specific excitation frequency f

## Slide 5: What makes 229mTh so unique ?
5
(expected/assumed) properties of 229mTh:
energy: 7.8(5) eV (indirect evidence)
wavelength: 159(10) nm
radiative t ≈ 104 s
DE/E ≈ 10-20
Dn ~ 10-4 Hz
since 40 years nuclear physicists seemed to chase a phantom:
presumed low-lying isomer in 229Th:
- 1976 (Kroger, Reich): < 100 eV
1990 (Reich, Helmer): -1 ± 4 eV
1994 (Reich, Helmer): 3.5 ± 1 eV
2005 (Guimaraes-Filho, Helene): 5.5 ± 1 eV
2007 (Beck et al.): 7.6 ± 0.5 eV
B.R. Beck et al., LLNL-PROC-415170 (2009)

## Slide 6: 229mTh: Nuclear Clock ?
6
lowest excitation energy of all ca. 176000 presently known excited nuclear states
 ultra-precise nuclear frequency standard ?
insensitivity of 229mTh nuclear transition frequency to external perturbations
 small nuclear moments
 largely immune to systematic frequency shifts:
Notes: Longest-lived nuclear isomer: 180mTa (> 10^15 years, never seen to decay)

## Slide 7: 229mTh and time dependence of fundamental constants
7
temporal variation in transition energy may provide enhanced
sensitivity by (102 – 105) for fine structure constant a/a
and strong interaction parameter (mq/LQCD)
.
Theories unifying gravity with other interactions suggest temporal and spatial
variations of the fundamental “constants” in an expanding universe
- Flambaum, PRL 97 (2006) - Hayes, Friar, PL B 650 (2007)
He, Ren, NP A 806 (2008) - Berengut, Flambaum et al., PRL 102 (2009)
Litvinova, Feldmeier et al., PRC 79 (2009) - Flambaum et al., Europhys. Lett. 85 (2009)
Flambaum, Wiringa, PRC 79 (2009) - Flambaum, Porsev, PRA 80 (2010)
Rellergert et al, PRL 104 (2010)
- near degeneracy of 229,229mTh results from cancellation between large
contributions from Coulomb energy (~109 eV)
dependencies on fundamental constants
 any variation would be enhanced in the transition frequency
current (theor.) limit of potential time variation:
Uzan, Rev. Mod. Phys. 75, 403 (2003)
Fujii et al., NP B573, 377 (2000)
Notes: Theories unifying gravity with other interactions suggest temporal and spatial variations of the fundamental “constants” in an expanding universe
(see, e.g., review: J.-P. Uzan, Rev. Mod. Phys. 75 , 403 (2003).
The fundamental constants may be slightly different near massive bodies .
There are some hints for the variation of different fundamental constants in quasar absorption spectra and big bang nucleosynthesis data.
However, a majority of publications report limits on the variations of the fundamental constants.
Dirac initiated the consideration of time-varying constants:
expressed, in his ‘‘Large Numbers hypothesis,’’ the opinion that very large (or small) dimensionless universal constants cannot be pure
mathematical numbers and must not occur in the basic laws of physics. He suggested, on the basis of this numerological principle, that these large
numbers should rather be considered as variable parameters characterizing the state of the universe.
 Dirac noticed that alpha_G mu/alpha_EM, representing the relative magnitude of electrostatic and gravitational forces between a proton and an
electron, was of thesame order as H_0e^2/m_ec^2 = delta alpha_EM /mu, representing the age of the universe in atomic time, so that the
five previous numbers can be ‘‘harmonized’’ if one assumes that alpha_G and delta vary with time and scale as the inverse of the cosmic time.
- grand unified theories (GUT), higher-dimensional theories (Kaluza-Klein and string theories)
a number of cosmological models taking these variations into account.
The development of high-energy physics theories such as multidimensional and string theories provides new motivations to consider the time variation of the fundamental constants. The observation of the variability of these constants constitutes one of the very few hopes to test directly the existence of extra dimensions and to test these high-energy physics models.
- Modern theories of high-energy physics offer new arguments to reconsider the variation of the fundamental constants
Constraints from: geological studies  alpha decay, beta decay, spontaneous fission
atomic spectra
cosmological constraints: CMB, nucleosynthesis  give no tight constraints
equivalence principle
- Experimental limit: Sortais et al., 2001)  (8.4+/- 13.8) x 10^-15 2sigma 24 months method: Atomic clock

## Slide 8: Sensitivity to variations of a
8
enhancement factor:
sensitivity of 229mTh transition frequency w to temporal variation of a= e2/hc:
DVC: difference in Coulomb energy between 229Th, 229mTh
(proton polarization by modified neutron distribution)
example:
for DVC = 100 keV, da/a = 10-16
 dw = 10-11 eV (= 2.4.103 Hz)
104 larger than limits on shifts in
atomic transitions
problem: - Coulomb energy cannot be directly measured
- VC needs to be calculated in nuclear models
- insufficient accuracy in present nuclear models
(e.g. Hartree-Fock, Hartree-Fock-Bogoliubov:
-300 keV < DVC (229Th) < 400 keV  - 4.104 < K < + 4.104 )
system | K | l [nm]
Sr | 0.06 | 699
Yb+ E2 | 0.91 | 436
Yb+ E3 | -6 | 467
Hg+ | -2.9 | 281.5
Al+ | 0.01 | 267
Ir17+ T1 | -20.6 | ca. 267
Ir17+ T2 | 32.2 | ca. 470
Cf16+* T1 | 75 | ca. 520
Cf16+* T2 | -46 | ca. 653
Th* (nuclear) | 8000 | ca. 160
Schmidt & Crespo,
Phys. Jour. Oct. 2016
Notes: Sensitivity factor K: relative shift of transition frequency as a function of alpha ( Crespo)
DeMille et al 2004, 2008: – enhancement in Cs2: cancellation between electron excitation and vibration energies
Flambaum 2006: Cancellations between rotational and hyperfine intervals
Δω/ω0 = Κ Δα/α , Enhancement K = 102 -103
Flambaum, Kozlov 2007: Cancellations between fine structure and vibrations
Δω/ω0 = Κ(Δα/α −1/4 Δμ/μ)
Enhancement K = 104 -105
Table: from atomic structure calculations (T1, T2: different optical transitions)

## Slide 9: Indirect Evidence for 229mTh
9
from energy difference of high-energy transitions → low isomer excitation energy
B.R. Beck et al., PRL 98 (2007) 142501
LLNL-PROC-415170 (2009)
E* (229mTh) = (7.8 ± 0.5) eV
E* (229mTh) = DE29 - DE42
data from X-ray micro-calorimeter

## Slide 10: Experimental Approach @ LMU
10
triodic
extraction
electrode
concept:
 4 vacuum chambers , 3 differential pump sections, overall length ~ 2 m
RF + DC
funnel
RF quadrupole
ion guide
Quadrupole
mass separator
MCP
CCD
233U
source
Buffer gas
stopping cell
Laval
nozzle
aperture
electrode
detection
system
10-6 mbar
10-2 mbar
40 mbar (He)
UV detection
229(m)Th2+,3+
populate the isomeric state via 2% decay branch in the a decay of 233U
spatially decouple 229(m)Th recoils from the 233U source
detect the subsequently occurring isomeric decay

## Slide 11: Experimental Setup
11
strictly UHV compatible, bakeable (180o)
typical: 2.8.10-10 mbar
operated at 40 mbar He 6.0
catalytically purified (< ppb)
220 Vpp, 850 kHz
4 V/cm
200 Vpp, 880 kHz
0.1 V/cm
Th2+: 925 kHz, 901.5 Vpp, 75.23 V
Th3+: 925 kHz, 600.5 Vpp, 50.15 V
m/Dm~ 150

## Slide 12: Experimental Setup
12
located at Maier-Leibnitz Laboratory, Garching:

## Slide 13: 233U ion sources
13
population of 229mTh via 2% a decay branch of 233U
2 different 233U sources were used:
source 1:
- 200 kBq 233UF4 evaporated onto 20 mm ø steel plate
- no radio-chemical purification before evaporation
- 232U contamination ≤ 10-6
- eff. 229(m)Th recoil activity: ca. 4000/s
source 2: (IRC Uni Mainz)
- 290 kBq electro-deposited onto 90 mm ø wafer
- radio-chemical purification before evaporation
- 232U contamination ≤ 10-6
- eff. 229(m)Th recoil activity: ca. 55000/s

## Slide 14: Ion Extraction from Buffer Gas Cell
14
L. v.d. Wense, B. Seiferle, M. Laatiaoui, PT, EPJ A51, 29 (2015)
mass scan of extracted ion species: efficient 229(m)Th3+ extraction
q=1
q=2
q=3
229Th+
233U+
233U2+
229Th2+
229Th3+
233U3+
element | 1+ [eV] | 2+ [eV] | 3+ [eV]
U | 6.1 | 11.6 | 19.8
Th | 6.3 | 11.9 | 18.3
Ra | 5.3 | 10.1 | 31.0
Fr | 4.1 | 22.4 | 33.5
Rn | 10.7 | 21.4 | 29.4
At | 9.3 | 17.9 | 26.6
Po | 8.4 | 19.3 | 27.3
Bi | 7.3 | 16.7 | 25.6
I(He+) = 24.6 eV
element | 1+ [%] | 2+ [%] | 3+ [%]
Th | 0.37(7) | 5.5(11) | 10(2)
Fr | 21.0(42) | 16.0(32) | ≤ 1.5.10-3
Rn | 5.8(12) | 9.3(19) | 0.053(11)
At | 8.6(17) | 13.0(26) | 0.033(7)
Po | 7.3(15) | 8.1(16) | ≤ 0.0021
Bi | 4.3(9) | 21.0(42) | 0.083(16)
Pb | 2.2(4) | 11.0(22) | ≤ 0.012

## Slide 15: Isomer Decay: Search for VUV Fluorescence
15
B. Seiferle, L. v.d. Wense, M. Laatiaoui, PT, EPJ D70, 58 (2016)
UV optical setup designed, built and commissioned (aligned):
 2 annular, parabolic mirrors (MgF2 coated, from Fraunhofer IOF, Jena)
from triode
MCP
mirror 1
mirror 2
mirror 2:
mirror 1:
50 mm ø collection
micro electrode

## Slide 16: VUV Optics Setup
16
ion collection on micro-electrode:
no fluorescence signal was observed
 radiative decay branch too weak ?
 search for dominant IC decay branch
 measure conversion electrons
L. v.d. Wense, PT, D. Kalb, M. Laatiaoui, Journal of Instrumentation 8, P03005 (2013)
2% 16% 65% 80% 40% 42% 49% 76% 10% 1.3.10-5
efficiency:
signal-to-noise ratio:
233U source 2 | 
eff. 229Th recoil activity | 55000 / s
detectable VUV photons | 0.72 / s
count rate/area | 81.82 / mm2s
dark count rate | 0.01 / mm2s
signal/noise ratio | 8182:1
VUV fluorescence ?

## Slide 17: Isomer Detection Process
17
MCP
CCD
detection
system
UV detection
triodic
extraction
electrode
RF + DC
funnel
RF quadrupole
ion guide
Quadrupole
mass separator
233U
source
Buffer gas
stopping cell
Laval
nozzle
aperture
electrode
229(m)Th2+,3+

## Slide 18: Isomer Detection Process
17
MCP
CCD
detection
system
triodic
extraction
electrode
RF + DC
funnel
RF quadrupole
ion guide
Quadrupole
mass separator
233U
source
Buffer gas
stopping cell
Laval
nozzle
aperture
electrode
229(m)Th2+,3+
 accumulate 229(m)Th ions directly onto MCP surface

## Slide 19: Isomer Detection Process
18
extracted 229(m)Th3+ ions: impinging directly onto MCP surface behind triode exit

## Slide 20
18
Isomer Detection Process
extracted 229(m)Th3+ ions: ‘soft landing’ on MCP surface

## Slide 21
18
Isomer Detection Process
electron capture on MCP surface: neutralization of Th ions

## Slide 22
18
Isomer Detection Process
isomer decay by Internal Conversion: electron emission
internal conversion (IC) energetically allowed for neutral thorium:
I(Th+, 6.31 eV) < E*(229mTh, 7.8 eV)
isomer lifetime expected to be reduced by ca. 109 (from ~104 s  ~ 10 ms)
Th ions: IC is energetically forbidden, radiative decay branch may dominate

## Slide 23
18
Isomer Detection Process
amplification of IC electron: electron cascade generated,
accelerated towards phosphor screen
internal conversion (IC) energetically allowed for neutral thorium:
I(Th+, 6.31 eV) < E*(229mTh, 7.8 eV)
isomer lifetime expected to be reduced by ca. 109 (from ~104 s  ~ 10 ms)
Th ions: IC is energetically forbidden, radiative decay branch may dominate

## Slide 24
18
electrons hit phosphor screen: visible light imaged by CCD camera
Isomer Detection Process
internal conversion (IC) energetically allowed for neutral thorium:
I(Th+, 6.31 eV) < E*(229mTh, 7.8 eV)
isomer lifetime expected to be reduced by ca. 109 (from ~104 s  ~ 10 ms)
Th ions: IC is energetically forbidden, radiative decay branch may dominate

## Slide 25: Direct Signal of IC Decay from 229mTh
19
clear signal from Th3+, Th2+
no signal from U3+, U2+
Th2+
Th3+
U2+
U3+
L. v.d. Wense, PT et al., Nature 533, 47-53 (2016)

## Slide 26: Verification Measurements
20
Background-corrected isomeric decay signals:
229Th2+
UMCP= -25 V
 isomeric decay
UMCP= -900 V
 ionic impact
233U2+
235U2+
- comparable mass peak amplitudes for
229Th2+, 233U2+ ion impact signals
- for UMCP= -25 V 233U2+ signal vanishes
- 229Th2+ signal remains
during extraction of 229Th2+
during extraction of 233U2+
- ionic impact signal decreases with UMCP
- 233U2+ signal drops to zero
- 229Th2+ signal remains, cutoff at Ekin=0
(rise: IC electrons back-attracted to
MCP surface by repelling triode)

## Slide 27: Potential Background Contributions
21
A) Background due to kinetic energy or charge state of impinging ions
B) Background signals from setup components
(source, gas stopping cell, extraction system, QMS , MCP system)
C) Signals from thorium atomic shell
(e.g. long-lived excited states, chemical reactions on MCP surface)
Signals from short-lived
daughter nuclides or
non- 229Th isomers
could all be excluded,
mostly by several ways

## Slide 28: Lively Echo to Publication
15

## Slide 29: Next steps: Halflife determination
22
- charged 229mTh2+: t1/2 > 1 min (limited by RFQ storage time)
- neutral 229mTh: pulsed extraction from RFQ
expected conversion coefficient: ca. 109
provides constraint for strength of photonic decay branch
(if IC cannot be suppressed, e.g. by suitable lattice implantation)
B. Seiferle et al., to be published
229mTh2+
t1/2 > 1 min.
229mTh
t1/2 : ?
Notes: Electron/gamma decay rate ratio

## Slide 30: Halflife: Neutral 229mTh
23
MCP signal of 229(m)Th2+ ion bunches
with different kinetic energies:
simulation:
measurement:
bunch width: ca. 10 ms
600- 800 229(m)Th2+,3+ ions/bunch
assumed: t1/2 = 7 ms
UMCP= -70V
B. Seiferle et al., to be published
ionic impact
isomeric decay
Notes: Simulations: - t1/2 = 7 microseconds assumed
- electron detection efficiency assumed to be 25x the one for ions

## Slide 31: Halflife: Neutral 229mTh
24
extracted Th3+
extracted: Th2+
based on expected charged isomeric half-life of a few 103 s:
confirms expected conversion coefficient of ca. 109
 photonic decay branch ??

## Slide 32: Halflife: Charged 229mTh
25
- 229mThq+: longer ion storage time needed ( UHV)
 cryogenic linear Paul trap:
M. Schwarz et al.,
Rev. Sci. Instr. 83, 083115 (2012)
- in operation at MPI-K (HD): CryPTEx  operating at 4 K (p(H2) ~ 10-15 mbar)
 ion storage time ≤ 30 h
 laser access ports
thanks to: MPIK (J. Crespo et al.), PTB (P. Schmidt)
prerequisite for laser manipulation
of 229mTh3+

## Slide 33: “Holy Grail”: Excitation Energy
26
Magnetic bottle spectrometer: large acceptance needed (~ 4p)
10000 229Th ions extracted/sec.  200 e-/s
Y. Yamakita et al., Rev. Sci. Instr. 71, 3042 (2000)
electron
detector
retarding
electrodes
guiding
solenoid
inhom.
B field
permanent
magnet
our present constraint: 6.31 eV < E(229mTh) < 18.3 eV
Notes: bottom part of this schematics is specific to the application targeted in [46], namely Penning ionization electron spectroscopy, where a beam of metastable rare-gas atoms is crossed with a continuous supersonic sample beam in the source region of the analyzer.
Ca. 1000x more efficient than hemispherical electron analyzers with 180-degree deflection geometry and small entrance aperture
The kinetic electron energy is analyzed by scanning the retarding field in a flight tube of the analyzer in the presence of a weak magnetic field.
Energy resolution: Delta E/E < B_f/B_i (exit/entrance values of inhomogeneous magnetic field)

## Slide 34: Excitation Energy
27
229mTh2+,3+ neutralization with subsequent IC:
- metallic catcher electrode
- but: how to control/avoid surface effects (work function) ?
finally expected:
DE < 50 meV
M.G. Helander et al., Applied Surface Science 256, 2602 (2010)
 contact-free neutralization: charge-transfer cell

## Slide 35
28
Laser diagnostics of isomer excitation
w1
229Th(g.s.)
w2
w1
229mTh
a: nuclear, b: electronic
after nuclear transition (via w2):
 change of nuclear moments, spin
change of hyperfine splitting,
total angular momenta
w1 out of resonance (~GHz)
 drop in resonance fluorescence
double resonance method
Dehmelt’s ‘electron shelving’
use closed 2-level system in electron shell:
Peik, Tamm, Eur. Phys. Lett. 61 (2003) 181

## Slide 36
29
229Th3+: suitable level scheme
simple structure: alkali-like (Rn core + single valence electron)
closed 3-level L system and closed 2-level system available
for laser cooling and fluorescence detection
6p6 6d 2D5/2
6p6 5f 2F7/2
6p6 7s 2S1/2
6p6 6d 2D3/2
6p6 5f 2F5/2
984 nm
690 nm
1087 nm
717 nm
~GHz
(metastable, ~1s)
constant resonance fluorescence scattering with closed optical transition
- after nuclear excitation: out of resonance
   spectroscopy of laser-cooled 229Th3+ (e.g. in linear Paul trap)

## Slide 37: Why better clocks at all ?
30
example: GPS navigation
GPS satellites
GPS
receiver
present technology:
- ‘thermal’ microwave atomic clocks
(Rb, Cs)
- GPS, GLONASS: active
- Galileo, Beidou, IRNSS:
under construction
 positioning precision: 1-10 m
goal: positioning to cm – mm
- autonomous driving
- freight-/ component tracking
- …..
requirements:
- better clocks (10-16 – 10-18)
- robust, small, low power consumption …
every time that clock precision has improved, new and
frequently unexpected applications have emerged
Notes: Not clock limited on short timescales, but advantage via superb longterm drift stability:
Longer resynchronization intervals
 improved system integrity: enabling autonomous operation within given acceptable
position ranging errors for time scales of days or weeks, instead of hours.
applications which can benefit from improved system integrity include precision airplane approaches at airports
- onboard deep space missions to aid in navigation and timekeeping.

## Slide 38: Further potential applications
31
Derevianko & Pospelov,
Nature Physics 10, 933–936 (2014)
networks of clocks can be used as 3D gravity sensors
 Ludlow, Boyd, Ye, Peik, Schmidt, Rev. Mod. Phys. 87, 637–701 (2015)
- best present clocks: detect gravitational shifts of ± 2 cm
- “relativistic geodesy” or “chronometric leveling”:
 allows long-distance potential difference measurements
precise, fast measurements of nuclear clock network:
e.g. monitor volcanic magma chambers, tectonic plate movements
topological dark matter:
clumped to point-like monopoles,
1D strings, 2D ‘domain walls’
Df: clock frequency difference
DU: gravitational potential difference
(networks of) ultra-precise clocks could be used
to search for dark matter
Notes: Dark matter search:

## Slide 39: The nuClock Consortium
32
http://www.nuclock.eu/
FET-OPEN project within EU Horizon 2020:
 experiment, theory, industrial R&D
TU Wien (T. Schumm et al., Coord.)
Univ. Jyväskylä (I. Moore et al.)
Univ. Heidelberg (C. Enss et al.)
MPI-K, HD (A. Pálffy et al.)
PTB Braunschweig (E. Peik et al.)
MPQ Garching (T. Udem et al.)
TOPTICA Photonics AG, Munich
LMU Munich (PT et al.)
associated:
- Okayama Univ., Japan (SPRING8)
- Metrology Light Source (MLS), Berlin-Adlershof
- U Mainz/ HIM (C. Düllmann et al.)
- Kerstin Ergenzinger (Berlin): artist, via FEAT (future emerging art and technology)

## Slide 40: Collaboration with PTB Braunschweig
33
E. Peik, M. Okhapkin et al.: targeting hyperfine structure of 229mTh1+,2+
collinear laser spectroscopy:
- laser interaction with 229Th ions
extracted from QMS
- measurement campaign started

## Slide 41: Summary
34
successful experimental approach based on spatial decoupling of population and deexcitation via buffer-gas stopping cell
efficient extraction of pure 229(m)Th2,3+ ions achieved
next steps: determination of halflife for neutral 229Th
towards determination of isomeric excitation energy
(magnetic bottle spectrometer )
started: setup of cryogenic Paul trap
 to achieve longer storage times for halflife measurement in charged 229mTh
 prerequisite also for laser manipulation of 229mTh3+
VUV optical detection system was designed and commissioned
radiative decay channel in neutral 229mTh drastically reduced (in favor of IC)
IC decay channel provided first direct (and unambiguous) identification of
isomeric ground-state transition in 229mTh
constraints of 229mTh properties: 6.3 eV ≤ E* ≤ 18.3 eV
t > 60 s

## Slide 42: we made a big step towards the ultimate goal of a Nuclear Clock ….
35
but many more are yet to come ….

## Slide 43: Thanks to ….
36
LMU Munich: L. v.d. Wense, B. Seiferle, J.B. Neumayr, H.-J. Maier, H.-F. Wirth,
D. Habs
GSI Helmholtzzentrum f. Schwerionenforschung, Darmstadt & Helmholtz-Institut Mainz:
M. Laatiaoui
Helmholtz-Institut Mainz & Johannes Gutenberg-Universität Mainz:
C. Mokry, J. Runke, K. Eberhardt, C.E. Düllmann, N.G. Trautmann
Thank you for your attention !