## Slide 2: Ionisation Profile Monitor Proposal for ELENA
IPM17 workshop, GSI
22/05/2015
Pierre Grandemange
CERN BE/BI/EA

## Slide 4: Extra Low Energy Antiproton
5.3MeV to 100keV
2.e7 pbar
4.e-12 mbar
Why an IPM?!!!

## Slide 5: Why an IPM for ELENA ?
  A scraper is already foreseen to monitor the beam profile : destructive detector
  The IPM is non/semi destructive
  Acquisition during a complete machine cycle
  Especially useful to characterise the electron cooling efficiency

## Slide 6: ELENA cycle
ELENA design report
ELENA parameter list

## Slide 7: IPM principle
BIPM principle drawing
Beam
Residual gas
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
V+
V-
Top electrode
Bottom electrode
MCP
Read Out

## Slide 8: IPM principle
MCP
Read Out
BIPM principle drawing

## Slide 9: Ionisation rate
 | antiproton flux | 2.e-7 /turn @ 100keV | = 2.9e12 /s
 | gas density | H2 @ 3.8e-12 mbar | = 9.2e10 /m3
 | gas ionisation cross section with antiprotons | @ 100keV | = 1.7e-20 m2
 | linear ionisation rate | @ 100keV | ~ 4600 ionisations/m/s
 | antiproton flux |  | 
 | gas density | H2 @ 3.8e-12 mbar | 
 | gas ionisation cross section with antiprotons | @ 100keV | 
 | linear ionisation rate | @ 100keV | 
4.6 ions /1cm/100ms

## Slide 10: Ionisation rate
Beam | Intensity [A] | Kinetic energy [MeV] | Gas pressure [mbar] | Ionisation rate [/m/s]
ELENA extraction | 4.6e-7 | 100 keV | 3.8e-12 | 4600
AD extraction | 1.1e-6 | 5.3 MeV | 1.e-11 | 1300
LEIR Ar11+ | 1.6e-4 | 4.2 MeV/u | 5.e-12 | 1.3e6
LEIR Pb54+ | 7.8e-4 | 4.2 MeV/u | 5.e-12 | 3.e7
Increase detection length
Increase acquisition time
Inject gas :
  Increase local pressure
  Increase ionisation probability
  Decrease antiproton lifetime
LEIR – 11/11/2014
Alexandre Frassier
BE/BI/EA
AD – 01/12/2014
Gas injection – 8.5e-9mbar
Alexandre Frassier
BE/BI/EA

## Slide 11: Gas injection ?
J. Phys. B: At Mol Opt. Phys. 44 (2011) 122001 (CERN PS194, ASACUSA)

## Slide 12: Ionisation in ELENA
No gas injected

## Slide 13: Ionisation in ELENA
CO2 @ 1.0e-11 mbar
9% average pressure rise

## Slide 14: blow up and large angle scattering

## Slide 16: BIPM detector
MCP
Top electrode
Read-out tubes
External dimensions: 206 x 140 x 128 mm
Beam aperture: 82 x 70 mm
Wilfried Devauchelle, 2015

## Slide 17: BIPM detector
Triple Z stack matched MCP
  Gain > 2.e8
  Long detection length : 84 mm
High vacuum compatible materials
  inox, alumina (AL2O3) and copper… and kapton…
  … what about vespel?!
Resistive glass
  Improve electric field quality in the bulk
Orbit correction electrodes
NEW

## Slide 18: Integration in ELENA
Horizontal BIPM +
NEXTorr D 1000-10
Vertical BIPM +
NEXTorr D 1000-10
Gas injection
Turbo-molecular
pump
Bellow
Bellow

## Slide 19: Acquisition chain
VME crate
BIPM V
BIPM H
CERN technical network
ELENA timing
1 VME crate
2 * VIPM cards
  DDC 264 integrator
2*4 channels positive HV power supply
2*4 channels negative HV power supply

## Slide 20: Cost estimates
BIPM | mechanics | 15 kCHF | 65 kCHF
 | MCPs | 30 kCHF | 
 | Resistive glasses | 20 kCHF | 
Vacuum chamber | Main tank | 16 kCHF | 31 kCHF
 | BIPM flanges | <10 kCHF | 
 | Support | <5 kCHF | 
Vacuum | Gas injection, valves, pumping | 50 kCHF | 50 kCHF
Acquisition | VME + CPU | 2kCHF | 23 kCHF
 | HV power supplies | 8 kCHF | 
 | VIPM cards | 3 kCHF | 
 | Cables | <10 kCHF | 
Total |  |  | 169 kCHF

## Slide 21: Conclusion
An IPM is a non destructive profile detector
Efficient to monitor beam cooling efficiency
Preliminary study promising
  Complete transport simulation still to be done
Detector design and ECR ready

## Slide 23: Ionisation in ELENA

## Slide 24: Gas injection ?

## Slide 25: BIPM vacuum chamber

## Slide 26: Integration in ELENA

## Slide 27: Schedule

## Slide 28: Schedule : detector

## Slide 29: Schedule

## Slide 30: Schedule

## Slide 31: Schedule

## Slide 32: Schedule

## Slide 33: Beam transport
Gerard Tranquille, 2015

## Slide 34: Beam transport
Gerard Tranquille, 2015

## Slide 35: Beam transport
Gerard Tranquille, 2015