## Slide 1
Bunch: A Tracking Code Based upon Analytic Field Computations in Use at GSI
Şerban Udrea, Peter Forck, GSI
Original analytic field solution: P. Strehl, M. Dolinska, R.W. Müller (2000)
Initial implementation: M. Herty, supervision P. Forck (2004)
Further development: S. Udrea, P. Forck (since 2015)
Outline of the talk:
Code description
Example of code input and results
Present issues and possible solutions
Summary and Outlook

## Slide 2
Simulation code: Theoretical background
Homogenous guiding external electric and magnetic fields
Analytical description of bunch charge density
Bunch electrostatic -field via analytical solution of the Poisson equation in free space and the frame of the bunch
Movement of bunches each time step, multiple bunches can be defined
Monte Carlo based selection of initial coordinates and velocities of the ions or electrons to be tracked
Trajectory computed by 4th order Runge-Kutta in moving bunch and guiding fields
Storage of initial and final coordinates, velocities and arrival time for each particle
History: Code produced by a PhD student in 2004
Language: C++ with specifics of Borland C++ Builder 6, which is not available anymore, maintenance difficult
Should be usable for LINAC and synchrotron beams 1 MeV/u < Ekin < 30 GeV/u

## Slide 3
Simulation code: Input considerations
Bunches have cylindrical symmetry: stretched (prolate) ellipsoids of revolution with the longer semi-diameter on the z axis, which is also the axis of movement. Spheres are also included as special cases and treated separately.
Density: homogeneous or parabolic
Solution of bunch field using curvilinear coordinates i.e. non-linear transformation
No boundary condition (i.e. free space = ‘open boundary’ is assumed)
Movement of bunches: initial implementation targeted non-relativistic LINACs, no magnetic field associated with the bunch movement
Lorentz-Transformation of fields and corresponding magnetic field got added later, an implementation bug recently discovered (2016) has been corrected
Only homogeneous guiding external E and B fields
Simple electron start velocities distribution, ions are considered to start at rest
Advantage: The bunches are described by few parameters, fast computations

## Slide 4
Prolate spheroidal coordinates
The prolate spheroidal coordinates  and  allow for solutions of the Poisson equation in terms of elementary functions. These coordinates are defined as follows:
and
and with the normalization and z, r being the usual cylindrical coordinates. corresponds to the bunch surface.

## Slide 5
Poisson equation and solution example
The Poisson equation in prolate spheroidal coordinates is:
For the case of a parabolic charge distribution the solution inside the bunch is given by simple polynomials:
In the present implementation the computation of the aij coefficients becomes unstable for extremely elongated bunches. D. Vilsmeier has shown that this is a numerical and not an analytical issue. Work is in progress to make the relevant code more robust and allow for computations in the case of ultra-relativistic bunches.

## Slide 6
Code input: Main window
Usage modes:
E & B field at fixed location
Single particle trajectory
IPM mode: Boundary dependent
BIF-mode: Time dependent
Actual parameters:
H2+ ion detection
Ex = 100 V/mm
 = 15 %
1 MHz rep. rate
Bunch 1 m length = 22 ns
1 cm transversal extension
parabolic density profile
1011 elementary charges
Non-relativistic computation

## Slide 7
Code input: IPM mode
Bounding box
& number of trajectories
Actual parameters:
H2+ ion detection
Ex = 100 V/mm
Bunch 1 m length
1 cm trans. extension
parabolic density distrib.
1011 charges
 = 15 %,
1 MHz rep. rate

## Slide 8
broadening for ion detection
differences for head  tail
Code output: IPM mode, ion detection
Actual parameter:
H2+ ion detection
Ex = 100 V/mm
Bunch 1m length = 22ns
1 cm trans. extension
parabolic density distrib.
1011 charges
 = 15 %
1 MHz rep. rate
initial coordinate
final x coordinate
final y coordinate

## Slide 9
no broadening for e- detection
Code Output: IPM mode, electron detection
Actual parameters:
electron detection
vini = 0
Bx = 100 mT
Ex = 1 kV/cm
Bunch 1 m length
1 cm trans. extension
parabolic density distrib.
1011 charges
 = 15 %,
1 MHz rep.
rate

## Slide 10
Usage of initial e- velocity distribution
Electron parametrization with ‘separated’ ansatz:
Energy: d / dE constant value for
0 < E < E1 ; linear decay for
E1 < E < E2 ; = 0 for E > E2
Angular: d / d Gaussian with center 1 and width 2
Improvements contributed by Dr. Jun He, Institute of High Energy Physics, Chinese Academy of Sciences

## Slide 11
Simulation with initial e- velocity distribution
Actual parameters:
electron detection
Bx = 100 mT
Ex = 1 kV/cm
Bunch 1 m length
1 cm trans. extension
parabolic density distrib.
1011 charges
 = 15 %
1 MHz rep.
rate
no significant difference compared to vini = 0 for this case

## Slide 12
Code input/output: BIF mode with H2+ ions
Actual parameters:
H2+ ion detection
Bunch 1 m length
1 cm trans. extension
parabolic density distrib.
1011 charges
 = 15 %
1 MHz rep. rate
H2+ fluorescence
 position after 100 ns

## Slide 13
Code input/output: BIF mode with N2+ ions
Actual parameters:
N2+ ion detection
Bunch 1 m length
1 cm trans. extension
parabolic density distrib.
1011 charges
 = 15 %
5 MHz rep. rate
N2+ fluorescence
 position after 100 ns

## Slide 14
Summary and Outlook
Features:
Easy to use GUI with real time capabilities
Based on analytical expressions for the bunch fields, allowing for fast computations
Homogeneous external E and B guiding fields
Density: (i.e. transversal KV-distr., longitudinal ‘air-bag’) used for tests or parabolic
Relativistic and non-relativistic bunches
For electrons non-zero start velocities can be used, the velocity distribution is based on a ‘separated’ ansatz
Outlook:
Rewrite parts of the code to increase numerical robustness and allow for strongly stretched bunches
Separate GUI code from the computational one and produce a new GUI based on modern portable libraries
Benchmark against other codes and also experiments