## Slide 1: IPM Simulations at Fermilab
23 May 2017
Randy Thurman-Keup

## Slide 2: Nova Era Main Injector / Recycler
Recycler accumulates protons from Booster synchrotron
  8 GeV
  ~5 x 1013 protons
Main Injector receives beam from Recycler
  8 GeV incoming
  Up to 120 GeV outgoing
    Nova neutrino experiment
  588 53-MHz rf buckets
    each bucket ~19 ns
    1 x 1011 protons per bucket
    rms bunch length typically ~1-3 ns

## Slide 3: IPM Concept
Magnet with vertical B field
Cathode
Field shaping electrodes
Electron Suppression Grid
Wire mesh gate
Microchannel Plate (MCP)
Anode strips
500 mm spacing
Beam
(into page)
Ions
Electrons
Ionization Happens

## Slide 4: Gated IPM Concept
Problem with MCP is short lifetime
  Plate is using up lifetime whenever beam is in the machine and the IPM voltage is on
  Voltage takes a while to raise and lower
Would like to be able to gate the charge to preserve the MCP
  Stop the electrons and ions from reaching the MCP
  Allow the electrons and ions an escape path from the IPM active region
    i.e. no Penning traps

## Slide 5: Gated IPM Concept
  The force on a charged particle is
  Assume that and
  Solve the differential equations and one gets the usual solution of circular motion in the plane, constant motion along and a drift along which in this case is , i.e. along the beam
  Putting in the values for the electric and magnetic fields gives us a drift velocity of ~10 cm/ms along the proton beam direction
    The electrons will have drifted beyond the MCP in ~1-2 ms

## Slide 6: MATLAB Simulation
Simulation tracks particles through arbitrary E and B fields
Uses interpolation to obtain the fields at any point from previously calculated field distributions
Propagates using a relativistic formula
Invert

## Slide 7: Matlab Simulation
Once the acceleration is determined, a discrete evaluation of the differential equation of motion is used to step the particles
The magnetic and electric fields are handled separately
  Magnetic contribution to the motion is only applied to the components perpendicular to the B field
  Magnitude of the velocity perpendicular to the B field is forced to be preserved, since the B field does no work
    This in particular helps with the tight spirals along the field lines

## Slide 8: Matlab Simulation
The electric and magnetic fields of the bunch are evaluated on a grid for various bunch parameters
  Shifted as a function of time to represent the moving beam
Electric field of IPM from a Poisson calculation (2D)
Magnetic field from 3-D magnet model
Ionized particle distributions are random in emission angle with 1/E2 energy distribution

## Slide 9: Gated-on IPM
Magnet with vertical B field
Cathode
Field shaping electrodes
Electron Suppression Grid
Wire mesh gate
Microchannel Plate (MCP)
Anode strips
B Field ~ 1 kg
E Field ~ 1 kV/m
ON
Electrons spiral down helically

## Slide 10: Gated-on IPM
Particles originating from single point
(resolution contribution)
Elapsed time ~ 1.7 ns
Anode Strip

## Slide 11: Gated-on IPM
Bunch offset refers to x
Particles originating from single point
(resolution contribution)

## Slide 12: Gated-on Expected Signal
From figure 7 of Sauli #, the number of primary ion pairs produced in one centimeter of a gas species i at one atmosphere of pressure by one minimum ionizing particle can be roughly parameterized as
Expressing this in terms of the proton bunch parameters and partial pressures in the beampipe one arrives at
At the peak of a Main Injector bunch, the number of ionization electrons is ~10 per anode strip (no MCP gain)
#F. Sauli, “Principles of Operation of Multiwire Proportional and Drift Chambers”, CERN 77-09, 3/5/77.

## Slide 13: Gated-off IPM
Magnet with vertical B field
Cathode
Field shaping electrodes
Electron Suppression Grid
Wire mesh gate
Microchannel Plate (MCP)
Anode strips
B Field ~ 1 kg
E Field ~ 0 kV/m
OFF
Electrons propagate into or out of the page

## Slide 14: Gated-off Fields
X Component of E field
Y Component of E field

## Slide 15: Gated-off Motion
Electron drift along beam direction
Single particle
Particle origination point

## Slide 16: Gated-off Behavior
Bunch Centers
Drift Velocity
1.2 cm / 150 ns = 8 cm/ms
Compared to
10 cm/ms analytically estimated
Y motion vs time

## Slide 17: Gated-off Ion Paths
Elapsed time is ~1.5 ms
Maybe Ok, since ions do not go past the gating grid…
However, secondary electrons from ion impacts on the MCP-side of the gating grid will still travel to the MCP

## Slide 18: Other Simulation Uses
Laser wire intensity monitor
  Tracking of laser-stripped electrons from H- beam into collector
H- Beam
Laser
Detector
Bending C-magnet
CST Model

## Slide 19: Laser Wire Intensity Monitor
Larger Detector Option
Smaller Detector Option

## Slide 20: Other Simulation Uses
Electron Beam Profiler
  Tracking of electrons from thermionic gun through proton beam to detector
    Deflector and proton bunch fields
    Deflector is modeled in Poisson (2D)
Proton Beam
Electron beam
Impact parameter
Deflection
Electron beam is deflected by electric and/or magnetic fields of proton beam

## Slide 21: Electron Beam Profiler
Ion Pump
60 keV Electron Gun
Kimball Physics
Pneumatic Beam Valve
Electrostatic Deflector
Ion Gauge
Ion Gauge
Pneumatic
Insertion Device
with OTR Stainless
Steel Mirror
Phosphor Screen
Optical Breadboard
~ 60 cm x 150 cm
Main Injector
beampipe
Optical components box

## Slide 22: Electron Beam Profiler

## Slide 23: IPM at IOTA
IOTA  Integrable Optics Test Accelerator
Accelerator ring designed primarily to study the behavior of a nonlinear integrable lattice
  V. Danilov and S. Nagaitsev, Phys. Rev. ST Accel. Beams 13, 084002 (2010)
The purpose of the nonlinear integrable lattice is to make beam dynamics more robust by generating large stable tune spreads and preserving dynamic aperture
  Studies require monitoring the evolution of the beam profile on short time scales to detect beam growth and instabilities
  Ideally profile measurements every turn

## Slide 24: IPM at IOTA
2.5 MeV, 1011 protons 40 m circumference (30 MHz or 2.34 MHz modulation)
Vacuum needs to be 10-11 Torr
Ionization cross section much higher due to low beam energy
  M.E. Rudd et al., Phys. Rev. A 28, 3244(1983)
  Balances the very high vacuum
Expected number of ionizations per turn is ~18
  Expected number of ionizations per bunch in MI is ~100

## Slide 25: Conclusions
The simulation tool works for not only IPM, but also other tracking needs
  Recently modified solver to use Runge-Kutta method
Questions about gated-off state of IPM
  Where do the electrons go when they reach the edge of the E field region?
    Need 3-D E field calculation (have CST; need time)
    May be difficult to precisely model details

## Slide 26: Extras

## Slide 27: Magnetic Field in Simulation
Measured
Model
0.0004 T
0.0005 T

## Slide 28: Fermilab
Source and Linac
Booster Synchrotron
Antiproton
Accumulator and
Debuncher
Recycler and
Main Injector
Tevatron
n to Nova

## Slide 29: Magnet Measurements
0.002 T
0.004 T
Old Shunt
New Shunt
IPM Active Region

## Slide 30: Magnet Measurements
B Field Line
Maximum Deviation

## Slide 31: Magnet Measurements
B Field Line
Deviation from top to bottom
Average value of 200 mm could be hall probe rotation; corresponds to ~0.1 degrees

## Slide 32: MI Orbit Perturbation
Measured magnet integrated field is
Maximum displacement around the ring for the measured field integral is
For the Main Injector and the maximum is 50 and the tune, , is 0.43