## Slide 1
U. Iriso
ESLS XXIII
Nov. 2015
Impact of vacuum quality in light sources: beam lifetime and ion instabilities
U. Iriso
ALBA - CELLS

## Slide 2
U. Iriso
ESLS XXIII
Nov. 2015
Beam Lifetime
  Analytical description
  Observations in Light Sources
Ion Instabilities
  Analytical description
  Observations in Light Sources
Conclusions
OUTLINE

## Slide 3: Lifetime: Particle Loss in LS
Main Lifetime contributors:
Gas Lifetime:
  Interactions with residual gas nucleus or electrons (elastic or inelastic)
Touschek effect:
  Interactions among beam particles with energy transfer.
Quantum Lifetime:
  Emission of radiation quanta when particles are close to the aperture limitations. Usually negligible, since it is ~1e5h or more.

## Slide 4: Elastic Gas Scattering
Deflections caused by the electrical force of the residual gas atoms
Number of residual particles (pressure): P↑→↓
Particle Charge: Z↑→↓
Beta function. b↑ →↓
Vacuum chamber: A↑→↑
Beam energy: ↑ →↑
gas
Beam
Simplified Eqs*:
Note for LS, e-elast ~ [2-3] orders of magnitude larger

## Slide 5: Inelastic Gas Scattering
Energy loss caused by radiation emission (mostly) at the vicinity of the gas atoms.
Number of residual particles (pressure): P ↑→↓
Charge of every particle: Z ↑→↓
RF acceptance. dacc↑→↑
gas
Beam
RF
Simplified Eqs*:
particle escapes the bucket potential well
Both shall be accounted for LS

## Slide 6: Touscheck Lifetime (I)
Limiting effect in LS (although not in the scope of this workshop)
Due to energy exchange between particles within the bunch, which can bring the particles out of the energy acceptance
It is not exponential, but assymptotic:
t complex expression*, but its main dependencies:
 Product t* Ib = ct , widely used in LS (instead of t)
VRF ↑→ RF acceptance dacc↑→↑
Beam density (coupling, bunch length). r↑→↓
Beam bunch intensity: Ib ↑→↓
*See Piwinsky Equation, Chao’s book

## Slide 7: Lifetime in LS
Lifetime in LS is dominated by Touscheck effect, except in MAX-IV prediction@500mA
Gas lifetime (including elastic & inelastic) only important at early commissioning phases or during installation of new IDs
Soleil: X.N. Gavalda, Phd Thesis
Diamond: I. Martin, priv. communications
ESRF: N. Carmignani, priv. communications
MAX-IV: S.C. Leeman, PRST-AB 12, 120701 (2009) – 500mA

## Slide 8: Gas Lifetime in LS: commissioning
Rule of thumb: Gas lifetime ~100h, when P-avg<1e-9, which is usually achieved after ~100 A*h
At ALBA, this was achieved after ~6 months of operation
D. Einfeld, IPAC11
E. Al-Dmour, XXIV SLS Workshop, 2016

## Slide 9: Installation of new components
Example: Complete Cell exchange in Diamond
Lifetime Product estabilized at ~50A*h
Pressure stabilized >100A*h
Courtesy of M.Cox and I. Martin (Diamond)

## Slide 10: Installation of new components
Example: New Insertion Device (Loreas) @ALBA
~3 weeks to decrease pressure ~1order of magnitude
~2 weeks to stabilize lifetime (from 18h to 24h)
Accumulated Dose: 80A*h
Lifetime
Pressure
3 weeks
a=-0.85

## Slide 11: Lifetime Calculator GUI
Used at ALBA Control Room to crosscheck machine performance
P@CCG, bx,y functions, exy, cross sections, etc calculated on-line --> also tgas & tTouscheck
Pressure~[20- 6]e-9mbar
tgas~ 85h
tTouscheck~30h
tMeasured~22.5h
tcalculated~23h
Example during conditioning of new vac. chamber
Developed by M.Alvarez
GUI – Simple View

## Slide 12: Lifetime Calculator GUI
Used at ALBA Control Room to crosscheck machine performance
P@CCG, bx,y functions, exy, cross sections, etc calculated on-line --> also tgas & tTouscheck
Developed by M.Alvarez
GUI – Expert View: allows you to control/measure all lifetime related params
RF parameters
e-related params
<b*P> params
te-elastic
te-inelastic
tn-elastic
tn-inelastic
Touscheck params

## Slide 13: Controlled pressure bump
Experiment goal: change gas lifetime w.o. varying Touscheck
Switch off Ion Pumps in one sector (out of 16).
NEG pumping on  pressure increase ~1 order of magnitude in the Cell

## Slide 14: Controlled pressure bump
At 50mA, the lifetime difference is only 10% .
At 150mA, the differences are barely noticeable, since Touscheck lifetime dominates
Courtesy of Z. Martí
Lifetime comparison at different beam currents

## Slide 15
U. Iriso
ESLS XXIII
Nov. 2015
Beam Lifetime
  Analytical description
  Observations in Light Sources
Ion Instabilities
  Analytical Description
  Observations in Light Sources
Conclusions
OUTLINE

## Slide 16: Ion Instabilities in LS
Rest gas ionization produced by e-beam generates ions inside vac. chamber
Ions are heavy particles and they usually feel only a sequence of attractive kicks from the bunches, which keep them confined near the beam core
If the ion trapping condition is fulfilled, the ion remains oscillating around the beam
The Ion Instabilities can be either:
  “Ion Trapping Instability” (ITI): multi-turn ion accumulation that degrades beam quality (cured typically with abort gap)
  “Fast Beam Ion Instability” (FBII), the ion production & accumulation occur within one turn, affecting mainly last bunches in the train.
Main consequences: emittance growth, tune shift, pressure rise...
See G. Rumolo and R. Nagaoka talks

## Slide 17: Ion Instability: ion generation
- Rest gas ionization produced by e-beam generates ions inside vac. chamber
~20 ions/bunch/m (ALBA, P=1pbar, sion = 2MB - CO)
Scattering ionization (depends on cross section sion)
Field ionization could also happen above a certain threshold, but negligible in current LS – may be relevant for CLIC Linacs

## Slide 18: Ion Instability: Trapping Condition
G. Rumolo -“Two stream
Instabilities” – USPAS
Transport through the drift space between bunches
Kick from the passing bunch
Bunch i
Bunch i+1
Tb
Ion of mass A

## Slide 19: Ion Instability: Trapping Condition
  Assumed Gaussian beams
  Ions with atomic mass > Acrit are trapped!
ALBA @150mA:
All ions can be trapped!!
It does not affect ALBA due to use of abort gaps and low pressure (~1e-10mbar)
Dependence on lattice position through (sx, sy)
Ion Motion easily expressed in matrix notation:
Stability if Tr(A) < 2:

## Slide 20: Ion Instability: Trapping Condition
  Assumed Gaussian beams
  Ions with atomic mass > Acrit are trapped!
Ion Motion easily expressed in matrix notation:
Stability if Tr(A) < 2:
Calculated with ex = 4 nm (left) and 0.2 nm (right) with SOLEIL parameters (1% coupling)
R. Nagaoka talk
- For low-e rings, Acrit increases

## Slide 21: Ion Instability: Osc. Frequency
From
x = Dx/TB
..
and
We get the ion oscillation frquency:
ALBA Case @150mA in one sector:
Inversely proportional to A
Between ~[10 – 300MHz]
Also depends on s-position
observable with spectrun analyser

## Slide 22: Ion Instabilities: tune shift
CO ions; P=1pbar; sion = 2MB
Nominal operation conditions
Tune shift small, but measurable
Induced tune shift due to focusing force:
An easier simplification from above equation is:
Note:
positive tune shift
For FBII, lion depends on the bunch #, so the tune shift depends on the bunch 3

## Slide 23: Fast Beam Ion Instability - FBII
The ions accumulate along one bunch train
Head and tail of the train are coupled through the ions
Coupled motion between ions & e-beam: ions “keep memory” of the offset of the generating bunch and transfer this information to the following bunches.
The driven oscillation is expected to be at a main frequency related to the ion oscillation frequency.
Raubenheimer et al. Phys. Rev. E 52, 5, 5487, Stupakov et al. Phys. Rev. E 52, 5, 5499
See analytical models at:

## Slide 24: Fast Beam Ion Instability - FBII
Analytical instability models* allow to estimate rise times:
With Ky the focusing strength
*Raubenheimer et al. Phys. Rev. E 52, 5, 5487, Stupakov et al. Phys. Rev. E 52, 5, 5499
This gives rise times ~2us range at ALBA, although coherence effects along the ring can increase this rise times by 1-2 orders of magnitude
Each case needs a careful analysis
Computer simulation codes (FASTION ad PyHEADTAIL**) can be used to carefully calculate these rise times.
**L.Mether, “Numerical model of FBII”, Proc. of HB2016
A.Chaterjee et al, PRST-AB 18 064402 (2015)

## Slide 25: Ion Instabilities Observations
Fast Beam Ion Instabilities observed in LS are produced artificially induced by injecting gas into the vacuum chamber
See examples at ALS & CESR
ALS experiment*:
all Ion Pumps off
Inject He: avg P from 0.25 to 80 nTorr
*J.Byrd et al, PRL 79, 1 (1997)

## Slide 26: Ion Instabilities Observations
Fast Beam Ion Instabilities observed in LS are produced artificially induced by injecting gas into the vacuum chamber
See examples at ALS & CESR
CESR experiment*:
Localized pressure bump of ~10m
Inject Ar and Kr: from 1 to 25 nTorr
*A.Chaterjee et al, PRST-AB 18 064402 (2015)
Beam Size observation
BBB feedback can damp instability
Observations match well with simulations using FASTION

## Slide 27: Ion Instabilities Observations
R. Nagaoka, IPAC’10
Soleil is so far the only LS affected by ions during operation
The beam spectrum for ions dominated instabilities show a distinct pattern wrt usual RW spectrum
RW dominated
Ions dominated
Beam Spectra and Pressure Rise in Soleil
To prevent this instability, Soleil runs with full filling pattern rather than partial filling (lower IB)
This prevents pressure to rise (due to thermal outgassing), and trigger instability
 Not Ion Trapping, but FBII

## Slide 28: Ion Instabilities Observations
Installation of CLIC SL Kicker @ALBA
(Data from 6/3/2017)
While conditioning the new vacuum chamber, injecting from 125mA to 135mA produced a:
-pressure rise: ~3e-8mbar
-beam blow up (by 20%)
-tune shift of 2e-4
-BBB feedback could not damp it
Compatible with ion instabilities in this case produced by larger atomic masses (see next)
DQ = 2e-4
DP: from 4 to 7e-8mbar
Dsy = 5um

## Slide 29: Ion Instabilities Observations
125 mA
135 mA
Installation of CLIC SL Kicker @ALBA
(Data from 6/3/2017)
RGA data showed peaks at A=52 and A=80, likely due to desorption produced by Macor rings
CLIC SL removed to guarantee operation

## Slide 30
Switch off Ion Pumps in one sector (out of 16).
NEG pumping on  pressure increase ~1 order of magnitude in the Cell
Check instability thresholds w. & w.o. pressure bumps
Controlled pressure bump
1pbar = 0.75nTorr

## Slide 31: Controlled pressure bump
Xi = (1,2), threshold ~80mA for both cases
But for normal pressure, the emittance increase is much violent. Co-existance of RW and Ions?
At ~120mA, beam size follows the same trend as the case with normal P
(larger Nb, ions “untrapped”?)
Further studies going-on
 Beam size increase with increasing current with & w.o. pressure bump

## Slide 32
U. Iriso
ESLS XXIII
Nov. 2015
Beam Lifetime
  Theoretical Equations
  Impact on current Light Sources
Ion Instabilities
  Analytical Equations
  Observations in Light Sources
Conclusions
OUTLINE

## Slide 33: CONCLUSIONS
Lifetime in LS is limited by Touscheck effect for machines with doses >100 A*h
Gas lifetime (elastic and inelastic) ~100h, while Touscheck lifetime ~20h.
Gas lifetime only relevant in commissioning periods, or after installation of new components
As a rule of thumb, need in ~100A*h to recover P<1e-9mbar (0.75nTorr)
As for the lifetime…

## Slide 34: CONCLUSIONS
Ion trapping condition is easily fulfill in LS. However, observations of ion instabilities are rare due to a very good vacuum conditions (Pavg < 5e-10mbar) .
Ion instabilities are only relevant in commissioning periods or after installation of new components in the vacuum chamber
FBII have only seen in artificially bad vacuum conditions (injecting Ar gas) and/or switching off Ion Pumps to bring P>10nTorr
Ion instabilities may co-exist with other instabilities (RW) , and active feedback may effectively damp them (CESR) or not (Soleil)
Soleil is (so far) the only machine whose operation is limited by ion instabilities (FBII).
Simulation codes exist (FASTION & PyHeadtail), but more benchmarking is appreciated
As for the ion instabilities…

## Slide 35: Acknowledgements
Many colleagues from ALBA and other labs contributed to this talk:
M. Alvarez, T. Guenzel, Z. Marti, R. Monge (ALBA)
I.Martin, M.Cox (Diamond)
N.Carmignani (ESRF)
X. Nuel (Soleil)
J. Sundberg (Max-IV)
G. Rumolo (CERN)

## Slide 36: Extra slides
http://inspirehep.net/record/846682/files/PhysRevSTAB.12.pdf
S.C. Leeman, Phys. Rev. ST Accel. Beams 12, 120701 (2009)

## Slide 38: Fast Beam Ion Instability - FBII
Analytical model available*
  Instability rise time equations, with & w.o. ion freq. spread along s
Raubenheimer et al. Phys. Rev. E 52, 5, 5487, Stupakov et al. Phys. Rev. E 52, 5, 5499
Lower ε = faster instability

## Slide 39: Elastic Gas Scattering
Deflections caused by the electromagnetic force of the residual gas atoms.
It can be due either by electrons or the nuclei (but the e- part is usually negligible for current LS)
Number of residual particles (pressure): P↑→↓
Particle Charge: Z↑→↓
Beam energy: ↑ →↑
Beta function. b↑ →↓
Beam size: sy↑→↑
gas
Beam
particle loss
Simplified Eqs:
Basic dependencies:

## Slide 40: Inelastic Gas Scattering
Energy loss caused by radiation emission (mostly) at the vicinity of the gas atoms.
In this case, electron and nuclei contributions are accounted
Number of rest gas atoms: P ↑→↓
Charge of every particle: Z ↑→↓
RF acceptance. dacc↑→↑
gas
Beam
RF
Simplified Eqs:
Basic dependencies:
particle escapes the bucket potential well

## Slide 41
Only SR08-CCG3 behaves “as expected” in the whole range.
For CCG1 and 2, after switching off certain pumps, there is a point in which both decrease even though the current increases: this (may) mean that after a certain P, you start the formation of a significant amount of gas ionization (or e-) which affects the pressure readings.