## Slide 1: Injection and optimization
Sabrina Appel, Accelerator Physics Department, GSI, Darmstadt
Notes: Proton Intensity from UNILAC
Expected proton intensity from UNILAC for pbar-chain

## Slide 2: Outline
Multi-Turn Injection
  Single plan multi-turn injection
  Two plan injection
    Skew quadrupoles
    Titled septum
Optimization
  Traditional
  New methods: Evolutionary algorithms
  Sensitivity analysis
X
Y
Septum

## Slide 3: Multi-turn injection (MTI) into SIS18
Measured MTI performance in SIS18
≈20 turns
Trev≈5 μs
Anode
Cathode
300 kV
SIS18 electrostatic injection septum
The beam from linac is injected in horizontal phase space until the machine acceptance is reached
MTI has to respect Liouville’s theorem: Injected beams only in free space
Loss at septum and acceptance should be as low as possible due to loss induced dynamic vacuum
Large frequency difference between UNILAC + SIS18
  During injection the rf is switch of
  Micro bunches filament to costing beam
SIS18 flexibility in providing a broad range of ions allow only Liouvilian injection schemes
Notes: Altitude

## Slide 4: Multi-turn injection into SIS18 (single)
Gain factor (maximize)
Beam loss (minimize)
Inj. emittance (maximize)
Multi-objectives
output
1-2 m
Optimization parameters
Incoming beam
Orbit bump
Injected turns
Horizontal tune
Horizontal emittance
Septum
Model in
simulation code
Horizontal
Constraints: Septum position, acceptance, ...
Notes: Altitude

## Slide 5: Multi-turn injection
Smaller beam emittance increase MTI performance
Available acceptance limited MTI performance
Besides the horizontal phase space, the vertical one can also be exploited, which can lead to higher gain factors
  Titled septum or skew quadrupoles
Single
Two
Emittance
Gain factor
Single plane:
Two plane:
X
Y
Titled septum
G.H. Rees in Handbook of accelerator physics and engineering
Notes: Reachable

## Slide 6: Multi-turn injection (Two plane)
Titled septum
Need new technical development
Titled septum and magnets in transfer line
Coordinate rotation system
Four additional bumpers (vertical)
BRing of
HIARF project
Skew quadrupoles
Using installed skew quadrupoles
Linear coupling of hor. and ver. phase space
Skew strength should be swift off after injection
Which gain factors can be reached for a given beam emittance and loss for SIS18 acceptance?
For conventional, skew and titled septum injection?
Turns
Emittance

## Slide 7: Injector brilliance depending
EMittance Transfer EXperiment (EMTEX)
L. Groening, S. Appel el: Demonstration of Flat Ion Beam Creation and Injection into a Synchrotron, Proc. of IPAC2015
flat beam
round beam
Amount of beam flatness is controlled by solenoid field
Twiss-parameters are preserved
Performance as function of injected emittance
Excellent agreement between simulation and measurement

## Slide 8: Numerical Optimization
The optimization problem is multi-objective
(several criterions to optimize)
The criterions can be contradicting:
Improving one criterion means worsening others
Pareto front:
Find set of optimal solutions instead of single one
Scan
Gradient
Traditional:
Gradient-based methods or parameter scans
Darwin Finches
J. Gould,
Voyage of the Beagle
New methods:
Genetic algorithms, particle swarms are smart parameter scans
A
B
D
C
Imagined
best solution
PA front

## Slide 9: Multi-turn injection into SIS18
Dependence of gain factor on loss
Loss-free injection could be found
Space charge results in a similar PA front, but with different injection settings
Optimization of loss
Genetic algorithms can improve MTI
Especially for longer injection GA discovers a much better solution
Optimization of loss and gain factor
Notes: dependence

## Slide 10: Multi-turn injection into SIS18
Optimization of loss, gain factor and beam emittance (injector)
This crucial information gives more flexibility for the injector upgrade layout.
  Ongoing: For MTI with skew quadrupoles and titled septum
allows to define a frame, in which the required beam parameter can be matched at best for a high performance
Dependence of interface parameter
Notes: dependence

## Slide 11: Skew quadrupoles
With linear coupling the injection loss could reduce from 15% to 1% for n = 20
Emittance development
Coupling parameters:
Limit

## Slide 12: Sensitivity analysis
MTI Parameters has been varied (few percent) and loss has been calculated
Sensitivity of MTI parameters request a online optimization
Probability
Loss [%]
Skew strength
Position at septum
beam size and beam shape
(Missmatch parameter)

## Slide 13: Proposal
1. Online optimization of injection
2. Skew injection
Evolutionary
algorithm
Control settings
Cycle
Current
Evolutionary algorithm available in python, C++, Java, ...
  Require:
    Full online control of all injection parameters
    Online measurement of current (low noise and fast)
Require:
  skew quadrupoles
  freely selectable tunes

## Slide 14
Thank you for your attention

## Slide 15: Sensitivity analysis
Sobol sensitivity analysis determines the contribution of each input parameter (first order) and their interactions between them (total order).
Beam
parameter
Sensitivity
MTI Parameters
Sensitivity of MTI parameters request a online optimization
X
Y
Position at septum
Missmatch parameter determine beam size and beam shape