## Slide 1: Preparing LEIR for the HL-LHC Era
A. Huschauer, H. Bartosik, S. Hancock, V. Kain
Presentation at Space Charge 2017, Darmstadt, Germany
4 October 2017
Space Charge 2017
Acknowledgements to all contributors:
S. Albright, M-E. Angoletta, G. Arduini, J. Axensalva, G. Bellodi, N. Biancacci, A. Blas, M. Bodendorfer, J. Borburgh, C. Carli, G. Franchetti, A. Frassier, S. Gilardoni, D. Küchler, M. Jaussi, D. Manglunki, M. Meddahi, M. Migliorati, M. O’Neil, Y. Papaphilippou, S. Pasinelli, G. Rumolo, F. Schmidt, R. Scrivens, V. Toivanen, G. Tranquille, F. Wenander

## Slide 2: Outline
Introduction
The LEIR intensity limitation
Space charge studies
LEIR performance increase
Summary and outlook

## Slide 3: Outline
Introduction
The LEIR intensity limitation
Space charge studies
LEIR performance increase
Summary and outlook

## Slide 4: The LHC Ion Injector Chain
LHC heavy ion (Pb) physics program
  about one month per year dedicated to heavy ion physics
  ion accumulator ring LEIR to achieve required phase space densities

## Slide 5: The Low Energy Antiproton Ring
Injection/extraction
Line (bi-directional)
Ion
Four 90∘ bending
dipoles
Quadrupole
triplets
Quadrupole
doublets

## Slide 6: The Low Energy Ion Ring
Injection region

## Slide 7: The Low Energy Ion Ring
Electron
cooler

## Slide 8: The Low Energy Ion Ring
Extraction
kickers
RF cavities + magnetic
extraction septum

## Slide 9: LEIR optics functions

## Slide 10: The NOMINAL cycle
RF capture: h=2 and double harmonic
Longitudinal Schottky spectrum of the
debunched beam:
cooling, dragging and stacking
Einj = 4.2 MeV/n
Eext = 72 MeV/n

## Slide 11: Outline
Introduction
The LEIR intensity limitation
Space charge studies
LEIR performance increase
Summary and outlook

## Slide 12: The LEIR intensity limitation – beam loss at RF capture
Beam loss at RF capture before 2015
  Extracted intensity was reported to saturate at 5.9 x 108 Pb54+ ions/bunch (equivalent to 6.4 x 1010 charges)
  Up to 50% of the beam was lost after RF capture and during the first part of acceleration
Proposed actions
  Studying the LEIR intensity limitations in the framework of the LIU project to achieve the HL-LHC goals
M. Bodendorfer

## Slide 13: Loss pattern after RF capture
Achievable intensity at extraction appeared to saturate

## Slide 14: The LEIR working point
Operational working point (Qx, Qy) = (1.82, 2.72)
normal resonances
- - - skew resonances
systematic resonances

## Slide 15: Outline
Introduction
The LEIR intensity limitation
Space charge studies
LEIR performance increase
Summary and outlook

## Slide 16: Variation of the longitudinal density
First hint towards importance of space charge effects due to dependency on line charge density.

## Slide 17: Space charge detuning
  space charge detuning significantly enhanced during RF capture  multiple resonance crossing
coasting beam
bunched beam

## Slide 18: Resonance identification
Tune diagram measurements show strong resonance excitation
  Sextupolar resonances close to the operational working point
  Very limited loss-free region
  Correct tuning of the working point crucial

## Slide 19: Resonance identification with IPM/BGI
Transverse profile evolution
Transverse emittance evolution
Beam intensity
Bare machine working point (cross) and space charge detuning

## Slide 20: Resonance identification with IPM/BGI
  Summary of measurements on previous slide
  Various resonances can be nicely identified

## Slide 21: Flattening the longitudinal distribution
Beams operationally captured using a double harmonic RF system
  Offset the capture frequency away from central beam energy to obtain flat line density profile
  New approach successfully operationally applied at the end of 2016: modulation of capture frequency during bunching to stir beam
capture frequency centered
frequency modulation
S. Hancock
S. Albright
capture frequency offset

## Slide 22: Resonance compensation
  Resonance compensation was systematically studied using the available sextupoles
  Certain pairs of sextupoles allow to compensate the resonance Qx + 2Qy = 7
  Also attempted to (rather unsuccessfully) compensate skew resonance 3Qy = 8
Polar scans of sextupole strength to determine maximum beam survival

## Slide 23: Resonance compensation
compensation ON

## Slide 24: New LEIR optics
Drastic change of the working point to avoid excited resonances
Limited flexibility of the lattice due to various optics constraints:
  injection efficiency
  cooling efficiency
  vertical aperture restriction at the bends

## Slide 25: New LEIR optics
  vertical aperture restriction at entrance and exit of main magnets
   no problem per se if blow-up can be reduced

## Slide 26: New LEIR optics
Tune scans show significantly improved resonance-free area compared to nominal optics

## Slide 27: Outline
Introduction
The LEIR intensity limitation
Space charge studies
LEIR performance increase
Summary and outlook

## Slide 28: Comparison early 2015 – end of 2016

## Slide 29: Outline
Introduction
The LEIR intensity limitation
Space charge studies
LEIR performance increase
Summary and outlook

## Slide 30: Summary and outlook
Remarkable performance improvement of Linac3 and LEIR since 2015
  LHC Pb-Pb design luminosity surpassed by a factor 3
  LHC p-Pb design luminosity surpassed by a factor 8
  Achieved record intensity of > 10 x 1010 charges at extraction
LIU/HL-LHC beam parameters have already been achieved at LEIR extraction
  Only minor hardware modifications necessary to achieve this milestone
  Additional work remains to be done in the other machines
Major remaining challenge: maintain high performance of LEIR and reduce sensitivity to machine settings
  Exploit resonance compensation, improved longitudinal setup, new optics, …

## Slide 32: Mitigation measures implemented

## Slide 33: Iso-adiabatic RF capture

## Slide 34: Disentangling the effect of the ramp and RF capture
  RF capture advance by few 100 ms
  Same loss characteristics  not related to the magnetic ramp
  Drastic vertical blow-up observed at RF capture
vertical beam profiles

## Slide 35: Resonance identification
Static tune scans using low intensity / small tune spread
  Tune at injection kept constant to preserve injection efficiency
  Working point moved during electron cooling period to reduce losses when crossing resonances

## Slide 36: Resonance compensation
Reduced strength of sextupoles after last injection
  Clear beneficial impact on resonance excitation and beam loss
standard sextupole settings
improved sextupole settings