## Slide 1
PS Studies
Space Charge Workshop 04/10/2017
F.Asvesta, H.Bartosik , A.Huschauer, Y.Papaphilippou, M.Serluca, G.Sterbini

## Slide 2: Overview
Motivation
Frequency Map Analysis
  On-momentum particles
  Off-momentum particles
Machine Development and Simulation Studies
  Vertical Tune Scans (space charge dominated)
  3rd Order Skew Resonance Compensation
  Vertical Tune Scans (non- space charge dominated)
Summary

## Slide 3: Motivation
Limitations towards the LIU goals for the PS performance connected to space charge:
Vertical integer resonance
The 8th order structural resonance (S. Machida, R.Wasef et.al).
Space charge tune spread in the PS
for LHC-type beams.

## Slide 4: Frequency Maps
Tracking on-momentum particles under the influence of space charge using the Py-ORBIT Frozen model
Tunes of individual particles
calculated over one synchrotron period
Diffusion:
Working Point
Resonance lines up to 8th order
Initial position in the transverse plane of the tracked particles

## Slide 5: Frequency Maps
Tracking off-momentum particles under the influence of space charge using the Py-ORBIT Frozen model
More particles trapped by the resonances due to the periodic crossing
Excitation of all the 8th order structural resonances

## Slide 6: Frequency Maps
Tracking off-momentum particles with the same longitudinal action () for
Particles initialized with the same initial longitudinal position and 0
Losses increase in steps since the particles cross the resonance at the same time in their synchrotron motion
Losses increase as we increase the number of turns since particles crossing the resonance gradually gain amplitude reaching the mechanical aperture
Longitudinal Phase Space

## Slide 7: Machine Development and Simulation Studies
Machine Studies
  Single Bunch
  Coupling Corrected
    In operation is enhanced to damp horizontal head tail instability
  Transverse Feedback ON
    In operation OFF
Simulation Studies
  PS non-linear lattice
    higher order multipoles from pole face windings in the main magnets
  Space charge frozen model
    electric field calculated for bi-Gaussian distribution using Bassetti Erskine formula

## Slide 8
Vertical chromaticity corrected
Vertical Tune Scan
4th / 8th
4th (skew)/ 8th
4th / 8th
3rd (skew)
4th / 8th
4th (skew) / 8th
4th / 8th
3rd (skew)
  Simulation for
  Experimental Data ( storage)
Discrepancy between measurement and simulation especially in terms of losses
Other resonances excited?

## Slide 9: 3rd Order Skew Resonance
Calculation of the resonance driving terms using PTC for the available skew sextupoles.
Various configurations of the sextupoles were tested while the resonance was dynamically crossed using a beam with a space charge tune spread .
Evaluating the beam losses in the time period of the tune change the best configuration for the resonance compensation was selected.
A vertical tune scan using an LHC type beam with a typical space charge tune spread of .
3rd (skew)
Losses are reduced close to the
but come to a second maximum as the tune is further increased
More resonances excited?

## Slide 10
Natural Chromaticity
3rd order skew resonance compensated
Vertical Tune Scan
3rd (skew)
4th / 8th
4th (skew) / 8th
4th / 8th
3rd
  Experimental Data ( storage)
4th / 8th
4th (skew)/ 8th
4th / 8th
3rd
3rd (skew)
  Simulation for
4th / 8th
4th (skew)/ 8th
4th / 8th
3rd (skew)
3rd
Simulation for 2% max Octupole excitation
Remnant fields from the octupoles used in some PS operational cycles (Multi Turn Extraction) seem to explain the behavior
Could degaussing of the octupoles reduce the losses?

## Slide 11
Machine Studies
  The effect of the 8th order structural resonance has been studied in terms of losses, emittance variation and profile evolution
  The resonance naturally excited in the PS, has been compensated using skew sextupoles
  The 4th order is also excited possibly due to the presence of remnant fields in the octupoles used during operation
Simulation Studies
  The full PS flat bottom has been simulated using the Py-ORBIT frozen model
  The simulation results cannot fully replicate the experimental data especially in terms of losses
Further studies
  Stability issues for high vertical tunes (Transverse Feedback)
  Degaussing of the octupoles used in operation
  PS model and simulation tools optimization
Summary & Outlook
Thank you for your attention

## Slide 12: Back up

## Slide 13: Resonance crossing

## Slide 14: Single Particle Tracking

## Slide 15: Vertical Beam Profiles
  Simulation for
  Experimental Data ( storage)

## Slide 16: Vertical Beam Profiles
Vertical
Profiles
Horizontal
Profiles
  Experimental Data ( storage)
Vertical
Profiles
Horizontal
Profiles
Simulation for 2% max Octupole excitation

## Slide 17
Resonance driving terms for the MTE octupoles
PS39
PS55
ODs
()