## Slide 1
Rob Ainsworth
Space Charge 2017
4th October 2017
Multi-bunch space charge effects for Slip-stacked beam in the Recycler

## Slide 2: Outline
Accelerator complex
    Slip-stacking
    PIP and beyond
Synergia
Simulations
    All plots presented are simulations (with exception of last one)
Summary

## Slide 3: Accelerator complex
H- linac
Booster
  h = 84
  15 Hz
  400 MeV -> 8 GeV
Recycler
  h = 588
  Slip-stack 12 batches (double bunch intensity)
Main Injector
  8 GeV -> 120 GeV

## Slide 4: Slip-stacking
Slip-stacking allows us to double the intensity of the bunches in the Recycler

## Slide 5: Power evolution
PIP
    700 kW (~0.5 x 1011 ppb)
    15 Hz Booster
    80 kV RF for recycler
    1260 Hz separation for slip-stacking
PIPII
    1.2 MW (~0.8 x 1011 ppb)
    20 Hz booster
    140 kV RF for recycler
    1680 Hz separation for slip-stacking
PIPIII
    2.4 MW
    No more slip-stacking, most likely replace booster with new RCS

## Slide 6: Synergia
Self-consistent 3D Particle-in-cell accelerator simulation C++ code
Specifically to simulate collective effects in accelerators
Designed from the beginning to run on large parallel computing systems (but it doesn't have to)
Library of Objects which are combined to create a simulation
Lattice, Bunch(es), Diagnostics (bunch measurements), Collectives, Propagation scheme, all under programmatic control
One or two co-propagating single bunch or multi-bunch beams
Simulations are python scripts (not another special purpose language)
Collective effects included with split-operator formalism:
Space Charge (validated with GSI space charge benchmark, multiple models)
Impedance (per-element) within bunch and bunch-to-bunch, γ < ∞ for boosters
Single Particle Optics (full tracking or polynomial approximation)
Magnets, RF cavities, Drifts, Apertures, Septa
Simulation parameters may be dynamically controlled throughout execution by altering the state of the simulation objects (ramping of accelerator elements)
Combine most suitable algorithms in each area for a complete simulation.

## Slide 7: Synergia
Synergia contains an internal test suite that verifies the correct operation of most modules. Particle tracking is verified with MAD-X/PTC and analytic calculations. Space charge kicks are verified with analytic calculations. Particles are labeled.
Synergia is actively used to model all of our circular machines:
Recycler, Main Injector, Booster, IOTA, Debuncher
Synergia is developed by the Acceleration Simulations Group within Fermilab’s Scientific Computing Division and is publicly available.
J. Amundson, P. Lebrun, Q. Lu, A. Macridin, L. Michelotti, C. S. Park, E. Stern, T. Zolkin.
https://web.fnal.gov/sites/synergia

## Slide 8: Recycler simulations - inputs
Realistic longitudinal distribution from tomography
Transverse distribution matched but using measured beam sizes
MAD8 input file
Using apertures, orbit bumps,

## Slide 9: Recycler simulations
Filament
50ms
Decelerate
1260Hz
50ms

## Slide 10: Space charge footprint

## Slide 11: Footprint vs turn
Mean of the footprint
Std of the footprint

## Slide 12: Effect on emittance

## Slide 13: Tunes + Chromaticity
Lower tunes
worsens growth
as expected
Higher Chromaticity
also increases growth
in general
Off-Momentum sees
slight improvement due
shift from chromaticity

## Slide 14: PIPII
80 to 140 kV
Separation
increased
from 1260
to 1680 Hz
15 Hz to 20 Hz

## Slide 15: Phase-offset
Base case
with
1.5ns
injection
offset
PIPII case
with
1.5ns
injection
offset

## Slide 16: Single bunch vs Slip-stacking
Compared single bunch double intensity with slip-stacked case
Tune shift bigger for longer in single bunch however, more tune space available without off-momentum bunch
Need to see when SS case begins to saturate

## Slide 17: Conclusions
As intensity increases, the space charge effects from slip-stacking result in emittance growth during the overlaps
PIP-II parameters help longitudinally (less uncaptured beam) however, the transverse growth is the same.
The effects can be minimized by optimizing the tunes and using an injection phase offset

## Slide 18: Next steps
81 bunch on 81 bunch simulation to determine when saturation occurs
Investigate resonance compensation of the 3rd to open up the tune space

## Slide 19: Back-up