## Slide 1: Rf-Cavity Design of the new FAIR post-Stripper Linac
Xiaonan Du, Linac-Department

## Slide 2
Introduction to UNILAC
Requirements to new post-stripper
Basics: shunt-impedance and time-transient factor
New drift tube shape design
Design of DTL cell lengths
Field stabilization
Outline:

## Slide 3: UNIversal Linear Accelerator UNILAC
pre-stripper HSI
(Hoch-Strom-Injektor)
acceleration to 1.4 MeV/u
post-stripper
acceleration up to 11.4 MeV/u
single-gap
resonators
energy fine tuning
stripper
increase q
sources and LEBTs
2.2 keV/u
RFQ
120 keV/u
IH-DTL
1.4 MeV/u
U4+ → U28+
Alvarez-DTL
3.6 / 4.8 / 5.9 / 8.6 / 11.4 MeV/u
6 SGRs
|ΔE| ≤ 5*(q/A) MeV/u

## Slide 4: Today‘s post-Stripper DTL
Alvarez tanks A1, A2a, A2b in operation since > 40 years
25 years expected lifetime
drift tubes are obviously damaged
copper plating shows bubbles & bumps
resources for maintanance increase rapidly

## Slide 5
DTL quadrupole strengths cannot deal with high intensity uranium beams for FAIR
To operate FAIR, the replacement of the post-stripper DTL is mandatory
Today‘s post-Stripper DTL

## Slide 6: Requirements to Upgraded UNILAC
ion A/q | ≤ 8.5, i.e. 238U28+ | 
beam current (pulse) * A/q | 1.76 (0.5% duty cycle) | mA
input beam energy | 2.2 | keV/u
output beam energy | 3.0 - 11.4 | MeV/u
normalized total output emittance, horizontal/vertical | 0.8 / 2.5 | mm mrad
beam pulse duration |  1000 | µs
beam repetition rate |  10 | Hz
operating frequency | 36.136 / 108.408 | MHz
length |  115 | m
design parameters after upgrade
main task of UNILAC is to serve as injector for FAIR
all ions with A>1 will pass the UNILAC`s post-stripper DTL

## Slide 7: Choice of “Alvarez“ Technology
several design options were proposed
they were systematically evaluated and benchmarked
decision process was defined by directorate and accompanied by external Committees
the decision was taken to chose the “Alvarez“ technology
the other options did not meet FAIR requirements w.r.t. beam quality, budget restrictions, maturity of technology

## Slide 8: Basics I: Shunt Impedance
cavity modeled by “lumped circuit“
beam
beam
inductivity
Ohmic losses (surface currents)
is “shunt impedance“
R: the higher, the better !!
external rf-power source providing:
compensation of Ohmic losses
energy gain of particle beam

## Slide 9: Basics II: Time-Transient-Factor TTF
TTF accounts for the finite time of particle transition through the gap
TTF
Ez: the acceleration field
Ez*cos(PI*z/L): the effective acceleration field
Integral of red curve
(effective voltage)
Integral of green curve
(voltage)
Lg
Lc
one “cell”
energy gain:

## Slide 10: New Cavity Design
Compared with existing cavities
new & advanced design tools
optimized drift tube shape
novel field stabilization scheme
improved manufacturing technology

## Slide 11: Drift Tube Shape Design
at corners with large curvature of the surface,
the surface field is higher w.r.t. the nearby area
→ optimized shape design with CST-MWS
irregular surface of the copper under microscope, there are metal whiskers and protruding on which the surface field is much higher than at nearby surfaces
→ need high surface quality with Cu-plating
the tube must provide for sufficient gap voltage w/o dark currents and/or HV-sparking
→ optimized shape design with CST-MWS

## Slide 12: Shape Design
the re-designed tube shape produces a homogeneous surface field
Former shape
new shape
tube shape profile for the five tanks
It is possible to design an individual shaped curve for each tube, but it is not mandatory:
entrance cells have highest Epeak in one cavity
one tube shape is suitable for others with similar cell length
unified tube shapes reduce the fabrication cost

## Slide 13: Shape Design: Curvature is the Key
θ to be reduced
180
create the curve that connects smoothly the inner and outer radii of the tube:
build tube with this curve and evaluate the surface field along this curve.
adjust this curve according to the field.
θ(n-1)
θ(n)
ds

## Slide 14: Two Options to Profit from new Shape
profit from this improvement: lower Epeak per shunt impedance
keep the peak surface field (Epeak) as today (1 Kilp.) and get 12% more shunt impedance (preferred)
keep shunt impedance as today and reduce Epeak by 17%, further reducing the break down probability
design options:

## Slide 15: Beta Profiles design Boundaries
Boundaries from Rf-Alimentation:
amplifiers reliably provide 1.35 MW (Pmax) power for every tank after few reflection and safety margin(1.8MW-1.35MW)
rf-power loss of the cavity from simulation : Ps ( 0.85 MW e.g.)
rf-power loss for real cavity with 20% lower Q factor w.r.t. simulated Q: Pr=Ps/0.8
beam power increase Pb (0.3 MW e.g.)
all cavities were designed with the boundary Pr + Pb ≤ Pmax
Other boundary conditions:
average accelerating field ( ≈ 2 MV/m )
maximum surface field ( ≈ 1 Kilp.)
input/output energy(1.4 /11.4 MeV)
total length (fit into existing tunnel, about 55 m)
constant tank diameter (1.8 m - 2 m)

## Slide 16: Beta Profiles
design of beta profile using CST-MWS to:
obtain accurate TTF from simulation instead from approximate formula
plug rf-parameters into the design process
Basic beta profiles design by analytical approach:
input energy → first cell---------------
get TTF with approximate formula -
calculate energy gain -----------------
calculate speed increase ------------
info for second cell --------------------
......
Advanced design method is combined with rf simulation

## Slide 17: Beta Profiles
prepare the universal flexible model of single cell (figure on right side).
loop>>>
assume the beta increase after this cell : Δβa(n)≈ Δβ(n-1)
calculate the cell length for this cell: Lc(n)=(β(n)+Δβa(n)/2)λ
  use average beta. could be more accurate if use particle tracing
  Δβ(n-1) is β increase of last cell, β(n) is input beta of this cell
update model with this cell length and guessed Lg/Lc
run the automatic optimization
  optimize Lg/Lc to get 108.4 MHz local frequency, the maximum Esurf will not be exceeded in first gap.
store results
  geometric and RF parameters of every cell is stored .
use output beta as input beta of next cell (β(n+1)).
end loop<<< If βmax or cell number or total power limit achieved.
βλ
(β+Δβ)λ
Lg
model of single gap

## Slide 18: All beta Profiles available
parameter list:
cell number
cell lengths
input energy
input beta
Veff
Zeff
TTF
Epeak(surface)
local frequencies (108.408 MHz)
power loss
total power (include beam power)
Lg / Ltube
tube shape curve for this cavity
...

## Slide 19: Summary of Latest Design
Design V5 | tank I 20160713 | tank II 20160713 | tank III 20160713 | tank IV 20160713 | tank V 20160713
energy [MeV/u] | 1.392 – 3.316 | 3.316 – 4.351 | 4.351 - 6.621 | 6.621 – 8.966 | 8.966 – 11.341
apperture radius [mm] | 15 | 17.5 | 17.5 | 17.5 | 17.5
rf-phase [deg] | -30 | -30 | -30 | -25 | -25
# cells | 55 | 20 | 43 | 35 | 31
Lgap / Lcell | 0.27 | 0.27 – 0.28 | 0.23 – 0.25 | 0.22 – 0.23 | 0.22 - 0.23
rf-length [m] | 10.54 | 4.99 | 12.78 | 12.41 | 12.53
Esurf,max [EK] | 1.00 | 1.00 | 0.96 | 0.98 | 0.96
Ploss,MWS [MW] | 0.885 | 0.555 | 0.870 | 0.842 | 0.853
Pbeam [MW] | 0.245 | 0.132 | 0.289 | 0.299 | 0.303
<Zeff> [MΩ/m] | 28.67 | 27.95 | 33.48 | 38.02 | 38.13
Eeff,mean (MV/m) | 1.55 | 1.76 | 1.51 | 1.61 | 1.61
Q | 115968 | 113382 | 118403 | 116668 | 114150

## Slide 20: Need of Field Stabilization
Magnetic field of TM010
TM011
TM012, TM013....
The modes of Alvarez cavity in ideal case (simulation)
in the real cavity the accelerating field from the operational mode may be disturbed by different kind of perturbations
if gap error occurs somewhere, the field of the entire cavity will be disturbed. The field deviation comprises fields from other modes
sources of perturbations:
mechanical errors
heat deformation
tuners, couplers
ports on the cavity wall
beam loading
dark current between gaps
alignment errors
...

## Slide 21: Stabilization: Equivalent Circuit
how does the current flows inside an Alvarez cavity? answer: along three transmission lines
standing wave solution:
differential equation for voltage:
about field
about frequencies
X. Du, et al., Phys. Rev. Accel. Beams 20, 032001 (2017)

## Slide 22: Stabilization: Use Stem Orientation
The key is to locally adjust the stem configuration until
transverse admittance (Y) along z axis as small as possible
section by section simulation and adjustment until
frequency of TE010 mode is modified to 108.4 MHz.
(a): current path inductance Ls; (b): capacitance C from the electric field between tank wall area (red) and drift tube area (blue)
designed stem configuration E with section by section simulation

## Slide 23: Stabilization: Use Stem Orientation
for operational mode Y (f = 108.4 MHz) ≈ Y ( f= 109 MHz) ,
If we adjust the field distribution of TM011(109MHz) mode to two flat sections (slope of field depends on Y) ,
Y (f = 109 MHz) could be minimized
Y (f = 108.4 MHz) may also be close to zero.
rotating one of the stems towards the lower side of the cavity will reverse the field slope. Choice of specific stems to be rotated will change cosine-type field distribution towards step function.
→ slope is cancelled by small Y
electric field map of original TM_011 field
designed stem configuration M with step function field

## Slide 24: Stabilization Scheme verified by CST-MWS Simulations
if the field is stabilized :
acceleration field is more stable
mode frequency of TM011 pushed away form operational mode (108.4 + 4 MHz)
slope of dispersion curve is increased
mode frequency of TE010 mode very close to 108.4 MHz
not stabilized:
stabilized:

## Slide 25: 1:3 Scaled Model Cavity
model Alvarez-cavity was built to measure the novel stabilization scheme (A. Seibel)
1154 mm
X. Du, et al., Phys. Rev. Accel. Beams 20, 032001 (2017)
A. Seibel et al., IPAC 2015, THPF027

## Slide 26: Summary and Outlook
rf-design of new post-stripper DTL available
all input for beam dynamics design available (see talk of A. Rubin on June 8th, this seminar)
new drift tube shape with improved shunt impedance
novel scheme of field stabilization
Alvarez-prototype with 11 drift tubes and a total cavity section length of 1.9 m will be manufactured and tested at nominal rf-power (talk of M. Heilmann on June 22nd, this seminar)
Thank you!