## Slide 1: The Cluster-Jet Target Gas System and Beam Adjustment Status
PANDA Collaboration Meeting 2017/2
Benjamin Hetz
Institut für Kernphysik
WWU Münster

## Slide 2: Status of the Cluster-Jet Target Gas System
Status at last meeting was:
  No stable cluster jet beam with liquid hydrogen in front of the nozzle
  Recurring nozzle clogging
  Broken Baratron due to metallic particles inside the gas system
time / min
Intensity/ arb. u.
Optical Monitor System

## Slide 3: Status of the Cluster-Jet Target Gas System
Status now:
  Spare hydrogen purifier
    max. pressure 17 bar
    no highest thicknesses until now (7 x 1014 atoms/cm2)
  Stable cluster beam
But still some nozzle clogging problems

## Slide 4: Status of the Cluster-Jet Target Gas System
Investigations on nozzle clogging problems:
  Intrinsic nozzle problem?
    Multiple alternative nozzles available which already showed similar thickness distributions
  Impurities from broken purifier?
    Exchange of whole gas supply system might be required
Both options in preparation

## Slide 5: Beam and Beam Line Adjustments
Pressure in collimator chamber a decade too high
  Skimmer-Collimator adjustment needed
  Check of effective pumping speed at collimator chamber
Beamline adjustement needed
  Monitor systems show not perfectly aligned beam
  Necessary for significant information about vacuum condition

## Slide 6: Beam and Beam Line Adjustments
Beamline adjustemts done by 4 level feet
  Coarse adjustments done
  Second fine adjustments done, but:
    Support frame to soft
    Cluster-jet source currently misaligned
Level Foot

## Slide 7: Investigations using the Optical Monitor System (OMS)
OMSset into operation by a former bachelor student
Located at Transition Vacuum Chamber
New bachelor student investigates relation between relative OMS information and absolute thickness information by moving rod system
Beam Direction

## Slide 8: Investigations using the Optical Monitor System (OMS)
Day 1
Day 2
Day 3
Stable beam conditions (moving rod system)
OMS data scaled to be comparable
Day 3 distribution of OMS scatters due to tests of optimal exposure time and other camera settings
T = 24 K, p = 15 bar

## Slide 9: Investigations using the Optical Monitor System (OMS)
First calibration results are promising
T = 24 K, p = 15 bar

## Slide 10: PANDA target @ COSY
Due to mentioned problems with the gas system:
  Minor delay in calibration and optimization studies at Münster
  Installation at COSY probably shifted to end of autumn/winter 2017
  First beam time slot in 2018

## Slide 11: Next Steps
Solve nozzle clogging and gas system problems
  Approches shown
Investigate and optimize vacuum conditions
Investigations of target thickness monitoring using the optical monitor system
  Signal intensity behaviour by different target stagnation conditions
  Matching with absolute thicknesses by moving rod system