## Slide 1
MESA Linac Module @ bERLinPro
Joint Accelerator Research JGU & HZB
“SRF Cryomodule testing for electron
accelerators under beam conditions”

## Slide 2
due to civil construction time accelerator construction can start end 2020
Picture: D. Simon
 | Basic Parameter
max. beam energy | 105 MeV (ERL mode) 155 MeV (external beam)
max. current in ERL operation | 1 mA (later 10 mA) (0.77-7.7 pC/bunch)
Number of recirculations | 2 (ERL mode) 3 (external beam)
MESA – Mainz Energy Recovery Superconducting Accelerator

## Slide 3
Picture: HZDR
Cryomodules of the 'Rossendorf'-type (2 x 9-cell TESLA/XFEL cavities), which are in use at ELBE will be used for MESA
→ we applied some adaptations in order to allow 1 mA ERL operation:
added tuners with piezo elements (XFEL/Saclay-type)
used sapphire windows at HOM feedthroughs
→ beam current of 10 mA may not be achievable with that type of cryomodule
Just today: String assembly successfully completed
2 modules will be tested at Mainz fall 2017 till spring 2018
MESA Cryomodules

## Slide 4
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell srf cavities
44 MeV
modified Cornell booster
3 x 2 cell srf cavities
4.5 MeV
srf-gun
1.4 cell srf cavities
1.5-2.3 MeV, single solenoid,
merger
dogleg
test and diagnostic line
(5mA@10MeV dump,
energy & slice diag.)
bERLinPro = Berlin Energy Recovery Linac Project
100 mA / low emittance technology demonstrator (covering key aspects of large scale ERL)
 | Basic Parameter
max. beam energy | 50 MeV
max. current | 100 mA (77 pC/bunch)
normalized emittance | 1 mm (0.5 mm)
bunch length (straight) | 2 ps or smaller (100 fs)
rep. rate | 1.3 GHz
losses | < 10-5
bERLinPro – Berlin Energy Recovery Linac Project
project started 2011, fully funded
building ready 2017
first electrons 2018
recirculation 2019/2020

## Slide 5
bERLinPro – Building / Infrastructure / Accelerator
Position to integrate
MESA Linac Module
(5m free space available)
MESA Cryomodule
(modified ELBE type)

## Slide 6
MESA Cryo Module @ bERLinPro – Research Program
Cryo & RF Qualification without beam
Detailed HOM studies
Test and comparison of different LLRF systems (uTCA based bERLinPro ↔ MESA)
Study of BBU threshold currents in the mA range, comparison of simulations and beam tests)
Study of BBU mitigation techniques (phase advance tuning, chromaticity, …)
Verification of calculated / measured HOM spectra with beam driven spectra in a wide range of parameters (average current, peak current, pulse length)
Beam tests of LLRF systems under different operation condition (cw, variable pulse trains, transients, …)
Beam dynamics studies with respect to achievable parameters space in terms of emittance, bunch charge, pulse length
Studies of beam halo and unwanted beam
Studies of Energy Recovery Efficiency at mA beam current level
Studies of Energy Recovery with “internal target” mock-ups (energy width, emittance increase, …)