## Slide 1: Status of MUCH Electronics
J. Saini, VECC, Kolkata

## Slide 2: Final Layout of CBM-MUCH readout to be used at FAIR
DPB board
DCS
DPB board
DCS
MUCH-Detector
FEE
FEE
FEE
FEE
GBTx
GBTx
DPB board
DCS
FLIB
FLES
Experimental cave
Green Cube
ECS
Control Network
Timing Network
120m
FLIB
CRI-Board
Low Voltage Distribution
High Voltage Distribution
Temperature and Gas flow Control units

## Slide 3: Present Layout of CBM-MUCH readout Chain for testing in India
DPB board
DCS
DPB board
DCS
MUCH-Detector
FEE
FEE
FEE
FEE
GBTx
DPB board
DCS
FLIB
FLES
Switch (IP Bus)
Control Network
Timing Network
Dual gain
STS/MUCH-XYTER
GBTx
Low Voltage Distribution
High Voltage Distribution

## Slide 4: Test setup at VECC
STS/MUCH-XYTER FEB-B based setup is ready for testing at VECC
Present chain is with TP-link media convertor based setup
First integration with GEM detector was done
Calibration of FEE is ongoing and we are facing major issues while calibrating this FEE board

## Slide 5: Setup at VECC
DAQ Machine with FLIB board
LV Distribution Board
AFCK Board with one gDPB and one nDPB FMC
AFCK with tDPB FMC
MUCH/STS-XYTER FEB-B
4-channel LV supply with each 300W channel output
TP-Link and Switch for IP-Bus

## Slide 6: First integration of GEM with MUCH-XYTER test result of VECC setup
Beam spot with Sr90 source
Photos Courtesy “Anand ji”

## Slide 7: Few STS/MUCH-XYTER calibration results from the test setup at VECC
Calibration done by internal pulser is not validated by external pulser
Calibration value calculated with internal and external pulser are giving same results
Online register update v/s offline register update are giving different results
V-ref_P and V-ref_N were varied to see the effect. Threshold changes but effect not stable.
Either initializing procedure or the chip setting is a problem. More results will be discussed by Gitesh in next presentation.

## Slide 8: Other Electronics development status at VECC for GEM-MUCH detector
MUCH specific FEE board
FMC’s for ROB-3 board for mCBM setup
Station-1 chamber PCB
Station-2 chamber PCB
HV distribution for GEM detectors
LDO’s for STS and MUCH detectors

## Slide 9: MUCH specific FEE board
Two ASIC design schematic ready
  Basic features of the FEE board
    64-channels per ASIC will be used
    2-uplink per ASIC and common clock and downlink for both the ASIC
    Size of maximum 11cms X 3.5cms
    Layout will be made considering new LDO’s from SCL Chandigarh
Layout work will start soon…!!!

## Slide 10
Illustrative figure for MUCH-XYTER based front end board
10cms
3cms

## Slide 11: Issues with ROB-3 FMC design
Till now link confusion is still going on to whether to use 6-FEE per ROB3 or 9-FEE per ROB3 as missing downlink and clock
We have total 42 uplinks, 8-downlinks and 8-clock while to use 9 independent FEE board it requires 9-downlinks and 9-clocks.
Wojtek suggested other lines on ROB-3 can be configured as downlink and clock (may be better then line jump over FEE’s)

## Slide 12: FMC’s for ROB-3 board for mCBM setup
Preliminary ROB-3 design is already received from Joerg Lennart
Preliminary FMC design received from Jochen Fruehauf
Design yet to get started at VECC.
Very urgent needs to get started soon…!!!

## Slide 13: Chamber PCB active region size
Slide From Ekata

## Slide 14: Station-1 chamber PCB
There were few errors in the last design so new design is ongoing
Parallel purchase procedure is started from Bose Institute to minimize time delays
Layout at very preliminary stage needs to gear up to meet the timeline of mCBM else we only have two M2 modules with bad sectors…!!!

## Slide 15: Station-2 chamber PCB
Basic pads are made in the layout
Boundaries are identified for FEE placements
Right now no idea of the technologies as communicating to vendors is still ongoing…!!!

## Slide 16: HV distribution system for CBM-MUCH-GEM detectors

## Slide 17: HV Segmentation on Drift PCB
It is a two layered PCB. For station 1 size is mentioned above. Thickness of this PCB is 3.2mm. This PCB contains both high and low voltage tracks

## Slide 18: Test Results of opto-coupler
Passed the Neutron dose test done at BARC-Mumbai which is required at 1meter away from beam line at MUCH station-1
Passed the required TID tests done at IUC-Kolkata.
Passed the basic tests along with detector performed with both 10cms X 10cms and final sized sector shaped detector for station-1

## Slide 19: Radiation hard LDO’s first prototype received from SCL Chandigarh
LDO delivered by SCL Chandigarh
Test circuit prepared by Piotr
LDO’s in the beam-line at COSY
Radiation hardness test was done by Piotr Koczon and group.
Three LDO chips have been irradiated with 2 GeV protons
and survived 4x1013 /cm2 (fourth board broken in preparation)

## Slide 20: Initial Prototypes received at VECC having desired current values
Two prototype meeting final electrical specifications were delivered to VECC i.e.
1.8 V / 1.6 A 1.2 V / 1.6 A

## Slide 21: Electrical test results
1.2V LDO was giving very good noise performance as compared to any other commercially available low noise LDO’s
These LDO’s showed good performance even on hanging arrangement made for the connections.
Radiation tests yet to be performed on these LDO’s

## Slide 22: Thank you for attention…!!!!