## Slide 1: Status of the PANDA Cluster-Jet Target Quarter 1/2018
PANDA Collaboration Meeting 2018/1
GSI Darmstadt, Germany
Benjamin Hetz
WWU Münster
Institut für Kernphysik
WWU Münster

## Slide 2: Long Term Stability of the PANDA Cluster-Jet Target
Stable cluster-jet beam:
  Using “designated” PANDA nozzle candidate
  Replaced broken H2 purification and gas system
      Solved exceptional nozzle clogging problems
  Thickness @ PANDA IP (optimization ongoing)
Setup in next to PANDA geometry and hardware configuration
Camera X
Camera Z
Skimmer
Skimmer
Jet Beam Direction

## Slide 3: Cluster-Jet Beam Monitor Systems
Absolute thickness monitor system (AMS)
  Absolute thickness information
  Destructive system (using moving rod through jet beam)
Optical monitor system (OMS)
  Relative thickness information
  Non-destructive system (using scattered light)
Both system yield information about:
  Jet beam thickness
  Jet beam width/form
  Jet beam stability
  Jet beam position in beamline
Needed for optimization of
  Target thickness
  Target alignment
  Accelerator beam line/interaction point vacuum

## Slide 4: Refined Absolute Thickness Monitor Systems (AMS)
First AMS at scattering chamber for automatic beam measurements
  “Jet beam stability”
Second simple, manual AMS
  Located at PANDA interaction distance
  “Thickness/vacuum optimization”
Third possible, manual AMS in preparation by our mechanical workshop
  Located at beam dump inlet
  “Perfect jet beam adjustment”
Drawback: destructive monitor system
in preperation
installed
installed
Automatic Absolute Thickness
Monitor System
rod position

## Slide 5: Refined Optical Monitor Systems (OMS)
Advantage: non-destructive System
Matched optical, relative thickness to absolute thickness monitor systems
  proportional response
OMS suited for target beam monitoring at PANDA without influence on jet beam/vacuum conditions
z axes
Scaled Ratio of OMS/AMS
Nozzle Pressure / bar
Daniel Klostermann, Bachelor Thesis
False colour Image of TVC, beam diameter approx. 2.4 mm
y axes
0
-2
-4
2
0
4
-4
4
Jet Beam Direction

## Slide 6: Mie Scattering (S. Grieser)
Cluster size/mass measurements in the regime of PANDA target operation conditions
New setup : 0° between rotation plane and glass fibre (prior 7°)
Spatial filter in front of glass fibre
Auxiliary construction to find out the centre
First measurements with cluster-jet beam in preparation
  Planned for spring 2018
Old Setup
New Setup

## Slide 7: New Nozzle Production Process (S. Grieser)
Galvanic deposition combined with laser production techniques
Minimal narrowest inner nozzle diameter
  Reached: 12 µm inner diameter
  @ PANDA IP distance
New Nozzles in preparation:
  Highest interest in the production of (10 – 30) µm inner diameter nozzles with thicknesses

## Slide 8: Studies on Vacuum Conditions
Measurements of flow rates into each chamber
Installation of slit collimator
Additional orifices installed/under investigation
Minimization of beam dump back flow rates
Determination of cluster-jet beam contribution
Work in progress
Special slit collimator used at the PANDA target source (size 800 mm x 210 mm used)

## Slide 9: PANDA Cluster-Jet Target at COSY
Approved beam time at the COSY accelerator in Jülich
  August 2018
  Installation during maintenance phase june 2018
Direct PANDA related target – ion beam interaction studies
  Vacuum conditions in presence of an ion beam
  Target influence on quality and lifetime of accelerator beam
  Investigation on cooling systems behaviour
    2 MeV electron cooler
    stochastic cooling
    barrier bucket
PANDA cluster-jet target placed at the COSY accelerator in Jülich (by Daniel Bonaventura)