## Slide 1: Applicability of digital silicon photomultipliers in RICH detectors
A.Yu. Barnyakov, M.Yu. Barnyakov, S.A. Kononov, E.A. Kravchenko, I.A. Kuyanov,
A.P. Onuchin, V.G. Prisekin
a Budker Institute of Nuclear Physics
b Novosibirsk State University
c Novosibirsk State Technical University
International Conference on the Advancement of Silicon Photomultipliers
11-15 June 2018
Schwetzingen, Germany

## Slide 2: Focusing Aerogel RICH (FARICH)
T.Iijima et al., NIM A548 (2005) 383 A.Yu.Barnyakov et al., NIM A553 (2005) 70
n=1.030 6.0mm
n=1.027 6.3mm
n=1.024 6.7mm
n=1.022 7.0mm
First sample of 4-layer aerogel
3-layer aerogel 115x115x41 mm3
Focusing aerogel improves proximity focusing design by reducing the contribution of radiator thickness into the Cherenkov angle resolution
Multi-layer monolith aerogels have been being produced by the Boreskov Institute of Catalysis in cooperation with the Budker INP since 2004.
Notes: Идея ФАРИЧ появилась в 2004 г.
Точность измерения черенковского угла связана с точностью измерения скорости, а значит с качеством разделения частиц.

## Slide 3: FARICH for Super Charm-Tau Factory
μ momentum range for τ → μγ at Ecm=4.2GeV
μ/π: MC simulation MPPC S10362 3x3mm, D=200mm, 4-layer aerogel
μ/π is required for LFV search in τ→μγ.
Target sensitivity on Br(τ→μγ) ~10-9
Proximity focusing RICH
21 m2 photon detector area
Use SiPMs due to 1T magnetic field
~106 pixels with 4 mm pitch
4-layer or gradient aerogel radiator

## Slide 4: SiPMs in RICH application (single photons)
Pros
High PDE
Sub-ns timing resolution
Immune to magnetic field
Active/Total area ratio
Very compact with low material budget
Cons
High dark count rate (10-100 kHz/mm2)
Radiation induced damage (~1010 n1MeV/cm2)
S. Korpar et al., NIM A 594 (2008) 13
A.Y. Barnyakov et al., NIM A 732 (2013) 352
S. Korpar et al., NIM A 766 (2014) 107
M. Contalbrigo, NIM A 787 (2014) 224
I. Balossino et al., NIM A 876 (2017) 89

## Slide 5: FARICH detector prototype with CPTA MRS APDs BINP e− test beam in 2011
4-layer aerogel focusing at 62 mm
n1=1,050 t1=6,2mm
n2=1,041 t2=7,0mm
n3=1,035 t3=7,7mm
n4=1,030 t4=9,7mm
Size: 100x100x31mm3
Lsc(400nm) = 43mm
32 CPTA MRS APDs with active pixel size 2.1x2.1mm2
DCR ~ 5 MHz/device

## Slide 6: Cherenkov ring observation with single pixels
Given a tracking system, wide beam and enough particle statistics, a single PD pixel is enough to build the distribution of Cherenkov photons on Rch (θch).
Many pixels can be combined to improve accuracy and align the tracking system with the photon detector
Sum of all pixels w.r.t. track position
Dark count background

## Slide 7: Analog SiPM vs Digital SiPM
Analog
Established technology
Great progress in improving parameters: PDE, DCR, RadHard
High active/total area ratio
Availability from different vendors
Need for external analog-to-digital readout electronics – bulky detector, higher power consumption
No control of individual SPADs
Digital
On-chip integration of readout electronics – no need for ASICs
Possibility to locate firing SPAD in low light applications – ~10 um resolution
Better timing resolution
Control of individual SPADs for inhibiting noisy ones
Different designs for different applications – cost issue
Limited possibilities for custom modifications due to CMOS production process

## Slide 8: DPC is an Integrated, Scalable Solution
fully integrated thanks to CMOS
fully digital signals
no ASIC needed
fully scalable
Digital SiPM
discrete, limited integration
analog signals to be digitized
dedicated ASIC needed
difficult to scale
Analog SiPM
Courtesy of Philips Digital Photon Counting

## Slide 9: DPC is an Integrated “Intelligent” Sensor by Philips Digital Photon Counting
FPGA
Clock distribution
Data collection/concentration
TDC linearization
Saturation correction
Skew correction
Flash
FPGA firmware
Configuration
Inhibit memory maps
32.6 mm
DPC3200-22-44 – 3200 cells/pixel
DPC6400-22-44 – 6396 cells/pixel
Courtesy of Philips Digital Photon Counting

## Slide 10: DPC readout units
Module
Geometrical efficiency ≈70%
Tile
pixel - single amp. channel 6396 cells (DPC6400-22) 3200 cells (DPC3200-22)
sensor - single time channel
7.88
7.15
3.20
3.88

## Slide 11: FARICH prototype with DPC
Square matrix 20x20 cm2
Sensors: DPC3200-22-44
3x3 modules = 6x6 tiles = 24x24 dies = 48x48 pixels in total
576 timing channels
2304 amplitude channels (pixels 3.2x3.9 mm2)
4 levels of FPGA readout: tiles, modules, bus boards, test board
4-layer aerogel
nmax = 1.046
Thickness 37.5 mm
Calculated focal distance 200 mm
Hermetic container with plexiglass window to avoid moisture condensation on aerogel

## Slide 12: PDPC-FARICH prototype beam test CERN PS/T10, 2012
Main objective:
  Proof of concept: full Cherenkov ring detection with a DPC array
Details:
Operation temperature is −40°C to suppress dark count rate
  Dead time is 720 ns.
  DCR(+25°C) ≈ 10 Mcps/sensor single photon detection is not feasible!
  DCR(-40°C) ≈ 100 kcps/sensor inefficiency is 7% .
2 stage cooling: LAUDA process thermostat + Peltiers.
Dry N2 constant flow to avoid condensation.

## Slide 13
p
e, μ, π, K
P = 6 GeV/c
PDPC-FARICH: Cherenkov ring
A.Yu. Barnyakov et al, NIM A 732 (2013) 352

## Slide 14: Clock skew correction between dies
Clock skew correction between dies
~80 photons/die
FWHM 66 ps
PiLas
DPC
optical fiber
diffusor
Hit times w.r.t. mean hit time in event

## Slide 15: Timing correction by Cherenkov ring data
Hit timing vs φ-position
Before
After

## Slide 16: Single photon timing resolution for Cherenkov light
Fit two gaussians plus constant.
90% of area is contained in the narrow gaussian.
σnarrow=48ps
Hit time w.r.t. fitted event time, ns
Hit time w.r.t. fitted event time, ns

## Slide 17: Number of photoelectrons
e, μ, π
protons
K
Npe = 12 after taking into account crosstalks. ~2x lower then expected.

## Slide 18: Absolute PDE measurement of DPC
T = −30°C
Hamamatsu S1336-8BQ
Thermostat
timestamps
missing
1/f
hit
LED ON:
LED OFF:
,
Dark count rate and dead time taken into account:
– live time ratio, determined only by dark counts coming before LED pulse.
per pulse is determined from photocurrent of PIN diode and calibrated ratio of test/monitor channels
Hit enable window

## Slide 19: Absolute PDE of DPC
PDE(470 nm)
19±1% in our measurement vs 36% by PDPC measurement
P(signal+dc)
Fit P(signal+dc) as function of Nγ and extract PDE

## Slide 20: Optical crosstalks in DPC
Crosstalk ways:
between pixels of the same die (3-4%) go likely via Si substrate
between neighboring dies (0.1-0.2%) go via protection glass
PCB
Pixel
Pixel
Protection glass
Epoxy OC
Pixel
Pixel
X-talks between pixels deteriorate position resolution

## Slide 21: Irradiation of DPC tiles proton beam (800 Mev/c) at COSY PS in FZ Jülich
Die-averaged cell DCR vs fluence
DPC tiles cooled to −18°C. Maximum fluence accumulated: 4∙1011 p/cm2

## Slide 22: Radiation hardness study of DPC
4∙109 n1MeV/cm2
2 times drop
Effect of radiative damage on DCR
Estimated PDE degradation due to DCR increase with inhibiting most noisy cells
Estimated die DCR vs active cell fraction
M.Yu. Barnyakov et al, NIM A 824 (2016) 83

## Slide 23: Desired characteristics of digital SiPMs for aerogel RICH
  PDE as high as possible: high active area ratio → amplitude dynamic range does not matter → large SPAD
  Room temperature operation → dark count rate at room temperature ≤ 10 kHz/mm2
  Dead time ratio ≤ 1%
  Position resolution σx ≤ 1 mm: may be realized by determining position of a fired SPAD in an array of size ~3x3 mm2
  SPTR ≤ 100 ps would be useful for DIRC-like detectors or suppressing uncorrelated background
  Radiation hard ≥1011 n1MeV/cm2, dead time ratio after irradiation ≤ 10-20%, or cheap enough to be replaced after degradation
  Fast analog output for generating trigger from rings

## Slide 24: Density of photoelectrons in aerogel RICH
PDE of MPPC S13361-3050
Pixel packing factor - 80%
Ring radius ~ 55 mm
Ring width FWHM ~ 3mm
→ 10% loss of photons for pixel size 2.5 mm
Number of fired pixels vs pixel size
Nph.e.

## Slide 25: Summary & conclusion
Digital SiPMs are promising sensor candidates for RICH applications in visible & NUV range and only one in strong magnetic fields
DPC parameters were studied: not quite suitable for aerogel RICH due to large dead time
Looking for other dSiPM solutions for application in Super Char-Tau Factory (Novosibirsk)
Welcome to collaboration!

## Slide 26: Thank you for your attention!

## Slide 27: Nice Cherenkov rings from aerogel detected by DPC at the e− beam at BINP
2-layer aerogel of 40mm thick
D=160 mm