## Slide 1
The Silicon Tracking System of the CBM experiment at FAIR
Johann M. Heuser, for the CBM Collaboration
GSI Helmholtz Center for Heavy Ion Research, Darmstadt, Germany
Compressed Baryonic Matter experiment at FAIR
track point measurement in high-rate collision environment: 105  107/s (A+A), up to 109/s (p+A)
physics aperture : 2.5    25, 0.3 m  z  1.0 m
8 tracking stations
double-sided silicon microstrip sensors
hit spatial resolution  25 µm
self-triggering front-end electronics
time-stamp resolution  5 ns
material :  0.3% – 1.5% X0 per station
p/p  1.8% (p > 1 GeV/c, 1 Tm field)
p+C, 29 GeV
central Au+Au, 8 A GeV
UrQMD + GEANT + CbmRoot
Silicon Tracking System in Dipole Magnet
Silicon Tracking System
System Integration
Silicon Microstrip Sensors
Read-out Electronics
Modules and Ladders
Demonstrators
front-end electronics board in cooling box
896 modules
8 tracking stations
18 mechanical half-units
C-frame
ultra-thin r/o cables
sensor
read-out + power electronics
106 ladders
0.5 mm/div
285/320 ± 15 µm thick
n-type silicon
double-sided segmentation
1024 strips of 58 µm pitch
strip length 2/4/6/12 cm
angle front/back: 7.5/0
read-out from top edge
double-metal routing on p-side
radiation tolerance 1  1014 neq (1 MeV) /cm2, 1 Mrad
material budget [ % X0 ]
2 x 4/5 modules on CF support
module assembly
ladder assembly
tab-bonding of Al-polyimide cables between ASICs and sensor
mounting of modules onto low-mass carbon-fiber supports
prototypes developed and produced: CiS/ Germany, Hamamatsu/Japan
6.2 x 2.2 cm2
6.2 x 4.2 cm2
6.2 x 6.2 cm2
6.2 x 12.4 cm2
STS Project Timeline
miniSTS
in demonstrator experiment miniCBM at GSI/SIS18
operation 2018 - 2021
2 tracking stations
  13 modules
  5 half-ladders
GBT read-out
FLESin DAQ node
Production Readiness : Nov. 2018
Detector construction 2019 – 2022
prototype modules
test at COSY, Feb. 2018
proton beam, 1.7 GeV/c
sensor 285 µm thick
128 channels /side read out
microcable 25 cm long
Assembly Centers: GSI-FAIR, JINR-VBLHEP
Detector ready for installation: 2023
assembly procedure defined and tested on mechanical dummy modules
performance:
noise: 1090 150 e (n) 1350 200 e (p)
r/o threshold: 7000 e
signal mean: 16720 e (n) 20300 e (p)
signal-to-noise: 153
hit detection eff.: > 95%
system in thermal enclosure
sensors at -5 C
cooling of electronics
with bi-phase CO2
sensor position precision  40 µm
STS modules
copper link (~1 m)
optical link (~50 m)
FLES input node
with FLIB
boards
in “Green Cube” computing center
optical link (~300 m)
in DAQ room
μTCA crate
with AFCK
boards
Common
GBTx
Readout Board
on detector
read-out chain for miniSTS
STS-XYTER v2.0 ASIC 8  on FEB-8
CBM06
miniSTS design
verification of :
ASIC under load
system aspects
data transport
tracking