## Slide 1: The Budker Institute of Nuclear Physics

## Slide 2: PANDA Magnet Preliminary Design Report

## Slide 3: 3D model of the Magnet.
Magnet with St. Steel Cryostat. The weight of magnet is ~14,5 t

## Slide 4: Dimensions of the Magnet.
Inner diameter is 1900 mm, Outer diameter is 2680 mm, length is 3090 mm

## Slide 5: Dimensions of the Coils (worked condition 4.5 K).
Outer diameter of coils is 2200 mm, length: two coils - 887 mm, one – 400 mm.

## Slide 6: The Cold mass. (CERN design)
2x 6 layers - 78 turns
1x 6 layers - 35 turns
10,95 мм x 7.93 мм,
NbTi / Cu d=1.4 мм
Magnetic field - 2 T
Current - 4.96 kA (3 T)
The design of Cold mass is based on the design of Cold mass of CERN.

## Slide 7: The Cold mass (3D-Model).
The Cold mass is based in to Cryostat with help of suspension, radial rods and longitudinal rods. For thermal bridges is used the flexible copper.
The weight of cold mass is ~5.6 t

## Slide 8: The Cold mass (dimension)
Inner diameter is 2096 mm, Outer diameter is 2280 mm, length is 2826 mm

## Slide 9: The Collector of Cold mass.
For cooling of Coil is used the collector with special aluminum profile which is welded on the outer shell of Cold mass.

## Slide 10: The Cryostat of The Magnet.
Inner diameter is 1900 mm, Outer diameter is 2680 mm, length is 3090 mm Material is St.St. The weight is ~8 t

## Slide 11: Configuration of the Cryostat
Thickness of the outer shell is 12 mm, Thickness of the inner shell is 8 mm , Thickness of the flanges is 40 mm, Thickness of the rings is 40 mm
The bolts – M12 – 2x36 ps. Sealing ring – d=8 mm

## Slide 12: Results of calculation of the Cryostat. Operation condition (p=0.1 MPa)

## Slide 13: Results of calculation of the Cryostat. Stress
The maximum equivalent stress is 43 MPa.

## Slide 14: Results of calculation of the Cryostat. Deformation
The maximum deformation is 0,1 mm.

## Slide 15: Results of calculation of the Cryostat. Operation condition (p=0.05 MPa)

## Slide 16: Results of calculation of the Cryostat. Stress
The maximum equivalent stress is 21.5 MPa.

## Slide 17: Results of calculation of the Cryostat. Deformation
The maximum deformation is 0,06 mm.

## Slide 18: The Shield of the Magnet.
Outer diameter is 2552 mm, Inner diameter is 2020 mm, length is 2900 mm
Thickness is 3 mm, Material is Al. The weight is ~0,45 t

## Slide 19: Break of the Shield .
The shield has 4 breaks isolated G10 bars with gaps. The shield is positioned into the cryostat with help Balls transfer units with G10 ring. On the outer and inner surface of the shield will be put 30 layers of superinsulation.

## Slide 20: The inner Shield.
Inner shell of the shield with flanges, ribs and pipeline.
For cooling of Shield is used the pipeline with special aluminum profile which is welded on the shell.

## Slide 21: The outer Shield.
Outer Shell of the shield with ribs, Balls and pipeline with special aluminum profile which is welded on the shell.

## Slide 22: The Shield into the Magnet.
The Shield is based on the outer shells of the cryostat with help of Balls transfer units with G10 ring. Flanges of shield are fixed with help of thread rivets and bolts.
Thermal bridges is fixed on the shell of shield with help of thread rivets and bolts.

## Slide 23: Fixation of the Shield into the Cryostat.
In the area of the target, the shield is fixed with help of bushes (G10) and bolts (8 places). Position of bolts for fixing the shield into the cryostat.

## Slide 24: Cross section of the Magnet.
In the radial direction the Cold mass is based into Cryostat with help suspensions and axis rods.

## Slide 25: The Suspensions.
The diameter of suspension is 16 mm, the length is 840 mm.
Material is Ti-5Al-2.5Sn

## Slide 26: The position of the suspension before and after cooling down.
After cooling down the suspension take a vertical position.

## Slide 27: Results of calculation of the Suspension. (temperature loads)
The weight load of the cold mass of ~63 kN.
Maximum radial decentering magnetic force of 51 kN (Specification F-DS-PND-004)

## Slide 28: Results of calculation of the Suspension. (temperature distribution)

## Slide 29: Results of calculation of the Suspension. (fixation)

## Slide 30: Results of calculation of the Suspension. Stress.
The equivalent stress of suspension is ~150 MPa.

## Slide 31: Results of calculation of the Suspension. Stress.
The maximum equivalent stress is 545 MPa.

## Slide 32: Results of calculation of the Suspension. Stress.
The maximum equivalent stress of fixing bolts is 250 MPa.

## Slide 33: Results of calculation of the Suspension. Stress.

## Slide 34: The Longitudinal rod. (right side)
In the axial direction the Cold mass is fixed with help longitudinal rods.
The diameter of longitudinal rods is 20 mm, the length is 1913 mm (right side).
Material is Ti-5Al-2.5Sn

## Slide 35: The Longitudinal rod. (left side)
The diameter of longitudinal rods is 20 mm, the length is 1123 mm (left side).
Material is Ti-5Al-2.5Sn

## Slide 36: The position of the longitudinal rods before and after cooling down.
After cooling down the axial rods take a horizontal position.

## Slide 37: Results of calculation of the longitudinal rods . (temperature loads)
Maximum axial decentering magnetic force of up to 168 kN
The initial tightening force is 3.7 kN (Specification F-DS-PND-004)

## Slide 38: Results of calculation of the longitudinal rods . (temperature distribution)

## Slide 39: Results of calculation of the longitudinal rods . (fixation)

## Slide 40: Results of calculation of the longitudinal rods . Stress
The equivalent stress of longitudinal rods is ~140 MPa.

## Slide 41: Results of calculation of the longitudinal rods . Stress
The maximum equivalent stress is 545 MPa.

## Slide 42: The Radial rods.
In the radial direction the Cold mass fixed with help radial rods. The diameter of radial rods is 12 mm, the length is 720 mm.
Material is Ti-5Al-2.5Sn

## Slide 43: Results of calculation of the radial rods . (temperature loads)
Maximum radial decentering magnetic force of 51 kN
The initial tightening force is 3.7 kN (Specification F-DS-PND-004)

## Slide 44: Results of calculation of the radial rods . (temperature distribution)

## Slide 45: Results of calculation of the radial rods . (fixation)

## Slide 46: Results of calculation of the radial rods . Stress
The equivalent stress of radial rods is ~120 MPa.

## Slide 47: Results of calculation of the radial rods . Stress
The maximum equivalent stress is 478 MPa.

## Slide 48: Results of calculation of the radial rods . Stress
The maximum equivalent stress of fixing bolts is 260 MPa.

## Slide 49: Diagram of position of the target`s axis in worked condition.
The length and position of fixation of the longitudinal rod, and position of the thermal bridges allow not to move the axis of the hole of the target.

## Slide 50: Diagram of position of the Cold mass axis in worked condition.
The length and position of fixation of suspensions, and position of the thermal bridges allow to move the axis of the Cold mass for 0,1 mm.

## Slide 51: Heat loads of the Cold mass and thermal Shield.
T=4.5K | Thermal load, W
Radiation | 2.2
Heat inflow to the cold mass supports | 0.52
Total: | 2.72
T=60K | 
Radiation | 95
Heat inflow to the cold mass supports | 13
Heat inflow to the shield supports | ?
Total: | 108

## Slide 52
Magnet assembly procedure
For assembling the magnet, it is possible to use an I-beam steel hot-rolled with parallel faces of shelves 70B2 (697 x 260 mm) GOST 26020-83.
The length of the beam is L = 9 m.
To roll inside, we can use rollers that are used to open doors (Roller skate Boerkey model AM-H)

## Slide 53
Magnet assembly procedure
Pic.1. Stand
Pic.2. Outer shell of cryostat
insertion.
Pic.3. Outer shell of cryostat
position.
Pic.4. Outer shield insertion.
Pic.5. Outer shield position.
Pic.6. Cold mass insertion.

## Slide 54
Magnet assembly procedure
Pic.8. Suspensions and axial
rods insertion.
Pic.7. Cold mass position.
Pic.9. Inner shield insertion.
Pic.10. Inner shield position.
Pic.11. Flange of shield insertion
and position.
Pic.11. Flange of shield insertion.

## Slide 55
Magnet assembly procedure
Pic.13. Flange of shield position.
Pic.14. Inner shell of cryostat
insertion.
Pic.15. Inner shell of cryostat
position.
Pic.16. Flange of cryostat
insertion and pos.
Pic.17. Flange of cryostat
insertion.
Pic.16. Flange of cryostat
position.

## Slide 56: Drawings of the PANDA Magnet

## Slide 57: Drawing of the Magnet.

## Slide 58: Drawing of the Magnet.

## Slide 59: Drawing of the Magnet.

## Slide 60: Drawing of the Magnet.

## Slide 61: Drawing of the Magnet.

## Slide 62: Drawing of the Cryostat.

## Slide 63: Drawing of the Cryostat.

## Slide 64: Drawing of the Cold mass.

## Slide 65: Drawing of the Cold mass.

## Slide 66: Drawing of the Shield.

## Slide 67: Drawing of the Shield.

## Slide 68: Drawing of the Magnet and Feed Box.

## Slide 69: Drawing of the Magnet, Feed Box and Frame.

## Slide 70: Drawing of the Magnet, Feed Box and Frame.

## Slide 71: 3D model of the Magnet and Feed Box.

## Slide 72: 3D model of the Yoke, Magnet, Feed Box, Frame.

## Slide 73: 3D model of the Yoke, Magnet, Frame, Feed Box and Platform.
To service the box, it is necessary to have the length of the Working platform min 600 mm from the box.

## Slide 74: 3D model of the Magnet, Yoke and Frame.

## Slide 75: Power supply of PANDA Magnet.

## Slide 76: Thank you for your attention!