## Slide 1: Status of the Cluster Target PANDA Collaboration Meeting 18/2 Stockholm, June 4th – 8th, 2018

## Slide 2: Studies at the Prototype Target and Numerical Simulations

## Slide 3: Simulations of Gas-Jet and Cluster-Jet Beams
Navier-Stokes Equations:
  Continuity equation (conservation of mass):
  Conservation of momentum:
      Field of force (gravity), Stress tensor (viscosity and pressure)
  Energy conservation
      : Heat supply
  Equation of state (ideal gas):
      : Specific inner energy

## Slide 4: Simulations of Gas-Jet and Cluster-Jet Beams
Navier-Stokes equations:
  Numerical fluid dynamics:
    Finite volume method
    Block structured grids
  Axial-symmetrical model (3d):
    Axial-symmetrical boundary conditions
Simulation package: OpenFOAM

## Slide 5: Simulations of Gas-Jet Beams: Velocity
Cern nozzle (Ø = 28 µm):
  bar, K, mbar
Simulations by S. Vestrick and P. Brand (WWU)

## Slide 6: Simulations of Gas-Jet Beams: Density (previously 1d)
Cern nozzle (Ø = 28 µm):
  bar, K, mbar
Simulations by S. Vestrick and P. Brand (WWU)

## Slide 7: Simulations of Gas-Jet Beams
Cern nozzle (Ø = 28 µm):
  bar, K, mbar
  Nozzle inlet: x = -1 mm, narrowest inner diameter: x = 0 mm,
  nozzle exit: x = 17 mm
Simulations by S. Vestrick and P. Brand (WWU)

## Slide 8: Simulations of Gas-Jet Beams
Cern nozzle (Ø = 28 µm):
  bar Previous Simulations (2d):
  K (A. Täschner, Münster, 2012)
  mbar

## Slide 9: Simulations of Gas-Jet Beams
Cern nozzle (Ø = 28 µm):
  bar, K, mbar
                Distance from nozzle exit: 20 mm
                Axis of symmetry: r = 0 mm
Simulations by S. Vestrick and P. Brand (WWU)

## Slide 10: Measurement on Laval Nozzle Geometry
Laval nozzle
  Produced at University of Münster
  CERN geometry
  Typically core beam visible
Narrowest inner diameter:
  1. measurement: 33.3 µm
  2. measurement: 35.1 µm
  Measurements performed with gaseous, supercritical and fluid hydrogen
    (Max.) target thicknesses: vs.
    Velocity decreased ( – m/s): vs.m/s
        Examples for bar, K

## Slide 11: Measurement on Laval Nozzle Geometry: Length
Impact of the nozzle length:
Laval nozzle with Ø: 35.1 µm
Measurements performed with gaseous, supercritical and fluid hydrogen
1./2. measurements:
  Test of reproducibility at full nozzle length (18 mm)
Continuous turn off: 1 mm per step
  Mechanical Workshop of University Münster

## Slide 12: Measurement on Laval Nozzle Geometry: Length

## Slide 13: Measurement on Laval Nozzle Geometry: Length

## Slide 14: Measurements at the PANDA Target

## Slide 15: PANDA Cluster Target
Operation of the cluster target in „PANDA-like“ setup
Studies on vacuum situation
Test of different collimator types
Variation of orifices between pumping stages
Preparation for installation at COSY

## Slide 16: Planned PANDA Setup with Cluster Target

## Slide 17
Beam dump
(prepared by the Genua group)

## Slide 20
Münster PANDA
(today) (20xx)

## Slide 21: Measurement of Cluster Beam Properties
Measurement of cluster beam
position
thickness distribution
size
vacuum situation
gas load
at the scattering chamber and
at the PANDA IP

## Slide 22: Beam Dump Efficiency: Gas in Last Dump Stage
Relevant pressure range

## Slide 23: Vakuum Studies
Hydrogen partial pressures with cluster beam on
  4.1x1014 H-atoms/cm2 at PANDA IP
  2.25 m behind the nozzle
Partial pressures from other gases and water completely negligible
Pumping speed at IP in Münster corresponds to the one later at PANDA (~ 100 l/s)

## Slide 24: Vakuum Studies
Study the effect of bouncing clusters or evaporation from clusters
  Subtraction of backstreaming gas from 3rd beam dump stage
    Switch cluster beam off
    Load 3rd beam dump stage with hydrogen gas so that the same pressure with cluster beam is obtained (i.e. 4x10-5 mbar)
  Appreciable effect only in 2nd beam dump stage

## Slide 25: Vakuum Studies
Obviously the obtained gas load to the IP result from
  Gas load from neighbouring chambers
  Conductance between the vacuum stages
  Possible evaporation of gas from clusters
  Possible bouncing clusters
The last two contributions seem to be significant

## Slide 26: Vakuum Studies
Further studies on this aspect in preparation
  Variation of orifices (limitation by cluster beam size)
  Variation of working points, i.e. stagnation conditions at the nozzle
Estimation for given example measurement:
  1.2x10-5 mbar ≙ 6.4x1011 atoms/cm3
  1 m of this pressure along the PANDA beam pipe corresponds to 6.4x1013 H-atoms/cm2, i.e. 15.6% of the target thickness

## Slide 27: New Operation Panel for the Pumping System
Temporary switch board exchanged by final panel
Full manual operation and remote control possible
  Valves
  Pumps
  Control via CRIO
  Readout of status lines (pumps, shutter)

## Slide 28: PANDA Target at COSY

## Slide 29: Cluster Target at COSY
Installation and operation of the complete PANDA cluster target at an internal COSY beam position
Well suited: WASA-at-COSY position including partially use of detectors + DAQ
Comparison with results from WASA pellet target
Installation of the beam dump: week 25
Installation of the cluster generator: week 27
→ realistic test of important
beam and target parameter

## Slide 30: Installation of the Cluster Target at COSY

## Slide 31: Installation of the Cluster Target at COSY

## Slide 32: Installation of the Cluster Target at COSY

## Slide 33: Installation of the Cluster Target at COSY
New concrete element ordered, but still not delivered

## Slide 34: Installation of the Cluster Target at COSY

## Slide 35: Modification of Beam Pipe and Scattering Chamber
Design and construction by FZ Jülich

## Slide 36: Modification of Beam Pipe and Scattering Chamber

## Slide 37: Modification of Beam Pipe and Scattering Chamber

## Slide 38: Monitoring System at the Beam Dump Section
In preparation at WWU

## Slide 39: Beam Time Request
Beam time period | Required beam time | Topics to be investigated
2018, week 32 | 1 week | Target commissioning
2018, 2nd half year (request to CBAC) | 1 week | Vacuum at IP Target adjustment studies during experimental runs Beam-target interaction
2019, 1st half year (planned) | 2 weeks (2x 1 week) | Beam-target interaction Vacuum at IP Beam/target effects on recorded data Development of new technologies
2019, 2nd half year (planned) | 2 weeks (2x 1 week) | Beam-target interaction Beam/target effects on recorded data Development of new technologies

## Slide 40
Thank you very much....

## Slide 41: Vakuum Studies
Total pressures with cluster beam on