## Slide 1
BINP
PANDA Magnet
S.Pivovarov, E.Pyta, M.Kholopov, BINP, Novosibirsk
PANDA Collaboration Meetig, 04-08th June 2018, Stockholm

## Slide 2: PANDA solenoid magnet, BINP responsibility.
Arrangement of the components of the PANDA solenoid.
Power supply and energy extraction system
Cable channel
Control Dewar box
Solenoid and yoke
Frame of solenoid

## Slide 3: 3D model of the Yoke, Platform and Frame, Cryostat, Control Dewar (for production at BINP).
Frame
Yoke
Cryostat
Control Dewar
The total weight of Yoke, Platform and Frame is ~340 t. The weight of Cryostat is 14.5 t. The weight of Control Dewar is ~2 t.

## Slide 4: Configuration 12th layers of Yoke
The thickness of the outer and inner plates is 60 mm, the thickness of the inner plates is 30 mm. The gap between the plates is 35 mm for installation of the muon detectors.

## Slide 5: Dimensions of the Yoke, Platform and Frame.
Height - 6350 mm, Width - 7930 mm (doors closed), Length - 4865 mm

## Slide 6: Dimensions of the Yoke, Platform and Frame. (The Doors opened)
Width - 9600 mm (doors open)

## Slide 7: Main Technical Data of Yoke
Upstream door with supports, rollers etc., weight | Left wing | t | 22.8
 | Right wing | t | 22.8
Downstream door with supports, rollers etc. | Left wing | t | 20.7
 | Right wing | t | 21.1
Octagonal barrel | Upper beam | t | 19
 | Inclined side beams, 4 pc. | t | 20.8
 | Vertical side beams, 2 pc. | t | 20.8
 | Bottom beam | t | 20.4
Platform beams, support frames and carriages |  | t | 57.8
Total weight |  | t | 341.1
Joke length |  | mm | 4875
Joke width | Closed wings | mm | 7930
 | Open wings | mm | 9600
Joke height |  | mm | 6350
Material |  |  | St3/St10

## Slide 8: Drawing of the Yoke, Platform and Frame.

## Slide 9: Drawing of the Yoke, Platform and Frame.

## Slide 10: 3D-Model of the Yoke of PANDA Magnet.
The iron yoke consists of a barrel part and sliding doors. The total weight of Yoke is ~280 t
Downstream Door
Upstream Door
Barrel part

## Slide 11: Drawing of the Yoke.

## Slide 12: Drawing of the Yoke.

## Slide 13: Drawing of the Barrel part of the Yoke.

## Slide 14: The octant of the Barrel part of the Yoke
The module consists of horizontal plates and side plates made by water cutting machine. This design of module has good rigidity and allows to reduce the number of welds.
Upper octant
Upper octant assembling scheme

## Slide 15: Drawing of the top Octant.

## Slide 16: Drawing of the top Octant.

## Slide 17: Drawing of the top Octant.

## Slide 18: Drawing of the top Octant.

## Slide 19: 3D- Model of the Downstream Door.

## Slide 20: Drawing of the Downstream Door.

## Slide 21: Drawing of the half Downstream Door.

## Slide 22: Drawing of the half Downstream Door.
35 mm gaps for installation of the muon chambers

## Slide 23: The Upstream Door.

## Slide 24: Drawing of the Upstream Door.

## Slide 25: Drawing of the half of Upstream Door.

## Slide 26: Drawing of the half of Upstream Door.

## Slide 27: 3D-Model of the Platform and Frame of PANDA Magnet.
The total weight of Platform and Frame is ~58 t
Rollers for the detector moving
Rail for the door wings close/open

## Slide 28: Drawing of the Platform and Frame.

## Slide 29: 3D model of the solenoid magnet.
Material of the vacuum shell of cryostat is stainless steel. The weight of magnet is ~14,5 t.

## Slide 30: Dimensions of the Magnet.
Inner diameter is 1900 mm, Outer diameter is 2680 mm, length is 3090 mm

## Slide 31: Dimensions of the Coils.
The position of the cold mass in axial direction is fixed in the area of the holes for the target. Solenoid consists from 3 coils. Outer diameter of coils is 2200 mm, length: two coils - 887 mm, one - 400 mm.
Holes for target pipe.

## Slide 32: Cross section of the Magnet.
Cold mass is based into Cryostat by suspensions and axis rods.

## Slide 33: The Suspensions.
The diameter of suspensions is 16 mm, the length is 840 mm. Material is Ti-5Al-2.5Sn

## Slide 34: The Longitudinal rod. (right side)
In the axial direction the Cold mass is fixed by longitudinal rods. The diameter of longitudinal rods is 20 mm, the length is 1913 mm (right side).Material is Ti-5Al-2.5Sn

## Slide 35: The Longitudinal rod. (left side)
The diameter of longitudinal rods is 20 mm, the length is 1123 mm (left side).
Material is Ti-5Al-2.5Sn

## Slide 36: The Radial rods.
In the radial direction the Cold mass fixed by radial rods. The diameter of radial rods is 12 mm, the length is 720 mm. Material is Ti-5Al-2.5Sn

## Slide 37: Drawing of the Magnet.

## Slide 38: Drawing of the Magnet.

## Slide 39: Drawing of the Magnet.

## Slide 40: Drawing of the Magnet.

## Slide 41: Drawing of the Magnet.

## Slide 42: The design of Cold mass.
2 Coils - 6 layers - 78 turns (2x3300 м)
1 Coil - 6 layers - 35 turns (1500 м)
Magnetic field - 2 T
Current - 4.96 kA (3 T)
Coil connection
The design of Cold mass is based on the design of Cold mass of CERN.

## Slide 43
Conductor
Figure 5. Cold mass cross-section.
Figure 6. Drawing of the conductor.
Table 4. Conductor mechanical and electrical parameters.
Thickness (after cold work) at 300 K | mm | 7.93 | ± 0.03
Width (after cold work) at 300 K | mm | 10.95 | ± 0.03
Critical current (at 4.2 K, 5 T) | A | > 14690 | 
Critical current (at 4.5 K, 3 T) | A | > 16750 | 
Overall Al/Cu/sc ratio |  | 10.5/1.0/1.0 | 
Aluminum RRR (at 4.2 K, 0 T) |  | > 1000 | 
Al 0.2% yield strength at 300 K | MPa | > 30 | 
Rutherford cable, 8 strands, extruded in Al matrix
Dimensions of cable: 10.9 x 7.93 mm

## Slide 44: The Cold mass (3D-Model).
The Cold mass is based in to Cryostat by suspensions, radial rods and longitudinal rods. For thermal bridges is used the flexible copper.
The weight of cold mass is ~5.6 t

## Slide 45: The Cold mass (dimension for condition 4.5K)
Inner diameter is 2096 mm, Outer diameter is 2280 mm, length is 2826 mm, Material of shell is Al 8083.

## Slide 46: The Collector of Cold mass.
For cooling of Coil is used the collector with special aluminum profile which is welded on the outer shell of Cold mass.

## Slide 47: Drawing of the Cold mass.

## Slide 48: Drawing of the Cold mass.

## Slide 49: The Cryostat of The Magnet.
Inner diameter is 1900 mm, Outer diameter is 2680 mm, length is 3090 mm. Material is St.St. The weight is ~8 t

## Slide 50: Configuration of the Cryostat
Thickness of the outer shell is 12 mm, Thickness of the inner shell is 8 mm , Thickness of the flanges is 40 mm, Thickness of the rings is 40 mm
The bolts – M12 – 2x36 ps. Sealing ring – d=8 mm

## Slide 51: Drawing of the Cryostat.

## Slide 52: Drawing of the Cryostat.

## Slide 53: The Shield of the Magnet.
Outer diameter is 2552 mm, Inner diameter is 2020 mm, length is 2900 mm
Thickness is 3 mm, Material is Al 8083. The weight is ~0,45 t

## Slide 54: Break of the Shield .
The shield has 4 breaks isolated G11 bars with gaps. The shield is positioned into the cryostat by Balls transfer units with G11 ring.
On the outer and inner surface of the shield will be covered 30 layers of MLI.

## Slide 55: The inner Shield.
Inner shell of the shield with flanges, ribs and pipeline .
For cooling of Shield is used the pipeline with special aluminum profile which is welded on the shell.

## Slide 56: The outer Shield.
Outer Shell of the shield with ribs, Balls transfer units and pipeline with special aluminum profile which is welded on the shell.

## Slide 57: The Shield into the Magnet.
The Shield is based on the outer shells of the cryostat by of Balls transfer units with G11 ring. Flanges of shield are fixed by of thread rivets and bolts.
Thermal bridges is fixed on the shell of shield by of thread rivets and bolts.

## Slide 58: Fixation of the Shield into the Cryostat.
In the area of the target, the shield is fixed by of bushes (G11) and bolts (8 places). Position of bolts for fixing the shield into the cryostat.

## Slide 59: Drawing of the Shield.

## Slide 60: Drawing of the Shield.

## Slide 61: Heat loads of the Cold mass and thermal Shield.
T=4.5K | Thermal load, W
Radiation | 2.2
Heat inflow to the cold mass supports | 0.52
Total: | 2.72
T=60K | 
Radiation | 95
Heat inflow to the cold mass supports | 13
Heat inflow to the shield supports | ?
Total: | 108

## Slide 62: 3D model of the Magnet and Control Dewar.

## Slide 63: Drawing of the Magnet and Control Dewar.

## Slide 64: Drawing of the Magnet, Feed Box and Frame.

## Slide 65: Drawing of the Magnet, Feed Box and Frame.

## Slide 66: 3D model of the Magnet, Yoke, Platform and Frame.

## Slide 67: Summary
Drawings of Iron Yoke and Frame are ready. The Novosibirsk Plant (Sibmash) started production of the first octant of the barrel part of the Iron Yoke.
Drawings of the Cryostat, Shield and Cold mass are ready.
The technology of winding coils and special tools are being developed in BINP.
PANDA solenoid magnet will be produced in the BINP Workshop.

## Slide 68: Thanks for your attention