## Slide 1: Operation status report
till 9.7. Ar from Chordis with 8.5 MeV / u for SIS
• source was driven down at 14:00, no test of control system update performed anymore
from 4.7. to 10.7. Ti from PIG for X8, from 5.7. also for Y7
• between 4.7. and 6.7. Attempts to increase the repetition rate in HSI (PIG to 25 Hz desired) causes failures on the HSI RF transmitters. reached 25 Hz on Friday.
• During weekend: 7 times Source change PIG -> very short service life (maybe because of bad settings)
from 6.7. Preparation ECR for Ti beam
• from 10.7. beamsettings for Y7 and X8.
• 11.-12.7. ECR source failure → defect oven (bake out, preparing)
10.7. source from terminal north was changed to Ag beam
• planned Ag47 + can´t be separated
• first Ag45 + used → low intensity, problems with injection to the SIS18
• for higher intensity the charge state was changed to Ag41 +
12.7. PIG prepared for Pb5+ , mass and charge separation

## Slide 2: Operation status report
9.7. 14:00 shut down of Ar source, no test of control system update performed anymore. Control system update should fix timing issues on the SIS and dipole. → timing problems between UNILAC and SIS18 (no beam inside SIS). Rollback 12.7. (FS)
S11MU2 fails about 1 time per hour, usually reset possible, about 1 time per shift RB necessary. Cause in the control system.
10.7. Water leak in the X branch (tube connection on XCMS2 was fixed)
When adjusting Ag used in the SIS transition from MA cavity to ferrite cavity. Start-up difficulties when setting in ParaModi • frequent failures of individual cavities -> beam loss on the ramp.
12.7. Night shift fire on HF gallery