## Slide 1
”3D-Printed Detectors” and Detector Integration modern manufacturing technologies and functional materials in detector system design ATLAS and CMS Endcap Design and Engineering Challenges Christian J. Schmidt 13.06.2018

## Slide 2: Towards 3D-printed Detectors and Detector Integration
Functional 3D-printing: Printed particle Detectors
  from CAD to batch-size 1 production
include functionality beyond mechanical shape:
    Low-Z, low R signal conductors  Laser/InkJet-Printed Circuits
    Complex metallic capillary cooling structures (as e.g. in Belle II upgrade)
    Semiconductor 3D-post processing (Si/Ge-Det. avoid rad. sensitive surface doping, integration of cooling lines etc.)
    3D-printed mechanical structures and interconnect
    Integration of optical and conductive data interconnect
    precision field cage degraders
    The forgotten realm in material thickness (2 to 50µm)
      precision high purity electrolytic deposition of none copper materials
      molecular plating of compounds for high purity surfaces
      realization of low-Z power and signal lines as well as via-connections  e.g. Ink-Jet print on 3D-Surfaces, enhance through galvanic build-up

## Slide 3: 3D-Plastic-Extrusion Printing more and more comonly used
3D-Printing used in detectors and instrumentation for mock-ups and communication
David Anderson at DENIM 2015 on the neutron instrument VISION

## Slide 4: @ GSI recent heavy use of 3D-Print for ordenary experimental work
Cheap ~ 5k€ machines serve to provide parts for many applications with little particular demands in material specs.
Scientists can easily make their own part  and they do!  no need to wait weeks for the workshop
The CBM-STS developments heavily employ one of 5 Ultimakers
Devices rentate in no time
Even small series of parts are being printed (~ several hundred)

## Slide 5: Detector Challenges
Full 4p coverage with negligible blind area and high granularity
Minimized material budget
Active Targets (the target itself enabled as detector) , structured targets
Detector power and DAQ
Detector power management
  power distribution
  cooling
GHz data transmission, impedance defined data lines
Integration of exotic, active materials
Integration of front-end electronics onto Germanium detectors

## Slide 6: Beyond Slicing, beyond plastics
Example: Hermle Additive Manufacturing
  Metal powder in a supersonic beam fused to substrate
  Combination with 5-axis milling center

## Slide 7: Extremely lightweight 3D-Cooling Structures
low mass in mobile technologies translates to low material budget
 example motor cylinder head
direct cooling translates to electronics power densities
 direct cooled drills and tools

## Slide 8: Technologies rapidly evolving but still mostly island solutions
mechanical 3D-printing for shape prototyping
functionality beyond shape step by step added
  electrical conductivity
  mechanical strength, mechanical bonding strength
  thermal conductivity
  material properties (e.g. sensor materials)
modern laser structuring tools allow 3D-shaping of dedicated, highly specialized sensor material
   CdZnTl high Z sensors
  Diamond Sensors, Diamond membrane sensors, 3D-Diamond
  Silicon/Germanium sensors
  ultra low noise detector compounds for astronomy, satellites and astrophysics

## Slide 9: Bionic Design  Engineering to be learned anew
3D additive manufacturing introduces new dimensions in engineering options
Challenge for intellectual exploration
Only people can exploit the full potential for future detectors
 need to let them work and play with new possibilities

## Slide 10: Equipment: Technological Directions
3D-Printers, additive manufacturing – ceramic, metallic, plastics....
Conductive ink-jet printers
Femtosecond ablation for high aspect ratio micro structures
Plasma etching along Bosch-Process
Laser Lithography
Laser assisted soldering and interconnect
LTO (low temperature oxide) capable LPCVD
Carbon-Fibre-Composite 3D laying robot

## Slide 11: New materials, examples
Carbon foam
Sinthetic graphite foil
  heat spreader tape with conductivity like diamond
  adhesive PET layer  assembly and HV isolation
  conduction lateral
  little conduction perpendicular to plane
Example taped CMS tracker module design, Wim de Boer et al
Airex  foam with up to 98% air content for rugged sandwich structures

## Slide 12: Example: fiber carbon composit structures
CBM-STS Beampipe
CBM-STS Silicon Detector Ladders

## Slide 13: The Phase 2 Upgrades of the ATLAS & CMS Trackers
The High-Luminosity LHC
High-luminosity operation will start in 2026
4000 fb-1 expected ultimate integrated luminosity over ten years
Both ATLAS & CMS will replace their inner tracking detectors
The new tracking detectors
Will consist of several thousands of detector modules
  O(200) m2 of silicon
Cooled with evaporative CO2 and operated below -30 °C
Examples of engineering challenges currently addressed

## Slide 14: CMS Phase 2 Tracker End Cap Design
Goal is to reduce material budget by a factor of 2
Backbone is a carbon fibre sandwich half-disk structure
  230 cm in diameter
  10 mm thickness
Modules are mounted from both sides onto structure
  < 100 μm positioning precision
20 half-disks are combined to build one end cap
  150 cm total length
now
then

## Slide 15: CMS Phase 2 Tracker End Cap Design
Six cooling sectors each with ~6 m length
Cooling pipes embedded in
  480 cooling and positioning inserts
  76 carbon foam heat spreaders spanning through the full thickness of the sandwich
Sandwich core is a mixture of structural and carbon foam
228 additional positioning inserts
Two types of glues used in the same assembly steps
  Structural & thermally conductive (boron nitride doped)

## Slide 16: CMS Phase 2 Tracker End Cap Design
Six cooling sectors each with ~6 m length
Cooling pipes embedded in
  480 cooling and positioning inserts
  76 carbon foam heat spreaders spanning through the full thickness of the sandwich
Sandwich core is a mixture of structural and carbon foam
228 additional positioning inserts
Two types of glues used in the same assembly steps
  Structural & thermally conductive (boron nitride doped)
Cooling and positioning inserts are currently glued onto pipe
Grooves in inserts are closed by lids to increase contact area to pipe
What if the insert could be printed around the cooling pipe
  no adhesive joint ➟ better thermal performance
  less assembly work

## Slide 17: Prototyping of Support Structures
Small Scale Prototype CMS Half-Disk Structure
35 cm x 40 cm in size
Two cooling loops and corresponding inserts and cooling blocks
Study assembly sequence and precision, and cooling performance
  Measured offset to nominal insert positions < 65 μm
< 65 μm
< 50 μm
ATLAS prototype of full-sized petal
60 cm x 40 cm in size
One cooling loop fully embedded in carbon foam
prototype
CAD

## Slide 18: Thermal Testing
The Key to Good Thermal Performance
Understanding of novel raw materials
  E.g. thermal impedance between cooling pipe and carbon foam
Development of machining, handling and processing techniques
  Especially if we drive usage beyond the specified regime
2.5 mm
Qualification of final support structures
  E.g. identify weak thermal contacts via IR thermography

## Slide 19: Diagnostics
Performance relies on high-quality adhesive bonds
For best mechanical stability and cooling performance
Ultrasonic inspection allows for non-destructive testing
Example: investigation of sandwich structure with carbon fibre facings
  10 mm x 10 mm void in adhesive bond area
  uniformity of adhesive bond between carbon foam and facing

## Slide 20: Microchannel Cooling
Cooling at the Next Level
Conventional cooling relies on thermal conduction between heat source and coolant
  Smaller temperature gradient typically means more mass
What if coolant could be brought closer to the heat source?
  Ideal for large power densities, e.g. pixel detectors
Microchannel cooling: ~100 μm wide channels etched in silicon substrate
  Heat conduction path < 1 mm
  Perfect match in terms of coefficient of thermal expansion (CTE)
      ➟ no thermal stress

## Slide 21: One Theme of Distributed Detector Lab: “3D-Printed Detectors” Modern Materials, Modern 3D Structuring Technologies, Modern Additive and Subtractive Machining and Engineering
RF carpets to stop
relativistic fragment ions
Stopping power ~ Structure3
3D-Printing-oriented Engineering
ultra lightweight structures
combined functionality
power management
complex metallic capillary cooling structures
    Integration of optical and conductive data interconnect
Necessary invest can be financed through the DDL, the brains we need to supply ourselves.

## Slide 22: GSI/FAIR Campus Masterplan indicates Area for DDL Infrastructure
New lab could find a site:
850 qm real estate
Construction limit 23m
Could give central home to:
  Germanium Detector Lab
  Experiment Electronics
  ASIC and Si-Pixel Lab
  Cryo-Detectors Lab
  3D-Printing Lab
  Material Sciences and Nano-Technologies Lab