## Slide 1
Systems Engineering for mechanical components
Requirement assurance during design und production
Christina Will

## Slide 2: Why systems engineering and requirement assurance?
Source: Ehrlenspiel, Kostengünstig Entwickeln und Konstruieren, Springer Verlag 2013 + http://imk.engineering/funktionsorientierter-entwurf.html
principle for mechanics = principle for electronics

## Slide 3: Legal aspects and target for FAIR
All partners which produce in the EU or will import into the EU
have to follow the legal rules of the EU.
The following regulations have to be followed:
  2006/42/EG Machinery directive
  89/391/EWG, 2007/30/EG Regulation to avoid accidents
  ProdSG- Act on making products available for the market
  2014/35/EU Low voltage regulation
  2014/68/EU Pressure Vessel regulation (i.n.)
For certification: Information guide „Manufacturing and operation of equipment designed for research purposes”, CE conformity and workplace safety, BGI/GUV-I 5139 E
Development
Production
Assembly
Commissioning
Operation
Permission in reference to Radiation Legal authorization
Notes: Equipment and Product safety Act

## Slide 4: Development and Management Tasks
Physical solution
Technical solution
Function
Operation
Management of documents
Classification
Management of approval and changes
Integrated product development
Configuration management
Management of variants
Project management
Management of product structure
Product lifecycle management
prove of planning
change management
prove of installation space
check of practicability of parameter
check of physical dimensioning
structuring of data model for product
check of plausibility of the simulations
check of necessary prototypes
confirmation for planning of beam lines
structure of product model known and plausible?
definition of connecting and feeding components
definition of interfaces
check of requirements by components on the system
prove of compatibility of the component to the system
check of realization of the requirements in the design
takeover of additional information about the components
check for mount ability
planning of quality assurance during production
prove of interfaces
as built documentation
reports of quality assurance
analyses for completeness
allocation of identifiers for components
operation plan
risk analyses
certification
preparation of assembly documentation
verification of assembly results
documentation of modifications
verification of component identification
proving of interfaces
manuals
verification of manuals
documentation of modifications
verification of requirements on the system
documentation of deviations
documentation of modifications
recording of operation modi
check of spare parts
documentation of operation

## Slide 5: Lessons learned
Definition of physical and technical requirements in context of system design as early as possible
Describing requirements in specifications and draft models
Conceptual design review (CDR) with model for checking of solution, checking of data integration, checking of interfaces, draft for documentation
Final design review (FDR) checking of data integration, checking of content incl. tolerances
First of Series (FoS): aim: no planned modification of design, only for checking if the design contains mistakes

## Slide 6: Main tasks
Minimize development costs
Development costs = Physical development + Technical development
Physical development = Parameter table and specifications
Technical development = DMU + specification drawings
Costs calculations while development and design process
Checking integrity of models in comparision to GSI/FAIR CAD-system
Minimize assurance costs
Using checklists
Checking solutions as early as possible in comparison to the defined requirements
Establish checking procedures for all components for CDR, FDR, FAT
Minimize production costs
Development of production documents in reference to minimize the costs for material and production
Checking drawings to avoid mistakes during production
Reuse of components to minimze production costs
Minimize assembly costs
Participation of all involved departments in the development of the components
Implementation of experiences of previous projects
Reuse of components to develop a common knowledge

## Slide 7: Technical Guidelines
Technical guidelines have to be seen:
As a collection of technical data that are used in GSI
As an intentionally written guideline and not as specification
In order to take into consideration the technical know-how
As information about for instance basic equipment of GSI/FAIR
As starting point for general standardization at GSI.
Content and Structure:
Technical guidelines:
Are part of the specifications as common approved information
Are used for knowledge management
Combine knowledge of different subject domains with technical solutions
Are a collection of best practice experiences
Are generally available
+ register with keywords
since 2005

## Slide 8: Model of Product data
Model of product
Product definition
f.i.
Product structure
Description: dip13_0
Drawing no.: FT-BEMH-ZU-0000055
CID: 07-00001-040-4
Representation of product
f.i.
technical calculations
FEM-Model
production programms
parameter tables
Presentation of product
adapted figure after : Aderl, Trippner, Step, Teubner Verlag Stuttgart, 20000

## Slide 9: From Physical to Technical Solution
Civil construction
Transfer of the physical solution into technical requirements:
Choosing the active principle for realization of function
Positioning of the function in the system (Ion optical Layout)
Definition of necessary space of the function
Definition of necessary media
Adaption of requirements from product life-cycle
IOL(Step)->CATIA SAP
Installation space for components
Requirements from product life-cycle
Specifications
Maintenance
Alignment
Emergency scenario
etc.

## Slide 10: Testing of Technical Solution
Contribution partner
WPL+SPL+QA+ Contribution partner
DMU+WPL+SPL+ corresponding specialists
DMU + WPL+QA
Contribution partner
1st step:
Conceptual design review
(CDR)
Specifications
Quality of product model
Quality of model structure
Feasibility of data exchange
Check of interfaces
Check of mechanical representations of physical items
Draft of QA-Plan
Draft of documentation
Fit to installation space
etc.
Checklist
not ok
ok
Checklist
Contribution partner
3D-model
DMU+WPL+SPL+ QA+ corresponding specialists
2nd step:
Final design review
(FDR)
Checklist
ok
DMU+WPL+SPL+QA+ corresponding specialists
1st step:
Conceptual design review
(CDR)
Checklist
ok
not ok
PDM
(CATIA/SAP, Archiv)
QA-Plan, Drawings, CID
3rd step:
Factory acceptancetest
(FAT)
QA-Plan
WPL+SPL+ QA+ Contribution partner
4th step:
Site
acceptance test
(SAT)
QA-Plan
not ok
ok
DMU-Digital Mockup
WPL-Work package leader
SPL- Subproject leader
QA- Quality assurence
CID- Component Identification no.
EDMS- Electronical data management (CERN)
EDMS
EDMS
EDMS
EDMS
EDMS
EDMS
Assembly
DMU
not ok
ok
EDMS

## Slide 11: CAD Integration
CATIA/SAP
Enterprise connector (Enco)
Inventor
Mechanical desktop
Solid Edge
Solid Works
STEP
Solid Edge
STEP/DXF, PDF
CATIA/SAP
Enterprise connector (Enco)
Inventor
Mechanical desktop
Solid Edge
Solid Works
STEP/DXF, PDF
Catia
Scenarios for CAD data creation, implementation and use
Archive for drawings
Archive for drawings
mostly no PDM-System
mostly no PDM-System
EDMS
EDMS
Assembly instruction
Maintenance instruction
Assembly drawing
input Catia /SAP
Beamline drawing
Auxiliary device drawing
Pre-Assembly drawing
EDMS
Installation preparation

## Slide 12: Testing of Technical Solution
Combination of 3D-models from different sources to one common overview
DMU
Proof of:
Completeness of product structure
Interfaces
Installation scenarios
Maintenance scenarios
Emergency scenarios
Development of models for beamlines as basis for:
Interface drawings
Drawings for installation
Digital representations as basis for installation and maintenace
A basis for simulations for remote manipulation of radioactive components
Combination of:
Models of different sources like civil construction, GSI and contribution partners
3D-Scans with CAD-Models as As-built-documentation

## Slide 13: Conclusions
Defining requirements of components in reference the needs of Systems Engineeing as early as possible
Definition of common product structures as basis for product management
Definition the conditions for data transfer
Common definition of design results
Definiton of roles for mutual information (following also processes of ISO9001)
Definition of approval procedures
…

## Slide 14
Thank you for attention!
Questions?