FAIR Challenges - Cover
FAIR Accelerator Facility Control:
Semi-Automation & Beam-Based Feedbacks
D. Ondreka,
Ralph J. Steinhagen
ARIES Accelerator Performance and Concept Workshop, 10th December 2018
Flemings Hotel, Frankfurt am Main, Germany
UK
Sweden
Slovenia
Finland
Russia
France
Germany
India
Poland
Romania
[Speaker Notes: Thanks for the introduction and thanks to the organisers for the invitation and the opportunity to present some of the beam dynamics, instrumentation and control highlights related to FAIR.]

---
Setting the Scene….
- FAIR ~4 x the size of existing GSI facility
  - non-linear operational complexity increase O(n2) → O(n5)
  - efficiency scalling εFAIR = εUNILAC·εSIS18·εSIS100·εSuper-FRS·εCR·εHESR· ...
- parallel operation of 5-7 distributed experiments
  - lasting typically only 4-5 days, few long-runners
  - large potential for cross-talk between users especially while setting-up
  - world-wide unique requirement: facility and key beam parameters reconfigured on a daily basis
    - energy, ion species, intensity, extraction type/length, …
- new challenges w.r.t. GSI:
  - operating beyond present beam parameter envelope, x10-100 higher intensities, x10 higher energies → machine protection & losses/activation become an important issue
  - high-intensity and higher-order feed-down effects require machine and beam parameter control well below the sub-percent level →beyond feed‑forward‑only (open-loop) modelling and machine reproducibility
  - need to operate FAIR with reduced skeleton crew consisting of only ~5‑6 operators (nights & weekends)
    - minimise putting unnecessary stress on crews ↔ ergonomics, human-centric design, (semi-)automation (this talk)

---
First Ingredient: Quasi-Periodic Operation I/II
Operation/Control Paradigm
Some important OP boundary conditions:
  1. Compared to GSI, FAIR facility size and complexity increases roughly by a factor 4
  2. Expect some improvement but 'Operator' & 'System Expert' will likely remain a scarce resource (N.B. ~5‑6 operators (nights & weekend) ↔ pool of ~35 operators)
One strategy option: 'One Operator per Accelerator Domain' vs. 'One Operator per Experiment':
Q1
UNILAC
SIS18
SIS100
SuperFRS
CR
CR
Q2
pLinac
SIS18
SIS100
p-Target
CR
HESR
UNILAC
SIS18
SIS100
Q3
CBM
UNILAC
SIS18
SIS100
Q4
APPA
UNILAC
SIS18
Qn
ESR etc.
Operator #1
Operator #2
Operator #3
Operator #4
Operator #1
Operator #2
Operator #3
Operator #4

---
First Ingredient: Quasi-Periodic Operation II/II
Beam-Production-Chains
Periodic beam patterns, dominated by one main experiment	– change every two weeks, some run for 2-3 days only:
FAIR Operational Challenge:
presently: 2 shifts for setup of 2 accelerators→ FAIR target: 1-2 shift(s) for setting up 5 accelerators + tighter loss control
Main strategy/recipe to optimise 'beam-on-target':
quasi-periodic cycle operation: limit major pattern changes by construction ↔ beam schedule planning (tools)
minimise overhead of context switches → smart tools, procedures & semi-automation, e.g. beam-based feedbacks, sequencer, …
courtesy D. Ondreka
SIS18
SIS100
Unilac
CBM + RIB ext. target (U73+) + AP (LE)
SIS18
SIS100
Unilac
ESR
RIB ext. target (U28+) + ESR
AP + RIB ext. target (U28+) + Biomat
SIS18
SIS100
HESR
Unilac
SIS18
SIS100
Unilac
ESR
RIB ext. target (U28+) + ESR
SIS18
SIS100
Unilac
CBM + RIB ext. target (U73+) + AP (LE)
AP + RIB ext. target (U28+) + Biomat
SIS18
SIS100
HESR
Unilac
[Speaker Notes: To give you a flavour of some of the parallel operation scenarios Depending on the individual experiment requirements we may need to switch between these patterns several times per day. We presently operate the combination of UNILAC and SIS18 with a beam-on-target figure of about 70% which is acceptable for such a small facility. With many of the experiments moving from SIS18 to SIS100 we need to improve this to maintain the same efficiency. Thus our main strategy for the time being is to 1. minimise the number of changes by design through grouping the right experiments already during the accelerator scheduling phase using smart tools, and to 2. minimise the overhead and speed at which these pattern changes can be performed. Here the use of smart tools, procedures & semi-automation, e.g. beam-based feedbacks and sequencer will hopefully the key to success.]

---
Second Ingredient: (Semi-)Automation
and Beam-Based Feedbacks at FAIR
… for efficient operation and commissioning → optimise routine task so that operation crew talents are utilised/focused on more important tasks that cannot be automated
Focus priorities on systems that have a big impact on setup, tracking and optimisation:
  - ‘biggest bang-for-the buck’ or ‘low-hanging-fruits’*:
    - ie. systems that are best understood, require least effort/know-how to integrate/implement
  - operationally critical or hard to achieve by-hand:
    - e.g. slow-extraction spill control, slow trajectory/focus drifts of beam-on-target
  - mitigating drifts that are driven by feed-down effects due to higher-order parameter tuning: e.g. orbit, tune
  - ...
Examples:
- beam-transmission-monitoring and other actual-vs-reference monitoring systems → identify, localise and fix failures/near‑misses as early as possible
- semi-automated multi-turn/optics/slow-extraction monitoring/correction/… setup tools → improve facility turn-around and setup times
- classic beam-based feedbacks on trajectory, orbit, tune, chromaticity, etc. → monitor and maintain tight parameter tolerances
- Sequencer taks – automation of tasks not yet covered by other routine tools → big time saver for large‑scale equipment acceptance/integration tests, recommissioning, or dry-runs
  - N.B. thousands of FAIR devices & machine proction systems that need to be periodically retested/validated

---
Beam-based Cycle-to-Cycle feedbacks
Generic Beam Control (focus on use-case)
1. Transmission Monitoring System
2. Orbit Control
Trajectory Control (threading, inj./extr., targets)
Q/Q'(') Diagnostics & Control
TL&Ring Optics Measurement + Control (LOCO, AC-dipole techniques etc.,)
1. RF Capture and (later) RF gymnastics
2. Longitudinal Emittance Measurement
3. Transverse emittance measurement
4. Transverse and longitudinal feedbacks
Machine-specific Beam-Based Systems:
- SIS18: multi-turn-Injection (N.B. highly non-trivial, complex subject), Slow-Extraction (K.O. exciter, spill‑structure, …)
- SIS100: Slow-Extraction (K.O. exciter, spill‑structure, …), RF Bunch Merging and Compression
- ESR, HESR & CR: Stochastic cooling, Schottky diagnostics, …, tbd.
Generic:
- Remote DAQ of Analog Signals	(strong impact on HKR migration/operation!)
- Facility-wide fixed-displays, facility & Machine Status (“Page One”)
- context-based monitoring of controls and accelerator Infrastructure,
Bread-and-Butter
systems for operation

---
Some notes on implementation
- Real-World challenges of FB & (semi-) automation: (hint: usually control theory or beam physic isn’t the problem)
  - not necessarily speed (ie. kHz → GHz range) – second-scale feedbacks or tools are often already quite sufficient for >90% of the problems
  - Computers are better than humans for repetitive/quantitative tasks, however: FBs are essentially only as good as
    - beam- or machine-parameter measurements they are based-upon
    - integration into the controls & operation environment and exception handling
      - interfaces, interfaces, interfaces….
      - long-term maintenance, upgrades, adaptations, ...
    - developer skills that needs to cover multiple domains: acc. HW, BI, RF, Controls, machine modelling, beam physics, …
    - overall strength depends on the reliability of the weakest link in the chain

---
Cycle-to-Cycle Orbit-FB Proof-of-Concept
B. Schlei, H. Liebermann, R. Steinhagen
H
Orbit-FB 'off'
Orbit-FB 'on'
(deselected faulty BPM:
GS07DX)
V
- some workarounds needed, but overall success and results look promising
  - need to follow-up: reliability, performance issues related to CO & BI + detailed integration before being put into regular operation
  - N.B. remaining horizontal oscillation due to uncorrected Δp/p mismatch → radial-loop/Energy-FB
position [mm]
time

---
Cycle-to-Cycle Macro-Spill-FB Proof-of-Concept
R. Steinhagen, H. Liebermann
reference
dN/dt spill rate
- some workarounds needed, but overall success and results look promising
  - need to follow-up: K.O. exciter power-limitation handling (easily for >10 Tm operation)
    - Alternative: FB using fast extraction quadrupole or main-quads
  - Desirable: direct FB signal from experimental detectors
animated GIF - link
Fill-to-Fill
FB on dN/dt
(DCCT-based)

---
Higher-Order Beam Parameter Stability
Example: LHC Tune Feedback Operation
- Tune-FB driving and accelerating early commissioning in 2009-2011
  - tunes kept stable to better than 10-3 for most part of the ramp and squeeze
- even though perturbations were unrelated to quads, feedback helped mitigating these feed-down effects while allowing OP crews to work on other more pressing issues … (N.B. BBQ instrumentation was key-ingredient to success)
reconstructed tunes with FF only
actual tunes
reconstructed bare tunes

---
Higher-Order Beam Parameter Stability
Example: Feedback Integration and Operation at LHC
- Most accelerator facilities: stability of actual observable became secondary
- trims become de-facto standard to assess the FB and machine performance and to improve machine modelling (done off-line)
Orbit-FB &
Radial-Loop
Trims (μrad)
Tune-FB trims
injection
flat-top
ramp
Q'(t)-FB trims
Energy (TeV)
Q'(t) not used on a day-to-day basis
β*-squeeze

---
FAIR Archiving System
https://edms.cern.ch/document/1176039/
… collect and store all pertinent accelerator data centrally to facilitate the analysis and tracking of the accelerator performance as well as its proper function.
- Combined Archiving and Post-Mortem storage concepts
- Aim at storing maximum reasonable amount of data
  - facilitates data mining (performance trends, rare failures, …)
  - key to understanding and improving accelerator performance
  - also: use feedback action to improve machine model (data mining)!
Post-Mortem
Archiving
N.B. importance: quantitative accelerator performance and bug/fault-tracking indicators

---
Digitization of Analog Signals at FAIR
https://edms.cern.ch/document/1823376/
traditional/old concept (underlying assumption: scopes/digitizers are expensive, RF switches are cheap)
targeted concept (underlying assumption: scopes/digitizers are cheap, RF switches are expensive)
~10 €/m
(short)
250-500 €/ch.
2-3 k€/ch.
200 -1000 €/ch.
~ 200 €/ch.
~10 €/m
(long)
device #1
Front-End
(FESA, C++)
device #1
digitizer
device #2
device #2
digitizer
~ 0.5 k€/ch.
...
...
Front-End
(FESA, C++)
device #(n)
device #(n)
ethernet
~ 10 MB/s
digitizer
Front-End
(FESA, C++)
2-3 k€/ch.
device #(n+1)
Front-End
(FESA, C++)
device #(n+1)
digitizer
...
...
Controls/
Operation
device #(n+m)
Front-End
(FESA, C++)
device #(n+m)
digitizer
start deployment ≥2018 (SIS18), crucial for:
migration to new FAIR Control Centre (FCC),
optimisation of commissioning & operation
automated tracking/isolation of faults (↔ post-mortem)
less-biased performance indicator
link: more details
on-demand measurement
(selected signals, error-case, …)
con:
high-reconfiguration overhead (manual)
limited test-coverage, trending
permanent monitoring
(error-case, trending, interlocks, beam-based feedbacks, …)
Controls/
Operation
RF Switch
BLL: Brain-Locked-Loop
Not routinely connected
(only error case)
flexible
grouping option
feedbacks

---
Digitization of Analog Signals at FAIR
Example: SIS18 Machine Status

---
Beam Transmission Monitoring (BTM)
https://edms.cern.ch/document/1823362/
transmission
beam instabilities, aperture constraints, slow beam parameter drifts
→
activation & machine protection
dynamic vacuum, ε-blow-up/tails,
slow-extraction, ...
→
cryo- & beam-halo collimators,
rad-hard magnets, extra shielding, ...
avoidable losses
(ALARA: should minimise before MP & Activation limits kick in)
less-avoidable losses
(may need to accept a given amount)
§§ Radiation Permit – limits on total dose per year (facility & external)
color white {{ dN_{collimator}(t) } over { dt }}
controlled losses
Fast current transformer (FCT)
DC current transformer (DCCT)
DCCT
/FCT
counter
I_{source}(t) = { dN_{source}(t)} over { dt }
Ion-Source
I_{target}(t) = { dN_{target}(t) } over { dt }
Experiment
primary (secondary)
ions-on-target/s
{ dN_{loss}(t) } over { dt }
un-controlled losses
online dosimetry (abs. reference)

---
FCC Fixed-Display & Workstation Layout
Information Density Hierarchy (↔ BTM Concept)
Information Density/Level of Detail
courtesy Achim Bloch-Späth
courtesy Achim Bloch-Späth

---
Transverse (horizontal) multi-turn injection
SIS18 Multi-Turn Injection (H-Phase-Space Painting)
Y. El-Hayek, S. Paret
From a linac
e.g. SIS-18, CERN PSB
courtesy Mike Barnes
Injection losses → dynamic vacuum pressure rise
(highly complex: easy to simulate ↔ hard to measure/tune with beam)
looking forward to: injection steering (BPMs) & turn-by-turn profiles (IPMs)
Simulation: with space charge
septum
Simulation: without space charge
septum
anode
(wires)
cathode
300 kV
SIS electrostatic injection septum
Measured MTI performance in SIS-18
Trev=5 μs
≈20 turns
[Speaker Notes: One of the first possible loss-mechanism is related to the multi-turn injection at the SIS18. By design SIS18 is filled up to or at least close to the mechanical acceptance of the machine using a horizontal multi-turn phase-space painting technique. The trick or goal is to fill the ellipse as dense as possible without causing an overlap with the injected beam emittance which would trigger losses and degradation of the beam vacuum. Now what complicates the setup is that the injected beam is further smeared out by space-charge effects, illustrated by this plot, and that up-to-now there is no direct online measurement of the profile or tails to tell whether there is still ample space or too tight packing. While these effects are easy to simulate, they are hard to measure or to optimise with beam. Presently, the primary diagnostic that is used until now are the beam current transformer and loss monitors. However, there are many parameters such as injection errors, Q/Q' errors, beam tails etc. that could affect these two observables equally. We have high-hopes, that in the future we can use also the BPMs more systematically to adjust the injection steering directly, and to check the phase-space stacking with the new turn-by-turn IPM that is to be installed for the next SIS18 restart.]

---
Slow Extraction from SIS-100
Intense Heavy-Ion Beams for NuSTAR & CBM
Optics, Q/Q'('',''') drive uncertainties on slow-extraction performance
→ remedy: control of the machine optics, Q/Q', linearisation prior to s.e., …
(highly complex, a lot of work ongoing)
Q, Q', ..
SIS18 Septum wires: Ø 0.1 mm
(W-Re alloy, mounted under tension)
(radiation resistant
warm magnets)
QD
QF
es. septum wires
mag. septum
Ion
Energy
N/s
spill
Power
U
28+
1.5 GeV/u
5E11
> 1 s
10 kW
Tracking simulations:
5 % (approx. 500 W) loss in the septum wires
U92+ beam loss in warm magnet > 5 W/m
Non-trivial machine protection:
protection of septa wires
down-stream absorbers setup
activation minimisation
angle
phase
orbit
seperatrix
[Speaker Notes: The counter-part of the multi-turn injection is the resonant slow-extraction which is important for both SIS18 and SIS100. Also similar to the mutli-turn injection this effect is much easier to simulate than to control in real-world applications. In most cases and most proton machines the extraction is setup by applying the design optics settings and optimised qualitatively by looking at the extraction efficiency and losses at the electro-static septa. This wouldn't be so dissimilar for high-intensity ions if the impact of ion losses onto the wires wouldn't be as severe. For the same energy, ions deposit orders of magnitude more energy than protons and are thus much more likely to destroy the septa wires. This obviously implies a good control of losses using absorber blocks down-stream of the electro-static wires as well as beam and optics parameters. The setup is done obviously first with low-intensity beams but this arbitrarily twiddling of beam parameters may be less than optimal. Thus we have high-hopes that we will be able to optimse this process by a systematic, more quantitative approach of controlling the optics, Q/Q' and other parameters that drive the slow-extraction performance. However, similar to the multi-turn injection, we'd all ideally like to be able to measure and map-out the phase-space diagram directly to have a direct one-to-one relationship between beam observable and control knob that drive the slow extraction performance.]

---
Sequencer Framework
Semi-automated Tests for HW and Beam Commissioning
 HW and beam commissioning require efficient tools for testing
- perform initial and acceptance tests, early detection of non-conformities and faults
- perform QA and regular re-validation tests
- considering size and complexity of FAIR, and limited resources:
  efficient and reliable execution and documentation of tests
 → Development of a Sequencer framework, as a core part of the FAIR control system to aid semi-automated testing
Sequencer architecture conceptually divided into:
- middle-tier sequencer service (run sequences,
  generate automated reports)
- the sequences with a subset of tasks (testing steps)
- graphical user interface (GUI) program
Operational experience so far:
- was tested and used already since Dry-runs in 2017
- establish process of writing Sequencer tasks parallel
  to development (in progress)
Sequencer GUI impression

---
Summary
- FAIR ~4x the size of GSI,
  - non-linear operational complexity increase O(n2) → O(n5)
  - 5-7 parallel experiments + typically lasting only 4-5 days → world‑wide unique requirement: reconfigure facility on a daily basis
  - new challenges w.r.t. GSI:
    - x10-100 higher intensities, x10 higher energies → machine protection & losses/activation become an important issue
    - high-intensity and higher-order feed-down effects require machine and beam parameter control on the sub-percent level →beyond static feed‑forward (open-loop) machine modelling and machine reproducibility
    - have to be able to operate FAIR with reduced OP skeleton crew of ~5-6 operators → minimise unnecessary stress on crews
- Beam-Based feedbacks and (semi-)automated setup tools are key ingredient for efficient operation and commissioning → optimise and automise routine task so that OP talents are utilised/focused on more important tasks that cannot be automated
  - actual-vs-reference monitoring system → identify, localise and fix failures/near‑misses as early as possible
  - classic beam-based feedbacks → monitor and maintain tight parameter tolerances
  - semi-automated setup tools → improve facility turn-around and setup times
  - Sequencer to automate tasks not yet covered by other tools → saves on tedious revalidation and conformity checks
- Real-World challenges of feedbacks & (semi-) automation
  - not necessarily speed – FB & tools operating on second-scales already quite sufficient for >90% of the problems
  - Computers are better than humans for repetitive/quantitative tasks but overall strength depends on the reliability of the weakest link in the chain (instrumentation, integration into controls/OPs, developer, ... )

---
GSI to FAIR Transition
GSI 3 → FAIR 8½ (11+) accelerator(-like) machines
p-Linac
SIS 18
SIS100
SIS 300
UNILAC
EH
EX
FRS
APPA
p-bar
SFRS
CBM
existing:
3 Ion-Sources
1 LINAC
1 synchrotron + 1 storage ring
13/7 transfer-lines (MEBT / HEBT)
3 experimental areas
ESR
CR
NESR
Cry-
Ring
HESR
(PANDA)
FLAIR
new:
1 proton source + linac
4 synchrotrons & storage rings
18 (26) transfer-lines
4 (5) experimental areas
MSV 0-3
MSV 4-6

---
Accelerator Experience & Efficiency
1995-2016: U. Scheeler, S. Reimann, P. Schütt et al.
constant
~ 75 ± 5 %
long-running “static”
experiments
Many || experiments
re-configuration ~ 1-2 weeks
→ FAIR base-line
*
Based on: U. Scheeler, S. Reimann, P. Schütt et al., “Accelerator Operation Report”, GSI Annual Scientific Reports 1992 – 2015 + 2016 (D. Severin)
https://www.gsi.de/en/work/research/library_documentation/gsi_scientific_reports.htm
N.B. ion source exchanges are factored out from UNILAC & SIS18 data (~ constant overhead)
Availability: experiments + detector tests + machine development + beam to down-stream accelerators;
Down-time: unscheduled down-time + standby; Operation: accelerator setup + re-tuning
* 2018 operation limitations:
only ½ UNILAC (w/o A3 & A4)
only 1 element in SIS18
Therapy Operation
(different accounting)

---
Accelerator Experience & Efficiency
or: .. how to move/transform accelerator operation from 3 (GSI) → 9 (FAIR) machines
bottom line (1st order):
an ‘average’ GSI/FAIR experiment lasts about 5 days
FAIR will accommodate about 5-6 parallel experiments
→ expect:
setup of new beam-production-chain (BPC) about once per day
longer BPCs (↔ number of sequential acc.) → larger complexity

---
FAIR Challenges & Constraints
… SIS18 Operation Experience & Efficiency
Beam-on-Target figure of merit (FoM) of ~75% → FAIR-BoT (efficiency εFAIR):
today
+ new operational challenges:
operating beyond present beam parameter envelope, x10-100 higher intensities, x10 higher energies → machine protection & losses/activation become an issue
“… have to improve!”

---
Control System Architecture Stack
Not exhaustive...
Control System Architecture Stack
Not exhaustive...
Presentation
Tier
Middle Tier
powerful servers
Resource Tier
FESA
???
Standard 3 tier model; distributed OO system
Modular design with well defined interfaces

---
Controls & FC2WG Topics
– more than “Control System” & Data Supply
primary aim: provide tools, extensions to, and integration of the existing basic technical system to ensure a swift, efficient commissioning and control of the accelerator facility
- Facility & Interface Analysis
  - Procedures: Hardware Commissioning (HWC), HWC-'Machine Check Out', Beam Commissioning (BC), BC-Stage A (pilot beams), BC-Stage B (intensity ramp-up), BC-Stage C (nominal/production operation) Beam parameters, FAIR performance model, optimisation, Accelerator & Beam Modes
- Beam Instrumentation & Diagnostics – System Integration (into operation and controls environment)
  - Intensity (DCCTs) & beam loss (BLMs) → Beam Transmission Monitoring System (BTM), trajectory & orbit (BPMs), Q/Q', optics (LOCO & phase-advance), longitudinal & transverse emittance (FCTs, WCM, screens, IPM, etc.), Δp/p, long. bunch shape (FCTs, Tomography), abort gap monitoring, ...
- Accelerator Hardware – System Integration (into operation and controls environment)
  - Power converter, magnets, magnet model, RF, injection/extraction kicker, tune kicker/AC-dipole, beam dump, collimation/absorbers, cryogenics, vacuum, radiation monitoring, k-modulation, technical infrastructure (power, cooling/ventilation), machine-experiment interfaces
- Control System
  - Archiving system, acquisition/digitization of analog signal , test-beds, timing, bunch-to-bucket transfer, cyber security, role-based-access, middleware, real-time & cycle-to-cycle feedbacks, daemons
- Components
  - post-mortem, management of critical settings (safe-beam settings), machine protection, interlocks, beam quality checks, daemons, 'facility status display', aperture model, ...
- Applications
  - Sequencer (semi-automated test/commissioning procedures), fixed-displays, ...
  - Beam-Based Applications & GUIs
topic started
topic active
topic not started